## Slide 1: Seismically Isolated Structures
Disclaimer
PRINCIPLES AND BACKGROUND
William McVitty, P.E., M.S., Andrew Taylor, S.E., Ph.D.
Notes: Graphic shows cover of the NEHRP Provisions FEMA P-1052.
The 2015 NEHRP Recommended Seismic Provisions are a new resource document that facilitates and translates the state-of-the-art knowledge into design practice. To help in understanding these new Provisions, design examples are also published which apply the new requirements of FEMA P-1051. This presentation complements the Chapter 15 design example of a seismically isolated building.
This set of instructional slides is the first of two 90 minute presentations. The first presentation provides information on the basic principles of seismic isolation and background on both the current and new seismic design requirements.

## Slide 2: Presentation Objectives
Present an overview of the design requirements with background on major revisions
Present basic principles of seismic isolation: What?, Why?, Where?, How?
Notes: A graphic shows the cover of the document FEMA P-1050-1, 2015 Edition, “NEHRP Recommended Seismic Provisions for New Buildings and Other Structures”
The objective of this presentation is to first describe the basic principles of seismic isolation. What is it? Why should you isolate a building? Where does isolation work well and not so well, and finally how it is applied in a real-life example with discussion on the types of isolation systems. The second part of the presentation gives an overview of the layout and content of the design requirements and gives background of some of the major changes recommended by the NEHRP Provisions.

## Slide 3: Basic Principles What is seismic isolation?
A flexible, sliding or rolling horizontal interface between the structure and the ground.
This interface lengthens the period of the structure away from dominant earthquake frequencies and is complemented with the ability to absorb energy.
Notes: The basic concept of seismic isolation (also referred to as base isolation) is to “de-couple” the “superstructure” (structure above the isolation interface) from potentially damaging ground motions by adding “seismic isolators” which support the structure above while permitting large relative horizontal displacement of the structure in an earthquake. The seismic isolators de-couple response from dominate short-period earthquake shaking by essentially making the fundamental-mode period of the isolated structure a couple of times longer than the period of the structure above the isolation system – that is, longer than the period of the same structure on a fixed base. In this manner, the large displacement of the isolation system gives a reduction in force in the structure above the isolation system. The ability of the isolators to absorb energy (or increase damping) further improves performance.

## Slide 4: Basic Principles What is seismic isolation?
Reference: Patent US 99973 A
Improvement in 150 years?
Capability to execute it using isolation hardware that exhibits reliable and predictable behavior over the lifetime of the structure
Not a new concept:
Notes: A figure shows a drawing from a United States Patent, No 199973, dated February 15, 1870, and issued to J. Touaillon. The drawing shows an elevation of a two-story masonry building, resting on top of a seismic isolation system. The seismic isolation system is also shown in the figure, and it consists of iron or steel ball bearings situated between two spherical depressions in iron or steel plates. The plate on top of the ball bearing has spherical depressions facing down, and the plate on top has spherical depressions facing up. The diameters of the spherical depressions are about twice the diameters of the steel ball bearings.
The concept of seismic isolation is not new and has not changed in the past 150 years, if not longer. The first US patent was in 1870 by Jules Touaillon and was a double concave spherical-ball rolling system. What has changed is our capability to execute the concept using isolation hardware which is more reliable and whose behavior can be predicted with a reasonable degree of accuracy.

## Slide 5: Basic Principles What is seismic isolation?
Reference: DIS Inc. with edits
Modern seismic design approaches: Fixed-base building:
Inelastic action occurs over the height of the building
Allow damage in many controlled areas
Notes: The figure shows an elevation of a fixed-base (as opposed to base isolated) moment frame building, five stories high and three bays wide. The frame is shown in the laterally displaced, or “swayed” position, pushed to the right. Red dots at the ends of most of the moment frame beams show the formation of plastic hinges in the beams at beam/column joints. The figure notes state “Allow damage in many controlled areas” and “Inelastic action occurs over the height of the building.”
In order to have economical designs with a low probability of collapse, the approach for fixed-base buildings is to design and detail for ductility (or damage) to occur in many, specifically located areas over the height of the structure. This ductility gives damping and also “softens” the building (changes the lateral stiffness) so that an abrupt and catastrophic failure has a low chance of occurring. However ductility also results in damage to the structure which requires repair or full replacement after an earthquake.

## Slide 6: Basic Principles What is seismic isolation?
Reference: DIS Inc. with edits
Inelastic action and displacement concentrated in a single level
Protect the structure by using an “engineered soft-story”
Modern seismic design approaches: Isolated building
Notes: The figure shows the same building as in the previous slide, but the building is now resting on top of a seismic isolation system. The building frame remains vertical, while the seismic isolation system is shown displaced to the right, indicating the seismic isolation system has absorbed most of the lateral ground displacement. There are no red dots at the end of any beams, illustrating that there is no inelastic response in the superstructure; all inelastic response occurs in the seismic isolation system. Figure notes state “Protect the structure by using an “engineered soft-story”” and “Inelastic action and displacement concentrated in a single level”
Conversely, the design approach for seismically isolated structures is to protect the buildings components and contents above the isolators by introducing an “engineered soft-story”. This is usually a single level at the base of the structure which has a much lower lateral stiffness than other levels. This “soft-story” is where most of the earthquake displacement and energy dissipation occurs. Furthermore, the inelastic action occurring in the isolation system is usually temporary and recoverable, whereas in a fixed-based building the inelastic action gives damage to the point where, as demonstrated in Christchurch 2011, it is unfeasible to repair.

## Slide 7: Basic Principles What is seismic isolation?
The effects of period lengthening and energy absorption:
Are best illustrated using acceleration and displacement response spectra. But what is a response spectrum?
Notes: There are two fundamental aspects of seismic isolation: period lengthening and damping. These two effects are best illustrated using a response spectrum. But how is a response spectrum created and what is it showing? The next few slides will help to answer these questions.

## Slide 8: Basic Principles What is seismic isolation?
A response spectrum is a plot of the maximum response (i.e. acceleration, displacement) of a family SDOF oscillators when that family of oscillators is subject to the same earthquake record.
Notes: We can think of a response spectrum is a way of showing how a range of different structures (heavy or light, and stiff or flexible, and high or low damping) will perform to a given excitation, such an earthquake. In more technical terms, a response spectrum is a plot of the maximum response (we are most familiar with acceleration, but can also be displacement or velocity) of a single-degree-of-freedom (SDOF) system when a range of different systems is subjected to the same excitation.

## Slide 9: Basic Principles What is seismic isolation?
Reference: A.W. Taylor
Acceleration response spectrum - Single earthquake
Notes: The figure shows three items: The first item at the upper left is an example earthquake response spectrum, with the horizontal axis labelled “Period, seconds”, running from 0 to 4 seconds, and the vertical axis labelled “Spectral Acceleration, g’s”, running from 0 to 2.5 g’s. The second item at the upper right is the acceleration response of a single-degree-of-freedom (SDOF) oscillator when subjected to the example earthquake, with the horizontal axis labelled “Time, seconds”, running from 0 to 25 seconds, and the vertical axis labelled “Acceleration, g” with no numerical scale shown. The third item located at the bottom center is a SDOF oscillator, consisting of a flexible rod fixed at the bottom end, with a lumped mass attached to the top end. This SDOF oscillator is labelled “Oscillator #1, Period T1”. An arrow points from the oscillator to the horizontal scale on the upper left response spectrum, at a period of 0.2 seconds. Another arrow points from the upper right accelerograph, beginning at the point of maximum recorded acceleration at about time 10 seconds, labeled “Max. = 2.1 g”, and pointing to the point on the response spectrum plot corresponding to 0.2 seconds on the horizontal scale. This arrow is labeled “Plot Maximum Response.”
When subjecting one SDOF oscillator, with given period (which is a function of its mass and stiffness), to a single earthquake, you will get a acceleration response plot as shown in the top right. From this we can simply take the maximum acceleration of the whole record and plot one point on the response spectrum (i.e. for period T and maximum spectral acceleration in g’s), which is indicated in the left figure. This whole process is then repeated for a number of different SDOF oscillators (with different periods). The many points on the response spectrum, which represent the many of different SDOF oscillators, can then be connected by a jagged line which forms the acceleration response spectrum for this single earthquake record.

## Slide 10: Basic Principles What is seismic isolation?
Acceleration response spectra - Several earthquakes
Notes: The figure shows an earthquake response spectrum plot with the horizontal axis labeled “Period, seconds” running from 0 to 4 seconds, and the vertical axis labeled “Spectral acceleration, g’s” running from 0 to 4 g’s. On the graphs are shown four earthquake response spectra with irregular shapes. The graph is titled “Acceleration response spectra – Several earthquakes”
The process in the previous slide can be repeated for several earthquakes. Here there are four different response spectrum’s for four different earthquake records. Note that they are rather variable, but we can start to see a trend forming.

## Slide 11: Basic Principles What is seismic isolation?
Dominant earthquake motion
Typically a reduced acceleration for long-period structures
Design acceleration response spectrum
Notes: The figure is the same as in the previous slide but one additional spectrum shown. This spectrum is not irregularly shaped, as the other spectra are, and it is labeled “”Smoothed” design spectrum from building code”. The remaining four spectra, which were shown on the previous slide, are labelled “”Jagged” spectra of actual earthquakes.” An arrow near the center of the graph, inclined downwards and to the right, is labeled “Typically a reduced acceleration for long-period structures.” A dashed-line box surrounds all of the spectra on the left side of the graph, over period range 0 to 1.25 seconds, and is labelled “Dominant earthquake motion”.
The general trend from actual recorded seismic events is that most of the energy is in the short-period/high-frequency range and hence short-period structures typically experience higher accelerations compared to long-period structures. The response spectrum used in design codes illustrates this finding and is a “smoothed” response spectrum of many individual earthquake records. No earthquake will ever look like this, but it shows the general behaviour of many earthquakes we have measured in the past.

## Slide 12: Basic Principles What is seismic isolation?
The response spectrum gives us a way to estimate the maximum response of a SDOF oscillator at a range of different periods.
Isolated buildings (and many other structures) exhibit a response that is dominated by their first oscillating mode – as if it were a SDOF oscillator.
Thus, by approximating an isolated building as a SDOF oscillator, the response spectrum can be used to estimate the maximum response.
Notes: So in summary, the response spectrum is simplified representation which is useful to estimate the behavior of seismically isolated buildings.

## Slide 13: Basic Principles What is seismic isolation?
Reference: DIS Inc.
Thus, looking at representative response spectra, what is the premise of seismic isolation?
Notes: The figure shows two graphs: an acceleration response spectrum on the left, and a displacement response spectrum on the right. In the left graph a horizontal arrow points to the right, labeled “Period Shift”. This arrow illustrates that acceleration response of the building is reduced as the period of the structure is shifted from low values (in the neighborhood of 0.5 seconds) to higher values (in the neighborhood of 2.5 seconds). The left graph also shows three different parallel acceleration plots, each plot for a different level of damping, showing that the acceleration response is decreased as damping is increased. On the right graph a horizontal arrow points to the right, labelled “Period Shift”. This arrow illustrates that displacement response of the building is increased as the period of the structure is shifted from low values (in the neighborhood of 0.5 seconds) to higher values (in the neighborhood of 2.5 seconds). The right graph also shows three different parallel acceleration plots, each plot for a different level of damping, showing that the displacement response is decreased as damping is increased.
The goals of seismic isolation is to elongate a buildings period and to also increase damping. The effect of this on the structures maximum acceleration and displacement is illustrated by these two characteristic response spectra.

## Slide 14: Basic Principles What is seismic isolation?
The flexible interface, when initiated by a major earthquake, shifts the period of the structure to a part of the spectrum which usually experiences lower accelerations.
Although there is an increase in displacements, this is concentrated at the isolation interface. The ability of the isolator to absorb energy (damping) reduces this displacement and further reduces accelerations.
Notes: This slide gives an explanation of the effects of period lengthening and energy absorption which were shown graphically on the previous slide.

## Slide 15: Basic Principles Why isolate?
Reference: Ron Hamburger
Earthquake intensity
Misconception: that code designed buildings are “earthquake-proof”
Buildings are primarily designed to be ductile = damage!
Notes: The figure shows four drawings of a simple two-story building, with each drawing illustrating a different level of earthquake damage. A large horizontal arrow, pointing to the right, appears below the four drawings and is labeled “Earthquake intensity.” The drawing on the left is labelled “Operational” and shows the building with no damage, and the lights on, indicating the building is open for business. The second drawing from the left is labelled “Immediate Occupancy” and shows the building without visible signs of damage, but the lights are off, indicating the building is not open for business. The third drawing from the left is labelled “Life Safety” and shows several cracks in the face of the building, the building sign is partially damaged, and the lights are off, indicating the building is not open for business and has sustained significant damage. The fourth drawing from the left is labelled “Collapse Prevention” and shows the sign has fallen from the building, the building has many large cracks, and the building is leaning to the right, indicating the building has sustained major damage and it is not occupiable.
We will now look at why we seismically isolate buildings. One common misconception by lay-people is that a building designed to the latest earthquake code is “earthquake-proof”. This misunderstanding was evident in Christchurch, New Zealand (which has similar codes to the USA) prior to the 2011 earthquake. Now people are well aware that the main intent of the code is life safety and damage is expected to occur in major earthquakes. Prior to 2011 there was only one base-isolated buildings in Christchurch, now with renewed awareness there are 14 isolated buildings completed or in construction.

## Slide 16: Basic Principles Why isolate?
Intent of the NEHRP Provisions:
  Avoid serious injury and life loss
  Avoid loss of function in critical facilities, and
  Reduce structural and non-structural repair costs where practicable
The degree to which these are achieved for different structural systems is highly variable.
Notes: The NEHRP Provisions describe the seismic-code performance objectives applicable in concept to all building types. The primary and minimum goal of the Standard is life-safety (avoiding serious injury and life loss). Minimizing the loss of function and economic losses is also envisioned, however the degree to which this is achieved is very different for a seismically isolated building vs. a conventional fixed-base building.
Functional and economic performance objectives are not explicitly addressed by seismic-code design requirements. Rather, it is hoped that additional design strength (i.e., Ie = 1.5) will adequately protect the structure from damage that could close a critical facility (i.e., hospital) and that somehow, nonstructural systems (and contents) can survive the shaking without loss of function or significant economic loss. However, it is difficult, if not impossible, to design nonstructural systems (and anchor contents) of a conventional fixed-base building such that significant economic and functional losses would not occur for the violent shaking.
The degree to which these objectives can be achieved depends on a number of factors including structural framing type, building configuration, structural and nonstructural materials and details, and overall quality of design and construction. In addition, large uncertainties as to the intensity and duration of shaking and the possibility of unfavorable response of a small subset of buildings or other structures may prevent full realization of these objectives.

## Slide 17: Basic Principles Why isolate?
Objectives | Conventional | Isolated
Deaths Serious injury and life loss not expected |  | 
Dollars No or minimal structural and non-structural repair costs |  | 
Downtime No or minor loss of function for all facilities |  | 
Isolation achieves a greatly improved seismic performance compared to most other conventional fixed-base seismic force resisting systems in a major earthquake.
Notes: The table has three columns, headed “Objectives”, “Conventional”, and “Isolated.” The first column headed “Objectives” has three rows labelled “Deaths”, “Dollars” and “Downtime.” “Thumbs Up” icons indicate favorable outcomes, and “Thumbs Down” icons indicate unfavorable outcomes. Under the Conventional column heading “Deaths” is a thumbs up, while “Dollars” and “Downtime” are both thumbs down. Under the Isolated heading, “Deaths”, “Dollars” and “Downtime” all have thumbs up.
The main reason why to isolate is to reduce structural, non-structural and contents damage and hence maintain operation after a major earthquake.
All seismically isolated buildings (not just critical facilities) are expected to have minimal repair costs and downtime, whereas a conventional building may be damaged to the point where it is uneconomical to rehabilitate. This is due to the inherent nature of isolation, for example it reduces both displacements and accelerations in the superstructure. Although not explicitly seeking damage control as an objective, indirectly the minimum requirements of the Standard will give limited damage as a consequence of ensuring proper isolation achieved. For example, the Standard limits the amount of inelastic action and drift that may occur in the superstructure to avoid detrimental coupling with the isolation system. Moreover, the Standard requires that the isolation devices be designed and tested to be functional under the effects of the Maximum Considered Earthquake (MCER).

## Slide 18: Basic Principles Where to isolate?
Greatest benefits of isolation realized in areas which have high seismicity
Notes: The figure shows a map of the continental United States. Colored contour plots indicate zones of seismicity, varying from low seismicity indicated with blue and green colors, to high seismicity indicated with orange and red colors. Areas of high seismicity include the entire west coast; parts of the central western U.S. near southern Montana, western Wyoming, and northern Utah; an area in the Mississippi River valley near Memphis; and an area near Charleston, South Carolina.
Ground motion intensity varies greatly across the United States as shown by this map. Typically, seismic isolation has been used in regions of high seismicity such as the coastal areas of California, Wasatch fault zone (e.g., Salt Lake City, Utah), the New Madrid seismic zone (e.g., Memphis, Tennessee) and the Charleston, South Carolina, seismic zone. Regions of high seismicity provide the greatest opportunity for realizing the benefits of isolation, but also the greatest challenges to the design of the isolation system to accommodate large earthquake displacements.

## Slide 19: Basic Principles Where to isolate?
Reference: Earthquake Protection Systems, Inc.
Natural candidates for isolation have been:
Essential facilities such as emergency operation centers that require continued functionality for public health and safety.
Notes: The slide contains two photographs. The photograph on the left shows the facade of the International Arrivals Terminal at San Francisco International Airport. The photograph on the right shows an aerial view of the Mills Peninsula Hospital.
Due to the major improvement in response of a seismically isolated building, there have emerged some candidates where isolation is commonly applied. These include a number of hospitals in California where continued function after a major earthquake are paramount, such as the Mills-Peninsula Bay Hospital in San Mateo and the San Francisco airport, where continued functionality is important for post-earthquake recovery.

## Slide 20: Basic Principles Where to isolate?
Reference: www.berkeleyheritage.com
Historical structures and museums that have low available ductility, valuable contents and require preservation.
Notes: The photograph shows Court of Appeals building in San Francisco.
Historical structures which pre-dated modern seismic design codes, governmental buildings and museums have also emerged as natural candidates. This is because the preservation of the structure and or contents is particularly important. Shown is the Court of Appeals building in San Francisco.

## Slide 21: Basic Principles Where to isolate?
Reference: Earthquake Protection Systems, Inc.
Business facilities such as data centers and factories that have high-value or hazardous contents and/or require continued functionality
Notes: The photograph shows an offshore oil drilling platform situated on a seismic isolation system.
Knowledgeable building owners who wish to protect their business asset and functionality have also taken to base isolation- examples include off-shore oil platforms, biotechnical companies such as Amgen in Seattle and high-tech companies such as Apple.

## Slide 22: Basic Principles Where to isolate?
Almost any building can be isolated, however there are several factors where it is more or less effective:
Buildings characteristics
Short-period structures (say T1<1.0 sec)
Heavy buildings
Overly flexible or tall structures
Slender buildings and Seismic Force Resisting Systems (SFRS) configurations that give large uplift forces
Notes: Technical speaking, any building can be seismically isolated, however there are a number of factors which make it more, or less suitable. Consideration of the buildings characteristics, site conditions, space and location of the isolation plane should made early in design. The following three slides outline the most important consideration.
Short and/or stiff buildings are best suited to isolation as they will benefit the most from period lengthening. High seismic weight is typically a detriment in seismic design due to high inertial forces; however it is much less of a concern in a seismically isolated building as isolators can accommodate large axial loads. Isolators perform well under compression and have little/no resistance to tension forces. Hence uplift in isolators presents difficult analysis, design and testing challenges and should be avoided.

## Slide 23: Basic Principles Where to isolate?
2. Site conditions
Stiff soils
Sites susceptible to basin amplification
Sloping sites that requires a stepped isolation plane
3. Space and installation
Isolation plane is above grade level
Close adjacent buildings (moat clearance)
Notes: Sites that have soft soils and basin effects may give more earthquake energy in periods which coincide with the period of the isolation system. This may lead to resonance of the seismically isolated building if it has little damping.
The location of the isolation plane may be the single most important cost consideration in the design of a seismically isolated building. Locating the isolation system below grade typically triggers several costly requirements: (1) a basement must be excavated and constructed, (2) retaining walls must be constructed around the basement, and (3) moat details must be provided.

## Slide 24: Basic Principles Where to isolate?
4. People
Long-term building owners
Businesses with valuable contents, critical functions
Appreciation and market demand for higher performance
Notes: The additional costs for the increased performance with seismic isolation is more easily justified by institutional owners with a long term interest in the seismic performance of a building, or business with high-value contents and want continued functionality.
Some markets, such as Japan and now New Zealand, have a demand for buildings with higher seismic performance. Historically this has not been seen in the US; however this may change after a major earthquake.

## Slide 25: Basic Principles How to isolate?
© 2004 Rutherford & Chekene
First we will show an example of how it was applied to the new de Young Museum, CA
Notes: The photograph shows a front view of the de Young museum in San Francisco.
An example of how seismic isolation is applied to protect contents (as well as function) is shown for the “new” de Young Museum in San Francisco, California. The new de Young Museum replaced an existing structure that was seismically deficient, having suffered significant structural damage during the 1989 Loma Prieta earthquake. The museum is located less than 8 km from the San Andreas Fault, and the need to protect the contents from earthquake damage prompted the owner to opt for base isolation of this low-rise building.
The museum building is seismically isolated with a combination of 76 high-damping elastomeric (rubber) bearings, 76 flat sliding bearings (sliders) and 24 fluid viscous dampers. Bearings and dampers are located in the crawl space below the first floor and interior courtyards, and do not affect museum architecture or function. Unless informed, visitors to the museum are not aware that the building is base isolated. The isolation system selected for the new de Young museum was one of 20 different systems considered for the museum and found by engineering evaluation to be the alternative that had the lowest base shear (best system for superstructure design), the lowest floor acceleration (best system for collection protection) and the lowest cost of the alternatives considered.

## Slide 26: Basic Principles How to isolate?
Delicate Glass Sculpture - Nijima and Ikehana Boats: “Chihuly at the de Young” (2008)
Notes: The photograph shows a museum exhibit of glass objects by the artist Dale Chihuly.
With isolation, the curators of the new de Young Museum can brace or anchor artifacts in a conventional manner and have more freedom with temporary exhibitions. In most cases, bracing can be avoided which would be problematic for many exhibits such as the glass sculpture shown in this slide. Base isolation also made design of the highly irregular superstructure easier, complying with the owner’s directive to have as many open spaces as possible.

## Slide 27: Basic Principles How to isolate?
© 2004 Rutherford & Chekene
Grade beams and crane installation
Notes: A photograph, taken during construction of the new de Young Museum, shows concrete foundations for individual isolators. The isolator foundations are connected by concrete grade beams.

## Slide 28: Basic Principles How to isolate?
Steel erection – 1st-floor above isolation bearings
© 2004 Rutherford & Chekene
Sliding Bearing
Rubber Bearing
Notes: This photo taken during construction of the new de Young Museum shows isolators (e.g., flat sliding bearing at an interior location and a high damping rubber bearing at a perimeter location) and 1st-floor steel framing.

## Slide 29: Basic Principles How to isolate?
© 2004 Rutherford & Chekene
Steel erection – upper floors
Notes: This photograph taken during construction of the new de Young Museum shows steel concentric-braces and upper-floor steel framing.

## Slide 30: Basic Principles How to isolate?
© 2004 Rutherford & Chekene
Crawl space - rubber bearings on pedestals
Notes: This photo taken in crawl space of the new de Young Museum before addition of fireproofing shows rubber bearings on reinforced-concrete pedestals. A total of 76 high-damping rubber bearings provide restoring force and tend to be located near the perimeter of the building to resist torsion (i.e., rotation of the building during an earthquake).

## Slide 31: Basic Principles How to isolate?
© 2004 Rutherford & Chekene
Crawl space – sliding bearing and supplementary fluid viscous damper
Notes: This photo taken in crawl space of the new de Young Museum after addition of fireproofing shows a typical stub column on top of a sliding bearing and a fluid viscous damper connected at one end to a 1st-floor girder above and at the other end to a reinforced-concrete pedestal and foundation below. A total of 76 flat sliders provide support and add damping (due to friction) without adding stiffness to the isolation system.
Due to the relatively close proximity to the fault and the potential for large ground motion “pulses,” the isolation system also incorporates a total of 24 fluid viscous dampers, providing additional displacement control. The covered “moat” around the perimeter of the building accommodates 36 inches of isolated structure displacement in any direction. This clearance includes substantial cushion on the calculated maximum earthquake displacement of 26 inches.

## Slide 32: Basic Principles How to isolate?
Isolation System Definition:
“The collection of structural elements that includes all individual isolator units, all structural elements that transfer force between elements of the isolation system, and all connections to other structural elements. The isolation system also includes the wind-restraint system, energy-dissipation devices, and/or the displacement restraint system if such systems and devices are used to meet the design requirements of this chapter.”
Notes: The next three slides describe the Standard’s terminology for the isolation system and elements.
The isolation system includes all the individual isolator units and other structural elements (e.g., connections) that transfer force from the isolator units to the foundation below and to structure above the isolation system. The isolation system also includes any supplemental energy-dissipation devices (e.g., viscous dampers).
In most applications, wind restraint is an inherent feature of the isolator unit – that is, the initial stiffness of rubber bearings (or the static friction level of sliding bearings) is typically large enough to resist wind design loads without significant displacement. Although uncommon, a displacement restraint system (e.g., moat bumpers, etc.) could be used to limit maximum considered earthquake displacement of the isolation system, provided it is shown that such restraint would not adversely affect the stability of structure above the isolation system.
The significance of this slide to earthquake engineering is that it shows how seismic isolation is implemented in practice.

## Slide 33: Basic Principles How to isolate?
Isolation Interface
Notes: A figure illustrates the isolation interface, the imaginary boundary between the upper portion of the structure which is isolated and the lower portion of the structure which is non-isolated and moves rigidly with the ground. The isolation interface is often referred to as the “plane of isolation,” although the isolation interface need not be located at single horizontal plane. In this figure the plane of isolation shifts from a low location at the left to a high location at the right.
This figure also illustrates the boundaries between (1) structure above the isolation system, (2) the isolation system, and (3) the structure below the isolation system. Typically, there is a heavy girder or slab just above isolator units to resist large P-Delta moments that occur at peak earthquake displacements of isolator units supporting vertical loads. In this capacity, the heavy girder or slab is considered an element of the isolation system, since it is required for stability of isolators.

## Slide 34: Basic Principles How to isolate?
Isolator Units (or Bearings):
Horizontally have low stiffness, re-centring ability and good energy dissipation.
Are vertically stiff and stable under the weight of the building and large displacement.
Have well established and repeatable mechanical properties with limited degradation
Notes: The Standard defines isolator units as horizontally flexible and vertically stiff elements, assuming that isolation system provides only horizontal isolation. The use of isolation systems that have no or very little restoring force is prohibited. While earthquake damage to buildings and their contents is due primarily to horizontal ground motions, vertical ground motions can adversely affect certain vibration-sensitive equipment and systems. Protection against damage due to vertical (as well as horizontal) ground motions would require a 3-dimensional isolation system, which is not practical for most applications (exceptions include special military facilities and possibly nuclear power plants).
As we discussed earlier, the concept of isolation is ancient and our improvement has been in the capability to construct isolator types which have reliable and predictable behavior. Therefore the Standard requires that the isolator units have well established (through qualification and prototype testing) mechanical properties, which are repeatable and that do not significantly degrade (i.e. the isolators a durable and stable).

## Slide 35: Basic Principles How to isolate?
Reference: MCEER-11-0004
SUNY, Buffalo, NY
Two of the most common types:
Elastomeric (rubber) Isolators
Consist of alternating layers of rubber and steel shims.
  Low- or high-damping rubber bearings
  Lead-rubber (LR) bearings
Notes: The photograph shows an elastomeric isolation bearing that has a wedge cut out of it to indicate the internal construction of the isolator. Internal alternating layers of rubber and steel are visible, with the rubber layers about 10 mm thick and the steel layers about 3 mm thick. Also visible at the interior of the bearing is a vertical lead cylinder which is inserted into a vertical hole at the center of the isolator.
The two most commonly used isolator types are elastomeric and sliding isolators. These types have been extensively tested and implemented over the past three decades.
The first seismic isolation systems in buildings in the United States were composed of either high-damping rubber (HDR) or lead-rubber bearings (low-damping rubber bearing with a lead core that adds damping). Elastomeric isolators are made of rubber (a visco-elastic material) which are constructed in alternating layers of steel and rubber in order to have high vertical stiffness and to avoid lateral shear buckling. There are three types: low damping (less the about 5%) and high damping rubber bearings, and lead-rubber bearings. LR bearings consist of low damping rubber and a central lead core which gives strengths and energy absorption ability.

## Slide 36: How to isolate?
Reference: MCEER-08-0007
SUNY, Buffalo, NY
Two most common type:
2. Sliding Isolators
Utilize a low-friction sliding interface, commonly PTFE (Teflon) on polished stainless steel.
  Concave sliding system
    Single-concave sliding surface
    Double-concave sliding surface
    Triple-pendulumTM bearings
  Flat sliding bearings (used with rubber isolators)
Notes: A drawing shows an isometric view and a cross section of a double friction pendulum isolation bearing. The top of the bearing is a steel dish facing downwards, and the bottom of the bearing is a steel dish facing upwards. Between the two dishes is an articulated slider consisting of a hinged assembly with an upper radius that matches the contour of the upper dish, and a lower radius that matches the contour of the lower dish. The interfaces between the articulated slider and the steel dishes consists of a polished stainless steel liner in each dish, and low-friction sliding material on the top and bottom surfaces of the articulated slider.
Other types of isolation systems in the United States include sliding systems, such as the friction pendulum system, or some combination of elastomeric and sliding isolators. The concave sliding isolators may be composed of single-concave sliding surface bearings (original “dish” concept), double-concave sliding surface bearings (each with two dishes, one facing up and one facing down), or triple-pendulum bearings (a more sophisticated version of the double-concave bearings). In each case, gravity is used as the restoring force of the concave sliding bearings.
Some applications at sites of very high seismicity (such as that of the de Young Museum in San Francisco) also use supplementary fluid-viscous dampers in parallel with either sliding or elastomeric bearings.

## Slide 37: Basic Principles Summary
What is seismic isolation?
Period shift and energy absorption (“engineered soft-story”)
Why isolate?
Improved seismic performance (deaths, dollars, downtime)
Where to isolate?
  Where continued functionality and avoidance of damage to structural/non-structural elements and contents is valued.
  Most effective where a building has a short-period, on stiff soils with little constraints on moat clearance and location of isolation plane.
How to isolate?
Presented one of many examples in the USA. Most common bearings are elastomeric (rubber) and sliding isolators (flat or concave).
Notes: This finishes our discussion on the basic principles of seismic isolation and gives a summary of the key answers to the “what, why, where and how” questions we proposed at the beginning.
The significance of this slide to earthquake engineering is that it summarizes the basic principles of seismic isolation.

## Slide 38: Design Requirements Overview
Notes: A diagram shows the relationship between the ASCE 7 Standard (ASCE 7), the NEHRP Provisions (NEHRP), the International Building Code (IBC), the NFPA 5000 Building Code (NFPA), and the California Building Code (CBC). ASCE 7 is located at the center of the diagram. Along the bottom of the diagram are shown the IBC, NFPA and CBC. Arrows point from the IBC, NFPA, and CBC to ASCE 7. In the upper left NEHRP is shown. There is a double-headed arrow between ASCE 7 and NEHRP.
Initial development of design requirements for base-isolated buildings only began around 1990, which helps explain why the requirements are still young and evolving. Today, model building codes (e.g., national model codes such as the IBC, or regional derivatives, such as the CBC) adopt by reference the seismic design requirements of ASCE 7. The requirements in ASCE 7 are typically based on NEHRP’s recommended provisions.
All the recommended new changes of the 2015 Provisions (i.e. Replacement of ASCE 7 Chapter 17) have been further developed and adopted into the upcoming ASCE/SEI 7-16, which is expected to be adopted by reference in the 2018 edition of the IBC. As such, the code requirements followed for the Chapter 15 design example are referred to as ASCE 7-16 (referred to simply as the Standard) requirements, instead off the NEHRP 2015 Provisions.
The most current version of the Standard, ASCE 7-10, has been adopted by the 2012 IBC (by reference). Most jurisdictions and regulatory authorities in the United States have (or will) adopt the 2012 IBC (or regional derivatives thereof).

## Slide 39: Background of Seismic Provisions Design Requirements Overview
Chapter 17, ASCE 7-2016 (the Standard) is divided into eight sections:
17.1 & 17.2: Definitions & General Requirements
17.3: Ground Motion Criteria
17.4, 17.5, 17.6: Analysis Procedures
17.7: Design Review
17.8: Testing
Notes: The Standard is divided into eight sections which give the analysis and design requirements specific to seismically isolated structures. The following slides will broadly go over the content of these Sections.

## Slide 40: Background of Seismic Provisions Design Requirements Overview
Minimum building separations
Permitted structural systems,
i.e. OCBF up to 160 ft
Different design actions for components above and below isolation system
Ie , ρ, Irregularities?
17.1 & 17.2: Definitions & General Requirements:
Structural System
Notes: The slide includes a photograph of the de Young museum during construction. This is titled “Structural System” There are four boxes surrounding the photograph, all with arrows pointing towards the photograph. Box 1 says “I-sub-e, rho, Irregularities?”. Box 2 says “Different design actions for components above and below isolation system.” Box 3 says “Permitted structural systems, i.e. OCBF up to 160 ft.” Box 4 says “Minimum building separations.”
The first two Sections of the Standard gives terminology definitions as well as general design requirements. These are the overarching instructions for the design of the structure above and below the isolation system, and of the isolation system itself.
For the structure above the isolation system it prescribes importance and redundancy factors, and specifies when the structural configuration shall be designated as irregular. Furthermore it states the mini mum building separations and specifies what the suitable actions are for the design of components above and below the isolation system.
Isolated buildings are also permitted to use ordinary concentrically braced frames (OCBF) up to 160 ft, even though Table 12.2-1 of the Standard limits the height of fixed-base OCBF buildings to 35 feet for this Seismic Design Categories D, E & F. This is permitted provided 1) the OCBF remains elastic for the MCER event and 2) the displacement capacity to which the isolation system lock-up or impact the moat wall shall be increased by a factor of 1.2.

## Slide 41: Background of Seismic Provisions Design Requirements Overview
Upper- & lower- bound properties
Inspection & replacement
Overturning and uplift stability
Vertical load combinations
Minimum Restoring Force
Wind and Fire Resistance
17.1 & 17.2: Definitions & General Requirements:
Isolation System
Notes: The figure shows the same photograph of the de Young museum during construction as was shown in the previous slide, except that the elements of the seismic isolation system are highlighted by red shading. This photograph is titled “Isolation System” There are six boxes surrounding the photograph, all with arrows pointing towards the photograph. Box 1 says “Wind and Fire Resistance”. Box 2 says “Minimum Restoring Force.” Box 3 says “Vertical Restoring Force.” Box 4 says “Overturning and uplift stability.” Box 5 says “Inspection & replacement.” Box 6 says “Upper- & lower-bound properties.”
There are a number of specific design requirements for the isolation system:
The isolation system is required to have a wind-restraint system, unless shown (by testing of isolator units) to not displace more than the amount permitted for fixed-base structure for design wind loads, and is required to have the same fire resistance as that of comparable structural elements of a fixed-base structure (i.e., columns in the basement of a fixed-base building).
Isolation systems with no or little amount of restoring force at large displacements (i.e., positive post-yield slope) are not permitted, this is to ensure that residual displacements do not accumulate in a given direction during repeated cycles of earthquake response.
At maximum considered earthquake displacement, isolators must be stable for “worst-case” vertical loads and the isolated structure must be safe against global overturning (although individual isolators are permitted to uplift during earthquake response, if such does not affect their stability).
Access must be provided for inspection and replacement of isolators, including pre-occupancy inspection of structural separation areas (moat clearance) and components that cross the isolation interface.
The determination of isolation systems properties shall account for the variability and uncertain due to aging and environmental conditions, variations observed during testing and manufacturing tolerances. This is done using the property modification factor approach and bounding analyses.

## Slide 42: Background of Seismic Provisions Design Requirements Overview
Yes, for Class A, B, C sites, where S1 0.6
Yes, for Class D and E sites, where S1 0.2
Yes, for Site Class F
Otherwise USGS website
17.3: Ground Motion Criteria
Question 1: Is a site-specific hazard analysis necessary?
Notes: A graph shows examples of several project-specific earthquake response spectra that could be used for design. These spectra are meant to be a schematic illustration only, so the details of the shapes and magnitudes of the spectra are not relevant.
On sites located close to major active faults, or with unstable or soft soil conditions, the two-parameter (S1, Ss) spectrum (a.k.a “ELF” or “USGS website” spectrum) obtained using the ground motion maps in combination with site factors (Fa, Fv) does not provide a good estimate of the spectral shape of design ground motions, particularly at longer periods. Studies of site-specific seismic hazards and site response can significantly improve the shape and amplitude of the design spectrum on such sites, and is therefore required for these structures.
Site-specific ground motion procedures have traditionally been required for seismically isolated buildings. Therefore specialist expertise will be required early in the design process.

## Slide 43: Background of Seismic Provisions Design Requirements Overview
17.3: Ground Motion Criteria
Question 2: What level of analysis is necessary?
For ELF and Response Spectrum procedures, simply use the response spectrum determined by answering Question 1.
For Response History Analysis, also have to select and scale ground motion records:
Notes: At the bottom of this slide are shown two earthquake accelerographs, with the vertical axes labeled “Acceleration Amplitude 1, (g)” and “Acceleration Amplitude 2, (g), with scales running from -0.8 g to 0.8 g. The horizontal axes are the time scale, running from 0 to 40 seconds. These two plots are meant to illustrate schematically that a typical earthquake record for seismic isolation design consists of two orthogonal components applied simultaneously to the structure.
Although seismically isolated buildings can be designed adequately using simple procedures, many base-isolated buildings in the US have been designed and or verified by using nonlinear response history analysis, where only the nonlinearity in the isolators need to be modelled. Response history analysis requires at least seven sets of scaled ground motions to be used. Shown is an a set of orthogonal horizontal acceleration histories for the 1989 Loma Prieta earthquake (Saratoga – Aloha Avenue recording station).

## Slide 44: Background of Seismic Provisions Design Requirements Overview
Reference: DIS Inc. with edits
M
Isolation system
βeff
keff
Three types:
1. Equivalent Lateral Force (ELF)
  Single-degree-of-freedom, displacement-based method.
  Assumes linear-elastic behaviour (effective stiffness and effective damping) of the nonlinear isolators.
  Always done, as it sets minima for checking forces and displacement of the more sophisticated dynamic analyses.
17.4, 17.5, 17.6: Analysis Procedures:
Notes: Three small figures appear at the bottom of this slide. The figure on the left shows a simple single-degree-of-freedom oscillator, consisting of a flexible shaft fixed at the bottom end, and with a lumped mass attached to the top end. The flexible shaft is labelled “Isolation System”. The center illustration is a load-displacement plot showing a typical hysteresis loop from a seismic isolation system. The area within the hysteresis loop is the energy dissipated by the isolation system during a single cycle of oscillation. This energy can be related to the damping of the isolation system, which is labeled “beta-sub-eff” on the drawing. There is also an inclined line from the origin of the plot to the upper right corner of the hysteresis loop, indicating the effective stiffness of the isolation system, and labeled “k-sub-eff”. The figure on the right is an elevation of a seismically isolated building, five stories high and 3 bays wide. The isolation system at the base of the building is visible, and it is shown in a displaced position towards the right. Horizontal arrows on the left at each floor level indicate the inertial forces generated by seismic response of the superstructure.
There are three analysis procedures in the Standard. In order of increasing sophisticating, these are the ELF, Response Spectrum and Response History procedures. The ELF analysis is always necessary, as it is used to evaluate results of the dynamic analysis and to obtain minima of response quantities.
The equivalent lateral force (ELF) procedure is a single-degree-of freedom displacement-based method that uses simple equations to determine an isolated structures response. Although the ELF procedure is considered a linear method of analysis, the equations incorporate amplitude-dependent values of effective stiffness and effective damping to account implicitly for the nonlinear properties of the isolation system. The equations assume that the superstructure is rigid and lateral displacements occur primarily in the isolation system. The method calculates the force of the base level, immediately above the isolation plane, and gives equations on how the remainder of the base shear is distributed among the other levels.

## Slide 45: Background of Seismic Provisions Design Requirements Overview
Reference: MCEER-11-0004
SUNY, Buffalo, NY
17.4, 17.5, 17.6: Analysis Procedures:
Dynamic Analysis: Response Spectrum
  Multi-modal analysis which uses a hybrid response spectrum
  Assumes linear-elastic behaviour (effective stiffness and effective damping) of nonlinear isolators.
Notes: There is a graph at the bottom of the slide, illustrating the hybrid response spectrum used for design. The upper curve is the 5 percent damped spectrum, while the lower curve is the response spectrum corresponding to the full damping of the isolated structure, including the damping contribution of the isolation system. The hybrid response spectrum follows the upper curve from a period of 0 to 1.4 seconds. Then a vertical line runs from the upper to the lower spectrum. The hybrid spectrum then follows the lower curve from 1.4 seconds out to 2.5 seconds at the right edge of the graph.
The response spectrum analysis is a multi-modal, linear-elastic analysis. The response spectrum specified for the analysis is the ≤5 percent damped spectrum that is then modified for the effects of higher damping. The ordinates of the 5 percent damped response spectrum for periods larger than upper bound Teff are divided by the damping reduction factor B for the effective damping of the isolated building. The reductions in demand due to higher damping apply only to the isolated modes; the non-isolated modes are assumed to be damped at 5 percent of critical or less.

## Slide 46: Background of Seismic Provisions Design Requirements Overview
17.4, 17.5, 17.6: Analysis Procedures:
Dynamic Analysis: Response History
  Most sophisticated analysis and can be used for all building types
  Model the nonlinear behaviour of isolators
  Require ground motion records and use the average results for design
Notes: There is a graph at the bottom of this slide. It shows earthquake displacement records for the isolation system, with the horizontal axis labeled “Time (seconds)” running from 0 to 40 seconds. The vertical axis is labeled “Displacement (inch)” running from -12 to 12 inches. One displacement record is labeled “X-direction” and the other “Y-direction”. Also shown on the graph is the square-root-of-sum-of-squares combination of the X and Y displacement records labeled “SRSS”
The NLRHA gives the most realistic estimate of an isolated buildings response. Typically the superstructure is modeled as elastic with nonlinear behavior confined to the isolation level. Two models are required, one with the isolator units upper-bound force-deflection properties and one using the lower-bound properties. Each model is subjected to at least seven different ground motion sets, where the values used in design (for each response parameter of interest) are taken as the average of the seven ground motion analyses maxima.
The illustration is the isolation systems displacement histories during one of its seven earthquakes. Its peak SRSS response is about 12 inches.

## Slide 47: Background of Seismic Provisions Design Requirements Overview
17.7: Design Review
At least one registered design professional shall provide an independent review.
Peer reviewer or panel should be formed before setting the design criteria (including site-specific ground motion criteria).
Notes: An independent review is required since the design of seismically isolated buildings is not familiar to most registered design professionals (RDP) and since it is usually used on critical facilities. This requirement has been relaxed to only one RDP in the latest cycle to expedite the process.

## Slide 48: Background of Seismic Provisions Design Requirements Overview
Because seismic isolators are:
  typically custom designed and proprietarily constructed, and
  manufactured using non-traditional materials (lead, elastomers, Teflon)
  Much like baked bread, their behavior (taste) may vary significantly between projects (batches) and suppliers (bakers)
17.8: Testing
The Standard has extensive testing requirements compared to other structural systems, why?
Notes: The Standard has extensive testing requirements when compared to other seismic force resisting systems. This is because the Standard permits a broad range of isolator products, as long as they meet certain basic requirements for stability, strength, degradation and reliability. Furthermore isolators have complex behavior and unique characteristics- isolators are usually custom designed and constructed using proprietary technologies, and are made of non-traditional civil engineering materials like composites, lead and elastomers. These features give uncertainty and variability in the isolators properties which must be assessed on a manufacturer- and project-specific basis.
The baked bread analogy is a way of comprehending this concept and is not far from the truth. For example rubber isolators can made from vast array of ingredients and are literally “cooked” (i.e. vulcanization of rubber). Poor ingredients (i.e. fillers) and poor manufacturing can drastically effect performance.

## Slide 49: Background of Seismic Provisions Design Requirements Overview
17.8: Testing
The three categories are:
1. Qualification testing
  Submitted by the manufacturer
  Qualitative requirement, may be used in establishing the isolators properties, longevity, or to develop models to be used in analysis
Notes: Detailed design of the isolator units typically is the responsibility of the manufacturer subject to design and testing (performance) criteria included in the construction documents (drawings and/or specifications). Performance criteria typically include a basic description and size(s) of isolator units, design criteria (e.g., loads, displacement capacity, force-deflection properties, etc.), quality assurance and quality control requirements (including QC testing of production units) and prototype testing requirements. The testing of isolators is broken down into three phases: qualification testing done by the manufacturer before the project, prototype testing done during he project before the final design, and production testing done after the bearings have been constructed.
The RDP has flexibility and authority to determine what data qualifies as qualification test data. However it is generally the responsibility of the manufacturer to conduct qualification testing. These tests may be used to aid in the establishment of nominal properties and lambda factors, to characterize the longevity of the isolator, and to develop models of the isolators for analysis.

## Slide 50: Background of Seismic Provisions Design Requirements Overview
17.8: Testing
2. Prototype testing
  Two isolators of each type require testing or may make use of previous test data from “similar” isolators
  Used to determine properties for design and modification factors λtest
  Test sequences and cycles also check wind loading, durability and stability of the isolators
Notes: There are two photographs at the right of this slide. The upper photograph shows a triple-friction-pendulum isolation bearing in a test machine. The lower photograph shows the same bearing, but disassembled after testing.
The Standard specifies a variety of prototype tests which serve a range of purposes. A key purpose is to establish and validate design properties. While these test are typically performed on project specific basis, they need only be performed once in a comprehensive manner (i.e. dynamically at earthquake velocities) to establish design properties for “standardized” isolator products. Prototype testing may be waived altogether if previous testing has been conducted on “similar” isolators which meet certain requirements specified in the Standard.
The prototype testing is also accompanied with “acceptance criteria” which, although convoluted, try to ensure that the isolation system:
has positive incremental restoring force capacity – the test specimens should have increasing resistance with displacement to verify that isolation system will not accumulate residual displacement in a given direction
has reliable force-deflection properties – the two test specimens should have the same effective properties and have limited variation in effective stiffness for repeated cycles of load at given displacement
is durable – test specimens should have limited degradation of their effective properties for repeated cycles of load such that the isolation system would still be functional during aftershocks
remains stable for maximum earthquake loads – the tests specimens must be shown capable of supporting maximum (and minimum) vertical load at maximum (MCER) earthquake displacement.

## Slide 51: Background of Seismic Provisions Design Requirements Overview
17.8: Testing
3. Production testing
  All isolators must be subjected to a combined compression and shear load cycle before being installed
  May be performed at slow-speed
  Verifies the quality of product
Notes: Production testing is intend to verify the quality of individual isolators and is also called quality control testing. The elastomeric isolators used for a project in China were installed without testing. As construction progressed, the loads increased on the isolators and several show signs of delamination. Hundreds of isolators were removed and replaced.

## Slide 52: Background of Seismic Provisions Revisions
Full replacement of ASCE 7 Chapter 17 recommended
Some major changes include:
Having a MCER-only basis for analysis and design.
A completely new section to systematically account for the variability in the isolation systems properties
Notes: A graphic shows the cover of the document FEMA P-1050-1, 2015 Edition, “NEHRP Recommended Seismic Provisions for New Buildings and Other Structures”
The NEHRP provisions incorporate the state-of-the-art in knowledge and research, and aim to improve building practices. Due to the large number of changes, the 2015 NEHRP Provisions have recommended a full replacement of Chapter 17 in ASCE 7.
The remaining slides will give background on seven of the more significant changes recommended by the NEHRP Provisions.

## Slide 53: Background of Seismic Provisions Revisions
Revision of ground motion criteria.
Expanded the range of applicability of the ELF procedure.
Revised equations for calculating the distribution of shear force over the height of the building.
Simplified approach for incorporating accidental mass eccentricity for NLRHA.
Additions and changes to the testing requirements.
Notes: The remaining slides will give background on the major changes listed here.

## Slide 54: Background of Seismic Provisions Revisions
1. MCER-only basis for design
Modified the elastic base shear calculation from the DBE event to the MCER event, but now using a consistent set of the upper- or lower- bound properties.
Consequently, the DBE event was removed completely from Ch 17.
Although not seeking damage-control as an objective, isolated buildings will have a better performance than other SFRS because:
The superstructure is designed to remain essentially elastic for the MCER event.
Isolation system is designed and tested for the MCER event.
Notes: To expedite design, the chapter has been re-written so that only the MCER event needs to be considered for design. The design basis earthquake (DBE) has been completely removed and all the relevant provisions updated to reflect this. In some cases, this has resulted in more conservative design requirements.
Previously the elastic base shear was calculated using lower-bound displacement and upper-bound effective stiffness, which was known to be inconsistent but conservative. Now it is calculated using a consistent set using the upper and lower bound properties.

## Slide 55: Background of Seismic Provisions Revisions
Isolation System Properties
Completely new section to systematically account for the variability and uncertainty in isolator properties.
Process is to use the property modification (λ) factor approach
Two parallel upper- and lower-bound analyses are conducted, where the governing case for each response parameter of interest is used for design.
Notes: There is a graph at the bottom of the slide. This graph shows two Force-Displacement hysteresis loops. One loop is for “upper bound” isolation properties, with a higher value of effective stiffness; the other loop is for “lower bound” isolation system properties, with a lower value of effective stiffness.
Bounding procedures are used as a simplifying and practical approach to account for the probabilistic range in isolator properties. Two analyses are necessary as either the maximum or minimum probable isolator properties may govern for design. For instance, an upper-bound analysis may govern the sizing of the building frame whereas a lower-bound analysis may govern the sizing of the isolation hardware and surrounding moat clearance.
Bounding procedures have already been used on many projects, for example the new de Young Museum. Therefore the Standard’s revisions are not a vast change in design practice, however are intended to give more guidance on what factors to consider when determining maximum and minimum probable isolator properties.

## Slide 56: Background of Seismic Provisions Revisions
Property modification (λ) factor categories:
λae.max and λae.min which account for aging and environmental effects. (i.e. aging, contamination, low temperatures)
λtest,max and λtest.min which account for scragging, hysteretic heating and speed of loading (observed in dynamic prototype testing)
λspec,max and λspec.min which account for manufacturing variations.
These are then combined using the following equations:
Notes: The concept of property modification factors was originally presented in Constantinou et al. (1999) and is already implemented in bridge design codes. The λ-factor approach is to assess the impact of a particular effect on the bearing properties (e.g. heating, aging, velocity, etc), and if the effect is appreciable then assigning it a λ-factor and accounting for the effect in analysis and design. For example, if an effect causes a 10% increase in a nominal property than it is assigned a λ value of 1.10 and contributes to the overall λmax factor. The λ-factors are determined through testing, rational analysis and engineering judgment.
In the equations shown, the Standard presumes a system property adjustment factor fa of 0.75, to account for the conservative assumption of having full aging and environmental effects when the governing earthquake occurs. Furthermore the upper and lower limits of 1.8 and 0.6 only apply for inexperienced manufacturers who have little/no test data. Hence these limits are rarely expected to apply and are intentionally wide.
The testing and specification λ-factors are explained further in the following two slides.

## Slide 57: Background of Seismic Provisions Revisions
Reference: MCEER-15-0005, SUNY, Buffalo, NY
Triple Friction PendulumTM dynamic test data
Lead-rubber bearing dynamic test data
Testing factors: λtest,max and λtest.min
Notes: Two graphs are shown on this slide. The upper graph shows load-displacement hysteresis loops for a lead-rubber isolation bearing tested under high rates of shear displacement. The lower graph shows load-displacement hysteresis loops for a friction pendulum isolation bearing under high rates of shear displacement.
High-speed dynamic cyclic testing of elastomeric (top left) and sliding (bottom right) isolators shows variable and degrading properties. These variations can be significant. Most analysis models do not account for the instantaneous changes in behaviour. They instead assume the strength of lead or friction coefficient is constant throughout the whole earthquake analysis, whereas in reality the properties are changing instantaneously due to heating effects, speed of loading, scragging and/or vertical load. Therefore bounding procedures are necessary to account for this variability in behaviour if it is not explicitly accounted for in the isolator’s nonlinear model already.

## Slide 58: Background of Seismic Provisions Revisions
Reference: MCEER-11-0004, SUNY, Buffalo, NY
Specification factors: λspec,max and λspec.min
Dynamic production test data of 42 identical isolators:
Notes: A graph is shown on this slide, titled “Dynamic production test data of 42 identical isolators.” The vertical axis is labeled “Average Friction” running from 0.040 to 0.070. The horizontal axis is labeled “Production Test Bearing Number” running from 0 to 42. The data from 42 tests are shown on the graph. A horizontal line labeled “Average” is shown at a value of 0.0573. Two horizontal lines labeled “Max” and “Min” are shown at 0.065 and 0.049. The test data lies between the Max and Min lines.
The specification λ-factors are a manufacturing tolerance assumed for design and usually written into specifications. This tolerance is required because the testing of a small number of prototype (or similar) bearings may not necessarily provide the best estimate of the nominal design properties. This potential discrepancy occurs because the average of two prototype test results may be at the upper or lower end of the range of a larger population.
This is illustrated in the figure above which gives the nominal (3-cycle average) coefficient of friction for identical isolators when tested dynamically after production. Say if the first two isolators were the prototype units used to determine properties for analysis, they would suggest a nominal value of 6.25%. However later in the project, after the construction and testing of all 42 of the isolators, the average value is shown to be 5.7%. This is a 0.91 factor of difference. Since design is usually done before production testing, the manufacturing variations must be accounted for in analysis. In this case a specification tolerance of +/- 10% would have been adequate (i.e. λspec,max=1.10 and λspec.min=0.90).

## Slide 59: Background of Seismic Provisions Revisions
Ground Motion Criteria- NLRHA
Only seven ground motions required (other structures in ASCE 7-16 require 11)
Includes specific scaling requirements for amplitude and spectrally matched ground motions
Need only apply motions to analysis model in one orientation.
Clarified scaling for both FN and FP components at near-fault sites.
Notes: Two graphs are shown at the right side of the slide. The top graph shows acceleration response spectra for seven different ground motions, as well as a smoothed “target” spectrum. The seven response spectra fall in a range both above and below the target spectrum. The lower graph is also an acceleration response spectrum plot. On this graph are shown the target response spectrum from the previous graph along with the average of the seven records from previous graph. The average response spectrum matches the target response spectrum closely over the period range of interests, from approximately 1.1 to 2.7 seconds.
The ground motion criteria for seismically isolated structures is different to that required for the NLRHA of other structures in ASCE 7-2016. This is a technical as well as philosophical debate and the isolation code subcommittee thought is was appropriate not to adopt 11 ground motions (Note: it would require at least 22 analyses since both upper- and lower-bound are required). The figures to the right shows amplitude scaled ground motions compared to the target spectrum, where the average of all seven motions is greater than the target spectrum in the period range of interest.

## Slide 60: Background of Seismic Provisions Revisions
ELF Procedure can be used to design more buildings
Relaxed permissible limits and criteria for the use of the equivalent lateral force (ELF) procedure.
This modification minimizes the need to perform complex and computationally expensive nonlinear response history analyses for many base isolated structures.
Notes: Two small figures appear at the bottom of this slide. The figure on the left shows a simple single-degree-of-freedom oscillator, consisting of a flexible shaft fixed at the bottom end, and with a lumped mass attached to the top end. The flexible shaft is labelled “Isolation System”. The figure on the right is a load-displacement plot showing a typical hysteresis loop from a seismic isolation system. The area within the hysteresis loop is the energy dissipated by the isolation system during a single cycle of oscillation. This energy can be related to the damping of the isolation system, which is labeled “beta-sub-eff” on the drawing. There is also an inclined line from the origin of the plot to the upper right corner of the hysteresis loop, indicating the effective stiffness of the isolation system, and labeled “k-sub-eff”.
The provisions are revised to permit increased use of the ELF procedure, recognizing that the ELF procedure works well for isolated structures whose response is dominated by a single-mode of vibration and whose superstructure is designed to remain essentially elastic (limited ductility demand) even for MCER ground motions. The ELF procedure is now permitted for design isolated structures at all sites (except Site Class F) as long as the superstructure is “regular” (as defined in new Section 17.2.2) and has a fixed-base period (T) that is well separated from the isolated period (Tmin), and the isolation system meets certain “response predictability” criteria (which most commonly used systems do meet). This change may help in the uptake of the technology.

## Slide 61: Background of Seismic Provisions Revisions
Reference: DIS Inc. with edits
ASCE 7-16
ASCE 7-10
4. ELF Procedure Structural Shear Distribution
New, more realistic vertical distribution of lateral forces associated with the ELF method of design
Notes: Two figures appear at the bottom of this slide. The left figure is titled “ASCE 7-10” and shows an elevation of a five story by three bay frame structure resting on top of a seismic isolation system. Horizontal arrows indicate the inertial force developed at each floor, according to ASCE 7-10. These arrows are short near the base of the structure, and their length increases over the height. The right figure is titled “ASCE 7-16”, and the building illustrated is the same as in the left figure. In the right figure, however, the horizontal arrows that indicate design forces according to ASCE 7-16 do not increase linearly over the height of the structure. Instead, the lengths of the arrows are nearly the same, with the shortest arrows appearing near the bottom story, and at the roof level.
The proposed revision to the vertical force distribution is based on recent analytical studies (York and Ryan, 2008). Linear theory of base isolation predicts that base shear is uniformly distributed over the height of the building, while the equivalent lateral force procedure of ASCE 7-10 prescribes a distribution of lateral forces that increase linearly with increasing height. The uniform distribution is consistent with the first mode shape of an isolated building while the linear distribution is consistent with the first mode shape of a fixed-base building. However, a linear distribution may be overly conservative for an isolated building structure, especially for one or two story buildings with heavy base mass relative to the roof.

## Slide 62: Background of Seismic Provisions Revisions
Case | Isolator Properties | Accidental Eccentricity
I | Lower Bound | No
Iia | Lower Bound | Yes, X direction
Iib | Lower Bound | Yes, Y direction
6. Establishing amplifications to account for accidental mass eccentricities
Only two additional analysis cases required, IIa and IIb:
The following amplification factors (ratio of Case IIa or IIb response to Case I response) are computed:
isolator displacement at the plan location with the largest isolator displacement;
story drift in the structure at the plan location with the highest drift, enveloped over all stories;
frame-line shear forces at each story for the frame with to the maximum drift.
Notes: The effects of accidental mass eccentricity in NLRHA are permitted to be accounted for using amplification factors, instead of explicitly modeling of accidental eccentric mass in four different segments. The method outlined in the commentary is to do two additional analyses with the worst case eccentricity (accidental + inherent) in the X- and Y- directions (i.e. IIa and IIb), and compute a number of amplification factors for displacements, drifts and forces.

## Slide 63: Background of Seismic Provisions Revisions
Reference: Earthquake Protection Systems, Inc.
7. Testing Requirements
Some changes include:
Move towards having dynamic testing (i.e. prototype testing now has dynamic sequences).
Specific “similarity” criteria added to define when prototype testing may be waived.
Production testing in combined compression in shear is now required for all (100%) of isolators.
Notes: There is a photograph on the right side of this slide. The photograph shows a large machine for testing sliding seismic isolation bearings. At the top of the photograph are five vertical hydraulic actuators that apply vertical load to the test bearing. At the bottom of the photograph is a sliding table that moves horizontally to apply lateral displacements to the test bearing.
The testing protocols (sequence and cycles) in the Standard can be traced back to historical documents where testing was performed quasi-statically. Now it is becoming recognized that most isolators have velocity dependency and that their dynamic behavior can be quite different to their quasi-static behavior. Hence, although not explicitly stated in the Standard, it is implied that some form of dynamic qualification and/or prototype testing be conducted on isolators before they are use in construction. Dynamic testing is important for sliding isolators.

## Slide 64: DISCLAIMER
NOTICE: Any opinions, findings, conclusions, or recommendations expressed in this publication do not necessarily reflect the views of the Federal Emergency Management Agency. Additionally, neither FEMA nor any of its employees make any warranty, expressed or implied, nor assume any legal liability or responsibility for the accuracy, completeness, or usefulness of any information, product or process included in this publication.
The opinions expressed herein regarding the requirements of the NEHRP Recommended Seismic Provisions, the referenced standards, and the building codes are not to be used for design purposes. Rather the user should consult the jurisdiction’s building official who has the authority to render interpretation of the code.
Any modifications made to the file represent the presenters' opinion only.