## Slide 1: Nonbuilding Structure Design Fundamentals By J. G. (Greg) Soules, P.E., S.E., SECB Originally developed by Harold O. Sprague, Jr., P.E.
17
Disclaimer
Notes: Introduction slide.
This unit is only a brief introduction to the subject of earthquake resistant design of nonbuilding structures.

## Slide 2: Seismic Design of Nonbuilding Structures
What are Nonbuilding Structures (NBS)?
Use of “Reference Documents”
NBS Sensitive to Vertical Ground Motions
NBS Supported by Other Structures
Structural Design Requirements
NBS Similar to Buildings
NBS Not Similar to Buildings
Tanks and Vessels
Suggested References
Notes: Slide 2 is the table of contents for the presentation.

## Slide 3: What are Nonbuilding Structures (NBS)?
Photo Courtesy of CB&I LLC
Photo Courtesy of CB&I LLC
Photo Courtesy of CB&I LLC
Notes: Slide 3 shows pictures of four very different nonbuilding structures to support the section of the presentation titled “What are Nonbuilding Structures?” – an elevated water tower in the shape of a peach (NBS not similar to a building), an egg shaped digester (NBS not similar to a building, a pipe rack (NBS similar to a building, and a column supported spherical pressure vessel (NBS not similar to a building).

## Slide 4: What are Nonbuilding Structures (NBS)?
A nonbuilding structure is any structure that was not designed for continuous human occupancy.
A nonbuilding structure may be supported by the earth or another structure.
Requirements for the seismic design of nonbuilding structures can be found in Chapter 15 of ASCE 7-16.
Notes: Slide 4 begins a discussion of what constitutes a nonbuilding structure.

## Slide 5: What are Nonbuilding Structures (NBS)?
  Many industrial structures are classified as either nonbuilding structures or nonstructural components.
  The intent of ASCE 7-16 is to provide a clear and consistent design methodology regardless of whether the structure is a nonbuilding structure or a nonstructural component.
  Central to the methodology is how to determine which classification is appropriate.
Notes: Slide 5 continues a discussion of what constitutes a nonbuilding structure.

## Slide 6: What are Nonbuilding Structures (NBS)?
  Table 17-1 provides the applicable chapters with the requirements for nonstructural components and nonbuilding structures supported by other structures.
Table 17-1 Applicability of the Chapters of the Standard |  | 
Supporting Structure | Supported Item | 
 | Nonstructural Component | Nonbuilding Structure
Building | Chapter 12 for supporting structure; Chapter 13 for supported item | Chapter 12 for supporting structure; Chapter 15 for supported item
Nonbuilding | Chapter 15 for supporting structure; Chapter 13 for supported item | Chapter 15 for both supporting structure and supported item
Notes:   Slide 6 shows Table 17-1, which provides the applicable chapters with the requirements for nonstructural components and nonbuilding structures supported by other structures. The requirements in these various chapters determine if the structure in question is a nonbuilding structure or a nonstructural component. Table 17-1 shown above is a simple road map to follow when a structure is supporting small or large components/other structures. If the supporting structure is a building, the supporting structure follows the requirements of Chapter 12. If the supporting structure is a nonbuilding structure (unoccupied structure), the supporting structure follows Chapter 15. Nonstructural components are to comply with Chapter 13 unless the nonstructural component weight equals or exceeds 25% of the combined weight of the supporting structure. When the nonstructural component weight equals or exceeds 25% of the combined weight of the supporting structure, the nonstructural component is then classified as a nonbuilding structure and must meet the requirements of Chapter 15.
  Additional discussion on determining if the structure is a nonstructural component or a nonbuilding structure can be found in Bachman, Robert and Dowty, Susan, “Nonstructural Component or Nonbuilding Structure?”, Building Safety Journal, International Code Council, April-May 2008.

## Slide 7: What are Nonbuilding Structures (NBS)?
Nonbuilding structures fall into two broad categories:
  those with structural systems similar to buildings and
  those with structural systems not similar to buildings.
Specific requirements for these two categories of nonbuilding structures appear in Sections 15.5 and 15.6 of ASCE 7-16 respectfully.
Notes: Slide 7 continues a discussion of what constitutes a nonbuilding structure.

## Slide 8: What are Nonbuilding Structures (NBS)?
  NBS Similar to Building
  NBS Not Similar to Building
Notes: Slide 8 shows photographs of a nonbuilding structure similar to a building and a nonbuilding structure not similar to a building. The photograph of the left is a pipe rack and represents a nonbuilding structure similar to a building. The photograph on the right is an elevated water tank and represents a nonbuilding structure not similar to a building.

## Slide 9: What are Nonbuilding Structures (NBS)?
Many (but not all) nonbuilding structures are treated differently than buildings for seismic design.
  Nonbuilding structures are designed for higher seismic forces because NBS do not incorporate elements normally found in buildings that increase damping and ductility.
  Examples of these missing elements are floors, diaphragms, and non-structural elements.
Notes: Slide 9 continues a discussion of what constitutes a nonbuilding structure.

## Slide 10: What are Nonbuilding Structures (NBS)?
  Without these additional elements, the dynamic behavior of nonbuilding structures can be more accurately determined.
  For this reason, the fundamental period of a nonbuilding structure is calculated from first principles using its structural properties and deformation characteristics.
  The restrictions and limits of Section 12.8.2 of ASCE 7-16 on period determination do not apply.
Notes: Slide 10 continues a discussion of what constitutes a nonbuilding structure.
ASCE 7-16 Section 12.8.2 requires that the fundamental period, T, used to determine the design base shear, V, does not exceed the approximate fundamental period, Ta, times the upper limit coefficient, Cu, provided in Table 12.8-1. This period limit prevents the use of an unusually low base shear for design of a structure that is, analytically, overly flexible because of mass and stiffness inaccuracies in the analytical model. For nonbuilding structures, ASCE 7-16 Section 15.4.4 allows the use of the fundamental period, T, of the nonbuilding structure because of the reduced likelihood of mass and stiffness inaccuracies in the analytical model.

## Slide 11: What are Nonbuilding Structures (NBS)?
Approximate Period for Buildings (12.8.2)
Fundamental Period for NBS (15.4.4)
Notes: Slide 11 shows examples of approximate period formulas (Ta) for buildings from Section 12.8.2 on the left and the alternative equation for the fundamental period (T) allowed in Section 15.4.4 known as the Rayleigh equation.
The approximate period equations used for buildings are based on curve fits and result in values less than those obtained using first principals. The approximate period equations for buildings produce reduced periods that account for the stiffening effects of floors, diaphragms, and non-structural elements.
For nonbuilding structures, a properly substantiated analysis may be used to determine the period of the nonbuilding structure. As an alternative, the equation shown above (Rayleigh equation) may be used. Period equations for many nonbuilding structures can be found in “Guidelines for Seismic Evaluation and Design of Petrochemical Facilities”, 2nd Edition, 2011, ASCE.

## Slide 12: What are Nonbuilding Structures (NBS)?
Fire Station
Downers Grove, IL
Photo Courtesy of CB&I LLC
Photo Courtesy of CB&I LLC
Photo Courtesy of CB&I LLC
Notes: Slide 12 shows three photographs of elevated water tanks that are also used as fire stations. The photo on the left shows an elevated water tank with a fire station at its base in Downers Grove, IL. The two photos on the right show different views of the fire station in the base of an elevated water tank in Haltom City, TX.
It is not always clear when a structure can be categorized as a nonbuilding structure. These photographs show elevated water tanks with fire stations in the base of the support tower.

## Slide 13: What are Nonbuilding Structures (NBS)?
Section 11.1.3 in ASCE 7-16 states: “Buildings whose purpose is to enclose equipment or machinery and whose occupants are engaged in maintenance or monitoring of that equipment, machinery or their associated processes shall be permitted to be classified as nonbuilding structures designed and detailed in accordance with Section 15.5 of this standard.”
Notes: Slide 13 continues a discussion of what constitutes a nonbuilding structure.
The paragraph was added to clarify that industrial buildings are permitted to be designed by the nonbuilding structures requirements of Chapter 15.

## Slide 14: What are Nonbuilding Structures (NBS)?
Examples of such structures are boiler buildings, aircraft hangers, steel mills, aluminum smelting facilities, and other automated facilities.
Photographs of these type of structures are shown in the following slides.
Occupancy restrictions should be reviewed in each case.
Notes: Slide 14 continues a discussion of what constitutes a nonbuilding structure.

## Slide 15: What are Nonbuilding Structures (NBS)?
Photo Courtesy of CB&I LLC
Boiler Building
Notes: Slide 15 shows a photograph of a boiler building, which can be classified as a nonbuilding structure.

## Slide 16: What are Nonbuilding Structures (NBS)?
Aircraft Hanger
https://www.aopa.org/-/media/images/legacy/aopa/home/news/all/2014/july/0724_hangar_policy.jpg?h=455&w=640&la=en&hash=7CB936FC1F00864F6148E5CE2F1FBB0EE6F19EC1
Notes: Slide 16 shows a photograph of an aircraft hanger, which can be classified as a nonbuilding structure.
While an aircraft hanger with occupancy only for maintenance qualifies as a nonbuilding structure, a hanger-like structure used by an aircraft manufacturer to assemble aircraft with large number of workers present for a significant time in not a nonbuilding structure.

## Slide 17: What are Nonbuilding Structures (NBS)?
Steel Mill
Notes: Slide 17 shows a photograph of a steel mill, which can be classified as a nonbuilding structure.

## Slide 18: What are Nonbuilding Structures (NBS)?
Aluminum Smelting Facility
http://www.alcoa.com/global/en/news/images/AvilesSmelter_large.jpg
Notes: Slide 18 shows a photograph of an aluminum smelting facility, which can be classified as a nonbuilding structure.

## Slide 19: Use of “Reference Documents”
Notes: Slide 19 shows representations of three commonly used reference documents – API Standard 650 “Welded Tanks for Oil Storage”, (on the left), ASME Boiler and Pressure Vessel Code (in the middle), and ACI 350.3 “Seismic Design of Liquid-Containing Concrete Structures and Commentary” (on the right).
API stands for American Petroleum Institute. ASME stands for the American Society of Mechanical Engineers. ACI stands for the American Concrete Institute.

## Slide 20: Use of “Reference Documents”
“Reference Documents or Reference Standards” are industry standards (such as API 650) for different NBS that have been accepted by ASCE 7 as modified by the provisions of Chapter 15.
Some of the “Reference Documents” listed in ASCE 7 have well defined seismic design procedures.
Notes: Slide 20 begins a discussion on the use of reference documents.

## Slide 21: Use of “Reference Documents”
For these “Reference Documents”, ASCE 7 provides “bridging” equations or modified requirements that alter the procedure provided in the “Reference Document”.
These modifications bring the “Reference Document” up to the same force and displacement level used by ASCE 7.
Notes: Slide 21 continues a discussion on the use of reference documents.
ASCE 7-16, in effect, rewrites portions of another standard to bring it into compliance with ASCE 7-16.

## Slide 22: Use of “Reference Documents”
15.7.7.2 Bolted Steel. Bolted steel water storage structures shall be designed in accordance with the seismic requirements of AWWA D103 with the following exceptions. The seismic design ground motion values shall be determined according to Section 11.4.
For Type 6 tanks, the overturning ratio, J, as determined using AWWA D103 Eq. 14-32 shall not exceed 0.785.
Notes: Slide 22 shows an example of modified requirements to a reference document.
In this example, the modified standard is AWWA D103 (Factory-Coated Bolted Carbon Steel Tanks for Water Storage). The modified requirement prevents the use of Type 6 tanks (base ring embedded in concrete) from having net uplift during the design seismic event. The R value used for a mechanically anchored tank is not compatible with this type of tank.

## Slide 23: Use of “Reference Documents”
The adopted version of the Reference Documents are listed in Chapter 23 of ASCE 7-16.
Unless approval is obtained from the “authority having jurisdiction”, a newer edition of the Reference Document may not be used for the seismic design of the nonbuilding structure.
Notes: Slide 23 continues a discussion on the use of reference documents.

## Slide 24: Use of “Reference Documents”
For the purpose of Chapter 15, material standards such as AISC 360, ACI 318, etc. are not considered “reference documents”.
Material standards are generic in nature and do not contain complete design requirements for specific classes of nonbuilding structures such as steel storage racks or tanks.
The order of precedence is the adopted building code (IBC), then ASCE 7, and finally the reference document (e.g. API 650).
Notes: Slide 24 continues a discussion on the use of reference documents.
The order of precedence of codes and standards is not well understood by many engineers.

## Slide 25: Use of “Reference Documents”
Notes: Slide 25 shows a reproduction of ASCE 7-16 Table C15.2-1. ASCE 7-16 Table C15.2-1 provides examples of how to apply the requirements of a reference document in conjunction with the requirements of ASCE 7-16 Chapter 15.

## Slide 26: NBS Sensitive to Vertical Ground Motions
The vertical ground motions of NEHRP Provisions Chapter 23, based on the work of Bozorgnia and Campbell (2004), were incorporated in Section 11.9.
These alternate ground motions are currently only used for certain NBS.
0.8CvSMS
0.3CvSMS
0.8CvSMS(0.15/Tv)0.75
Notes: Slide 26 begins a discussion on nonbuilding structures sensitive to vertical ground motions. The right side of the slide shows the vertical response spectrum from ASCE 7-16 Section C11.9 (Figure C11.9-1).
The procedure for defining the MCER vertical response spectrum in ASCE 7 is a modified version of the procedure taken from the 2009 NEHRP Provisions. Unlike the procedure contained in the 2009 NEHRP Provisions, the procedure provided in Section 11.9 is keyed to the MCER spectral response acceleration parameter at short periods, SMS.

## Slide 27: NBS Sensitive to Vertical Ground Motions
Specific provisions added for liquid and granular storage tanks/vessels, suspended structures (such as boilers) and nonbuilding structures incorporating horizontal cantilevers.
These provisions replace the 0.2SDS value incorporated in ASCE 7-05 with Sav determined from the vertical response spectrum and combined with the horizontal effect using prescribed load combinations.
Notes: Slide 27 continues a discussion on nonbuilding structures sensitive to vertical ground motions.

## Slide 28: NBS Supported by Other Structures
Photo Courtesy of CB&I LLC
Photo Courtesy of CB&I LLC
Photo Courtesy of CB&I LLC
Notes: Slide 28 three photographs of nonbuilding structures supported by other structures. The photograph on the left shows 4 vertical vessels (nonbuilding structures) supported on a two tier high braced frame. The photograph in the upper right shows vertical vessels (nonbuilding structures) supported at various elevations in a process (braced frame) structure. The photograph in the lower left shows a horizontal vessel (nonbuilding structure) supported at the top of a braced frame being unloaded from a transporter.

## Slide 29: NBS Supported by Other Structures
Nonbuilding structures supported by other structures see amplified seismic forces in a similar manner as nonstructural components.
Section 15.3 of ASCE 7-16 provides extensive guidance on the design of nonbuilding structures supported by other structures.
There are 3 possible outcomes when the provisions of Section 15.3 are used.
Notes: Slide 29 begins a discussion on nonbuilding structures supported by other structures.

## Slide 30: NBS Supported by Other Structures
15.3.1 Less Than 25 percent Combined Weight Condition
15.3.2 Greater Than or Equal to 25 Percent Combined Weight Condition
  15.3.2 (1) Rigid (T < 0.06 sec) Nonbuilding Structure
  15.3.2 (2) Flexible Nonbuilding Structure
Notes: Slide 30 continues a discussion on nonbuilding structures supported by other structures.
The slide lists the three possible options for designing nonbuilding structures supported by other structures. These options are discussed in detail in the next few slides.

## Slide 31: NBS Supported by Other Structures
15.3.1 Less Than 25 percent Combined Weight Condition
  Weight of the NBS is less than 25 % of the combined effective seismic weights of the NBS and supporting structure.
  Design seismic forces of the NBS are determined in accordance with Chapter 13 where values of Rp and ap are determined according to Section 13.1.5.
  Supporting structure designed in accordance with the requirements of Chapter 12 or Section 15.5 as appropriate with the weight of the NBS considered in the determination of the effective seismic weight, W.
Notes: Slide 31 continues a discussion on nonbuilding structures supported by other structures.
This option applies to relatively small nonbuilding structures and is relatively easy to evaluate.

## Slide 32: NBS Supported by Other Structures
15.3.1 Less Than 25 percent Combined Weight Condition
  This represents the dividing line between Chapter 13 and Chapter 15.
  Eq. 13.3-1 is used to calculate the seismic force, Fp, on the supported nonbuilding structure:
Notes: Slide 32 continues a discussion on nonbuilding structures supported by other structures. Equation 13.3-1 (Fp) from ASCE 7-16 is shown at the bottom of the slide.
If the nonbuilding structure weighs less than 25% of the combined weight of the nonbuilding structure and its supporting structure, the nonbuilding structure is then treated as a nonstructural component using the provisions of ASCE 7-16 Chapter 13.

## Slide 33: NBS Supported by Other Structures
15.3.2 (1) ≥ 25 percent Combined Weight Condition and Rigid (T < 0.06 sec)
  Supporting structure designed in accordance with the requirements of Chapter 12 or Section 15.5.
  R value of combined system taken as the R value of the supporting structural system.
  NBS and attachments to be designed for the forces using the procedures of Chapter 13.
  The value of Rp is taken as equal to the R value of the NBS set forth in Table 15.4-2, and ap is taken as 1.0.
Notes: Slide 33 continues a discussion on nonbuilding structures supported by other structures.

## Slide 34: NBS Supported by Other Structures
15.3.2 (1) ≥ 25 percent Combined Weight Condition and Rigid (T < 0.06 sec)
  This procedure is similar to that for the case where the supported nonbuilding structure is less than 25% of the combined mass.
  Eq. 13.3-1, with Rp = R (Chapter 15), is used to calculate the seismic force, Fp, on the supported nonbuilding structure:
Notes: Slide 34 continues a discussion on nonbuilding structures supported by other structures. Equation 13.3-1 (Fp) from ASCE 7-16 is shown at the bottom of the slide.

## Slide 35: NBS Supported by Other Structures
15.3.2 (1) ≥ 25 percent Combined Weight Condition and Rigid (T < 0.06 sec)
  Very few supported nonbuilding structures qualify as rigid.
  There is a great temptation to assume that the supported NBS is rigid due to the resulting ease of calculation and lower loads.
  Honestly evaluate the period of the supported NBS, taking into account fluid-structure interaction and the flexibility of the supporting floor beams.
Notes: Slide 35 continues a discussion on nonbuilding structures supported by other structures.
It is important to note that this option (large rigid nonbuilding structure) does not apply to very many nonbuilding structures. Most large nonbuilding structures qualify as flexible. The period of the nonbuilding structure must be computed and be less than 0.06 seconds for this provision to be used. The designer cannot just assume that the nonbuilding structure is rigid.

## Slide 36: NBS Supported by Other Structures
15.3.2 (2) ≥ 25 percent Combined Weight Condition and Flexible (T ≥ 0.06 sec)
  NBS and supporting structure to be modeled together in a combined model with appropriate stiffness and effective seismic weight distributions.
  Combined structure to be designed according to Section 15.5 using the lesser R value of the NBS or the supporting structure.
  NBS and attachments are to be designed for the forces determined in the combined analysis.
Notes: Slide 36 continues a discussion on nonbuilding structures supported by other structures.
This option is the most common situation for large nonbuilding structures supported by other structures. A combined model of the nonbuilding structure and the supporting structure must be created and evaluated. This requirement has forced a change in the way large equipment is ordered. In the past, the large equipment (such as a pressure vessel) was ordered long before the structural engineer became involved. Now, the structural engineer must become involved earlier in the project. The combined model does not have to be very detailed. A simple “stick” model can often be used. Examples of this combined analysis can be found in “Guidelines for Seismic Evaluation and Design of Petrochemical Facilities”, 2nd Edition, 2011, ASCE.

## Slide 37: NBS Supported by Other Structures
15.3.2 (2) ≥ 25 percent Combined Weight Condition and Flexible (T ≥ 0.06 sec)
  This is the most common situation.
  Because the combined structure is to be designed using the lesser R value of the NBS or the supporting structure, the use of a high R value system (e.g. special concentrically braced frame) offers no economic advantage.
Notes: Slide 36 continues a discussion on nonbuilding structures supported by other structures.
While high R value systems offer no economic advantage in this case, use of high R value systems may still be desirable to obtain improved performance of the structure.

## Slide 38: Structural Design Requirements
NBS that have specific seismic design criteria established in reference documents are designed using the reference documents as modified by ASCE 7-16 Chapter 15.
Where reference documents do not exist, NBS are designed in compliance with Sections 15.5 and 15.6 and the additional requirements of Section 15.4.1.
Notes: Slide 38 begins a discussion on the general design requirements for nonbuilding structures.
With the exception of storage racks, only NBS not similar to buildings have reference documents with specific design criteria. Nonbuilding structures similar to buildings must meet the requirements of ASCE 7-16 Sections 15.5 and 15.6 and the additional requirements found under Section 15.4.1.

## Slide 39: Structural Design Requirements
For NBS without a reference document, the following additional requirements apply:
  Structural system is chosen from Tables 12.2-1 or 15.4-1 for NBS similar to buildings.
  Structural system is chosen from Table 15.4-2 for NBS not similar to buildings.
  Higher minimum base shear values are required with some exceptions.
Notes: Slide 39 continues a discussion on the general design requirements for nonbuilding structures.
The additional requirements presented in the slide are not all of the additional requirements found in Section 15.4.1. Only the most significant additional requirements are discussed.

## Slide 40: Structural Design Requirements
For NBS without a reference document, the following additional requirements apply:
  The accidental torsion requirements of section 12.8.4.2 need not be accounted for in nonbuilding structures if certain criteria is met – low R-value, regular, and inherent torsion accounted for.
  Primary factors that contribute to the effects of accidental torsion are frequently not present in many nonbuilding structures.
Notes: Slide 40 continues a discussion on the general design requirements for nonbuilding structures.
The accidental torsion requirements of Section 12.8.4.2 were formulated primarily for use in building structures. The primary factors that contribute to accidental torsion are lateral force resisting systems that are located primarily near the center of the structure rather than the perimeter, disproportionate concentration of inelastic demands in system components, the effects of nonstructural elements, uncertainties in defining the structure’s stiffness characteristics, and spatial variation (and rotational components of ground motions) of horizontal input motions applied to long structures. Inherently torsionally resistant systems as defined in section 15.4.1 item 5 with R values less than or equal to 3.5 are not expected to have inelastic demands of a level that would require additional consideration of accidental torsion. Additionally,
nonbuilding structures rarely contain significant non-structural elements that are not accounted for explicitly in the design of these structures and typically have very well-known mass and stiffness characteristics

## Slide 41: Structural Design Requirements
The importance factor, Ie, and risk category for nonbuilding structures are based on the relative hazard of the contents and the function.
The value of Ie is to be the largest value determined by the following:
  Applicable reference document listed in Chapter 23,
  The largest value as selected from Table 1.5-2, or
  As specified elsewhere in Chapter 15.
Notes: Slide 41 continues a discussion on the general design requirements for nonbuilding structures.

## Slide 42: Structural Design Requirements
The drift limit of Section 12.12.1 need not apply to nonbuilding structures.
Drifts are calculated using strength level seismic forces and the tabulated Cd factor.
P-delta effects must be considered where they are critical to the function or stability of the structure.
Notes: Slide 42 continues a discussion on the general design requirements for nonbuilding structures.
A rational analysis must indicate that the drift limit can be exceeded without adversely affecting structural stability or attached or interconnected components and elements such as walkways and piping.
Many nonbuilding structures are designed using ASD (Allowable Design Stress) methods ASCE 7 requirements are written in terms of strength level forces so the drift must be checked with strength level seismic forces.
P-delta effects must always be checked for nonbuilding structures.

## Slide 43: Structural Design Requirements
ASCE 7-16 Section 15.4.9 provides specific requirements for anchoring NBS to concrete or masonry.
  Anchors in concrete must meet ACI 318 Chapter 17 requirements.
  Anchors in masonry must meet TMS402 requirements.
  Postinstalled anchors must be seismically qualified.
Notes: Slide 43 continues a discussion on the general design requirements for nonbuilding structures.
Many nonbuilding structures rely on the ductile behavior of anchor bolts to justify the response modification factor, R, assigned to the structure. Nonbuilding structures typically rely more heavily on anchorage to provide system ductility. The additional requirements of Section 15.4.9 provide additional anchorage strength and ductility to support the response modification factors assigned to these systems. The addition of Section 15.4.9 provides a consistent treatment of anchorage for nonbuilding structures.

## Slide 44: Structural Design Requirements
ASCE 7-16 Section 15.4.9 provides specific requirements for anchoring NBS to concrete or masonry.
Substitution of F1554 Grade 55 anchors for F1554 Grade 36 anchors is NOT allowed when anchors are designed as ductile anchors in accordance with ACI 318 Section 17.2.3.4.3(a) or where the design must meet the requirements of Sections 15.7.5 or 15.7.11.7b (tanks and vessels).
Notes: Slide 44 continues a discussion on the general design requirements for nonbuilding structures.
ASTM F1554 allows the supplier to substitute Grade 55 anchors for Grade 36 anchors without notification or permission from the engineer of record. Substituting a higher strength bolt when the designer specifies a lower strength bolt in order to force the bolt to stretch can lead to unnecessary damage or failure of the structure, especially tanks and vessels. To fulfill this requirement, the engineer of record will need specify to the party purchasing the anchors that substitution of the specified bolt strength is not allowed.

## Slide 45: Structural Design Requirements
Shallow Foundations on Liquefiable Sites
  Nonbuilding structures generally are not permitted to be supported on shallow foundations at liquefiable sites.
  Section 15.4.10.1 will allow shallow foundations for NBS on liquefiable sites if it can be demonstrated that the structure’s foundation, superstructure and connecting systems can be designed to accommodate the soil strength loss, lateral spreading and total and differential settlements induced by MCEG earthquake ground motions.
Notes: Slide 45 continues a discussion on the general design requirements for nonbuilding structures.
Section 12.13.7 allows shallow foundation to be built on liquefiable soils with a number of restrictions. Many nonbuilding structures are sensitive to large foundation settlements. This sensitivity is due to restraint imposed by interconnecting piping and equipment and the buckling sensitivity of shell structures. Therefore, in order to build these structures on shallow foundations on liquefiable soils, it must be demonstrated that the foundation, nonbuilding structure not similar to buildings, and connecting systems can be designed for the soil strength loss, the anticipated settlements from lateral spreading, and total and differential settlements induced by MCEG earthquake ground motions.

## Slide 46: NBS Similar to Buildings
Photo Courtesy of CB&I LLC
Notes: Slide 46 shows two photographs of nonbuilding structures similar to buildings. The photograph on the left is a process structure used in an LNG facility. The photograph on the right is a suspended boiler in a power plant.

## Slide 47: NBS Similar to Buildings
NONBUILDING STRUCTURE SIMILAR TO A BUILDING: A nonbuilding structure that is designed and constructed in a manner similar to buildings, responds to strong ground motion in a fashion similar to buildings, and has a basic lateral and vertical seismic force-resisting system conforming to one of the types indicated in Tables 12.2-1 or 15.4-1.
Notes: Slide 47 begins a discussion on nonbuilding structures similar to buildings.
The slide shows the definition of a nonbuilding structure similar to a building from ASCE 7-16 Section 11.2.

## Slide 48: NBS Similar to Buildings
  Provisions found in Section 15.5.
  Designed and constructed with structural systems similar to buildings.
  Have dynamic response similar to buildings.
  Specific requirements given for:
      Pipe Racks (15.5.2)
      Storage Racks (15.5.3)
      Electrical Power Generating Facilities (15.5.4)
      Structural Towers for Tanks and Vessels (15.5.5)
      Piers and Wharves (15.5.6)
Notes: Slide 48 continues a discussion on nonbuilding structures similar to buildings.

## Slide 49: NBS Similar to Buildings
Pipe Racks
  Free-standing pipe racks are designed in accordance with Section 12.8 (Equivalent Lateral Force Procedure) or 12.9 (Linear Dynamic Analysis) and Section 15.4 (Structural Design Requirements).
  Single-column pipe racks that resist lateral loads should be designed as inverted pendulums.
Notes: Slide 49 continues a discussion on nonbuilding structures similar to buildings.
The complete structural design of pipe racks is discussed in “Design of Structural Steel Pipe Racks” by Richard M. Drake and Robert J. Walter, AISC Engineering Journal, 4th Quarter, 2010.

## Slide 50: NBS Similar to Buildings Pipe Racks
ASCE 7-16 Table 15.4-1 sets forth the option of lower R values and less restrictive height limits for structural systems commonly used in pipe racks.
The lower R values and increased height limits of ASCE 7-16 Table 15.4-1 apply to nonbuilding structures similar to buildings.
The lower R values cannot be applied to building structures.
Notes:   Slide 50 continues a discussion on nonbuilding structures similar to buildings.
  The background for the option of lower R values and less restrictive height limits is discussed in Slide 51.

## Slide 51: NBS Similar to Buildings Pipe Racks
The option of lower R values and less restrictive height limits for structural systems listed in ASCE 7-16 Table 15.4-1 is based on good performance of these systems in past earthquakes.
The R value versus height limit trade-off recognizes that the size of some nonbuilding structures is determined by factors other than traditional loadings and results in structures that are much stronger than required for seismic loadings.
Therefore, the ductility demand is generally much lower than that for a corresponding building.
Notes:   Slide 51 continues a discussion on nonbuilding structures similar to buildings.
  Performance of nonbuilding structures in a recent major seismic event is discussed in Soules, J. G., Bachman, R.E., and Silva, J.F., “Chile Earthquake of 2010 – Assessment of Industrial Facilities around Concepción”, American Society of Civil Engineers, Structural Engineering Institute, Reston, VA, 2016. Additional background information on this topic can be found in Soules, J. G., “The Seismic Provisions of the 2006 IBC – Nonbuilding Structure Criteria,” Proceedings of 8th National Conference on Earthquake Engineering, San Francisco, CA, April 18, 2006. The intent is to obtain the same structural performance at the increased heights.

## Slide 52: NBS Similar to Buildings Pipe Racks
Notes: Slide 52 shows a reproduction of ASCE 7-16 Table 15.4-1. The entry circled shows a “Steel Ordinary Concentrically Braced Frame with Unlimited Height”. This option allows an ordinary concentrically braced frame to be designed and constructed with unlimited height in SDC F. This option requires no seismic detailing and the use of an R value of 1.5.

## Slide 53: NBS Similar to Buildings Pipe Racks
Typical Steel Pipe Rack
Photo Courtesy of CB&I LLC
Notes: Slide 53 shows a reproduction of ASCE 7-16 Table C15.5-1 at the top of the slide and a picture of a typical steel pipe rack at the bottom of the slide.
The option of lower R values and less restrictive height limits proves to be economical in most situations because of the relative cost of materials and construction labor. ASCE 7-16 Table C15.5-1 reproduced above illustrates the R values and height limits for a 70-ft-high steel ordinary moment frame (OMF) pipe rack.

## Slide 54: NBS Similar to Buildings Storage Racks
Storage Racks, Steel: A framework or assemblage, comprised of cold-formed or hot-rolled steel structural members, intended for storage of materials, including, but not limited to, pallet storage racks, selective racks, movable-shelf racks, rack-supported systems, automated storage and retrieval systems (stacker racks), push-back racks, pallet-flow racks, case-flow racks, pick modules and rack-supported platforms. Other types of racks, such as drive-in or drive-through racks, cantilever racks, portable racks or racks made of materials other than steel, are not considered steel storage racks for the purpose of this standard.
Notes: Slide 54 shows the very detailed definition of a steel storage rack from ASCE 7-16 Section 11.2.

## Slide 55: NBS Similar to Buildings Storage Racks
Storage racks are commonly found in large warehouse-type retail stores such as Lowe’s or Home Depot.
ASCE 7-16 Section 15.5.3 provides requirements for two types of storage racks:
  Steel Storage Racks designed to ANSI/RMI MH16.1 and
  Steel Cantilevered Storage Racks designed to ANSI.RMI MH16.3.
Notes: Slide 55 continues a discussion on storage racks.

## Slide 56: NBS Similar to Buildings Storage Racks
MH 16.1 and MH 16.3 are designed to be stand-alone standards to be adopted by reference.
Basic provisions developed during creation of FEMA 460 “Seismic Considerations for Steel Storage Racks”.
Notes: Slide 56 continues a discussion on storage racks. A reproduction of the cover art from FEMA 460 “Seismic Considerations for Steel Storage Racks” is shown on the right side of the slide.

## Slide 57: NBS Similar to Buildings Storage Racks
One area in MH 16.1 and MH 16.3 where the requirements are lacking is the anchorage requirements.
The anchorage provisions of MH 16.1 and MH 16.3 are not in conformance with ASCE 7-16.
Notes: Slide 57 continues a discussion on storage racks. A photograph of typical anchorage used on storage racks is shown on the right side of the slide.
The additional anchorage provisions include complying with ASCE 7-16 Section 15.4.9 ( requires use of ACI 318 Chapter 17) for anchorage design, the anchors must be sized using overstrength load combinations of ASCE 7-16 Sections 2.3.6 or 2.4.3, and the anchors must be designed for any bending created when shims are used.

## Slide 58: NBS Similar to Buildings Storage Racks
Typical Steel Storage Rack
Typical Steel Cantilevered Storage Rack
http://www.mhi.org/rmi
http://www.mhi.org/rmi
Notes: Slide 58 shows a photograph of a typical steel storage rack on the left and a picture of a typical steel cantilevered storage rack on the right.

## Slide 59: NBS Similar to Buildings Electrical Power Generating Facilities
Electrical power plants closely resemble building structures and their performance in seismic events has been good.
The lateral bracing system of choice has been the ordinary concentrically braced frame.
Based on acceptable past performance, Table 15.4-1 permits the use of ordinary concentrically braced frames with both lower R values and less restrictive height limits.
Notes: Slide 59 begins a discussion on structural towers for tanks and vessels.
The option of lower R values and less restrictive height limits was previously discussed in the presentation on pipe racks.

## Slide 60: NBS Similar to Buildings Structural Towers for Tanks and Vessels
Section 15.5.5 applies to structural towers that are not integral with the supported tank.
Elevated water tanks designed in accordance with AWWA D100-11 (2011) are not subject to Section 15.5.5.
A structural tower supporting a tank or vessel is considered integral with the supported tank vessel where the tank or vessel shell acts as a part of the seismic force-resisting system of the supporting tower.
Notes: Slide 60 begins a discussion on structural towers for tanks and vessels.

## Slide 61: NBS Similar to Buildings Structural Towers for Tanks and Vessels
Structural Tower Not Integral with Supported Tank
Structural Tower Integral with Supported Tank
Photo Courtesy of CB&I LLC
Photo Courtesy of Chevron
Notes: Slide 61 shows an example of a structural tower that is not integral with the supported tank is shown on the left. An example of a structural tower that is integral with the supported tank is shown on the right of the slide. Examples of structural towers that are integral with the supported tank include column supported elevated water tanks designed to AWWA D100 and column supported liquid and gas spheres designed to ASME BPVC Sect VIII.

## Slide 62: NBS Similar to Buildings Piers and Wharves
The seismic requirements of ASCE 7-16 only apply to piers and wharves that are accessible to the general public such as cruise ship terminals and piers with retail or commercial offices or restaurants.
Piers and wharves not accessible to the general public, such as a container terminal, are not within the scope of ASCE 7-16.
Notes: Slide 62 is a discussion on piers and wharves.
Current industry practice recognizes the distinct differences between the two categories of piers and wharves described in the standard. Piers and wharves with public occupancy, described in Section 15.5.6.2, are commonly treated as the “foundation” for buildings or building like structures; design is performed using the standard, likely under the jurisdiction of the local building official. Piers and wharves without occupancy by the general public are often treated differently and are outside the scope of the standard; in many cases, these structures do not fall under the jurisdiction of building officials, and design is performed using other industry-accepted approaches.

## Slide 63: NBS Not Similar to Buildings
Photo Courtesy of GE Power
http://www.publicdomainpictures.net/view-image.php?image=2832&picture=large-ferris-wheel
Notes: Slide 63 shows three photographs of nonbuilding structures not similar to buildings. The photograph on the left is an amusement park structure. The photograph in the center is a Steel Tubular Support Structures for Onshore Wind Turbine Generator (WTG) System. The photograph on the right is a Ground-Supported Cantilever Wall.

## Slide 64: NBS Not Similar to Buildings
  Provisions found in Sections 15.6 and 15.7.
  Designed and constructed with structural systems NOT similar to buildings.
  Have dynamic response NOT similar to buildings.
Notes: Slide 64 begins a discussion on nonbuilding structures not similar to buildings.

## Slide 65: NBS Not Similar to Buildings
  Specific requirements given for:
      Earth-Retaining Structures (15.6.1)
      Chimneys and Stacks (15.6.2)
      Amusement Structures (15.6.3)
      Special Hydraulic Structures (15.6.4)
      Secondary Containment Systems (15.6.5)
      Telecommunication Towers (15.6.6)
      Steel Tubular Support Structures for Onshore Wind Turbine Generator Systems (15.6.7)
      Ground-Supported Cantilever Walls or Fences (15.6.8)
      Tanks and Vessels (15.7)
Notes: Slide 65 continues a discussion on nonbuilding structures not similar to buildings.

## Slide 66: NBS Not Similar to Buildings Earth-Retaining Structures
Section 15.6.1 requires that all earth-retaining structures in Seismic Design Categories D, E, and F be designed for lateral earth pressures caused by earthquake ground motions.
Lateral earth pressures to be determined in accordance with Section 11.8.3.
https://www.cefns.nau.edu/capstone/projects/CENE/2014/Landfill-RDC/Retaining%20Wall%20pics.jpg
Notes: Slide 66 discusses earth-retaining structures. A sketch of a typical cantilever retaining wall is shown on the right of the slide.
Earth-retaining walls are permitted to be designed for seismic loads as either yielding or nonyielding walls. Cantilevered reinforced concrete or masonry retaining walls shall be assumed to be yielding walls and shall be designed as simple flexural wall elements.
No reference document exists for this type of nonbuilding structure.
The risk category is to be determined by the proximity of the earth-retaining structure to other buildings and structures. If failure of the earth-retaining structure would affect the adjacent building or structure, the risk category shall not be less than that of the adjacent building or structure.

## Slide 67: NBS Not Similar to Buildings Chimneys and Stacks
Section 15.6.2 provides specific requirements for chimneys and stacks of concrete or steel.
  Concrete chimneys and stacks are to be designed to ACI 307 as modified by Section 15.6.2.2.
  Extensive detailing requirements are given for large breach openings in concrete chimneys and stacks.
  Steel stacks are to be designed to ASME STS-1.
Notes: Slide 67 discusses chimneys and stacks. A photograph of a large breach opening in a stack is shown on the right of the slide.
The design of stacks and chimneys to resist natural hazards generally is governed by wind design considerations. The exceptions to this general rule involve locations with high seismicity, stacks and chimneys with large elevated masses, and stacks and chimneys with unusual geometries.
Concrete chimneys typically possess low ductility, and their performance is especially critical in the regions around large (breach) openings because of reductions in strength and loss of confinement for vertical reinforcement in the jamb regions around the openings. Earthquake-induced chimney failures have occurred in recent history (in Turkey in 1999) and have been attributed to strength and detailing problems (Kilic and Sozen 2003). The detailing requirements in 15.6.2.2 address these issues.

## Slide 68: NBS Not Similar to Buildings Amusement Structures
No specific requirements are provided in 15.6.3 for amusement structures other than to comply with Section 15.4 “Structural Design Requirements”.
No reference document exists for this type of nonbuilding structure.
http://www.publicdomainpictures.net/view-image.php?image=2832&picture=large-ferris-wheel
Notes: Slide 68 discusses amusement structures. A photograph of a Ferris wheel is shown on the right of the slide.

## Slide 69: NBS Not Similar to Buildings Special Hydraulic Structures
Special hydraulic structures are structures that are contained inside liquid containing structures.
Exposed to liquids on both wall surfaces under normal operating conditions.
Section 15.6.4 provides only basic guidance.
Notes: Slide 69 discusses special hydraulic structures. A sketch of a typical hydraulic structure is shown on the right of the slide.
Special hydraulic structures are subjected to out-of-plane forces only during an earthquake where the structure is subjected to differential hydrodynamic fluid forces. Examples of special hydraulic structures include separation walls, baffle walls, weirs, and other similar structures.
The most common special hydraulic structures are baffle walls and weirs that are used in water treatment and wastewater treatment plants. Because there are openings in the walls, during normal operations the fluid levels are equal on each side of the wall, exerting no net horizontal force. Sloshing during a seismic event can exert large forces on the wall, as illustrated in the slide figure. The walls can fail unless they are designed properly to resist the dynamic fluid forces.
No reference document exists for this type of nonbuilding structure.

## Slide 70: NBS Not Similar to Buildings Secondary Containment Systems
Per Section 15.6.5, secondary containment systems, such as impoundment dikes and walls, are to meet the requirements of the applicable standards for tanks and vessels.
Secondary containment systems are to withstand the effects of the MCER ground motion where empty and an aftershock of two-thirds of the MCER ground motion where full.
Notes: Slide 70 discusses secondary containment systems.
Secondary containment is designed for the MCER assuming that the primary containment releases its contents during an MCER event. Therefore, the secondary containment must remain in tact during the MCER event in order to contain the release. Section 15.6.5 reflects the judgment that designing all impoundment dikes for the MCER ground motion when full and sizing all impoundment dikes for the sloshing liquid height is too conservative. Designing an impoundment dike as full for the MCER assumes failure of the primary containment and occurrence of a significant aftershock. Such significant aftershocks (of the same magnitude as the MCER ground motion) are rare and do not occur in all locations. Although explicit design for aftershocks is not a requirement of the standard, secondary containment must be designed full for an aftershock to protect the general public. The use of two-thirds of the MCE ground motion as the magnitude of the design aftershock is supported by Bath’s law, according to which the maximum expected aftershock magnitude may be estimated to be 1.2 scale units below the main shock magnitude.
The risk assessment and risk management plan described in Section 1.5.3 are used to determine where the secondary containment must be designed full for the MCER. The decision to design secondary containment for this more severe condition should be based on the likelihood of a significant aftershock occurring at the particular site, considering the risk posed to the general public by the release of hazardous material from the secondary containment.

## Slide 71: NBS Not Similar to Buildings Telecommunication Towers
No specific requirements are provided in 15.6.6 for telecommunication towers other than to comply with Section 15.4 “Structural Design Requirements”.
No reference document exists for this type of nonbuilding structure.
Notes: Slide 71 discusses telecommunication towers. A photograph of a telecommunication tower is shown on the right of the slide.
Telecommunication towers support small masses, and their design generally is governed by wind forces. Although telecommunication towers have a history of experiencing seismic events without failure or significant damage, seismic design in accordance with ASCE 7-16 is required.

## Slide 72: NBS Not Similar to Buildings Steel Tubular Support Structures for Onshore Wind Turbine Generator (WTG) Systems
No specific requirements are provided in 15.6.7 for WTG structures other than to comply with Section 15.4 “Structural Design Requirements”.
No reference document exists for this type of nonbuilding structure.
Photo Courtesy of GE Power
Notes: Slide 72 discusses steel tubular support structures for onshore wind turbine generator (WTG) systems. A sketch of a typical WTG structure is shown on the right of the slide.
The most common support structures for large onshore wind turbine generator systems are steel tubular towers. Recommendations for the design of these structures can be found in American Society of Civil Engineers/ American Wind Energy Association (ASCE/AWEA). (2011), “Recommended Practice for Large Land-based
Wind Turbine Support Structures”. ASCE/AWEA RP2011. ASCE/AWEA RP2011 applies to wind turbines having a rotor-swept area greater than 2153 ft2 (200 m2). These recommendations are to be used in conjunction with seismic lateral forces determined in accordance with Section 15.4 because ASCE/AWEA RP2011 is not a reference standard adopted by ASCE 7-16. ASCE/AWEA RP2011 is not written in mandatory language.

## Slide 73: NBS Not Similar to Buildings Ground-Supported Cantilever Walls or Fences
Walls or fences ≥ 6 ft. are to be designed to resist earthquake ground motions in accordance with Section 15.4.
Detailed plain and ordinary plain concrete or masonry walls or fences and ordinary plain AAC walls or fences are not permitted in SDC C, D, E and F.
Notes: Slide 73 discusses ground-supported cantilever walls or fences. A photograph of a ground-supported cantilever wall is shown on the right of the slide.
Ground-supported cantilever walls and fences constructed from masonry, concrete, timber, or a combination of materials, including steel, are common. Such walls are often used as sound barrier walls or to limit access to residential subdivisions. Ground-supported cantilever walls and fences include walls supported by a footing and pier and panel/pilaster and panel wall systems as long as these systems are not supported laterally in the out-of-plane direction above grade.
Many improperly designed ground-supported cantilever walls and fences constructed from masonry or concrete have experienced problems and have failed during seismic events as evidenced in Section 6.3.9.1 of FEMA E-74, Reducing the Risks of Nonstructural Earthquake Damage – A Practical Guide.

## Slide 74: Tanks and Vessels
Photo Courtesy of CB&I LLC
Photo Courtesy of CB&I LLC
Photo Courtesy of CB&I LLC
Notes: Slide 74 shows three photographs of tanks and vessels. The photograph on the left is of a tank farm. The photograph in the center is an elevated water tank. The photograph on the right are column supported spherical pressure vessels.

## Slide 75: Tanks and Vessels
  15.7.1 General
  15.7.2 Design Basis
  15.7.3 Strength and Ductility
  15.7.4 Flexibility of Piping Attachments
  15.7.5 Anchorage
  15.7.6 Ground-Supported Storage Tanks for Liquids
  15.7.7 Water Storage and Water Treatment Tanks and Vessels
  15.7.8 Petrochemical and Industrial Tanks and Vessels Storing Liquids
  15.7.9 Ground-Supported Storage Tanks for Granular Materials
  15.7.10 Elevated Tanks and Vessels for Liquids and Granular Materials
  15.7.11 Boilers and Pressure Vessels
  15.7.12 Liquid and Gas Spheres
  15.7.13 Refrigerated Gas Liquid Storage Tanks and Vessels
  15.7.14 Horizontal, Saddle-Supported Vessels for Liquid or Vapor Storage
Notes: Slide 75 begins a discussion on the seismic requirements for tanks and vessels. The outline of Section 15.7 is shown in the slide. The sections shown in bold and blue are discussed in detail in the following slides.
The requirements (Section 15.7) for tanks and vessels are separated from other nonbuilding structures not similar to buildings due to the shear volume of different types of tanks and vessels, different reference standards, and specific design provisions that apply only to tanks and vessels.
Most of the seismic design requirements are contained in reference documents specified throughout Section 15.7.

## Slide 76: Tanks and Vessels Design Basis
Seismic loads in liquid tanks are made up of three components:
  impulsive (rigid mass of the tank shell, roof, and part of the product)
  convective (sloshing mass of the liquid)
  vertical
Notes: Slide 76 discusses the three seismic load components in liquid storage tanks. The figure to the right is a generalized tank model including the impulsive and convective masses.
Sections 15.7.1 (General) and 15.7.2 (Design Basis) cover the unique aspects of the seismic design of tanks and vessels. The following is the currently accepted method for the dynamic modeling of the tank and its contents:
When a liquid-filled tank is subjected to ground acceleration, the lower portion of the contained liquid, identified as the impulsive component of mass, mi, acts as if it were a solid mass rigidly attached to the tank wall. As this mass accelerates, it exerts a horizontal force, Pi, on the wall; this force is directly proportional to the maximum acceleration of the tank base. This force is superimposed on the inertia force of the accelerating wall itself, Ps. Under the influence of the same ground acceleration, the upper portion of the contained liquid responds as if it were a solid mass flexibly attached to the tank wall. This portion, which oscillates at its own natural frequency, is identified as the convective component, mc, and exerts a horizontal force, Pc, on the wall. The convective component oscillations are characterized by sloshing whereby the liquid surface rises above the static level on one side of the tank and drops below that level on the other side.

## Slide 77: Tanks and Vessels Design Basis
Convective (sloshing) forces to be evaluated at 0.5% damping at convective period Tc.
  1.5 is used to convert 5% damping to 0.5% damping
Impulsive and convective components to be combined by direct sum or SRSS.
Vertical earthquake forces must be considered (hydrodynamic hoop forces and vertical inertia forces).
Notes: Slide 77 continues the discussion of the unique design considerations for tanks and vessels storing liquids.

## Slide 78: Tanks and Vessels Strength and Ductility
Connection of the anchors to tank to develop the lesser of the strength of the anchor or Ω0 times the calculated anchor force.
Penetrations, manholes, and openings in shell must maintain the strength and stability of the shell.
Support towers using tension-only bracing shall be designed such that the full cross section of the tension element can yield during overload conditions
Notes: Slide 78 discusses some of the strength and ductility requirements for tanks and vessels.
As is the case for building structures, ductility and redundancy in the lateral support systems for tanks and vessels are desirable and necessary for good seismic performance. Tanks and vessels are not highly redundant structural systems, and therefore ductile materials and well-designed connection details are needed to increase the capacity of the vessel to absorb more energy without failure. The critical performance of many tanks and vessels is governed by shell stability requirements rather than by yielding of the structural elements. For example, contrary to building structures, ductile stretching of anchor bolts is a desirable energy absorption component where tanks and vessels are anchored. That is why the connection to the shell and the anchor rod embedment are designed to be stronger than the anchor rod. The performance of cross-braced towers is highly dependent on the ability of the horizontal compression struts and connection details to develop fully the tension yielding in the rods. In such cases, it is also important to preclude both premature failure in the threaded portion of the connection and failure of the connection of the rod to the column before yielding of the rod.

## Slide 79: Tanks and Vessels Strength and Ductility
There are 4 special considerations for tanks and vessels that will be discussed in the following slides:
  The importance of providing piping flexibility (15.7.4).
  The importance of anchor rod stretch (15.7.5).
  The importance of providing seismic freeboard (15.7.6.1.2).
  Special design requirements for vessel support skirts.
Notes: Slide 79 highlights four special considerations that will be discussed in later slides.

## Slide 80: Tanks and Vessels Flexibility of Piping Attachments
Notes: Slide 80 reproduces ASCE 7-16 Table 15.7-1 (Minimum Design Displacements for Piping Attachments)
  The lack of flexibility in the piping connections to tanks is a continuing source of seismic damage to ground supported storage tanks. Design of piping systems connected to tanks and vessels are to consider the potential movement of the connection points during earthquakes and provide sufficient flexibility to avoid release of the product by failure of the piping system. The piping system and supports are to be designed so as not to impart significant mechanical loading on the attachment to the tank or vessel shell. Mechanical devices that add flexibility, such as bellows, expansion joints, and other flexible apparatus, are permitted to be used where they are designed for seismic displacements and defined operating pressure.
The displacements shown are ASD level displacements. The piping system and tank connection are to be designed to tolerate Cd times the displacements given in Table 15.7-1 without rupture, although permanent deformations and inelastic behavior in the piping supports and tank shell are permitted.

## Slide 81: Tanks and Vessels Flexibility of Piping Attachments
Flexibility Provided
Flexibility Not Provided
Courtesy of Paul B. Summers, P.E., S.E.
Courtesy of Paul B. Summers, P.E., S.E.
Notes: Slide 81 shows examples of piping flexibility. The photograph on the left shows a proper flexible detail. The photograph on the right shows a detail with no flexibility.
The good, the bad, and the ugly (right picture is bad and ugly) of piping connections. The connection on the right was in a west coast refinery and would have failed in a major seismic event. It has since been fixed.

## Slide 82: Tanks and Vessels Anchorage
Many nonbuilding structures rely on the ductile behavior of anchor bolts to justify the R value assigned to the structure.
Anchor bolts used for tanks and vessels must stretch under seismic loads to provide the required ductility.
Stretched Bolt on Stack
February 27, 2010 Chile Earthquake
Added Washers
Notes: Slide 82 begins a discussion on anchorage for tanks and vessels. The photograph on the right shows a stretched anchor bolt on a steel stack after the February 27, 2010 Chile Earthquake. The steel stack was otherwise undamaged.

## Slide 83: Tanks and Vessels Anchorage
    Section 15.7.5 requires anchor bolt embedment design to meet ACI 318-14 Chapter 17.
    Section 15.7.5 requires anchorage to meet the requirements of Section 15.4.9.
    Anchor embedment into the concrete must be designed to develop the steel strength of the anchor in tension (ACI 318 Eq. 17.4.1.2).
    The anchor must have a minimum gauge length of eight diameters.
Notes: Slide 83 continues the discussion on the design of anchorage for tanks and vessels.
All of the requirements shown above are to insure that the anchor rod stretches before it pulls out of the concrete.

## Slide 84: Tanks and Vessels Anchorage
    The load combinations with overstrength of Section 12.4.3 are not to be used to size the anchor bolts for tanks, horizontal and vertical vessels.
    Oversized anchors will not be able to stretch and therefore, not provide the required ductility.
    These requirements only apply to structures located in SDC C, D, E, and F.
Notes: Slide 84 continues the discussion on the design of anchorage for tanks and vessels.
The bottom line in this discussion is to NOT oversize the anchor rods for tanks and vessels.

## Slide 85: Tanks and Vessels Anchorage
Notes: Slide 85 shows a sketch of a cast-in-place anchor with anchor reinforcement on the left and a sketch showing graphically the definition of bolt gauge length.
These sketches show the end result of the previously discussed requirements concerning anchor rod embedment design. Anchor reinforcement (left figure) will have to be provided in most cases around the anchor rod to develop the tensile capacity of the anchor rod.

## Slide 86: Tanks and Vessels Ground-Supported Storage Tanks for Liquids
Impact of the sloshing wave on the tank roof or forcing the floating roof into a fixed roof is a continuing source of seismic damage to ground supported storage tanks.
Occasionally, external floating roofs are forced outside of the tank shell by the sloshing wave and end up landing on the shell or the seal catches the shell.
Loss of a floating roof in any of these cases often results in a fire.
This damage can be eliminated by providing sufficient seismic freeboard.
Notes: Slide 86 begins a discussion on the required freeboard for ground-supported storage tanks for liquid.
Damage to tanks still occurs due to insufficient seismic freeboard.

## Slide 87: Tanks and Vessels Ground-Supported Storage Tanks for Liquids
TABLE 15.7-3 MINIMUM REQUIRED FREEBOARDa |  |  | 
Value of SDS | Risk Category |  | 
 | I or II | III | IV
SDS < 0.33g | Not Required | Not Required | δs
SDS ≥ 0.33g | Not Required | 0.7δs | δs
aSee Section 15.7.6.1.2.
Notes: Slide 87 shows a reproduction of the ASCE 7-16 Table 15.7-3 for minimum required freeboard. The equation for freeboard is shown below the table.
The table shown in the slide lists the freeboard requirements. Please note that if the tank or vessel is an essential facility whose operation is required after a seismic event, the provision shown in Section 15.7.6.1.2 allowing the seismic freeboard to be eliminated if secondary containment is provided DOES NOT APPLY.
An essential facility, such as a fire water tank, must be able to operate after the seismic event. The fire water tank will likely not be able to operate if the roof is heavily damaged.

## Slide 88: Tanks and Vessels Ground-Supported Storage Tanks for Liquids
SLOSHING WAVE DAMAGE
Photo Courtesy of CB&I LLC
Notes: Slide 88 shows two photographs of tanks with damage from the sloshing wave.

## Slide 89: Tanks and Vessels Elevated Tanks and Vessels for Liquids and Granular Materials
Photo Courtesy of CB&I LLC
Skirt supported vessels fail in buckling, which is not a ductile failure mode.
To prevent collapse, ASCE 7 Section 15.7.10 and Table 15.4-2 require skirt supported vessels to be checked for seismic loads based on R/I = 1.0 if the structure falls in Risk Category IV or if an R-value of 3.0 is used in the design.
Notes: Slide 89 begins a discussion special requirements for the design of skirt supported vessels. The right side of the slide shows a photograph of a skirt supported vertical vessel.

## Slide 90: Tanks and Vessels Elevated Tanks and Vessels for Liquids and Granular Materials
Notes: Slide 90 shows a portion of Table 15.4-2 showing detailing requirements and corresponding R values for skirt supported vessels.

## Slide 91: Tanks and Vessels Elevated Tanks and Vessels for Liquids and Granular Materials
Special design requirements for vessel support skirts are required when the vessel falls in Risk Category IV or when R = 3 is used.
Notes: Slide 91 shows an excerpt on the right side from Section 15.7.10.5 (Evaluation of Structures Sensitive to Buckling Failure). The highlighted portion shown states “structures specified in this standard to be designed to subsections a and b below and those that are assigned as Risk Category IV shall be designed to resist the seismic forces as follows:”
The requirements noted in the slide require that the skirt support remain elastic during the design earthquake event.

## Slide 92: Tanks and Vessels Elevated Tanks and Vessels for Liquids and Granular Materials
The R/I = 1.0 check will typically govern the design of the skirt over using loads determined with an R-factor of 3 in a moderate to high area of seismic activity.
The only benefit of using an R-factor of 3 in this case is in the design of the foundation.
The foundation is not required to be designed for the R/I = 1.0 load.
Notes: Slide 92 continues the discussion on the special requirements for skirt supported vessels.

## Slide 93: Tanks and Vessels Elevated Tanks and Vessels for Liquids and Granular Materials
For the R/I = 1.0 load, the skirt can be designed based on critical buckling (factor of safety of 1).
The critical buckling strength of a skirt can be determined using a number of published sources.
The two most common methods for determining the critical buckling strength of a skirt are ASME BPVC Section VIII, Division 2 Paragraph 4.4 using a factor of safety of 1.0 and AWWA D-100 Section 13.4.3.4.
Notes: Slide 93 continues the discussion on the special requirements for skirt supported vessels.
Examples of this critical buckling check of a skirt support can be found in the ASCE 7-16 Chapter 15 commentary.

## Slide 94: Suggested References
  Bachman, Robert and Dowty, Susan, “Nonstructural Component or Nonbuilding Structure?”, Building Safety Journal, International Code Council, April-May 2008.
“Guidelines for Seismic Evaluation and Design of Petrochemical Facilities”, 2nd Edition, 2011, ASCE
Notes: Slide 94 lists suggested references to aid in the seismic design of nonbuilding structures. These references contain pertinent information of the design of nonbuilding structures and have been referenced in the presentation notes.

## Slide 95: Suggested References
“Design of Structural Steel Pipe Racks” by Richard M. Drake and Robert J. Walter, AISC Engineering Journal, 4th Quarter, 2010.
Soules, J. G., “The Seismic Provisions of the 2006 IBC – Nonbuilding Structure Criteria,” Proceedings of 8th National Conference on Earthquake Engineering, San Francisco, CA, April 18, 2006.
Notes: Slide 95 lists suggested references to aid in the seismic design of nonbuilding structures. These references contain pertinent information of the design of nonbuilding structures and have been referenced in the presentation notes.

## Slide 96: Suggested References
Soules, J. G., Bachman, R.E., and Silva, J.F., “Chile Earthquake of 2010 – Assessment of Industrial Facilities around Concepción”, American Society of Civil Engineers, Structural Engineering Institute, Reston, VA, 2016.
Notes: Slide 96 lists a suggested reference to aid in the seismic design of nonbuilding structures. This reference contains pertinent information of the design of nonbuilding structures and have been referenced in the presentation notes.

## Slide 97: Questions?
Notes: Slide 97 is the “question” slide.

## Slide 98: DISCLAIMER
NOTICE: Any opinions, findings, conclusions, or recommendations expressed in this publication do not necessarily reflect the views of the Federal Emergency Management Agency. Additionally, neither FEMA nor any of its employees make any warranty, expressed or implied, nor assume any legal liability or responsibility for the accuracy, completeness, or usefulness of any information, product or process included in this publication.
The opinions expressed herein regarding the requirements of the NEHRP Recommended Seismic Provisions, the referenced standards, and the building codes are not to be used for design purposes. Rather the user should consult the jurisdiction’s building official who has the authority to render interpretation of the code.
Any modifications made to the file represent the presenters' opinion only.