## Slide 1: Structures with Supplemental Energy Dissipation Devices
Disclaimer
DESIGN EXAMPLE
William McVitty, P.E., M.S., Andrew Taylor, S.E., Ph.D
Notes: Graphic shows cover of the NEHRP Provisions FEMA P-1052.
The 2015 NEHRP Recommended Seismic Provisions are a new resource document that facilitates and translates the state-of-the-art knowledge into design practice. To help in understanding these new Provisions, design examples are also published which apply the new requirements of FEMA P-1051. This presentation complements the Chapter 16 design example of structures that incorporate supplemental energy dissipation devices.
This set of instructional slides is the second of two 90 minute presentations. The first presentation provided background on supplemental energy dissipation devices and major changes to their seismic design requirements.

## Slide 2: Presentation Objectives
Illustrate application of the new NEHRP Provisions through a design example
  Seven story office building in region of high seismicity
  Steel moment frame with supplemental fluid viscous dampers
  Note: A full replacement of Chapter 18, ASCE 7-2016 (the Standard) was recommended.
Notes: A graphic shows the cover of the document FEMA P-1050-1, 2015 Edition, “NEHRP Recommended Seismic Provisions for New Buildings and Other Structures”
The objective of this second presentation is to illustrate the application of the NEHRP Provisions requirements. This is achieved through the design of a seven story steel moment frame office building, located in a region of high seismicity (seismic design category D), which is supplemented with nonlinear fluid viscous damping devices.
Due to the large number of editorial and technical changes, the 2015 NEHRP Provisions have recommended a full replacement of Chapter 18 in the 2016 edition of ASCE 7 (referred to hereafter as the Standard).

## Slide 3: Overview of Design Example
Project Information
Design Process
Design Considerations
  Design Decisions & Preliminary Design
Structural Analysis
    Damper Properties & Nonlinear Response History Analysis
Design of SFRS and
Design of Damping System
Notes: This presentation closely follows the design example sections.

## Slide 4: 1. Project Information
Structural Description
Notes: This slide contains a drawing of the structural frame of a building that is 7 stories high, 5 bays wide, and 7 bays long.
This example uses a seven-story office building located in a region of high seismicity, classified as Seismic Design Category D. The building has steel special moment resisting frames (SMRF) around the perimeter and fluid viscous dampers (FVD) in interior frames. The design of the SMRF without energy dissipation devices, for a comparable area of seismicity, is illustrated in Chapter 9 of the NEHRP design examples. The details of that building are directly adopted as a starting point for this example.

## Slide 5: 1. Project Information
Structural Description: Typical Plan
Notes: This slide shows the plan view of the building, 5 bays wide by 7 bays long.
The building has a rectangular plan configuration measuring 175 feet, in the East-West direction and 125 feet wide in the North-South direction. The seismic force resisting system (SFRS) consists of steel special moment resisting frames (SMRF) with prequalified Reduced Beam Section (RBS) connections located on the perimeter bays of the building along Gridlines A, H, 1 and 6.

## Slide 6: 1. Project Information
Structural Description: Typical Elevation
Notes: This slide contains a drawing of an elevation of the building, 7 bays wide and 7 stories tall. In addition there is a penthouse above the 7th story.
The typical story height is 13 feet, 4 inches but with a first story height of 22 feet, 4 inches. The building has a penthouse that extends 16 feet above the roof level of the building and covers the area bounded by Gridlines C, F, 3 and 4 (see previous slide).

## Slide 7: 1. Project Information
Structural Description: SFRS Gridlines 1 and 6
Notes: This slide contains an elevation of one of the special moment frames on gridlines 1 and 6. The sizes of beams and columns are shown on the diagram.
The member sizes for the SFRS are directly adopted from the Chapter 9 analysis and are shown here for Gridlines 1 and 6.

## Slide 8: 1. Project Information
Structural Description: SFRS Gridlines A and H
Notes: This slide contains an elevation of one of the special moment frames on gridlines A and H. The sizes of beams and columns are shown on the diagram.
The SFRS member sizes are shown here for Gridlines A and H.

## Slide 9: 1. Project Information
Reference: Taylor Devices
Structural Description: Damping System
Fluid Viscous Dampers (FVD)
Notes: This slide shows a drawing of a cross section of a fluid viscous damper. In addition there is a photograph of an elevation of two structural framing bays showing two diagonal braces, each with a fluid viscous damper arranged in line with the brace.
Supplemental damping is primarily used to limit deformations in structural components, and thus to achieve a higher performance level. For this design example, fluid viscous dampers (FVDs) are arbitrarily selected as the supplemental energy dissipation devices (or simply “dampers"). The key components of a FVD are shown along with an example of its implementation in a building.

## Slide 10: 1. Project Information
Stories 3-7
Stories 1-2
Structural Description: Damping System
Notes: This slide contains two drawings of the plan view of the building. The building is 5 bays wide by 7 bays long. The left plan is labeled “Stories 1-2.” This plan has four damper bays in each direction. The right plan is labeled “Stories 3-7”. This plan has two damper bays in each direction.
The plan view of the bays with damping devices for stories 1 to 2 and 3 to 7 are shown. To meet the architect’s requirement of having no diagonal bracing members around the perimeter of the building, supplemental damping devices are located on gravity framing lines on the interior of the structure on Gridlines B, G, 2, and 5. More damping devices were required in the lower story's (as will be shown later by preliminary design).

## Slide 11: 1. Project Information
Structural Description: Damping System Gridlines 2 & 5
Notes: This slide contains a drawing of the structural frame elevation at Gridlines 2 and 5. Damper locations are shown. In stories 1 and 2 there are two bays containing dampers, while in the remaining upper stories there is only only one bay containing a damper.

## Slide 12: 1. Project Information
Structural Description: Damping System Gridlines B & G
Notes: This slide contains a drawing of the structural frame elevation at Gridlines B and G. Damper locations are shown. In stories 1 and 2 there are two bays containing dampers, while in the remaining upper stories there is only only one bay containing a damper.

## Slide 13: 1. Project Information
Seismic Weight:
Penthouse roof = 94 kip
Lower roof = 1537 kip
Typical floor = 1920 kip
Total seismic weight, W
= 94 kips + 1,537 kips + 6 (1,920 kips) = 13,151 kips
Notes: The seismic weight of the building is calculated for each floor and totals 13,151 kips.

## Slide 14: 1. Project Information
   §11.4.7 Site-specific hazard analysis required
Ground Motion Criteria
Site Hazard and Soil Conditions
  Region of high-seismicity
  Seismic Design Category D
  Soil site class D
Spectral Accelerations
  SDS = 0.93 (SMS = 1.4)
  SD1 = 0.6 (SM1 = 0.6)
  S1 = 0.5
Notes: A graph shows examples of several project-specific earthquake response spectra that could be used for design. These spectra are meant to be a schematic illustration only, so the details of the shapes and magnitudes of the spectra are not relevant.
The building is located in a region of high seismicity, classified as SDC “D”. Since the building is also located on site class D soils, a site-specific hazard analysis is required to determine the target response spectrum to be used for design.

## Slide 15: 1. Project Information
Ground Motion Criteria
Analysis Procedure = Nonlinear Response History Analysis (NLRHA)
Therefore need to select and scale ground motion records:
Nearest active fault > 3 miles away
Therefore apply ground motions in only one random orientation to analysis model
Notes: This slide contains two graphs showing earthquake accelerographs, representing the two orthogonal components of a recorded earthquake ground motion.
Ground motions must be selected and scaled since NLRHA is used.

## Slide 16: 1. Project Information
Ground Motion Criteria
Selected seven ground motions from actual earthquake recordings that have similar hazards to the building site.
Notes: Contrary to Chapter 16 NLRHA (which requires 11 ground motions), Chapter 18 requires a minimum of seven ground motions selected and scaled by a specialist.

## Slide 17: 1. Project Information
Ground Motion Criteria
Scaling method = Amplitude scaling
Period range of interest = 0.2T1D to1.25T1M
        = 0.58 to 3.9 seconds
Notes:   A graph shows several earthquake acceleration response spectra. A smoothed target response spectrum is shown in black. Seven earthquake response spectra are shown as dashed lines. A spectrum showing the average of the seven earthquake spectra is shown in red. This red spectrum matches fairly closely the target spectrum over the period range 1 to 4 seconds.
Amplitude scaling is the chosen scaling method. The period range of interest is calculated as the product of 0.2 and the shorter period in the east-west direction (2.9 sec) and the product of 1.25 and the longer period in the north-south direction (3.1 sec), giving a scaling range of 0.58 to 3.9 seconds. This assumes that the building remains elastic at both the design basis and MCER hazard levels and that the FVD’s have little influence on the buildings fundamental period.
The response spectrum for each of the horizontal ground motion components is calculated and the combined square root sum of the square (SRSS) of the two components for each ground motion is shown. The average SRSS spectrum of the seven ground motions (red line) must be above the corresponding spectral acceleration ordinate of the target spectrum over the period range of 0.58 to 3.9 seconds. As shown, in the scaling meets this requirement of the Standard.

## Slide 18: 2. Design Process
Project & Ground Motion Criteria
Preliminary Design of SFRS (without dampers)
Preliminary Design of Damping System
Final Specifications
Damping Device Maximum and Minimum Properties
Nonlinear Response History Analysis
(trial and error iterations)
Re-check SFRS (with dampers included)
Notes: An illustration shows the steps for design of a damped building. The steps are numbered from I through VII, and are to be followed sequentially.
This slide illustrates the typical sequence of tasks for design. Preliminary design involved adopting the seismic force resisting system (SFRS) member sizes directly from the Chapter 9 NEHRP example.

## Slide 19: 3. Design Considerations
Performance goals?
Amount of added damping?
Analysis procedure selection?
Viscous damper velocity exponent?
Placement and configuration of dampers?
Notes: Before progressing with detailed design, there are a number of considerations.

## Slide 20: 3. Design Considerations
Performance Goals?
Resist minor and moderate earthquakes without damage.
Resist major earthquakes without failure of the damping system, or significant damage to structural and nonstructural components, or major disruption to facility function.
Achieved by sizing the SFRS to remain “essentially” elastic at the MCER level, with virtually all earthquake energy dissipated by the FVDs.
Notes: The use of supplemental damping devices is a design strategy to limit earthquake damage and protect facility function. Although the Standard allows comparable performance to conventional SFRS, this project aims to limit inelastic response of the structural system, which directly reduces the damage in the building that would otherwise be occurring (in a fixed-base building). Furthermore the structure and damping system are designed and tested for the MCER hazard instead of the design earthquake (DE).

## Slide 21: 3. Design Considerations
Added Damping?
Buildings 1-15 floors ~ 15-25%
Taller buildings ~ 5-15%
Target 20% added damping in the fundamental mode of vibration
Notes: A reduction in ductility demand in the SFRS is facilitated through displacement reductions, which come from increased damping provided by the FVD. However with increased damping typically comes increased base shear (depending on the FVD properties), which will need to be accommodated in the design of the structure and foundations. Nevertheless, in some cases the structural analysis may show benefits from higher damping ratios, greater than 35-45 percent. However at these high damping levels the damper costs starts going past the point of diminishing returns.

## Slide 22: 3. Design Considerations
Analysis Procedure Selection?
Nonlinear Response History
Alternative Procedures:
  Response Spectrum
  Equivalent Lateral Force
Use Nonlinear Response History Procedure
Notes: The Standard is formatted such that NLRHA is the preferred analysis method.

## Slide 23: 3. Design Considerations
FVD Velocity Exponent, α?
Linear, α = 1.0
Nonlinear, α = 0.3 – 0.5
Example uses α = 0.38
Notes: This slide contains two graphs. The left graph has horizontal axis labeled “Velocity (inch/sec)”, and vertical axis labeled “Force (kips)”. A solid straight line runs diagonally from the lower left corner to the upper right corner of the graph. This line is labeled “Linear Fluid Viscous Damper, alpha = 1.0”. A dashed line begins at the origin in the corner and forms a parabolic arc to the right, approaching a value about mid-way up the graph at the right edge. This line is labeled “Nonlinear Fluid Viscous Damper, alpha = 0.4” The graph on the right shows two lines that are nearly elliptical in shape. The solid line, corresponding to the linear damper, is a smooth ellipse, while the dashed line, corresponding to the nonlinear damper, forms an ellipse with slightly squared off corners. The nonlinear damper curve falls generally outside the linear damper curve.
The differing force-displacement behaviour of nonlinear and linear fluid viscous dampers (FVD) are illustrated. Consult with the manufacturer on the selection of the velocity exponent.

## Slide 24: 3. Design Considerations
FVD Velocity Exponent, α?
Interest in using nonlinear dampers:
  Capable of more energy dissipation per cycle for the same displacement amplitude
  Safeguard by limiting the transmission of damping force at velocities in excess of design values
Notes: This slide contains two graphs. The lower graph has horizontal axis labeled “Velocity (inch/sec)”, and vertical axis labeled “Force (kips)”. A solid straight line runs diagonally from the lower left corner to the upper right corner of the graph. This line is labeled “Linear Fluid Viscous Damper, alpha = 1.0”. A dashed line begins at the origin in the corner and forms a parabolic arc to the right, approaching a value about mid-way up the graph at the right edge. This line is labeled “Nonlinear Fluid Viscous Damper, alpha = 0.4” The upper graph shows two lines that are nearly elliptical in shape. The solid line, corresponding to the linear damper, is a smooth ellipse, while the dashed line, corresponding to the nonlinear damper, forms an ellipse with slightly squared off corners. The nonlinear damper curve falls generally outside the linear damper curve.
The main benefits of nonlinear FVDs are illustrated.

## Slide 25: 3. Design Considerations
FVD Velocity Exponent, α?
However:
  Highly nonlinear damping device can negatively impact the performance of non-structural components
  For nonlinear dampers, the maximum velocity (damper force) and maximum displacement (maximum shear force) are not out-of-phase.
Linear dampers recommended when used in-line with seismic isolation system
Notes: In some cases, the nonlinear FVD may not give the best performance.
Shake-table testing has shown that linear FVD give better performance than nonlinear FVD when used in-line with a base isolation system. Hence the use of FVD in isolation systems in the United States has progressed from nonlinear towards the use of linear FVD’s.

## Slide 26: 3. Design Considerations
Placement and Configuration of Dampers?
Positioned to reduce torsion and/or structural irregularities
Notes: This slide contains two drawings. The left drawing is a plan view of the building, 5 bays wide by 7 bays long. There are two bays of dampers in each direction. The right drawing shows an elevation of the building at a gridline containing dampers. At floors 1 and 2 there are two dampers per floor, and at the remaining upper floors there is one damper per floor.
The FVDs can be positioned to reduce torsion (by positioning them away from the center of stiffness), or may be positioned to reduce soft-story irregularities.

## Slide 27: 3. Design Considerations
Note: Patented. Reference: MCEER, SUNY, Buffalo, NY
Reference: Taylor Devices
Used in design example
Placement and Configuration of Dampers?
Three basic configurations:
  Diagonal
  Horizontal, In-line
  Geometric Amplification (toggle)
Notes: There are three small drawings at the bottom of this slide. The drawing on the left shows an elevation of a building with three stories, three bays wide. There is one damper per story configured as a diagonal brace. The drawing at the center shows an elevation of a building with three stories, three bays wide. There is one damped bay per floor. The dampers are configured in a horizontal orientation at the tip of chevron (inverted “V”) braces. The right drawing shows a single structural bay with a scissors brace configured between the lower right corner and about the one-third point of the upper beam.
There are three primary ways of configuring a FVD in a building. The displacement across the damper (i.e. effectiveness) increases from a) to c) configurations.

## Slide 28: 3. Design Considerations
Placement and Configuration of Dampers?
Large number of smaller dampers or small number of larger dampers?
Based on experience (Taylor 1999):
  Least expensive FVD are 300-600 kip range
  Cost of one 300 kip < ten 30 kip FVDs
Notes: Manufacture experience from past projects may be used in optimizing the number and size of dampers.

## Slide 29: 3. Design Considerations
Placement and Configuration of Dampers?
Iterative process:
  Start with multiple dampers of the same size and distribute throughout the structure
  Use the next larger damper size to reduce the number of dampers, until:
    The quantity of dampers goes below 32
    Damper force rating goes above 600 kip
    Structure behaves less efficiently since the dampers are not distributed advantageously
Notes: This process was proposed by Taylor 1999, and was used in the example.

## Slide 30: 3. Design Considerations
Step 1: Create mathematical model of building without dampers and conduct modal analysis
T1 = 3.1 seconds (north-south)
T2 = 2.9 seconds (east-west)
Preliminary Design
Based on method presented in Christopoulos and Filiatrault, 2006
Notes: This slide contains an isometric view of the framing system for the entire building, 5 bays wide, by 7 bays long, by 7 stories high. Also shown on this slide are views of two elevations of the building, one elevation in the longitudinal direction and the other in the transverse direction. Both elevations show the frames swaying to the side under applied lateral earthquake loads.
There is many different ways to conduct preliminary design. The Christopoulos and Filiatrault (2006) procedure calculates the linear viscous damping coefficients required of dampers at each story in order to achieve a certain damping ratio in a particular mode. The method assumes stiffness proportional damping.

## Slide 31: 3. Design Considerations
Preliminary Design
Step 2: Select an added damping for each primary mode. For example, 20% for modes 1 and 2
Step 3: Calculate the pseudo braced building periods
Tps,1 = 2.67 seconds
Tps,2 = 2.46 seconds
Notes: The pseudo (fictitious) braced period is calculated for 20% added damping in the first and second modes.

## Slide 32: 3. Design Considerations
Preliminary Design
Step 4: Add pseudo braces to the ETABS model (in locations where the dampers will be) with stiffnesses calibrated so the mode shapes are maintained and the mode 1 and 2 periods equal the pseudo braced periods calculated in Step 3.
Notes: To maintain the mode shape, the brace stiffnesses are calibrated according to the lateral stiffness of the unbraced structure.

## Slide 33: 3. Design Considerations
Pseudo braces Gridlines B and G
Trial added stiffness, with upper stories stiffnesses relative to this trial value to maintain first mode shape
Preliminary Design
Step 4: North-South direction:
Notes: There is an illustration on this slide showing an elevation of the building in the transverse direction, 5 bays wide by seven stories tall. A red box surrounds the center bays over the entire building height. This red box is labeled “Pseudo braces Gridlines B and G”. Diagonal braces are shown in these bays.
Shown are the pseudo braces added to the ETABS model for the N-S direction.

## Slide 34: 3. Design Considerations
Mode shape maintained
T1,ps = 2.67
Note: Requires only one iteration in selecting the pseudo stiffness
Preliminary Design
Step 4:
Notes: Two structural frames are shown in this drawing. The left frame is an elevation of a transverse section through the building, 5 bays wide by 7 stories tall. The center bays contain a diagonal brace at every story. The frame is shown displaced laterally under the influence of earthquake loads. The right frame is similar to the left frame, but no braces are shown in any bay. The frame is shown displaced laterally under the influence of earthquake loads. This frame is labeled “Mode shape maintained”.
The pseudo-braced building has a period which matches that calculated in Step 3 and has the same mode shape as the unbraced structure.

## Slide 35: 3. Design Considerations
Takes one iteration to give agreement
Preliminary Design
Step 4: North-South direction:
Notes: The values shown are for the second (final) iteration.

## Slide 36: 3. Design Considerations
Preliminary Design
Step 5: Calculate required linear viscous damping constant for each story
Notes: Based on stiffness proportional damping, the linear damping constants for horizontally- and diagonally-aligned FVDs is calculated.

## Slide 37: 3. Design Considerations
Preliminary Design
Reduce number of dampers to one type:
  Use linear FVD with damping coefficient of 50 kip-sec/inch
  Add two more bays of dampers in each direction in story's 1 and 2 and use linear FVD
Notes: It is not practical to use different damping coefficients at every level, and in each principle direction, thus engineering judgement is used to reduce the number of FVD to one type.

## Slide 38: 3. Design Considerations
Stories 3-7
Stories 1-2
Preliminary Design
Layout of FVD of one type:
Notes: There are four drawings shown on this slide. The upper two drawings show longitudinal and transverse elevations of the building. In both elevations there are two dampers per story at floors 1 and 2, and one damper per story at the remaining floors above. The lower two drawings are plan views of the building. The left plan is labeled “Stories 1-2” and shows four damper bays in each direction. The right plan is labeled “Stories 3-7” and shows two damper bays in each direction.
The elevation and plan views of the number and location of FVDs is shown.

## Slide 39: 3. Design Considerations
Preliminary Design
Equivalent nonlinear damping coefficient:
Using the CL of 50 kip-sec/inch and assuming a circular frequency of 2.1 rad/sec, displacement amplitude of 2.5 inches and α = 0.4, gives a nonlinear damping coefficient CNL of 120kip-sec/inch
Notes: This provides a rough initial estimate of order-of-magnitude of FVD nonlinear properties, which can later be refined by consulting with the manufacturer and by using nonlinear response history analysis to optimize parameters of interest.

## Slide 40: 4. Structural Analysis
Maximum and Minimum Damper Properties
Require two separate analyses at each hazard level (DBE and MCER): one using the maximum damper properties, and one using the minimum properties.
Governing case is used for design.
These bounding analyses envelope the probable behaviour of the damping devices
Notes: This is a new section in Chapter 18.

## Slide 41: 4. Structural Analysis
Maximum damper stroke occurs using minimum properties
Maximum damper force occurs using maximum properties
Maximum and Minimum Damper Properties
Illustration: Force-Displacement Behavior for Maximum and Minimum Analyses, GM5 Record for Damper on 1st Story in East-West Direction:
Notes: This slide contains a graph showing hysteresis loops from testing of fluid viscous dampers. A point is marked at the left extreme of the data shown. This point is labeled “Maximum damper stroke occurs using minimum properties.” A point is marked at the lower extreme of the data shown. This point is labeled Maximum damper force occurs using maximum properties.”
This illustrates that the governing design parameters (forces, displacements, etc) may be from either the analysis using maximum or minimum properties.

## Slide 42: 4. Structural Analysis
Maximum and Minimum Damper Properties
The maximum and minimum properties are determined using the property modification factor approach.
  Maximum property = λmax × property of interest
  Minimum property = λmin × property of interest
Where:
Notes: The λmax and λmin factors are applied to each nominal mechanical property of interest and therefore set the maximum and minimum damper properties, respectively.

## Slide 43: 4. Structural Analysis
Maximum and Minimum Damper Properties
Behaviour of FVD:
Previously manufactured and tested device:
  Damping constant, C = 128 kip-sec/inch
  Velocity exponent, α = 0.38
Notes: In the damper force Equations: v is the velocity, C is the damping coefficient, α is the velocity exponent in the range of 0.1 to 2.0 and sgn is the signum function (i.e. sign of the velocity, whether positive of negative).
Since it may be more cost effective with less uncertainty in properties; a device which has already been produced and tested is adopted. This FVD is quite similar to that calculated from preliminary design (nonlinear damping constant of 120 and velocity exponent of 0.4).

## Slide 44: 4. Structural Analysis
Maximum and Minimum Damper Properties
Prototype test data
Notes: This slide contains a graph with the vertical axis labeled “force” and the horizontal axis labeled “velocity”. Experimental data from damper tests are shown on this plot. The data generally form a pattern in the shape of an inclined “S”. Also shown on this plot are S-shaped lines indicating upper and lower bounds of permissible damper properties. The experimental data fall between the upper and lower bounds.
The previous prototype testing of the dampers were conducted under the following conditions:
Force-velocity characteristic tests, all conducted at ambient temperature of 70° F. 10 full cycles performed at various amplitudes.
Temperature tests, three fully reversible cycles conducted at various velocities at the following temperatures 40, 70 and 100° F
This test data are assumed to be consistent with the sequence and cycles of Standard §18.6.1 (however this example does not address this).

## Slide 45: 4. Structural Analysis
Maximum and Minimum Damper Properties
Property modification factors:
  Aging and environmental effects do not need to be considered for this particular device (enclosed and conditioned space), thus λae,max = λae,min= 1.0
  The variations observed in prototype testing (i.e. heating effects) are essentially bounded by ±10%, thus λtest,max =1.10 and λtest,min =0.9
  Highly engineered devices with little variations due to manufacturing, thus λspec,max =1.05 and λspec,min = 0.95
Notes: The property modification factors account for changes in damper properties over its design life, during seismic motions and due to manufacturing variations.

## Slide 46: 4. Structural Analysis
Maximum and Minimum Damper Properties
Limits of Equations 18.2-3a and 18.2-3b do not apply, thus:
Only applied to the damping coefficient, C
  Cmax = 147.2
  Cmin = 108.8
Notes: These values are allowed to be less than the maximum and minimum limits of Standard §18.2.4.5 since they are based on similar prototype test data. These maximum and minimum factors are applied to the damping coefficient only. There is no independent variation considered for the nonlinear exponent α, since varying the damping coefficient in effect also captures the variation (if any) of the α value.

## Slide 47: 4. Structural Analysis
Nonlinear Response History Analysis
Example modelling assumptions:
  Included all structural elements
  Explicitly modelled in-plane diaphragm stiffness
Notes: This slide contains an isometric view of the framing system for the entire building, 5 bays wide, by 7 bays long, by 7 stories high.
The key assumptions of the ETABS mathematical model are outlined.

## Slide 48: 4. Structural Analysis
Nonlinear Response History Analysis
Example modelling assumptions:
  Include axial stiffness of brace installed in-line with FVD’s (2000 kip/inch)
  Beams for gravity framing modelled with end moment releases (pinned connections)
  3% inherent damping, applied to all modes
  SFRS modelled and designed to remain (essentially) elastic
Notes: The key assumptions of the ETABS mathematical model are outlined.

## Slide 49: 5. Design of SFRS
Configuration and Detailing
Must have an independent SRFS in each principal direction
Provides a complete lateral load path and conforms with a type listed in Table 12.2-1 of the Standard
Notes: This slide contains a drawing of the plan view of the building. The locations of the seismic force resisting system, which are steel moment frames, are shown by red ellipses. One ellipse surrounds the 5 center bays at the top of the plan on grid 1 and another surrounds the 5 center bays at the bottom of the plan on grid 6. One ellipse surrounds all 5 bays at the left of the plan on grid A and another surrounds all 5 bays at the right of the plan on grid H.
The SFRS is a steel special moment resisting frame (SMRF) and is designed and detailed as if the damping system was disconnected and this process is illustrated in Chapter 9 of these design examples. This is the first step in design as the Standard does not have any relaxation on the height, seismic design category, redundancy limitations or detailing requirements (i.e. RBS connections, strong-beam weak-column) for a SRFS in a structure with damping devices.

## Slide 50: 5. Design of SFRS
Minimum Base Shear
Eqs. 18.2-1 and 18.2-2:
For no vertical or horizontal irregularities and 20% added plus 3% inherent damping:
Notes: Regardless of the effectiveness of the damping system, the SFRS must have a minimum strength as outlined.

## Slide 51: 5. Design of SFRS
Minimum Base Shear
Equivalent Lateral Force Procedure per Chapter 12:
Notes: This calculation is the same as for buildings without supplemental damping systems.

## Slide 52: 5. Design of SFRS
Minimum Base Shear
Minimum base shear allowed by Chapter 18:
SFRS in each principal direction must (at least) remain elastic for this base shear, regardless of the effect of supplemental dampers.
Notes: The minimum elastic base shear is 464 kip.

## Slide 53: 5. Design of SFRS
Strength Design of SMRF
Three design checks:
  The minimum base shear of 464 kip (no dampers)
  Demands from the NLRHA (dampers included) at the design earthquake level
Since the SMRF is modelled as essentially elastic in the NLRHA at the MCER level
  Demands must be no more than 1.5 times the expected capacity of the frame
Notes: There are 2 key SFRS design checks and a third depending on the projecting specific performance requirements as well as modelling assumptions.

## Slide 54: 5. Design of SFRS
&
Mode 1 + Mode 2 + Etc.
Strength Design of SMRF
Check 1: Minimum base shear (no dampers)
  Response spectrum (modal) analysis
Notes: There are three drawings on this slide. The left drawing shows the smoothed design response spectrum for the building. The second and third drawings show the displaced shapes of the first and second vibration modes of the building. These mode shapes are labeled “ Mode 1 + Mode 2 + Etc.”
Response spectrum or modal superposition analysis can be used calculate demands for Check 1.

## Slide 55: 5. Design of SFRS
Vb,modal,reduced = 2376×0.125 = 297 kip thus scale up by 464/297 = 1.56
Gridline A & H SFRS Shears (North-South direction)
Strength Design of SMRF
Reduced Elastic Demand: Design earthquake response spectrum, elastic earthquake forces multiplied by Ie/R = 0.125 and scaled up to the minimum base shear (i.e. 0.75V/Vmodal,reduced)
Notes: This slide contains an elevation of a transverse section of the building, 5 bays wide by 7 stories tall. On each beam and column the magnitude of the design shear force is indicated.
Since the base shear from the response spectrum (modal) analysis is less than the minimum requirement, all demands are scaled up by a factor.

## Slide 56: 5. Design of SFRS
Reference: AISC
Strength Design of SMRF
Factored Nominal Capacity: Nominal yield strength with strength reduction factor, ϕ, of 0.9.
The selected RBS dimensions are a=0.625bbf, b=0.75d and c = 0.18bbf.
The W21x73 beam between Gridlines D and E at Story 3 has a factored nominal capacity of:
Notes: This slide contains a drawing of a “Reduced Beam Section” or RBS connection between a column and a beam. The distinguishing feature of this connection is the reduction in the width of the beam flanges a short distance from the face of column. This configuration forces plastic hinging in the beam to occur away from the column face.
For a capacity designed SMRF, the RBS will be one of the first parts of the frame to start yielding. Calculation of the moment capacity at the center of the RBS is shown for a W21x73 beam.

## Slide 57: 5. Design of SFRS
< 1.0 O.K
Acceptable drift limits usually governing sizing of steel MRF members instead of strength criteria
Strength Design of SMRF
D/C Ratios: Modal Response Spectrum Reduced Demands divided by Factored Nominal Capacity Ratios for Gridline 1 SMRF, No Dampers
Notes: This slide shows an elevation of a longitudinal section of the building, 7 bays wide by seven stories tall. On each beam of the moment frames the demand to capacity ratio (DCR) is shown. The values of all DCRs are less than 1.0.
The Figure shows that the sizing of the frame is of adequate strength to meet the minimum base shear requirement of the Standard as no D/C ratio is greater than 1.0. Even for the conventional design of the SMRF (i.e. per Chapter 9) the minimum base shear using modal response spectrum is allowed to be taken as 0.85V . This along with an increase in forces to account for accidental eccentricity would give D/C ratios for the frame of about 15-20% larger than that in the Figure. This is still well below a D/C close to 1.0, which one may seek to optimize design. The reason for this is that the sizing of beams, and hence columns (due to strong-column, weak-beam requirements), are typically controlled by considerations for drift (Hamburg et al. 2009).

## Slide 58: 5. Design of SFRS
Strength Design of SMRF
Now progress with sizing of the damping system (i.e. Section 6)
The re-checking of the SMRF (with the dampers included) is shown in the next slides:
Notes: The next step in design is to determine the size and capacity of the elements of the damping system.

## Slide 59: 5. Design of SFRS
SRFS is nearly elastic (=1.0) at the design earthquake level
This check exceeds the requirements of the Standard
D/C Ratios: Unreduced elastic demand over factored nominal capacity
Strength Design of SMRF
Check 2: Demands from the NLRHA (dampers included) at the design earthquake level:
Notes: This slide contains a drawing of a longitudinal elevation of the building, 7 bays wide by 7 stories tall. Demand-to-capacity ratios (DCRs) are shown for the nonlinear time history analysis with dampers included. Some of the beams at floors 3 and 4 have DCRs greater than 1.0.
This figure is of the steel moment resisting frame on Grid 1 (or 6). The numbers on each beam are the absolute maximum of the positive or negative moment divided by the elastic capacity of the RBS. A number above 1.0 indicate that steel yielding is occurring. For low damage design (which exceeds the Standard) it is preferable that the frame remains elastic/undamaged.

## Slide 60: 5. Design of SFRS
D/C = 445/475 = 0.94
Strength Design of SMRF
Unreduced Elastic Demand: Average from the seven ground motions is used. The demands are elastic, unreduced forces on the frame with load combinations, and are the absolute maximum of the positive and negative moments at each end of the beam
Notes: This slide shows the same elevation of the building as was shown in the previous slide. In addition there is a graph on the right showing in more detail the demand to capacity ratios over the entire length of one of the beams on the third floor. In this case the maximum demand capacity ratio for any location on that beam is 0.94.
This slide shows in more detail how each D/C value is the enveloped (absolute maximum flexural demand is taken) for each beam in the steel moment resisting frame.

## Slide 61: 5. Design of SFRS
D/C > 1.0 = Ductility = Damage!
Dampers included
No dampers
Strength Design of SMRF
Comparison of performance at design earthquake level
D/C Ratio = Elastic, unreduced design earthquake demands divided by factored nominal capacities
Notes: This slide contains two drawings of a longitudinal elevation of the building, 7 bays wide by seven stories tall.
The effectiveness of supplemental FVDs is shown. On the left is the steel moment resisting frame with NO dampers. The values are the flexural demand divided by capacity for each beam. These values indicate ductile behaviour (i.e. steel yielding) and thus damage. On the right is the SMRF WITH dampers. The D/C for nearly all the beams are close to or less than 1.0, which indicates that they remain with the elastic range (i.e. little damage).

## Slide 62: 5. Design of SFRS
Strength Design of SMRF
Check 3: Validity of the linear-elastic SMRF modelling assumption. Therefore check the NLRHA MCER demands are no more than 1.5 times the expected capacity of the frame capacities (= “essentially elastic” definition)
Expected Capacity: Expected yield strength with strength reduction factor, ϕ, of 1.0.
Notes: The Standard allows the SRFS to yield and become damaged, hence this check exceeds the minimum requirements.

## Slide 63: 5. Design of SFRS
Thus the SMRF performs essentially elastically for the MCER event = Higher seismic performance
< 1.5 O.K
No need to explicitly model the nonlinear behaviour of the frame.
Strength Design of SMRF
Notes: This slide contains a drawing of an longitudinal elevation of the building, 7 bays wide by 7 stories tall. Demand to capacity ratios are shown on each beam. Some demand to capacity ratios are greater than 1, but all values are less than 1.5.
As desired in the project objectives, the structure is relatively undamaged in a major earthquake.

## Slide 64: 5. Design of SFRS
   Governs
Permissible Drifts
Are checked only at the MCER level with the dampers included and have three limits:
  3% limit
  1.9 times Table 12.12-1 limit = 3.8%
  1.5R/Cd times Table 12.12-1 limit = 1.5 × 8/5.5 × 2% = 4.4%
Notes: This slide contains an image of a simple structural frame, one bay wide and two stories high. The figure shows the frame swaying to the right, illustrating that lateral forces cause lateral drift of the frame.
The maximum permissible story drift is 3%.

## Slide 65: 5. Design of SFRS
  Maximum drift = 2.0% × torsional amplification factor
  = 2.0% × 1.14 = 2.3% < 3.0% O.K
  Minimum Properties
  Maximum Properties
Permissible Drifts
MCER NLRHA Average Results:
Notes: The story drift history (i.e. drift vs. time) is calculated for each ground motion by subtracting the node displacement at the floor below from a vertically aligned node from the floor above. The maximum drift, at any instant in time, from each of the ground motions is then averaged to give the MCER drifts in the Tables for maximum and minimum damper propertie. The maximum drift at any story, in either principal direction, is 2.0%. This value needs to be increased to account for accidental eccentricity. As per torsion analysis, a drift amplifier of 1.14 is applicable, giving a drift demand of 2.3% which is less than the 3% limit.

## Slide 66: 6. Design of Damping System
Designed to remain elastic (nominal material strengths and ϕ=0.9) for MCER demands.
MCER NLRHA average (of seven motions) results:
  Minimum Properties
  Maximum Properties
Notes: The damping devices shall be sized to elastically resist the forces, displacements and velocities from the MCER ground motions. The critical damper forces and displacements are highlighted.

## Slide 67: 6. Design of Damping System
Corresponding velocity at peak force:
Design force for damper (increase for torsion and redundancy)
Damper displacement capacity (increase for torsion and redundancy)
Notes: Since the redundancy criteria of §18.2.4.6 are not satisfied for stories 3-7, the devices at these stories must be capable of sustaining the force and displacement associated with a velocity equal to 1.3 times the maximum calculated velocity. For ease of construction and to control damper and detailing costs, all dampers will be designed for this penalty to maintain one type of damper.

## Slide 68: 6. Design of Damping System
Nonlinear Fluid Viscous Damper Device Details:
Notes: The key specifications for the nonlinear FVD are outlined.

## Slide 69: 6. Design of Damping System
Reference: Taylor Devices
Notes: This slide contains a drawing of a typical fluid viscous damping device. An end view and side view of the device are shown.
A suitable device is available from a manufacturer as highlighted.

## Slide 70: 6. Design of Damping System
Damping System Framing
Include: Braces in-line with the dampers, their connections, the framing (beams and columns) which encompass the damping devices and the collectors and diaphragm
Size to remain elastic for MCER demands using nominal capacities and ϕ, of 1.0.
Notes: This slides contains a drawing of a simple structural frame one story high and three bays wide. In the left bay is shown a fluid viscous damper in line with a diagonal brace. The damper, right column of the left bay, and horizontal beam of the center bay are circled and labeled “DS” for Damping System. The two columns and beam of the right bay form a moment resisting frame, and are circled and labeled “SFRS” for Seismic Force Resisting System.
The damping system involves not only the FVD devices, but a range of elements.

## Slide 71: 6. Design of Damping System
Reference: Miyamoto International
Damping System Framing – Brace in-line with FVD
Notes: The slide shows a photograph of a single diagonal brace in a structural framing bay. There is a fluid viscous damper in line with the brace. This brace is labeled “Brace in-line with FVD”
For example, the steel brace in series with the FVD device needs to be designed.

## Slide 72: 6. Design of Damping System
Damping System Framing – Brace in-line with FVD
Design criteria:
  Required brace axial stiffness of 2000 kip/inch
  Force-controlled design axial force of
  1.08 (mass eccentricity) × 1.2 (force-controlled) × 375 = 486 kip
  Note: Damper design force = 447 kip
Notes: The axial force action in the brace is judged to be “force-controlled” as reliable inelastic capacity is not achievable without significant strength decay.

## Slide 73: 6. Design of Damping System
Damping System Framing – Brace in-line with FVD
Required brace area:
Notes: The required area of the steel brace to give at least 2000 kip/in stiffness is shown.

## Slide 74: 6. Design of Damping System
> 486 O.K
Damping System Framing – Brace in-line with FVD
Buckling capacity of HSS 14 x 5/8 :
Notes: The sizing of the steel brace is more than sufficient.

## Slide 75: 6. Design of Damping System
Other elements not addressed in this presentation include:
Column design
Connection design, for example gusset plates, splices, collector beams, foundations.
Diaphragm and beam/collector design
Performance due to wind and comparison to seismic design.
Notes: This slide lists other design considerations for a supplemental damped structure.

## Slide 76: DISCLAIMER
NOTICE: Any opinions, findings, conclusions, or recommendations expressed in this publication do not necessarily reflect the views of the Federal Emergency Management Agency. Additionally, neither FEMA nor any of its employees make any warranty, expressed or implied, nor assume any legal liability or responsibility for the accuracy, completeness, or usefulness of any information, product or process included in this publication.
The opinions expressed herein regarding the requirements of the NEHRP Recommended Seismic Provisions, the referenced standards, and the building codes are not to be used for design purposes. Rather the user should consult the jurisdiction’s building official who has the authority to render interpretation of the code.
Any modifications made to the file represent the presenters' opinion only.