## Slide 1: Structures with Supplemental Energy Dissipation Devices
Disclaimer
BACKGROUND
William McVitty, P.E., M.S., Andrew Taylor, S.E., Ph.D.
Notes: Graphic shows cover of the NEHRP Provisions FEMA P-1052.
The 2015 NEHRP Recommended Seismic Provisions are a new resource document that facilitates and translates the state-of-the-art knowledge into design practice. To help in understanding these new Provisions, design examples are also published which apply the new requirements of FEMA P-1051. This presentation complements the Chapter 16 design example of structures that incorporate supplemental energy dissipation devices.
This set of instructional slides is the first of two 90 minute presentations. It provides the background on supplemental energy dissipation devices and their seismic design requirements.

## Slide 2: Presentation Objectives
Present background on:
  Intent of seismic requirements
  Energy dissipation devices
  Example projects
Overview of major revisions
  Full replacement of Chapter 18 of ASCE 7 (the “Standard ”) is recommended
Notes: A graphic shows the cover of the document FEMA P-1050-1, 2015 Edition, “NEHRP Recommended Seismic Provisions for New Buildings and Other Structures”
The first part of this presentation provides a background on key concepts of the seismic provisions, types of energy dissipations devices and some real-life examples. The second part of the presentation gives an overview of the layout and content of the seismic design requirements and highlights some of the major changes recommended by the NEHRP Provisions.

## Slide 3: Intent of Seismic Requirements
Reference: MCEER, SUNY, Buffalo, NY
1st key concept:
Applicable to all types of energy dissipation devices (or “dampers”)
  Dampers absorb and dissipate vibration energy through relative movement across the damper
  Many types: metallic yielding, friction, viscoelastic, pure viscous and other (self-centering systems)
Notes: Along the bottom of this slide there are six small “force-displacement” hysteresis loops illustrating different types of damping devices. The first graph shows a diamond-shaped loop, the second shows a square loop, the third an inclined elliptical loop, the fourth a horizontal elliptical loop, the fifth a “pinched” hysteresis loop, and the sixth an extremely pinched hysteresis loop.
The requirements of the Standard apply to a wide range of damping systems. It applies to all systems that dissipate seismic energy which are not listed as a seismic force-resisting system in Table 12.2 of the Standard.

## Slide 4: Intent of Seismic Requirements
Reference: DIS Inc.
  Hence, the Standard requires design and thorough testing of dampers for MCER level displacements, velocities and forces.
Notes: There are two figures on this slide. The left figure shows force-displacement loops for tests of a viscous wall damper. The right figure shows a testing machine for validating the performance of fluid viscous dampers (hydraulic dampers).
Since the types of dampers can be vastly different, and can involve non-traditional civil engineering materials, or moving parts, the Standard has thorough testing requirements to quantify and validate their performance and quality.

## Slide 5: Intent of Seismic Requirements
2nd key concept:
Dampers supplement the seismic-force resisting systems (SFRS)
  The SFRS must provide a complete lateral load path as if the dampers did not exist.
  Minimum Vb limit for SFRS and ductile detailing requirements may not be relaxed
  Damping system (DS) and SFRS defined independently
Notes: The Standard requires that the damping system also have a SFRS (see Standard Table 12.2-1) that provides a complete load path. The SFRS must comply with the requirements of the Standard (i.e. minimum base shear), except that the damping system may be used to meet drift limits. Thus, the detailing requirements that are in place for structures without damping systems may not be relaxed for structures which include damping systems.

## Slide 6: Intent of Seismic Requirements
Notes: There are four drawings shown on this slide. Each drawing shows a single story structure. The top drawing is four bays wide, the second drawing is three bays wide, the third drawing is three bays wide, and the fourth drawing is one bay wide. In each drawing there is a single diagonal brace containing a fluid viscous damper. In the first drawing the brace is in the far left bay. In the second drawing the brace is in the far left bay. In the third drawing the brace is in the center bay. In the fourth drawing the brace is in the single bay. In each drawing the far right bay is a moment frame consisting of two columns and the beam, and is labeled SFRS for seismic force resisting system. In each drawing other elements are circled and labeled “DS” for damping system. The damping system always include the diagonal brace, connected framing elements that resist forces developed by the damper, and any other elements required to link the DS to the SFRS.
The damping system (DS), which includes the damping devices and surrounding structural elements, is defined separately from the SFRS even though the two systems may share common elements as shown.

## Slide 7: Intent of Seismic Requirements
3rd key concept:
Requirements permit performance comparable to a conventional SFRS
  Damping system primarily used to reduce drift, and may justify reducing member sizes.
  But typically used to achieve a higher levels of seismic performance
Notes: The Standard provides minimum design criteria with performance objectives comparable to those for a structure with a conventional SFRS. For example, the primary factor affecting steel special moment resisting frame (SMRF) member size selection is the need to control drifts below permissible levels. Hence the damping system may be used to reduce drifts, and hence member sizes. However supplemental dampers are usually used to achieve higher performance levels than a conventional SFRS.

## Slide 8: Intent of Seismic Requirements
  Achieved by designing the SFRS to have limited ductility, and directing energy dissipation into devices that are readily replaceable (or require no replacement)
Notes:   The table has three columns, headed “Objectives”, “Conventional”, and “Isolated.” The first column headed “Objectives” has three rows labelled “Deaths”, “Dollars” and “Downtime.” “Thumbs Up” icons indicate favorable outcomes, and “Thumbs Down” icons indicate unfavorable outcomes. Under the Conventional column heading “Deaths” is a thumbs up, while “Dollars” and “Downtime” are both thumbs down. Under the Isolated heading, “Deaths”, “Dollars” and “Downtime” all have thumbs up.
  Since severe earthquakes are very rare events and limiting damage may be costly for conventional SFRS, the building codes only enforce a design philosophy intended to provide safety by avoiding collapse, while permitting extensive structural and nonstructural damage. Conversely, by designing the SFRS to remain essentially elastic and directing dissipation of earthquake-induced energy into damping systems not part of the vertical load resisting structure, the intent (of the Standard) is to improve performance by reducing repair costs and business interruption.

## Slide 9: Intent of Seismic Requirements
4th key concept:
Response history analysis is the preferred analysis method
Notes: The figure in this slide shows an isometric view of the structural frame of a building that is 7 stories high and 5 by 7 bays in plan. Along the two major axes of the building frame are shown two earthquake accelerographs, indicating that earthquake ground motion components are applied in the analysis to each major axis of the structure.
Elastic methods of analysis have been shown to give a reasonable estimate of responses, however are not straightforward to apply and have their limitations. Current practice and computing power has evolved such that nonlinear response history analysis is the common and preferred analysis tool used to calculate peak responses.

## Slide 10: Energy Dissipation Devices
More reliable and many practical applications
Yet to gain confidence for seismic applications in the USA
Types:
Active & Semi-Active: control building motion by adjusting the dampers properties (i.e. damping, stiffness). Require a computerized control system and power source.
Passive: No need for external power source
Notes: Active and semi-active damping systems are more of academic interest in the USA. Passive dampers, which are mechanical systems that require no external power source, have been used on hundreds of structures world-wide.

## Slide 11: Energy Dissipation Devices
Passive Damper Types:
Three categories of force-displacement (energy dissipation) behavior:
  Displacement-dependent/activated
  Velocity-dependent/activated
  Other systems
Notes: The way in which passive dampers absorb and dissipate energy can be classified in to three groups: Displacement-dependent, velocity-dependent and other.

## Slide 12: Energy Dissipation Devices
Reference: MCEER, SUNY, Buffalo, NY
Passive Damper Types:
Displacement-dependent/activated
Notes: The figure in this slide contains four drawings arranged in a grid. The upper two drawings show a metallic yielding damping device on the left, and a friction sliding device on the right. The lower two drawings show force-displacement hysteresis loops. The left hysteresis loop corresponds to the metallic yielding device, and the loop shown has a diamond shape. The right hysteresis loop corresponds to the friction sliding device and the loop shown has a rectangular shape.
Displacement-dependent devices have a hysteretic force-displacement behaviour whereby energy is dissipated by yielding of metals or through sliding friction.

## Slide 13: Energy Dissipation Devices
Reference: MCEER, SUNY, Buffalo, NY
Passive Damper Types:
Added damping and stiffness (ADAS) system
Notes: This slide contains a schematic drawing of a single structural portal frame, consisting of two columns and a beam. Inside the portal frame are two braces forming a chevron (inverted “V”) shape. At the apex of the two braces is a yielding metallic damping device. The device is activated by relative lateral movements between the beam and the apex of the two braces.
One (of many) examples of the metallic yielding devices is triangular shaped flexural-yielding plates used at the top of a chevron brace (aka the ADAS system).

## Slide 14: Energy Dissipation Devices
Passive Damper Types:
Cast steel yielding brace system (YBS)
Reference: Cast Connex and Dr. M. Gray
Notes: The figure on this slide shows a single structural bay of a building frame, consisting of a column on the left and right, and a beam at the top and the bottom. A diagonal brace is arranged across this framing bay. In line with the structural steel brace is a yielding brace system device. Also shown to the right of this figure is a photograph of a yielding brace system device, and a plot of the hysteresis loops generated by that device.
Another example of a metallic yielding device is the cast steel yielding brace system, whereby the triangulated fingers of the YBS connector yield (primarily) in flexure.

## Slide 15: Energy Dissipation Devices
Reference: Symans et al., ASCE 2008
Passive Damper Types:
Slotted-bolted friction damper
Notes: This slide contains a photograph of a slotted-bolted friction damper installed in a diagonal structural brace. The device consists of a series of plates and sheets of frictional sliding material bolted around the diagonal brace.
One (of many) examples of the friction devices is the slotted-bolted friction device used in-line with a diagonal brace.

## Slide 16: Energy Dissipation Devices
Reference: MCEER, SUNY, Buffalo, NY
Passive Damper Types:
Velocity-dependent/activated
Notes: The slide contains two graphs of hysteresis loops. The left graph is labeled “Viscoelastic Solid or Fluid Device”, which has a hysteresis loop that is an inclined ellipse. The right graph is labeled “Viscous Fluid Device”, which has a hysteresis loop that is a horizontal ellipse, without any inclination of the ellipse axis.
Viscoelastic devices operate by deformation of the viscoelastic solid material or viscoelastic fluid, where their stiffness and damping is frequency dependent. They are termed “viscous” as the damping force is proportional to velocity. A purely viscous device (i.e. zero stiffness and independent of frequency) is the fluid viscous damper.

## Slide 17: Energy Dissipation Devices
Reference: http://www.siecorp.com/
Reference: MCEER, SUNY, Buffalo, NY
Viscoelastic material
Passive Damper Types:
Solid viscoelastic (VE) dampers
Notes: The slide contains an illustration of a simple structural frame consisting of a column on the left and on the right, and a beam at the top and at the bottom. Running diagonally in this frame is a structural steel brace, and in-line with the brace is a damping device labeled “Viscoelastic damper”. Also shown on the right of the slide is a photograph of a viscoelastic damper, which consists of a central plate and two side plates. Between the central plate and the two side plates are layers of viscoelastic material.
Here is an example of a viscoelastic damper installed in-line with a diagonal brace.

## Slide 18: Energy Dissipation Devices
Reference: DIS Inc.
Passive Damper Types:
Fluid viscous wall damper
Notes: On this slide there is a photograph of a fluid viscous wall damper. The wall damper consists of a trough containing a viscous fluid. A vertical metal plate is submerged in this trough. When the plate moves through the fluid along the axis of the trough, damping forces are generated. Another figure shows a viscous wall damper installed in a structural steel frame. The trough is connected to a beam below, and the plate is connected to a beam above. Lateral movement of the building frame causes relative movement of the plate through the trough of viscous fluid.
For fluid viscous wall dampers, the relative movement between floors causes a vane to move through viscous fluid and hence creates a damping force.

## Slide 19: Energy Dissipation Devices
Courtesy: Taylor Devices
Device used in design example
Reference: Taylor Devices
Passive Damper Types:
Fluid viscous damper (FVD)
Notes: This slide shows a drawing which is a longitudinal section through a fluid viscous damper (FVD). The FVD is a hydraulic cylinder. As the cylinder is shortened and elongated, internal fluid is forced through orifices in the interior of the device. This restricted fluid flow creates damping forces.
The elements of a fluid viscous damper are relatively few, however the detailing of these devices (i.e. orificing, seals, etc.) vary greatly. By moving the piston rod back and forth, fluid passes through the piston head orifices to create a damping force.

## Slide 20: Energy Dissipation Devices
Reference: MCEER, SUNY, Buffalo, NY
Passive Damper Types:
Other systems
Notes: This slide contains two plots showing hysteresis loops. The left plot is a “pinched” loop, and is labeled “Fluid Restoring Force/Damping Device”. The right plot is an extremely pinched loop, and is labeled “Frictional-Spring Device with Recentering Capability”.
Dampers that cannot be classified as displacement- or velocity-dependent are classified as “other” systems. Examples are dampers with fluid restoring force and friction-spring or metallic-yielding post-tensioned systems that have re-centering ability.

## Slide 21: Example Projects
  Basic configurations of dampers
  Metallic yielding (hysteretic) dampers
  Viscous wall dampers
  Fluid viscous dampers:
    Test results of improved performance
    Building example
Notes: First we will outline the basic configurations of dampers. Then we will give project examples for a select few types of dampers, namely, metallic yielding, viscous wall dampers and fluid viscous dampers.

## Slide 22: Example Projects
1. Three Basic Configurations
  Diagonal
  Horizontal, In-line
  Geometric Amplification (toggle)
Notes: In terms of damping configuration, there are three basic ways to incorporate dampers into a building: a) diagonal bracing, b) horizontal bracing and c) toggle or geometric amplification configurations. The damper increases in effectiveness from configuration a) to c). For example, the relative movement across the damper, arising from story drifts, is greater if the damper is configured horizontally compared to at an angle.

## Slide 23: Example Projects
Reference: Taylor Devices
1. Configurations
  Diagonal
Notes: This slide contains an elevation of a simple building frame 3 stories high and 3 bays wide. In the center bay of each story a diagonal brace is shown, and these braces are labeled “Dampers”. The figure is titled “Diagonal Bracing with Dampers.”

## Slide 24: Example Projects
Reference: Taylor Devices
Configurations
  Diagonal
Notes: Two photographs are shown on this slide. The left photograph shows a building under construction. In the center of the photograph are two fluid viscous dampers arranged as diagonal braces in two separate structural framing bays. The right photograph shows a single structural framing bay with two dampers arranged in a chevron, or inverted “V”, configuration. Each leg of the “V” contains a single fluid viscous damper that is in-line with the structural steel brace.
Examples of diagonally configured dampers is shown here (arbitrarily for fluid viscous dampers, but applicable for other damper types).

## Slide 25: Example Projects
Courtesy: Taylor Devices
Reference: Taylor Devices
1. Configurations
  Horizontal
Notes: This slide contains two drawings of dampers installed in a 3-bay by 3-story structural frame. The left drawing shows dampers installed using chevron braces, or inverted “V” braces. The dampers are not in line with each brace, but are arranged horizontally at the tip of the “V”. One end of each damper is connected to the tip of the “V”, and the other end is connected to a bracket on the beam above. The right drawing shows fluid viscous dampers installed in parallel with a seismic isolation system. One end of each damper is connected to the superstructure above the isolation system, and the other end is connected to a concrete plinth which projects upward from the foundation.
The horizontal configuration of the dampers is shown schematically. Dampers can be used in a dual system with base isolation.

## Slide 26: Example Projects
Reference: Taylor Devices
© 2004 Rutherford & Chekene
1. Configurations
  Horizontal
Notes: This slide contains two photographs of fluid viscous dampers installed in structures. The type of installations correspond to the two drawings shown on the previous slide. In the left photograph dampers are shown installed in a horizontal configuration at the tip of of the “V” where two inclined braces meet (in this case the inclined braces are pointing down rather than up). The right photograph shows a fluid viscous damper installed in parallel with a seismic isolation system.
Examples of horizontally configured dampers are shown here for a braced frame and seismic isolation system (arbitrarily for fluid viscous dampers, but applicable for other damper types).

## Slide 27: Example Projects
Note: Patented
Reference: MCEER, SUNY, Buffalo, NY
1. Configurations
  Geometric Amplification
Notes: This slide shows three structural framing bays with dampers installed in a mechanism to create geometric amplification of the displacements imposed on the damper pistons. These are labeled “Upper Toggle”, “Scissor Jack”, and “Reverse Toggle”. In first and third cases the diagonal braces has a hinge near mid-length, and the damper piston is attached between this hinge and a fixed location on the surrounding frame. For the scissor jack two diagonal braces with hinges in the middle are attached to the same two locations on the structural frame. The two braces are spread apart at the locations of the hinges, and a damper is connected between the hinges.
The most effective configurations (in terms of movement across the damper) is the toggle and scissor-jack configurations. However these configurations may be patented.

## Slide 28: Example Projects
Reference: Taylor Devices
Note: Patented
Reference: Dist. Prof. M. Constantinou
1. Configurations
  Geometric Amplification
Notes: This slide contains two photographs. The photograph on the left shows a scissors damper configuration, while the photograph on the right shows a toggle brace configuration.
Examples of scissor and toggle configured dampers are shown here (arbitrarily for fluid viscous dampers, but applicable for other damper types).

## Slide 29: Example Projects
2. Metallic yielding devices
Union House, Auckland, New Zealand (1980s)
Notes: This slide contains two photographs. The photograph on the right is a view of the Union House in Auckland, New Zealand, which is a 13 story building with a diamond grid of diagonal braces on the exterior. The left photograph shows a typical location where brace ends are connected to the structure. Each brace connects to a triangular plate projecting out from the structural frame. This plate yields in flexure during an earthquake, creating hysteretic damping.
An early example of using metallic-yielding dissipation devices so that the structure as a whole remains undamaged can be seen in New Zealand. External cross-bracing are connected to steel plates at the base of the structure, which flexurally yield when the braces undergo tension and compression.

## Slide 30: Example Projects
Reference: http://www.siecorp.com/
2. Metallic yielding devices
ADAS system in Wells Fargo Bank building, San Francisco.
Notes: This slide contains two photographs. The left photograph shows a yield metal device, known as Added Damping and Stiffness, or ADAS, at the top of a pair of chevron (inverted “V”) braces. The right photograph is a view of the building where these damping devices are installed.
The added stiffness and damping system was implemented in the Wells Fargo building using a chevron configuration.

## Slide 31: Example Projects
Reference: www.starseismic.net
2. Metallic yielding devices:
  In the past: Buckling-restrained brace (BRB) = steel yielding device that supplements a special moment resisting frame (SMRF) building.
Notes: There are two small drawings on this slide. The left drawing shows a compression brace that is laterally constrained from buckling by a series of evenly spaced rollers over the length of the brace. The right drawing shows the internal arrangement of a buckling restrained brace, in which the internal steel brace is prevented from buckling laterally by a casing and grout that constrain lateral movement of the brace.
Prior to the development of the Buckling-Restrained Brace (BRB) frame, one could have designed the system using Chapter 18 where the BRB is a displacement-dependent damper that supplements a SMRF.

## Slide 32: Example Projects
Reference: NIST GCR 15-917-34
Reference: www.starseismic.net
2. Metallic yielding devices:
  In the past: Buckling-restrained brace (BRB) = steel yielding device that supplements a special moment resisting frame (SMRF) building.
Notes: There are two drawings on this slide. The one on the left is identical to the drawings described on the previous slide. The right drawing shows an elevation of a structural frame four stories high by three bays wide. Buckling restrained braces are shown installed in a chevron configuration in the left bay of each floor.
Prior to the development of the Buckling-Restrained Brace (BRB) frame, one could have designed the system using Chapter 18 where the BRB is a displacement-dependent damper that supplements a SMRF.

## Slide 33: Example Projects
Accounts for energy dissipation ability
2. Metallic yielding devices:
  Now the BRB is permitted to be the primary load path and does not require a SMRF:
Notes: However to foster implementation, proponents of the BRB have progressed the system such that it is regarded as the primary lateral load path and designed in a similar manner to a conventional braced frame using its own response modification factor, R.

## Slide 34: Example Projects
Reference: J. Love
Dampers
3. Viscous Wall Dampers (VWD)
California Pacific Medical Center
Notes: There is a photograph on this slide showing the California pacific Medical Center under construction.
119 viscous wall dampers provide supplemental damping to the welded steel moment resisting frames. They are used to reduce both floor accelerations and inelastic demand in primary structural members. According to the engineers, the damped frame provided significant savings in steel material over conventional SMRF and base isolation solutions. The VWD can be strategically placed between windows.

## Slide 35: Example Projects
Reference: DIS Inc
Installation
Transport
Testing
3. Viscous Wall Dampers
California Pacific Medical Center
Notes: There are three photographs on this slide. The left photograph shows a viscous wall damper in a test machine. The center photograph shows two viscous wall dampers mounted vertically on the bed of a truck for transportation to the job site. The right photograph shows a viscous wall damper being installed in a building.
Full scale prototype testing was conducted at UCSD and production testing was conducted at the manufacturers facilities. The 10,000 pound VWD’s needed to be transported and installed in a upright position.

## Slide 36: Example Projects
Reference: MCEER, SUNY, Buffalo, NY
Similar force and drift for 3 times excitation
With fluid viscous dampers (22% total damping)
100% of El Centro
No fluid viscous dampers (2% total damping)
33% of El Centro
4. Fluid Viscous Dampers – Test results
Notes: These slide contains two shear force vs. displacement hysteresis plots. The plot on the left is labeled “No fluid viscous dampers” and the hysteresis loops show virtually no dissipation of energy. The loops are nearly straight, inclined, lines with no area between the ascending and descending branches. The right plot is labeled “With fluid viscous dampers” and shows elliptical hysteresis loops, indicating that significant energy dissipation is being created by the dampers.
Shake-table testing of buildings which implement fluid viscous dampers have shown greatly reduces drifts, and also reduced forces if the structure remains elastic, compared to the structure without dampers.

## Slide 37: Example Projects
Reference: Taylor Devices
4. Fluid viscous dampers:
  San Francisco Civic Center
Notes: There are two photographs on this slide. The left photograph shows a man standing next to a fluid viscous damper that has been installed in line with a diagonal brace. The right photograph shows a building with fluid viscous dampers installed in line with the diagonal braces.
Fluid viscous dampers have been used on many projects, including the San Francisco Civic Center.

## Slide 38: Design Requirements Overview
Notes: A diagram shows the relationship between the ASCE 7 Standard (ASCE 7), the NEHRP Provisions (NEHRP), the International Building Code (IBC), the NFPA 5000 Building Code (NFPA), and the California Building Code (CBC). ASCE 7 is located at the center of the diagram. Along the bottom of the diagram are shown the IBC, NFPA and CBC. Arrows point from the IBC, NFPA, and CBC to ASCE 7. In the upper left NEHRP is shown. There is a double-headed arrow between ASCE 7 and NEHRP.
Today, model building codes (e.g., national model codes such as the IBC, or regional derivatives, such as the CBC) adopt by reference the seismic design requirements of ASCE 7. The requirements in ASCE 7 are typically based on NEHRP’s recommended provisions.
All the recommended new changes of the 2015 Provisions (i.e. Replacement of ASCE 7 Chapter 18) have been further developed and adopted into the upcoming ASCE/SEI 7-16, which is expected to be adopted by reference in the 2018 edition of the IBC. As such, the code requirements followed for the Chapter 16 design example are referred to as ASCE 7-16 (referred to simply as the Standard) requirements, instead off the NEHRP 2015 Provisions.

## Slide 39: Design Requirements Overview
Chapter 18, ASCE 7-2016 (the Standard) is divided into seven sections:
18.1 & 18.2: Definitions & General Requirements
18.3: Nonlinear Response-History Procedure
18.4: Seismic Load Conditions and Acceptance Criteria for Nonlinear Response-History Procedure
18.5: Design Review
18.6: Testing
18.7: Alternative Procedures and Corresponding Acceptance Criteria
Notes: The ordering of the Standard is focused towards NLRHA.

## Slide 40: Revisions
Full replacement of ASCE 7 Chapter 18 recommended
Notes: A graphic shows the cover of the document FEMA P-1050-1, 2015 Edition, “NEHRP Recommended Seismic Provisions for New Buildings and Other Structures”
Due to the larger number of editorial as well as technical changes, the NEHRP Provisions have recommended a full replacement of Chapter 18.

## Slide 41: Revisions
There were technical changes to:
  Ground motion criteria
  Procedure selection
  Determination of damper properties
  System redundancy
  Assumptions for response history analysis
  Acceptance criteria of response history analysis
  Number of design reviewers
  Testing requirements
Notes: The major technical changes are stated here and are discussed in more detail in the following slides.

## Slide 42: Revisions
Site-specific hazard analysis is usually required to determine the target response spectrum
New USGS design value maps and site coefficients and new site-specific analysis requirements which, depending on the site location and site conditions, may have a significant effect on design
Ground motions criteria - Target spectrum
Notes: A graph shows examples of several project-specific earthquake response spectra that could be used for design. These spectra are meant to be a schematic illustration only, so the details of the shapes and magnitudes of the spectra are not relevant.
On sites located close to major active faults, or with unstable or soft soil conditions, the two-parameter (S1, Ss) spectrum (a.k.a “ELF” or “USGS website” spectrum) obtained using the ground motion maps in combination with site factors (Fa, Fv) does not provide a good estimate of the spectral shape of design ground motions, particularly at longer periods. Studies of site-specific seismic hazards and site response can significantly improve the shape and amplitude of the design spectrum on such sites, and are usually required for damped buildings.

## Slide 43: Revisions
Only seven ground motions required
Scaling and orientation of ground motions depend on proximity to fault
Amplitude or spectrally matched scaling to meet or exceed target spectrum over a specific period range of interest
Ground motion criteria - Selection and scaling
Notes:   A graph shows several earthquake acceleration response spectra. A smoothed target response spectrum is shown in black. Seven earthquake response spectra are shown as dashed lines. The earthquake records that these spectra represent are listed in a table above the graph. A spectrum showing the average of the seven earthquake spectra is shown in red. This red spectrum matches fairly closely the target spectrum over the period range 1 to 4 seconds.
  For nonlinear response history analysis of supplemental damped buildings, the selection and scaling of ground motions is different to that required by Chapter 16. The minimum number of ground motion records is set to 7 which is consistent with Chapter 17 and current professional practice. Ground motion selection and scaling should be conducted by an expert, experienced with hazards of the region.

## Slide 44: Revisions
Procedure selection
Nonlinear response history analysis (NLRHA) is emphasized as the primary analysis tool.
Equivalent lateral force (ELF) and response spectrum (RS) procedures have been placed at the back of the Chapter and are presented as “alternative methods”.
Notes: Three figures are shown at the bottom of this slide. They are arranged in an equation format, such that (left figure) + (center figure) = (right figure). The left figure shows two earthquake accelerographs, representing two orthogonal components of an earthquake acceleration record. The center figure is a drawing of a building structural frame, indicating the computer model of the building. The right figure shows hysteresis loops of structural dampers, indicating the resulting damper response calculated using the ground motion components and the building model.
NLRHA is permitted for all building types and seismic hazards. It is the most used approach and was the basis for development of the elastic (ELF and RS) procedures.
Furthermore, the NLRHA gives the most realistic prediction of seismic response. This is because the degree to which a damped structure is able to accomplish its performance goals depends on the inherent properties of the structure, the properties of the dampers and its connecting elements, the characteristics of the ground motion, and the limit state being investigated. Given the potentially large variation in each of these parameters, it is usually necessary to perform an extensive suite of nonlinear response-history analyses.

## Slide 45: Revisions
Variability in production dampers properties which on the average differ from the properties measured in prototype testing.
Changes during seismic motion
Changes over design life
Types of λ factors:
  λae,max and λae,min which account for aging and environmental effects.
  λtest,max and λtest,min which account for variations observed during prototype testing.
  λspec,max and λspec,min which account for manufacturing variations
3. Determination of damper properties
Introduction of property modification (λ) factor approach and explicit requirement of separate upper- and lower-bound analyses
Notes: Property modification values are introduced to account for variations in damper properties during manufacturing and while in-service. These factors are used to allow the designer to perform upper and lower bound analysis to ensure that the forces and drifts are estimated more appropriately.

## Slide 46: Revisions
3. Determination of damper properties
Maximum and minimum dampers properties
Prototype testing:
Notes: This slide contains a graph with the vertical axis labeled “force” and the horizontal axis labeled “velocity”. Experimental data from damper tests are shown on this plot. The data generally form a pattern in the shape of an inclined “S”. Also shown on this plot are S-shaped lines indicating upper and lower bounds of permissible damper properties. The experimental data fall between the upper and lower bounds.
This section is added to allow for enveloping analysis based on maximum and minimum damper properties obtained by application of the lambda factors. When these values are not known, it is permitted to use 85% and 120% of nominal values as the maximum and minimum values to account for cumulative effect of variations.
Results from prototype testing are shown. The solid line depicts the nominal force-velocity relationship of the nonlinear fluid viscous damper with the dotted lines representing a 10% and 20% change in the damping constant value CNL. When test data such as this is used to determine damper properties, the max and min λ factor limits (of 85% and 120%) need not apply.

## Slide 47: Revisions
Redundant system
Non-redundant system, increase damper capacities
4. System Redundancy
Require at least 4 dampers in any story in either principal direction, and at least 2 dampers either side of the center of stiffness in either principal direction, otherwise increase damper capacity by a 1.3 factor
Notes: This slide contains two drawings of the plan view of two buildings. Each building is 5 bays wide by 7 bays long. The left building is labeled “Non-redundant system, increase damper capacities.” This building has only two damper bays in each direction. The right building is labeled “Redundant system”. This building has four damper bays in each direction.
This new section is added to distinguish between redundant and non-redundant systems. The provisions are similar to language of ASCE 41 in which larger force and displacement damper capacities are required when less than 2 dampers in each direction are located on each side of center of mass at any story.

## Slide 48: Revisions
Less than 1.5 therefore steel moment frame is permitted to be modeled as linear
5. Assumptions for NLRHA
Need to explicitly model nonlinear behavior of structural members if demand-to-capacity ratio is greater than 1.5, using expected material strengths and ϕ of 1.0.
Notes: This slide has a drawing of the elevation of a building that is 7 stories tall by 7 bays wide. Demand-to-capacity ratios (DCRs) are shown on each moment frame beam. Beams with DCRs less than 1 are colored green. Those with DCRs greater than 1 are colored red. A note points to all of the red beams indicating “Less than 1.5 therefore steel moment frame is permitted to be modeled as linear.”
The section is revised to directly account for the nonlinear behavior of structural members and connections. The exception in ASCE 7-10 allowed for elements (with the exception of damper devices) being modeled as elastic elements so long as demand to capacity ratio (DCR) values were less than 1.5 at DE. The exception is now revised to allow for elastic modeling of members as long as DCR is less than 1.5 at MCER using expected (vs. nominal) material properties and a phi factor of 1.0. The change reflects that the NL analysis is almost exclusively at MCER intensity.

## Slide 49: Revisions
I.e. 3% constant damping all modes
5. Assumptions for NLRHA
Limited analysis is conducted at the design basis earthquake level. Used to check the SFRS.
Inherent damping reduced to 3% unless test data supports higher levels
Notes: A graph appears at the bottom of this slide. The horizontal axis is labeled “Time (seconds)” and the vertical axis is labeled “Energy (kip-ft.)” Three ascending lines begin at time 5 seconds. The black line is labeled “Input Energy” and ascends steeply, eventually leveling off at about 10,500 kip-ft. This line is above the other two lines. The grey dashed line is labeled “Modal Damping” and it ascends gradually, leveling off at about 1,000 kip-ft. The blue dashed line is labeled “Nonlinear Viscous Damping” and it ascends rapidly, leveling off at a value of about 9,500 kip-ft.
Limited analysis is conducted at DE. The purpose of the DE analysis is to check the seismic force resisting system incorporating the effect of both seismic and damping forces.
Inherent damping ratio is reduced to 3% to account for typical damping that is expected in new buildings. In addition, since properly designed damping devices would add significant supplementary damping to the building, the use of 5% inherent damping is not warranted. As shown in the energy balance for an earthquake, the energy dissipation due to inherent damping should make up only a small portion of the total input energy.

## Slide 50: Revisions
5. Assumptions for NLRHA
May account for accidental mass eccentricity using amplification factors
EXCEPTION: It is permitted to account for the effects of accidental eccentricity through the establishment of amplification factors on forces, drifts and deformation that permit results determined from a analysis using only the computed centered-of-mass configuration to be scaled to bound the result of all the mass-eccentric cases.
Notes: The requirement to account for accidental mass eccentricity intended to increase the design actions. It accounts for effects such as: a) plan distributions of mass being different from that assumed in design, b) non-uniform properties of the SFRS (i.e. strength, stiffness) and/or damping devices, and c) rotational and torsional ground motions.
Requirements are added similar to other chapters of ASCE 7-16, and an exception is provided. The rationale behind this is to avoid doing (unnecessarily) large amounts of analysis to calculate the worst case of accidental eccentricity. Guidance on how to determine amplification factors is provided in commentary.

## Slide 51: Revisions
5. Assumptions for NLRHA
Response Parameters:
  The average of at least seven earthquake records are permitted for design.
  Using less than 7 records and taking the maximum value has been removed from the Standard.
Notes: Seven pairs of records are used for analysis. Consistent with past practice, the average values of response obtained from analysis is allowed to be used in design.

## Slide 52: Revisions
6. Acceptance criteria for NLRHA
All elements of the SFRS are checked under two conditions:
  Minimum base shear requirements (without damping system)
  Demands from NLRHA at design basis earthquake level (including damping system)
Notes: The SFRS shall to satisfy its usual design requirements (i.e. Chapter 12, as if it had no damping system) but as altered by Chapter 18. In addition, the SFRS elements are checked for combined effect of seismic and damper forces at the design basis earthquake level.

## Slide 53: Revisions
Reference: ASCE 7
6. Acceptance criteria for NLRHA
Allowable drifts of the SFRS are checked only at the MCER with the dampers included and have three limits:
  3% limit
  1.9 times Table 12.12-1 limit
  1.5R/Cd times Table 12.12-1 limit
Notes: This slide contains an image of a simple structural frame, one bay wide and two stories high. The figure shows the frame swaying to the right, illustrating that lateral forces cause lateral drift of the frame.
With dampers added, results of NLRHA are used to check dampers vs. limits as specified in Chapter 12 and modified for RHA.
Drift ratios are evaluated at MCER only. The limiting values are computed by applying a factor of 1.5 (MCE/DE ratio) to various drift limits of:
3% (1.5 * 2% drift of Chapter 12, where 2% is common value for most risk categories)
Value from Chapter 12 (depending on number of stories, framing, and risk category) times factors of either:
  1.5 R/Cd where R/Cd is used to bring drifts up to limits allowed in Chapter 12 when methods other than RHA is used.
  1.9 (=1.5*1.25 where 1.25 is allowed in ASCE 7-10 Chapter 16 when RHA is used)

## Slide 54: Revisions
7. Number of Design Reviewers
At least one registered design professional shall provide an independent review.
Peer reviewer or panel should be engaged early since they must review project design criteria (including site-specific ground motion criteria) and preliminary design.
Notes: Review requirements are specified and clarified in the Standard. The requirements have been relaxed to only one RDP in the latest cycle to expedite the process.

## Slide 55: Revisions
Reference: MCEER, SUNY, Buffalo, NY
More reasonable test program:
  10 cycles 0.33 MCER intensity
  5 cycles 0.67 MCER intensity
  3 cycles 1.0 MCER intensity
Number of cycles at full MCER intensity reduced from five to three cycles
The testing frequency of 1/(1.5T1) assumes some softening of the combined SFRS and DS
8. Testing Requirements - Sequence and cycles of prototype testing
Notes: This slide contains two graphs showing the results of tests on a damper. The upper graph has a horizontal axis labeled “Displacement” and vertical axis labeled “Force”. Rounded hysteresis loops indicate the force-displacement relationship for this damper. The lower graph has a horizontal axis labeled “velocity” and vertical axis labeled “force”. Test data is shown at several different velocities. In addition, upper and lower bound limits are shown. All of the test data falls between the upper and lower bound limits.
ASCE 7-10 required five cycles at MCER intensity which was deemed excessive, and the test program did not address performance at smaller intensities. To address this issue, a sequential set of cyclic test is incorporated at increments of 1/3, 2/3 and 1.0 times the MCER intensity with more appropriate numbers of cycles, and fewer cycles at larger intensities.

## Slide 56: Revisions
Reference: DIS Inc.
Production test(s) shall be performed first
Devices shall be tested to experience the MCER force from analysis
8. Testing Requirements - Sequence and cycles of prototype testing
Notes: There is a photograph at the right side of this slide, showing a load frame for testing fluid viscous dampers.
The production test shall be performed prior to all other tests (to establish base line properties for comparison), so that comparison between production damping devices and prototype tested damping devices are meaningful. Furthermore, language is added to ensure that devices are tested to experience the MCER force obtained from the analysis.

## Slide 57: Revisions
Prototype testing need not be perform for every project. The similarity requirements are now defined more clearly:
  Similar dimensions, internal construction and pressures.
  Same type and materials.
  Same manufacturing and quality control procedures.
  Tested at similar displacements and forces.
8. Testing Requirements – Similarity requirements
Notes: Previous similarity requirements gave the registered design professional full discretion. Now the Standard provides more direction on what criteria are relevant.

## Slide 58: Revisions
Reference: DIS Inc.
Every single device used in construction must be tested (100% production tests) due to recent observations of unacceptable behavior.
But, need not be done on damping devices that undergo damage due to testing.
8. Testing Requirements – Production testing
Notes: There is a photograph at the right side of this slide. It shows a large frame for testing viscous wall dampers.
Requirements for production testing are added. The 100% testing is due to recent observations of failures or unacceptable behavior of hardware that has not been tested. For example the California State Buildings 8 and 9 in Oakland, CA were fitted in 2007 with viscous damping devices of which 75% were installed without testing and with the remaining 25% to be tested prior to installation. Several tested devices showed abnormal behavior that necessitated the removal, testing and re-building of the installed dampers.
An exception was also added to the Standard for devices that undergo damage subject to production testing. An alternate procedure is developed to require at least one device of each size is tested (in addition to other requirements developed by the RDP).

## Slide 59: DISCLAIMER
NOTICE: Any opinions, findings, conclusions, or recommendations expressed in this publication do not necessarily reflect the views of the Federal Emergency Management Agency. Additionally, neither FEMA nor any of its employees make any warranty, expressed or implied, nor assume any legal liability or responsibility for the accuracy, completeness, or usefulness of any information, product or process included in this publication.
The opinions expressed herein regarding the requirements of the NEHRP Recommended Seismic Provisions, the referenced standards, and the building codes are not to be used for design purposes. Rather the user should consult the jurisdiction’s building official who has the authority to render interpretation of the code.
Any modifications made to the file represent the presenters' opinion only.