## Slide 1: Structures with Supplemental Energy Dissipation Devices
Disclaimer
Summary
William McVitty, P.E., M.S., Andrew Taylor, S.E., Ph.D
Notes: Graphic shows cover of the NEHRP Provisions FEMA P-1052.
The 2015 NEHRP Recommended Seismic Provisions are a new resource document that facilitates and translates the state-of-the-art knowledge into design practice. To help in understanding these new Provisions, design examples are also published which apply the new requirements of FEMA P-1051. This presentation complements the Chapter 16 design example of structures that incorporate supplemental energy dissipation devices.
This set of instructional slides is a 60 minute condensed version of the Part 1: Background and Part 2: Design Example presentations (90 minute each) .

## Slide 2: Presentation Objectives
Present background on:
  Intent of seismic requirements
  Overview of major revisions
Illustrate application of the new NEHRP Provisions:
  Seven story office building in region of high seismicity
  Steel moment frame with supplemental fluid viscous dampers
Notes: A graphic shows the cover of the document FEMA P-1050-1, 2015 Edition, “NEHRP Recommended Seismic Provisions for New Buildings and Other Structures”
The first part of this presentation provides a background on key concepts of the seismic provisions and highlights some of the major changes recommended by the NEHRP Provisions. The second part of this presentation illustrates the design of a seven story steel moment frame office building, located in a region of high seismicity (seismic design category D), which is supplemented with nonlinear fluid viscous damping devices.

## Slide 3: Design Requirements Overview
Notes: A diagram shows the relationship between the ASCE 7 Standard (ASCE 7), the NEHRP Provisions (NEHRP), the International Building Code (IBC), the NFPA 5000 Building Code (NFPA), and the California Building Code (CBC). ASCE 7 is located at the center of the diagram. Along the bottom of the diagram are shown the IBC, NFPA and CBC. Arrows point from the IBC, NFPA, and CBC to ASCE 7. In the upper left NEHRP is shown. There is a double-headed arrow between ASCE 7 and NEHRP.
Today, model building codes (e.g., national model codes such as the IBC, or regional derivatives, such as the CBC) adopt by reference the seismic design requirements of ASCE 7. The requirements in ASCE 7 are typically based on NEHRP’s recommended provisions.
All the recommended new changes of the 2015 Provisions have been further developed and adopted into the upcoming ASCE/SEI 7-16, which is expected to be adopted by reference in the 2018 edition of the IBC. As such, the code requirements followed for the NEHRPP Chapter 16 design example are referred to as ASCE 7-16 (referred to simply as the Standard) requirements, instead off the NEHRP 2015 Provisions.

## Slide 4: Intent of Seismic Requirements
Reference: MCEER, SUNY, Buffalo, NY
1st key concept:
Applicable to all types of energy dissipation devices (or “dampers”)
  Dampers absorb and dissipate vibration energy through relative movement across the damper
  Many types: metallic yielding, friction, viscoelastic, pure viscous and other (self-centering systems)
Notes: Along the bottom of this slide there are six small “force-displacement” hysteresis loops illustrating different types of damping devices. The first graph shows a diamond-shaped loop, the second shows a square loop, the third an inclined elliptical loop, the fourth a horizontal elliptical loop, the fifth a “pinched” hysteresis loop, and the sixth an extremely pinched hysteresis loop.
The requirements of the Standard apply to a wide range of damping systems. It applies to all systems that dissipate seismic energy which are not listed as a seismic force-resisting system in Table 12.2 of the Standard.

## Slide 5: Intent of Seismic Requirements
Reference: DIS Inc.
  Hence, the Standard requires design and thorough testing of dampers for MCER level displacements, velocities and forces.
Notes: There are two figures on this slide. The left figure shows force-displacement loops for tests of a viscous wall damper. The right figure shows a testing machine for validating the performance of fluid viscous dampers (hydraulic dampers).
Since the types of dampers can be vastly different, and can involve non-traditional civil engineering materials, or moving parts, the Standard has thorough testing requirements to quantify and validate their performance and quality.

## Slide 6: Intent of Seismic Requirements
2nd key concept:
Dampers supplement the seismic-force resisting systems (SFRS)
  The SFRS must provide a complete lateral load path as if the dampers did not exist.
  Minimum Vb limit for SFRS and ductile detailing requirements may not be relaxed
  Damping system (DS) and SFRS defined independently
Notes: The Standard requires that the damping system also have a SFRS (see Standard Table 12.2-1) that provides a complete load path. The SFRS must comply with the requirements of the Standard (i.e. minimum base shear), except that the damping system may be used to meet drift limits. Thus, the design requirements that are in place for a SFRS without supplemental damping systems (i.e. height and seismic design category restrictions, redundancy limitations, RBS connection and strong-beam weak-column detailing requirements) may not be relaxed for SFRS which include supplemental damping systems.

## Slide 7: Intent of Seismic Requirements
Notes: There are four drawings shown on this slide. Each drawing shows a single story structure. The top drawing is four bays wide, the second drawing is three bays wide, the third drawing is three bays wide, and the fourth drawing is one bay wide. In each drawing there is a single diagonal brace containing a fluid viscous damper. In the first drawing the brace is in the far left bay. In the second drawing the brace is in the far left bay. In the third drawing the brace is in the center bay. In the fourth drawing the brace is in the single bay. In each drawing the far right bay is a moment frame consisting of two columns and the beam, and is labeled SFRS for seismic force resisting system. In each drawing other elements are circled and labeled “DS” for damping system. The damping system always include the diagonal brace, connected framing elements that resist forces developed by the damper, and any other elements required to link the DS to the SFRS.
The damping system (DS), which includes the damping devices and surrounding structural elements, is defined separately from the SFRS even though the two systems may share common elements as shown.

## Slide 8: Intent of Seismic Requirements
3rd key concept:
Requirements permit performance comparable to a conventional SFRS
  Damping system primarily used to reduce drift, and may justify reducing member sizes.
  But typically used to achieve a higher levels of seismic performance
Notes:   A table is shown at the bottom of this slide. The table has three columns, headed “Objectives”, “Conventional”, and “Isolated.” The first column headed “Objectives” has three rows labelled “Deaths”, “Dollars” and “Downtime.” “Thumbs Up” icons indicate favorable outcomes, and “Thumbs Down” icons indicate unfavorable outcomes. Under the Conventional column heading “Deaths” is a thumbs up, while “Dollars” and “Downtime” are both thumbs down. Under the Isolated heading, “Deaths”, “Dollars” and “Downtime” all have thumbs up.
The Standard provides minimum design criteria with performance objectives comparable to those for a structure with a conventional SFRS. For example, the primary factor affecting steel special moment resisting frame (SMRF) member size selection is the need to control drifts below permissible levels. Hence the damping system may be used to reduce drifts, and hence member sizes.
However supplemental dampers are usually used to achieve higher performance levels than a conventional SFRS. by designing the SFRS to have limited ductility, and directing energy dissipation into devices that are readily replaceable (or require no replacement).

## Slide 9: Revisions
Full replacement of ASCE 7 Chapter 18 (the “Standard”) recommended
Notes: A graphic shows the cover of the document FEMA P-1050-1, 2015 Edition, “NEHRP Recommended Seismic Provisions for New Buildings and Other Structures”
Due to the large number of editorial and technical changes, the 2015 NEHRP Provisions have recommended a full replacement of Chapter 18 in the 2016 edition of ASCE 7 (the Standard).

## Slide 10: Revisions
There were technical changes to:
  Ground motion criteria
  Procedure selection
  Determination of damper properties
  System redundancy
  Assumptions for response history analysis
  Number of design reviewers
  Testing requirements
Notes: The major technical changes are stated here and are discussed in more detail in the following slides.

## Slide 11: Revisions
Site-specific hazard analysis is usually required to determine the target response spectrum
New USGS design value maps and site coefficients and new site-specific analysis requirements which, depending on the site location and site conditions, may have a significant effect on design
Ground motions criteria - Target spectrum
Notes: A graph shows examples of several project-specific earthquake response spectra that could be used for design. These spectra are meant to be a schematic illustration only, so the details of the shapes and magnitudes of the spectra are not relevant.
On sites located close to major active faults, or with unstable or soft soil conditions, the two-parameter (S1, Ss) spectrum (a.k.a “ELF” or “USGS website” spectrum) obtained using the ground motion maps in combination with site factors (Fa, Fv) does not provide a good estimate of the spectral shape of design ground motions, particularly at longer periods. Studies of site-specific seismic hazards and site response can significantly improve the shape and amplitude of the design spectrum on such sites, and are usually required for damped buildings.

## Slide 12: Revisions
Only seven ground motions required
Scaling and orientation of ground motions depend on proximity to fault
Amplitude or spectrally matched scaling to meet or exceed target spectrum over a specific period range of interest
Ground motion criteria - Selection and scaling
Notes:   A graph shows several earthquake acceleration response spectra. A smoothed target response spectrum is shown in black. Seven earthquake response spectra are shown as dashed lines. The earthquake records that these spectra represent are listed in a table above the graph. A spectrum showing the average of the seven earthquake spectra is shown in red. This red spectrum matches fairly closely the target spectrum over the period range 1 to 4 seconds.
  For nonlinear response history analysis of supplemental damped buildings, the selection and scaling of ground motions is different to that required by Chapter 16. The minimum number of ground motion records is set to 7 which is consistent with Chapter 17 and current professional practice. Ground motion selection and scaling should be conducted by an expert, experienced with hazards of the region.

## Slide 13: Revisions
Procedure selection
Nonlinear response history analysis (NLRHA) is emphasized as the primary analysis tool.
Equivalent lateral force (ELF) and response spectrum (RS) procedures have been placed at the back of the Chapter and are presented as “alternative methods”.
Notes: Three figures are shown at the bottom of this slide. They are arranged in an equation format, such that (left figure) + (center figure) = (right figure). The left figure shows two earthquake accelerographs, representing two orthogonal components of an earthquake acceleration record. The center figure is a drawing of a building structural frame, indicating the computer model of the building. The right figure shows hysteresis loops of structural dampers, indicating the resulting damper response calculated using the ground motion components and the building model.
NLRHA is permitted for all building types and seismic hazards. It is the most used approach and was the basis for development of the elastic (ELF and RS) procedures.
Furthermore, the NLRHA gives the most realistic prediction of seismic response. This is because the degree to which a damped structure is able to accomplish its performance goals depends on the inherent properties of the structure, the properties of the dampers and its connecting elements, the characteristics of the ground motion, and the limit state being investigated. Given the potentially large variation in each of these parameters, it is usually necessary to perform an extensive suite of nonlinear response-history analyses.

## Slide 14: Revisions
Variability in production dampers properties which on the average differ from the properties measured in prototype testing.
Changes during seismic motion
Changes over design life
Types of λ factors:
  λae,max and λae,min which account for aging and environmental effects.
  λtest,max and λtest,min which account for variations observed during prototype testing.
  λspec,max and λspec,min which account for manufacturing variations
3. Determination of damper properties
Introduction of property modification (λ) factor approach and explicit requirement of separate upper- and lower-bound analyses
Notes: Property modification values are introduced to account for variations in damper properties during manufacturing and while in-service (i.e. envelope behavior). These factors are used to perform bounding analysis where the governing case (for each parameter of interest) is used for design. Require two separate analyses at each hazard level (DBE and MCER): one using the maximum damper properties and one using the minimum damper properties.

## Slide 15: Revisions
3. Determination of damper properties
Maximum and minimum dampers properties
Prototype testing:
Notes: This slide contains a graph with the vertical axis labeled “force” and the horizontal axis labeled “velocity”. Experimental data from damper tests are shown on this plot. The data generally form a pattern in the shape of an inclined “S”. Also shown on this plot are S-shaped lines indicating upper and lower bounds of permissible damper properties. The experimental data fall between the upper and lower bounds.
When there is insufficient test data to determine λ-factors, it is permitted to use 85% and 120% of nominal values as the maximum and minimum values. Results from prototype testing are shown. The solid line depicts the nominal force-velocity relationship of the nonlinear fluid viscous damper with the dotted lines representing a 10% and 20% change in the damping constant value CNL. When test data such as this is used to determine damper properties, the max and min λ factor limits (of 85% and 120%) need not apply.

## Slide 16: Revisions
Redundant system
Non-redundant system, increase damper capacities
4. System Redundancy
Require at least 4 dampers in any story in either principal direction, and at least 2 dampers either side of the center of stiffness in either principal direction, otherwise increase damper capacity by a 1.3 factor
Notes: This slide contains two drawings of the plan view of two buildings. Each building is 5 bays wide by 7 bays long. The left building is labeled “Non-redundant system, increase damper capacities.” This building has only two damper bays in each direction. The right building is labeled “Redundant system”. This building has four damper bays in each direction.
This new section is added to distinguish between redundant and non-redundant systems. The provisions are similar to language of ASCE 41 in which larger force and displacement damper capacities are required when less than 2 dampers in each direction are located on each side of center of mass at any story.

## Slide 17: Revisions
EXCEPTION: It is permitted to account for the effects of accidental eccentricity through the establishment of amplification factors on forces, drifts and deformation that permit results determined from a analysis using only the computed centered-of-mass configuration to be scaled to bound the result of all the mass-eccentric cases.
5. Assumptions for NLRHA
May account for accidental mass eccentricity using amplification factors
Notes: The requirement to account for accidental mass eccentricity intended to increase the design actions. It accounts for effects such as: a) plan distributions of mass being different from that assumed in design, b) non-uniform properties of the SFRS (i.e. strength, stiffness) and/or damping devices, and c) rotational and torsional ground motions.
Requirements are added similar to other chapters of ASCE 7-16, and an exception is provided. The rationale behind this is to avoid doing (unnecessarily) large amounts of analysis to calculate the worst case of accidental eccentricity. Guidance on how to determine amplification factors is provided in commentary.

## Slide 18: Revisions
6. Number of Design Reviewers
At least one registered design professional shall provide an independent review.
Peer reviewer or panel should be engaged early since they must review project design criteria (including site-specific ground motion criteria) and preliminary design.
Notes: Review requirements are specified and clarified in the Standard. The requirements have been relaxed to only one RDP in the latest cycle to expedite the process.

## Slide 19: Revisions
Reference: MCEER, SUNY, Buffalo, NY
More reasonable test program:
  10 cycles 0.33 MCER intensity
  5 cycles 0.67 MCER intensity
  3 cycles 1.0 MCER intensity
Number of cycles at full MCER intensity reduced from five to three cycles
The testing frequency of 1/(1.5T1) assumes some softening of the combined SFRS and DS
7. Testing Requirements - Sequence and cycles of prototype testing
Notes: This slide contains two graphs showing the results of tests on a damper. The upper graph has a horizontal axis labeled “Displacement” and vertical axis labeled “Force”. Rounded hysteresis loops indicate the force-displacement relationship for this damper. The lower graph has a horizontal axis labeled “velocity” and vertical axis labeled “force”. Test data is shown at several different velocities. In addition, upper and lower bound limits are shown. All of the test data falls between the upper and lower bound limits.
ASCE 7-10 required five cycles at MCER intensity which was deemed excessive, and the test program did not address performance at smaller intensities. To address this issue, a sequential set of cyclic test is incorporated at increments of 1/3, 2/3 and 1.0 times the MCER intensity with more appropriate numbers of cycles, and fewer cycles at larger intensities.

## Slide 20: Revisions
Reference: DIS Inc.
Every single device used in construction must be tested (100% production tests) due to recent observations of unacceptable behavior.
But, need not be done on damping devices that undergo damage due to testing.
7. Testing Requirements – Production testing
Notes: There is a photograph at the right side of this slide. It shows a large frame for testing viscous wall dampers.
Requirements for production testing are added. The 100% testing is due to recent observations of failures or unacceptable behavior of hardware that has not been tested.
An exception was also added to the Standard for devices that undergo damage subject to production testing. An alternate procedure is developed to require at least one device of each size is tested (in addition to other requirements developed by the RDP).

## Slide 21: Overview of Design Example
Project Information
Design Process
Design Considerations
  Design Decisions & Preliminary Design
Structural Analysis
    Damper Properties & Nonlinear Response History Analysis
Design of SFRS and
Design of Damping System
Notes: This presentation closely follows the design example sections.

## Slide 22: Project Information
Seismic weight, W = 13,151 kips
Structural Description
Notes: This slide contains a drawing of the structural frame of a building that is 7 stories high, 5 bays wide, and 7 bays long.
This example uses a seven-story office building located in a region of high seismicity, classified as Seismic Design Category D. The building has steel special moment resisting frames (SMRF) around the perimeter and fluid viscous dampers (FVD) in interior frames. The design of the SMRF without energy dissipation devices, for a comparable area of seismicity, is illustrated in Chapter 9 of the NEHRP design examples. The details of that building are directly adopted as a starting point for this example.

## Slide 23: Project Information
Structural Description: Typical Plan
Notes: This slide shows the plan view of the building, 5 bays wide by 7 bays long.
The building has a rectangular plan configuration measuring 175 feet, in the East-West direction and 125 feet wide in the North-South direction. The seismic force resisting system (SFRS) consists of steel special moment resisting frames (SMRF) with prequalified Reduced Beam Section (RBS) connections located on the perimeter bays of the building along Gridlines A, H, 1 and 6.

## Slide 24: Project Information
Structural Description: Typical Elevation
Notes: This slide contains a drawing of an elevation of the building, 7 bays wide and 7 stories tall. In addition there is a penthouse above the 7th story.
The typical story height is 13 feet, 4 inches but with a first story height of 22 feet, 4 inches. The building has a penthouse that extends 16 feet above the roof level of the building and covers the area bounded by Gridlines C, F, 3 and 4 (see previous slide).

## Slide 25: Project Information
Structural Description: SFRS Gridlines 1 and 6
Notes: This slide contains an elevation of one of the special moment frames on gridlines 1 and 6. The sizes of beams and columns are shown on the diagram.
The member sizes for the SFRS are directly adopted from the Chapter 9 analysis and are shown here for Gridlines 1 and 6.

## Slide 26: Project Information
Structural Description: SFRS Gridlines A and H
Notes: This slide contains an elevation of one of the special moment frames on gridlines A and H. The sizes of beams and columns are shown on the diagram.
The SFRS member sizes are shown here for Gridlines A and H.

## Slide 27: Project Information
Reference: Taylor Devices
Structural Description: Damping System
Fluid Viscous Dampers (FVD)
Notes: This slide shows a drawing of a cross section of a fluid viscous damper. In addition there is a photograph of an elevation of two structural framing bays showing two diagonal braces, each with a fluid viscous damper arranged in line with the brace.
Supplemental damping is primarily used to limit deformations in structural components, and thus to achieve a higher performance level. For this design example, fluid viscous dampers (FVDs) are arbitrarily selected as the supplemental energy dissipation devices (or simply “dampers"). The key components of a FVD are shown along with an example of its implementation in a building.

## Slide 28: Project Information
Stories 3-7
Stories 1-2
Structural Description: Damping System
Notes: This slide contains two drawings of the plan view of the building. The building is 5 bays wide by 7 bays long. The left plan is labeled “Stories 1-2.” This plan has four damper bays in each direction. The right plan is labeled “Stories 3-7”. This plan has two damper bays in each direction.
The plan view of the bays with damping devices for stories 1 to 2 and 3 to 7 are shown. To meet the architect’s requirement of having no diagonal bracing members around the perimeter of the building, supplemental damping devices are located on gravity framing lines on the interior of the structure on Gridlines B, G, 2, and 5. More damping devices were required in the lower story's (as will be shown later by preliminary design).

## Slide 29: Project Information
Structural Description: Damping System Gridlines 2 & 5
Notes: This slide contains a drawing of the structural frame elevation at Gridlines 2 and 5. Damper locations are shown. In stories 1 and 2 there are two bays containing dampers, while in the remaining upper stories there is only only one bay containing a damper.

## Slide 30: Project Information
Structural Description: Damping System Gridlines B & G
Notes: This slide contains a drawing of the structural frame elevation at Gridlines B and G. Damper locations are shown. In stories 1 and 2 there are two bays containing dampers, while in the remaining upper stories there is only only one bay containing a damper.

## Slide 31: Project Information
   §11.4.7 Site-specific hazard analysis required
Ground Motion Criteria
Site Hazard and Soil Conditions
  Region of high-seismicity
  Seismic Design Category D
  Soil site class D
Spectral Accelerations
  SDS = 0.93 (SMS = 1.4)
  SD1 = 0.6 (SM1 = 0.6)
  S1 = 0.5
Notes: A graph shows examples of several project-specific earthquake response spectra that could be used for design. These spectra are meant to be a schematic illustration only, so the details of the shapes and magnitudes of the spectra are not relevant.
The building is located in a region of high seismicity, classified as SDC “D”. Since the building is also located on site class D soils, a site-specific hazard analysis is required to determine the target response spectrum to be used for design.

## Slide 32: Project Information
Ground Motion Criteria
Analysis Procedure = Nonlinear Response History Analysis (NLRHA)
Therefore need to select and scale ground motion records:
Nearest active fault > 3 miles away
Therefore apply ground motions in only one random orientation to analysis model
Notes: This slide contains two graphs showing earthquake accelerographs, representing the two orthogonal components of a recorded earthquake ground motions.
Ground motions must be selected and scaled since NLRHA is used.

## Slide 33: Project Information
Ground Motion Criteria
Scaling method = Amplitude scaling
Period range of interest = 0.2T1D to1.25T1M
        = 0.58 to 3.9 seconds
Notes:   A graph shows several earthquake acceleration response spectra. A smoothed target response spectrum is shown in black. Seven earthquake response spectra are shown as dashed lines. A spectrum showing the average of the seven earthquake spectra is shown in red. This red spectrum matches fairly closely the target spectrum over the period range 1 to 4 seconds.
Amplitude scaling is the chosen scaling method. The period range of interest is calculated as the product of 0.2 and the shorter period in the east-west direction (2.9 sec) and the product of 1.25 and the longer period in the north-south direction (3.1 sec), giving a scaling range of 0.58 to 3.9 seconds. This assumes that the building remains elastic at both the design basis and MCER hazard levels and that the FVD’s have little influence on the buildings fundamental period.
The response spectrum for each of the horizontal ground motion components is calculated and the combined square root sum of the square (SRSS) of the two components for each ground motion is shown. The average SRSS spectrum of the seven ground motions (red line) must be above the corresponding spectral acceleration ordinate of the target spectrum over the period range of 0.58 to 3.9 seconds. As shown, in the scaling meets this requirement of the Standard.

## Slide 34: Design Process
Project & Ground Motion Criteria
Preliminary Design of SFRS (without dampers)
Preliminary Design of Damping System
Final Specifications
Damping Device Maximum and Minimum Properties
Nonlinear Response History Analysis
(trial and error iterations)
Re-check SFRS (with dampers included)
Notes: An illustration shows the steps for design of a damped building. The steps are numbered from I through VII, and are to be followed sequentially.
This slide illustrates the typical sequence of tasks for design. Preliminary design involved adopting the seismic force resisting system (SFRS) member sizes directly from the Chapter 9 NEHRP example.

## Slide 35: Design Considerations
Performance goals?
Amount of added damping?
Viscous damper velocity exponent?
Placement and configuration of dampers?
Notes: Before progressing with detailed design, there are a number of considerations.

## Slide 36: Design Considerations
Performance Goals?
Resist minor and moderate earthquakes without damage.
Resist major earthquakes without failure of the damping system, or significant damage to structural and nonstructural components, or major disruption to facility function.
Achieved by sizing the SFRS to remain “essentially” elastic at the MCER level, with virtually all earthquake energy dissipated by the FVDs.
Notes: The use of supplemental damping devices is a design strategy to limit earthquake damage and protect facility function. Although the Standard allows comparable performance to conventional SFRS, this project aims to limit inelastic response of the structural system, which directly reduces the damage in the building that would otherwise be occurring (in a fixed-base building). Furthermore the structure and damping system are designed and tested for the MCER hazard instead of the design earthquake (DE).

## Slide 37: Design Considerations
Added Damping?
Buildings 1 -15 floors ~ 15-25%
Taller buildings ~ 5-15%
Target 20% added damping in the fundamental mode of vibration
Notes: A reduction in ductility demand in the SFRS is facilitated through displacement reductions, which come from increased damping provided by the FVD. However with increased damping typically comes increased base shear (depending on the FVD properties), which will need to be accommodated in the design of the structure and foundations. Nevertheless, in some cases the structural analysis may show benefits from higher damping ratios, greater than 35-45 percent. However at these high damping levels the damper costs starts going past the point of diminishing returns.

## Slide 38: Design Considerations
FVD Velocity Exponent, α?
Linear, α = 1.0
Nonlinear, α = 0.3 – 0.5
Example uses α = 0.38
Notes: This slide contains two graphs. The left graph has horizontal axis labeled “Velocity (inch/sec)”, and vertical axis labeled “Force (kips)”. A solid straight line runs diagonally from the lower left corner to the upper right corner of the graph. This line is labeled “Linear Fluid Viscous Damper, alpha = 1.0”. A dashed line begins at the origin in the corner and forms a parabolic arc to the right, approaching a value about mid-way up the graph at the right edge. This line is labeled “Nonlinear Fluid Viscous Damper, alpha = 0.4” The graph on the right shows two lines that are nearly elliptical in shape. The solid line, corresponding to the linear damper, is a smooth ellipse, while the dashed line, corresponding to the nonlinear damper, forms an ellipse with slightly squared off corners. The nonlinear damper curve falls generally outside the linear damper curve.
The differing force-displacement behaviour of nonlinear and linear fluid viscous dampers (FVD) are illustrated. Consult with the manufacturer on the selection of the velocity exponent. There is interest in using nonlinear dampers because:
Capable of more energy dissipation per cycle for the same displacement amplitude
Safeguard by limiting the transmission of damping force at velocities in excess of design values

## Slide 39: Design Considerations
Placement and Configuration of Dampers?
Positioned to reduce torsion and/or structural irregularities
Notes: This slide contains two drawings. The left drawing is a plan view of the building, 5 bays wide by 7 bays long. There are two bays of dampers in each direction. The right drawing shows an elevation of the building at a gridline containing dampers. At floors 1 and 2 there are two dampers per floor, and at the remaining upper floors there is one damper per floor.
The FVDs can be positioned to reduce torsion (by positioning them away from the center of stiffness), or may be positioned to reduce soft-story irregularities.

## Slide 40: Design Considerations
Note: Patented | Reference: MCEER, SUNY, Buffalo, NY
Reference: Taylor Devices
Used in design example
Placement and Configuration of Dampers?
Three basic configurations:
  Diagonal
  Horizontal, In-line
  Geometric Amplification (toggle)
Notes: There are three small drawings at the bottom of this slide. The drawing on the left shows an elevation of a building with three stories, three bays wide. There is one damper per story configured as a diagonal brace. The drawing at the center shows an elevation of a building with three stories, three bays wide. There is one damped bay per floor. The dampers are configured in a horizontal orientation at the tip of chevron (inverted “V”) braces. The right drawing shows a single structural bay with a scissors brace configured between the lower right corner and about the one-third point of the upper beam.
There are three primary ways of configuring a FVD in a building. The displacement across the damper (i.e. effectiveness) increases from a) to c) configurations.

## Slide 41: Design Considerations
Step 2: Select an added damping for each primary mode. For example, 20% for modes 1 and 2
Step 3: Calculate the pseudo braced building periods
Step 1: Create mathematical model of building without dampers and conduct modal analysis
Preliminary Design
Based on method presented in Christopoulos and Filiatrault, 2006
Notes: This slide contains an isometric view of the framing system for the entire building, 5 bays wide, by 7 bays long, by 7 stories high.
There is many different ways to conduct preliminary design. The Christopoulos and Filiatrault (2006) procedure calculates the linear viscous damping coefficients required of dampers at each story in order to achieve a certain damping ratio in a particular mode. The method assumes stiffness proportional damping.

## Slide 42: Design Considerations
Pseudo braces Gridlines B and G
Preliminary Design
Step 4: Add pseudo braces to the ETABS model (in locations where the dampers will be) with stiffnesses calibrated so the mode shapes are maintained and the mode 1 and 2 periods equal the pseudo braced periods calculated in Step 3.
Notes: An elevation of the structural frame is shown in this drawing. The frame is 5 bays wide by 7 stories tall. The center bay at each story contain a diagonal brace at every story. The frame is titled “Pseudo braces Gridlines B and G”.
To maintain the mode shape, the brace stiffnesses are calibrated according to the lateral stiffness of the unbraced structure.

## Slide 43: Design Considerations
Preliminary Design
Step 5: Calculate required linear viscous damping constant for each story
Notes: Based on stiffness proportional damping, the linear damping constants for horizontally- and diagonally-aligned FVDs is calculated.

## Slide 44: Design Considerations
Preliminary Design
Reduce number of dampers to one type:
  Use linear FVD with damping coefficient of 50 kip-sec/inch
  Add two more bays of dampers in each direction in story's 1 and 2 and use linear FVD
Notes: It is not practical to use different damping coefficients at every level, and in each principle direction, thus engineering judgement is used to reduce the number of FVD to one type.

## Slide 45: Design Considerations
Preliminary Design
Equivalent nonlinear damping coefficient:
Using the CL of 50 kip-sec/inch and assuming a circular frequency of 2.1 rad/sec, displacement amplitude of 2.5 inches and α = 0.4, gives a nonlinear damping coefficient CNL of 120kip-sec/inch
Notes: This provides a rough initial estimate of order-of-magnitude of FVD nonlinear properties, which can later be refined by consulting with the manufacturer and by using nonlinear response history analysis to optimize parameters of interest.

## Slide 46: Structural Analysis
Behaviour of FVD:
Previously manufactured and tested device nominal properties:
  Damping constant,
  C = 128 kip-sec/inch
  Velocity exponent,
  α = 0.38
Maximum and Minimum Damper Properties
Notes: This slide contains a graph with the vertical axis labeled “force” and the horizontal axis labeled “velocity”. Experimental data from damper tests are shown on this plot. The data generally form a pattern in the shape of an inclined “S”. Also shown on this plot are S-shaped lines indicating upper and lower bounds of permissible damper properties. The experimental data fall between the upper and lower bounds.
In the damper force Equations: v is the velocity, C is the damping coefficient, α is the velocity exponent in the range of 0.1 to 2.0 and sgn is the signum function (i.e. sign of the velocity, whether positive of negative).
Since it may be more cost effective with less uncertainty in properties; a device which has already been produced and tested is adopted. This FVD is quite similar to that calculated from preliminary design (nonlinear damping constant of 120 and velocity exponent of 0.4).

## Slide 47: Structural Analysis
Maximum and Minimum Damper Properties
Property modification factors:
  Aging and environmental effects do not need to be considered for this particular device (enclosed and conditioned space), thus λae,max = λae,min= 1.0
  The variations observed in prototype testing (i.e. heating effects) are essentially bounded by ±10%, thus λtest,max =1.10 and λtest,min =0.9
  Highly engineered devices with little variations due to manufacturing, thus λspec,max =1.05 and λspec,min = 0.95
Notes: The property modification factors account are quantified in this slide. These values are manufacturer- and project-specific.

## Slide 48: Structural Analysis
Maximum and Minimum Damper Properties
Limits of Equations 18.2-3a and 18.2-3b do not apply, thus:
Only applied to the damping coefficient, C
  Cmax = 147.2
  Cmin = 108.8
Notes: These values are allowed to be less than the maximum and minimum limits of Standard §18.2.4.5 since they are based on similar prototype test data. These maximum and minimum factors are applied to the damping coefficient only. There is no independent variation considered for the nonlinear exponent α, since varying the damping coefficient in effect also captures the variation (if any) of the α value.

## Slide 49: Structural Analysis
NLRHA Modelling Assumptions
Included all structural elements
Explicitly modelled in-plane diaphragm stiffness
Include axial stiffness of brace installed in-line with FVD’s (2000 kip/inch)
Beams for gravity framing modelled with end moment releases (pinned connections)
3% inherent damping, applied to all modes
SFRS modelled and designed to remain (essentially) elastic
Notes: The key assumptions of the ETABS mathematical model are outlined.

## Slide 50: Design of SFRS
Minimum Base Shear
Minimum base shear allowed by Chapter 18:
SFRS in each principal direction must (at least) remain elastic for this base shear, regardless of the effect of supplemental dampers.
Notes: Regardless of the effectiveness of the damping system, the SFRS must have a minimum strength as outlined (designed as if the dampers were disconnected). The calculation of the Equivalent Lateral Force (ELF) base shear of 618 kip is the same as for buildings without supplemental damping systems. The minimum elastic base shear allowed by Chapter 18 is 464 kip since there are no structural irregularities.

## Slide 51: Design of SFRS
Strength Design of SMRF
Three design checks:
  The minimum base shear of 464 kip (no dampers)
  Demands from the NLRHA (dampers included) at the design earthquake level
Since the SMRF is modelled as essentially elastic in the NLRHA at the MCER level
  Demands must be no more than 1.5 times the expected capacity of the frame
Notes: There are 2 key SFRS design checks and a third depending on the projecting specific performance requirements as well as modelling assumptions.

## Slide 52: Design of SFRS
< 1.0 O.K
Acceptable drift limits usually governing sizing of steel MRF members instead of strength criteria
Strength Design of SMRF
Check 1: D/C Ratios Modal Response Spectrum Reduced Elastic Demands divided by Factored Nominal Capacity Ratios for Gridline 1 SMRF, No Dampers
Notes: This slide shows an elevation of a longitudinal section of the building, 7 bays wide by 7 stories tall. On each beam of the moment frames the demand to capacity ratio (DCR) is shown. The values of all DCRs are less than 1.0.
The Figure shows that the sizing of the frame is of adequate strength to meet the minimum base shear requirement of the Standard as no D/C ratio is greater than 1.0. Even for the conventional design of the SMRF (i.e. per Chapter 9) the minimum base shear using modal response spectrum is allowed to be taken as 0.85V. This along with an increase in forces to account for accidental eccentricity would give D/C ratios for the frame of about 15-20% larger than that in the Figure. This is still well below a D/C close to 1.0, which one may seek to optimize design. The reason for this is that the sizing of beams, and hence columns (due to strong-column, weak-beam requirements) in steel special moment resisting frames (SMRF), are typically controlled by considerations for drift (Hamburg et al. 2009).

## Slide 53: Design of SFRS
SRFS is elastic (~1.0 or less) at the design earthquake level
This check exceeds the requirements of the Standard
D/C Ratios: Unreduced elastic demand over factored nominal capacity
Strength Design of SMRF
Check 2: Demands from the NLRHA (dampers included) at the design earthquake level:
Notes: This slide contains a drawing of a longitudinal elevation of the building, 7 bays wide by 7 stories tall. Demand-to-capacity ratios (DCRs) are shown for the nonlinear time history analysis with dampers included. Some of the beams at floors 3 and 4 have DCRs greater than 1.0.
This figure is of the steel moment resisting frame on Grid 1 (or 6). The numbers on each beam are the absolute maximum of the positive or negative moment divided by the elastic capacity of the RBS. A number above 1.0 indicate that steel yielding is occurring. For low damage design (which exceeds the Standard) it is preferable that the frame remains elastic/undamaged. The D/C ratios for the SMRF on Gridline 1 are show a much better seismic performance since the frame is elastic at the design earthquake level.

## Slide 54: Design of SFRS
Strength Design of SMRF
Check 3: Validity of the linear-elastic SMRF modelling assumption. Therefore check the NLRHA MCER demands are no more than 1.5 times the expected capacity of the frame capacities (= “essentially elastic” definition)
Otherwise explicitly model the nonlinear behaviour of the steel SMRF.
Notes: The Standard allows the SRFS to yield and become damaged, hence satisfying this check exceeds the minimum requirements. However this check is required to validate modelling assumptions.

## Slide 55: Design of SFRS
< 1.5 O.K
No need to explicitly model the nonlinear behaviour of the frame.
Thus the SMRF performs essentially elastically for the MCER event = Higher seismic performance
Strength Design of SMRF
Notes: This slide contains a drawing of an longitudinal elevation of the building, 7 bays wide by 7 stories tall. Demand to capacity ratios are shown on each beam. Some demand to capacity ratios are greater than 1, but all values are less than 1.5.
As desired in the project objectives, the structure is relatively undamaged in a major (MCE_R) earthquake.

## Slide 56: Design of SFRS
   Governs
Reference: ASCE 7
Permissible Drifts
Are checked only at the MCER level with the dampers included and have three limits:
  3% limit
  1.9 times Table 12.12-1 limit = 3.8%
  1.5R/Cd times Table 12.12-1 limit = 1.5 × 8/5.5 × 2% = 4.4%
Notes: This slide contains an image of a simple structural frame, one bay wide and two stories high. The figure shows the frame swaying to the right, illustrating that lateral forces cause lateral drift of the frame.
The maximum permissible story drift is 3%.

## Slide 57: Design of SFRS
  Maximum drift = 2.0% × torsional amplification factor
  = 2.0% × 1.14 = 2.3% < 3.0% O.K
  Minimum Properties
  Maximum Properties
Permissible Drifts
MCER NLRHA Average Results:
Notes: The story drift history (i.e. drift vs. time) is calculated for each ground motion by subtracting the node displacement at the floor below from a vertically aligned node from the floor above. The maximum drift, at any instant in time, from each of the ground motions is then averaged to give the MCER drifts in the Tables for maximum and minimum damper propertie. The maximum drift at any story, in either principal direction, is 2.0%. This value needs to be increased to account for accidental eccentricity. As per torsion analysis, a drift amplifier of 1.14 is applicable, giving a drift demand of 2.3% which is less than the 3% limit.

## Slide 58: Design of Damping System
  Minimum Properties
  Maximum Properties
Designed to remain elastic (nominal material strengths and ϕ=0.9) for MCER demands.
MCER NLRHA average (of seven motions) results:
Notes: The damping devices shall be sized to elastically resist the forces, displacements and velocities from the MCER ground motions. The critical damper forces and displacements are highlighted.

## Slide 59: Design of Damping System
Corresponding velocity at peak force:
Design force for damper (increase for torsion and redundancy)
Damper displacement capacity (increase for torsion and redundancy)
Notes: Since the redundancy criteria of §18.2.4.6 are not satisfied for stories 3-7, the devices at these stories must be capable of sustaining the force and displacement associated with a velocity equal to 1.3 times the maximum calculated velocity. For ease of construction and to control damper and detailing costs, all dampers will be designed for this penalty to maintain one type of damper.

## Slide 60: Design of Damping System
Nonlinear Fluid Viscous Damper Device Details:
Notes: The key specifications for the nonlinear FVD are outlined.

## Slide 61: Design of Damping System
Reference: Taylor Devices
Damping System Framing
Include: Braces in-line with the dampers, their connections, the framing (beams and columns) which encompass the damping devices and the collectors and diaphragm
Size to remain elastic for MCER demands using nominal capacities and ϕ, of 1.0.
Notes: This slides contains a drawing of a simple structural frame one story high and three bays wide. In the left bay is shown a fluid viscous damper in line with a diagonal brace. The damper, right column of the left bay, and horizontal beam of the center bay are circled and labeled “DS” for Damping System. The two columns and beam of the right bay form a moment resisting frame, and are circled and labeled “SFRS” for Seismic Force Resisting System. This slide also contains a photograph of a single structural bay containing a diagonal brace with a single fluid viscous damper in line with the brace.
The damping system involves not only the FVD devices, but a range of elements which must be checked for MCER demands.

## Slide 62: DISCLAIMER
NOTICE: Any opinions, findings, conclusions, or recommendations expressed in this publication do not necessarily reflect the views of the Federal Emergency Management Agency. Additionally, neither FEMA nor any of its employees make any warranty, expressed or implied, nor assume any legal liability or responsibility for the accuracy, completeness, or usefulness of any information, product or process included in this publication.
The opinions expressed herein regarding the requirements of the NEHRP Recommended Seismic Provisions, the referenced standards, and the building codes are not to be used for design purposes. Rather the user should consult the jurisdiction’s building official who has the authority to render interpretation of the code.
Any modifications made to the file represent the presenters' opinion only.