## Slide 1: Seismically Isolated Structures
Disclaimer
SUMMARY
William McVitty, P.E., M.S., Andrew Taylor, S.E., Ph.D
Notes: Graphic shows cover of the NEHRP Provisions FEMA P-1052.
The 2015 NEHRP Recommended Seismic Provisions are a new resource document that facilitates and translates the state-of-the-art knowledge into design practice. To help in understanding these new Provisions, design examples are also published which apply the new requirements of FEMA P-1051. This presentation complements the Chapter 15 design example of a seismically isolated building.
This set of instructional slides is a 60 minute condensed version of the Part 1: Principles and Background and Part 2: Design Example presentations (90 minute each) .

## Slide 2: Presentation Objectives
Background on major revisions
Illustrate application of new NEHRP Provisions through a design example
  Isolated three-story emergency operation center (EOC) located in a region of high seismicity
Present basic principles of seismic isolation: What?, Why?, Where?, How?
Notes: A graphic shows the cover of the document FEMA P-1050-1, 2015 Edition, “NEHRP Recommended Seismic Provisions for New Buildings and Other Structures”
The objective of this presentation is to first describe the basic principles of seismic isolation. What is it? Why should you isolate a building? Where does isolation work well and not so well, and how it is applied with discussion on the types of isolation systems. The second part of the presentation gives background of some of the major changes recommended by the NEHRP Provisions. The third part of the presentation shows application of the Provisions through a design example.

## Slide 3: What is seismic isolation?
A flexible, sliding or rolling horizontal interface between the structure and the ground.
This interface lengthens the period of the structure away from dominant earthquake frequencies and is complemented with the ability to absorb energy.
Notes: The basic concept of seismic isolation (also referred to as base isolation) is to “de-couple” the “superstructure” (structure above the isolation interface) from potentially damaging ground motions by adding “seismic isolators” which support the structure above while permitting large relative horizontal displacement of the structure in an earthquake. The seismic isolators de-couple response from dominate short-period earthquake shaking by essentially making the fundamental-mode period of the isolated structure a couple of times longer than the period of the structure above the isolation system – that is, longer than the period of the same structure on a fixed base. In this manner, the large displacement of the isolation system gives a reduction in force in the structure above the isolation system. The ability of the isolators to absorb energy (or increase damping) further improves performance.

## Slide 4: What is seismic isolation?
Reference: DIS Inc.
Thus, looking at representative response spectra, what is the premise of seismic isolation?
Notes: The figure shows two graphs: an acceleration response spectrum on the left, and a displacement response spectrum on the right. In the left graph a horizontal arrow points to the right, labeled “Period Shift”. This arrow illustrates that acceleration response of the building is reduced as the period of the structure is shifted from low values (in the neighborhood of 0.5 seconds) to higher values (in the neighborhood of 2.5 seconds). The left graph also shows three different parallel acceleration plots, each plot for a different level of damping, showing that the acceleration response is decreased as damping is increased. On the right graph a horizontal arrow points to the right, labelled “Period Shift”. This arrow illustrates that displacement response of the building is increased as the period of the structure is shifted from low values (in the neighborhood of 0.5 seconds) to higher values (in the neighborhood of 2.5 seconds). The right graph also shows three different parallel acceleration plots, each plot for a different level of damping, showing that the displacement response is decreased as damping is increased.
The flexible interface, when initiated by a major earthquake, shifts the period of the structure to a part of the spectrum which usually experiences lower accelerations. Although there is a increase in displacements, this is concentrated at the isolation interface. The isolators ability to absorb energy (damping) reduces this displacement and further reduces accelerations.

## Slide 5: Why isolate?
Objectives | Conventional | Isolated
Deaths Serious injury and life loss not expected |  | 
Dollars No or minimal structural and non-structural repair costs |  | 
Downtime No or minor loss of function for all facilities |  | 
Isolation achieves a greatly improved seismic performance compared to most other conventional fixed-base seismic force resisting systems in a major earthquake.
Notes: The table has three columns, headed “Objectives”, “Conventional”, and “Isolated.” The first column headed “Objectives” has three rows labelled “Deaths”, “Dollars” and “Downtime.” “Thumbs Up” icons indicate favorable outcomes, and “Thumbs Down” icons indicate unfavorable outcomes. Under the Conventional column heading “Deaths” is a thumbs up, while “Dollars” and “Downtime” are both thumbs down. Under the Isolated heading, “Deaths”, “Dollars” and “Downtime” all have thumbs up.
The main reason why to isolate is to reduce structural, non-structural and contents damage and hence maintain operation after a major earthquake.
All seismically isolated buildings (not just critical facilities) are expected to have minimal repair costs and downtime, whereas a conventional building may be damaged to the point where it is uneconomical to rehabilitate. This is due to the inherent nature of isolation, for example it reduces both displacements and accelerations in the superstructure. Although not explicitly seeking damage control as an objective, indirectly the minimum requirements of the Standard will give limited damage as a consequence of ensuring proper isolation achieved. For example, the Standard limits the amount of inelastic action and drift that may occur in the superstructure to avoid detrimental coupling with the isolation system. Moreover, the Standard requires that the isolation devices be designed and tested to be functional under the effects of the Maximum Considered Earthquake (MCER).

## Slide 6: Where to isolate?
Reference: www.berkeleyheritage.com and Earthquake Protection Systems, Inc.
Essential facilities such as emergency operation centers that require continued functionality for public health and safety.
Historic structures and museums that have low available ductility, valuable contents and require preservation.
Business facilities such as data centers and factories that have high-value or hazardous contents and/or require continued functionality
Notes: There are two photographs on the right side of the slide. The top photograph shows the historic U.S. Court of Appeals building in San Francisco, and the bottom photograph shows an offshore oil drilling platform.
Due to the major improvement in response of a seismically isolated building, there have emerged some natural candidates where isolation is commonly applied.

## Slide 7: Where to isolate?
Almost any building can be isolated, however there are several factors where it is more or less effective:
Buildings characteristics
Short-period structures (say T1<1.0 sec)
Heavy buildings
Overly flexible or tall structures
Slender buildings and Seismic Force Resisting Systems (SFRS) configurations that give large uplift forces
Notes: Technical speaking, any building can be seismically isolated, however there are a number of factors which make it more, or less suitable. Consideration of the buildings characteristics, site conditions, space and location of the isolation plane should made early in design. The following three slides outline the most important consideration.
Short and/or stiff buildings are best suited to isolation as they will benefit the most from period lengthening. High seismic weight is typically a detriment in seismic design due to high inertial forces; however it is much less of a concern in a seismically isolated building as isolators can accommodate large axial loads. Isolators perform well under compression and have little/no resistance to tension forces. Hence uplift in isolators presents difficult analysis, design and testing challenges and should be avoided.

## Slide 8: Where to isolate?
2. Site conditions
Stiff soils
Sites susceptible to basin amplification
Sloping sites that requires a stepped isolation plane
3. Space and installation
Isolation plane is above grade level
Close adjacent buildings (moat clearance)
Notes: Sites that have soft soils and basin effects may give more earthquake energy in periods which coincide with the period of the isolation system. This may lead to resonance of the seismically isolated building if it has little damping.
The location of the isolation plane may be the single most important cost consideration in the design of a seismically isolated building. Locating the isolation system below grade typically triggers several costly requirements: (1) a basement must be excavated and constructed, (2) retaining walls must be constructed around the basement, and (3) moat details must be provided.

## Slide 9: How to isolate?
Isolator Units (or Bearings):
Horizontally have low stiffness, re-centring ability and good energy dissipation.
Are vertically stiff and stable under the weight of the building and large displacement.
Have well established and repeatable mechanical properties with limited degradation
Notes: The Standard defines isolator units as horizontally flexible and vertically stiff elements, assuming that isolation system provides only horizontal isolation. The use of isolation systems that have no or very little restoring force is prohibited.
Seismic isolation is an old concept and our improvement has been in the capability to construct isolator types which have reliable and predictable behavior. Therefore the Standard requires that the isolator units have well established (through qualification and prototype testing) mechanical properties, which are repeatable and that do not significantly degrade (i.e. the isolators a durable and stable).

## Slide 10: How to isolate?
Reference: MCEER-11-0004
SUNY, Buffalo, NY
Two of the most common types:
Elastomeric (rubber) Isolators
Consist of alternating layers of rubber and steel shims.
  Low- or high-damping rubber bearings
  Lead-rubber (LR) bearings
Notes: The photograph shows an elastomeric isolation bearing that has a wedge cut out of it to indicate the internal construction of the isolator. Internal alternating layers of rubber and steel are visible, with the rubber layers about 10 mm thick and the steel layers about 3 mm thick. Also visible at the interior of the bearing is a vertical lead cylinder which is inserted into a vertical hole at the center of the isolator.
The two most commonly used isolator types are elastomeric and sliding isolators. These types have been extensively tested and implemented over the past three decades.
Elastomeric isolators are made of rubber (a visco-elastic material) which are constructed in alternating layers of steel and rubber in order to have high vertical stiffness and to avoid lateral shear buckling. There are three types: low damping (less the about 5%) and high damping rubber bearings, and lead-rubber bearings. LR bearings consist of low damping rubber and a central lead core which gives strengths and energy absorption ability.
The significance of this slide to earthquake engineering is that it shows how seismic isolation is implemented in practice.

## Slide 11: How to isolate?
Reference: MCEER-08-0007
SUNY, Buffalo, NY
Two most common type:
2. Sliding Isolators
Utilize a low-friction sliding interface, commonly PTFE (Teflon) on polished stainless steel.
  Concave sliding system
    Single-concave sliding surface
    Double-concave sliding surface
    Triple-pendulumTM bearings
  Flat sliding bearings (used with rubber isolators)
Notes: A drawing shows an isometric view and a cross section of a double friction pendulum isolation bearing. The top of the bearing is a steel dish facing downwards, and the bottom of the bearing is a steel dish facing upwards. Between the two dishes is an articulated slider consisting of a hinged assembly with an upper radius that matches the contour of the upper dish, and a lower radius that matches the contour of the lower dish. The interfaces between the articulated slider and the steel dishes consists of a polished stainless steel liner in each dish, and low-friction sliding material on the top and bottom surfaces of the articulated slider.
Other types of isolation systems in the United States include sliding systems, such as the friction pendulum system, or some combination of elastomeric and sliding isolators. The concave sliding isolators may be composed of single-concave sliding surface bearings (original “dish” concept), double-concave sliding surface bearings (each with two dishes, one facing up and one facing down), or triple-pendulum bearings (a more sophisticated version of the double-concave bearings). In each case, gravity is used as the restoring force of the concave sliding bearings.
Some applications at sites of very high seismicity (such as that of the de Young Museum in San Francisco) also use supplementary fluid-viscous dampers in parallel with either sliding or elastomeric bearings.

## Slide 12: Design Requirements Overview
Notes: A diagram shows the relationship between the ASCE 7 Standard (ASCE 7), the NEHRP Provisions (NEHRP), the International Building Code (IBC), the NFPA 5000 Building Code (NFPA), and the California Building Code (CBC). ASCE 7 is located at the center of the diagram. Along the bottom of the diagram are shown the IBC, NFPA and CBC. Arrows point from the IBC, NFPA, and CBC to ASCE 7. In the upper left NEHRP is shown. There is a double-headed arrow between ASCE 7 and NEHRP.
Today, model building codes (e.g., national model codes such as the IBC, or regional derivatives, such as the CBC) adopt by reference the seismic design requirements of ASCE 7. The requirements in ASCE 7 are typically based on NEHRP’s recommended provisions.
All the recommended new changes of the 2015 Provisions have been further developed and adopted into the upcoming ASCE/SEI 7-16, which is expected to be adopted by reference in the 2018 edition of the IBC. As such, the code requirements followed for the Chapter 15 design example are referred to as ASCE 7-16 (referred to simply as the Standard) requirements, instead off the NEHRP 2015 Provisions.
The most current version of the Standard, ASCE 7-10, has been adopted by the 2012 IBC (by reference). Most jurisdictions and regulatory authorities in the United States have (or will) adopt the 2012 IBC (or regional derivatives thereof).

## Slide 13: Revisions
Full replacement of ASCE 7 Chapter 17 (the “Standard”) recommended
Notes: A graphic shows the cover of the document FEMA P-1050-1, 2015 Edition, “NEHRP Recommended Seismic Provisions for New Buildings and Other Structures”
The NEHRP provision incorporate the state-of-the-art in knowledge and research, and aim to improve building practices. Due to the large number of technical and editorial changes, the 2015 NEHRP Provisions have recommended a full replacement of the Standard.

## Slide 14: Revisions
1. MCER-only basis for design
Modified the elastic base shear calculation from the DBE event to the MCER event, but now using a consistent set of the upper- or lower- bound properties.
Consequently, the DBE event was removed completely from Ch 17.
Notes: To expedite design, the chapter has been re-written so that only the MCER event needs to be considered for design. The design basis earthquake (DBE) has been completely removed and all the relevant provisions updated to reflect this. In some cases, this has resulted in more conservative design requirements.

## Slide 15: Revisions
Isolation System Properties
Completely new section to systematically account for the variability and uncertainty in isolator properties.
Process is to use the property modification (λ) factor approach
Two parallel upper- and lower-bound analysis are conducted, where the governing case for each response parameter of interest is used for design.
Notes: There is a graph at the bottom of the slide. This graph shows two Force-Displacement hysteresis loops. One loop is for “upper bound” isolation properties, with a higher value of effective stiffness; the other loop is for “lower bound” isolation system properties, with a lower value of effective stiffness.
Bounding procedures are used as a simplifying and practical approach to account for the probabilistic range in isolator properties. Two analyses are necessary as either the maximum or minimum probable isolator properties may govern for design. For instance, an upper-bound analysis may govern the sizing of the building frame whereas a lower-bound analysis may govern the sizing of the isolation hardware and surrounding moat clearance. B
Bounding procedures have already been used on many projects, for examples the new de Young Museum where the upper & lower bound force-displacement relations of combined elastomeric (76 HDR) and 76 sliding bearings are shown. Therefore the Standard’s revisions are not a vast change in design practice, however are intended to give more guidance on what factors to consider when determining maximum and minimum probable isolator properties.

## Slide 16: Revisions
Property modification (λ) factor categories:
λae.max and λae.min which account for aging and environmental effects. (i.e. aging, contamination, low temperatures)
λtest,max and λtest.min which account for scragging, hysteretic heating and speed of loading (observed in dynamic prototype testing)
λspec,max and λspec.min which account for manufacturing variations.
These are then combined using the following equations:
Notes: The concept of property modification factors was originally presented in Constantinou et al. (1999) and is already implemented in bridge design codes. The λ-factor approach is to assess the impact of a particular effect on the bearing properties (e.g. heating, aging, velocity, etc), and if the effect is appreciable then assigning it a λ-factor and accounting for the effect in analysis and design. For example, if an effect causes a 10% increase in a nominal property than it is assigned a λ value of 1.10 and contributes to the overall λmax factor. The λ-factors are determined through testing, rational analysis and engineering judgment.
In the equations shown, the Standard presumes a system property adjustment factor fa of 0.75, to account for the conservative assumption of having full aging and environmental effects when the governing earthquake occurs. Furthermore the upper and lower limits of 1.8 and 0.6 only apply for inexperienced manufacturers who have little/no test data. Hence these limits are rarely expected to apply and are intentionally wide.

## Slide 17: Revisions
Ground Motion Criteria- NLRHA
Only seven ground motions required (other structures in ASCE 7-16 require 11)
Includes specific scaling requirements for amplitude and spectrally matched ground motions
Need only apply motions to analysis model in one orientation.
Clarified scaling for both FN and FP components at near-fault sites.
Notes: Two graphs are shown at the right side of the slide. The top graph shows acceleration response spectra for seven different ground motions, as well as a smoothed “target” spectrum. The seven response spectra fall in a range both above and below the target spectrum. The lower graph is also an acceleration response spectrum plot. On this graph are shown the target response spectrum from the previous graph along with the average of the seven records from previous graph. The average response spectrum matches the target response spectrum closely over the period range of interests, from approximately 1.1 to 2.7 seconds.
The ground motion criteria for seismically isolated structures is different to that required for the NLRHA of other structures in ASCE 7-2016 (i.e. Chapter 16). This is a technical as well as philosophical debate and the isolation code subcommittee thought is was appropriate not to adopt 11 ground motions. The figures to the right shows amplitude scaled ground motions compared to the target spectrum, where the average of all seven motions is greater than the target spectrum over the period range of interest.

## Slide 18: Revisions
Reference: DIS Inc. with edits
ASCE 7-16
ASCE 7-10
4. ELF Procedure Structural Shear Distribution
New, more realistic vertical distribution of lateral forces associated with the ELF method of design
Notes: Two figures appear at the bottom of this slide. The left figure is titled “ASCE 7-10” and shows an elevation of a five story by three bay frame structure resting on top of a seismic isolation system. Horizontal arrows indicate the inertial force developed at each floor, according to ASCE 7-10. These arrows are short near the base of the structure, and their length increases over the height. The right figure is titled “ASCE 7-16”, and the building illustrated is the same as in the left figure. In the right figure, however, the horizontal arrows that indicate design forces according to ASCE 7-16 do not increase linearly over the height of the structure. Instead, the lengths of the arrows are nearly the same, with the shortest arrows appearing near the bottom story, and at the roof level.
The proposed revision to the vertical force distribution is based on recent analytical studies (York and Ryan, 2008), which gives a more realistic distribution for base-isolated structures.

## Slide 19: Revisions
Case | Isolator Properties | Accidental Eccentricity
I | Lower Bound | No
Iia | Lower Bound | Yes, X direction
Iib | Lower Bound | Yes, Y direction
5. Establishing amplifications to account for accidental mass eccentricities
Only two additional analysis cases required, IIa and IIb:
The following amplification factors (ratio of Case IIa or IIb response to Case I response) are computed:
isolator displacement at the plan location with the largest isolator displacement;
story drift in the structure at the plan location with the highest drift, enveloped over all stories;
frame-line shear forces at each story for the frame with to the maximum drift.
Notes: The effects of accidental mass eccentricity in NLRHA are permitted to be accounted for using amplification factors, instead of explicitly modeling of accidental eccentric mass in four different segments. The method outlined in the commentary is to do two additional analyses with the worst case eccentricity (accidental + inherent) in the X- and Y- directions (i.e. IIa and IIb), and compute a number of amplification factors for displacements, drifts and forces.

## Slide 20: Revisions
Reference: Earthquake Protection Systems, Inc.
6. Testing Requirements
Some changes include:
Move towards having dynamic testing (i.e. prototype testing now has dynamic sequences).
Specific “similarity” criteria added to define when prototype testing may be waived.
Production testing in combined compression in shear is now required for all (100%) of isolators.
Notes: There is a photograph on the right side of this slide. The photograph shows a large machine for testing sliding seismic isolation bearings. At the top of the photograph are five vertical hydraulic actuators that apply vertical load to the test bearing. At the bottom of the photograph is a sliding table that moves horizontally to apply lateral displacements to the test bearing.
The testing protocols (sequence and cycles) in the Standard can be traced back to historical documents where testing was performed quasi-statically. Now it is becoming recognized that most isolators have velocity dependency and that their dynamic behavior can be quite different to their quasi-static behavior. Hence, although not explicitly stated in the Standard, it is implied that some form of dynamic qualification and/or prototype testing be conducted on isolators before they are use in construction. Dynamic testing is important for sliding isolators.

## Slide 21: Overview of Design Example
Project Information
Design Steps
Preliminary Design
Isolation System Properties
Equivalent Lateral Force (ELF) Procedure
Dynamic Analysis
  Vertical Response Spectrum
  Response History
Testing Requirements
Notes: This presentation closely follows the design example sections and is ordered in the way that design progresses.

## Slide 22: Project Information
Structural Description
Seismic Weight = 10,200 kip (D+0.5Lred)
Notes: This illustration shows an Emergency Operations Centre (EOC), which is a three story, steel frame structure with a large, centrally located mechanical penthouse. Story heights are 14 feet at the first floor to accommodate computer access flooring and other architectural and mechanical systems and 12 feet at the second, third and penthouse floors. The roof and penthouse roof decks are designed for significant live load to accommodate a helicopter landing pad and to meet other functional requirements of the EOC.

## Slide 23: Project Information
Notes: This illustration shows the structure plan, which is regular and symmetrical in configuration, and which has plan dimensions of 100 feet by 150 feet at all floors except for the penthouse. The penthouse is approximately 50 feet by 100 feet in plan. Columns are spaced at 25 feet in both directions. 35 lead-rubber bearings are used to isolate the building and are located beneath each column.
This figure shows typical floor framing - 4 bays x 6 bays. The beams sizes on the base level, just above the isolators, are larger and with moment-resisting connections.

## Slide 24: Project Information
Notes: This figure is a plan view showing penthouse roof framing, measuring 50 feet by 100 feet.
Note the labeling of the longitudinal (X-direction) in the left-right direction of the page, and transverse (Y-direction) in the up-down direction of the page.

## Slide 25: Project Information
This structure is purposely configured to the minimize uplift (tension) demands, through:
  Increasing the number of bays with bracing at lower stories.
  Locating braces at interior (rather than perimeter) gridlines since they have greater gravity loading.
  Avoiding common end columns for bracing in the transverse and longitudinal directions.
Notes: Early in the project the designer should consider how they can configure the structure to minimize uplift forces on the bearings. Isolation bearings are rather poor at sustaining tension loads and it adds complication to analysis and testing if designing for uplift.
The following slides show how the framing was configured to minimize tension in the bearings.

## Slide 26: Project Information
Notes: This figure is an elevation view showing longitudinal bracing on Lines B and D. The lateral force resisting system consists of a roughly symmetrical pattern of concentrically braced frames. These frames are located on Gridlines B and D in the longitudinal direction and on Gridlines 2, 4 and 6 in the transverse direction. It should be noted that the locations of the braced frames spread out gradually, and the number of braces increases, from the top of the building to the bottom. This distributes overturning forces to many bays, which minimizes the uplift force in any individual bay.

## Slide 27: Project Information
Notes: This figure is similar to the figure on the previous slide, but it shows two transverse cross sections, illustrating transverse bracing on Lines 2 and 6 on the left, and Line 4 bracing on the right. As in the previous slide, braces are spread out near the base of the building to minimize uplift forces in any individual bay.

## Slide 28: Project Information
Performance Criteria:
Emergency Operation Center: Occupancy Category IV
Project specific goals are to:
Resist minor and moderate earthquakes without damage.
Resist major earthquakes without failure of the isolation system, or significant damage to structural and nonstructural components, or major disruption to facility function.
Implicitly achieved by using a Standard-compliant isolated building, accordingly:
  Occupancy Importance Factor: Ie = 1.0 for all isolated structures (Ie = 1.5 for other conventional Category IV structures)
Notes: Seismic isolation is an appropriate design strategy for EOCs and other essential facilities where the goal is to limit earthquake damage and protect facility function. Although damage control is not an explicit objective of the Standard, the design to limit inelastic response of the structural system directly reduces the level of damage in an isolated building that would be otherwise be occurring (in a fixed-base building). Furthermore the structure and isolation system are designed and tested for the MCER hazard instead of the DBE.

## Slide 29: Project Information
   §11.4.7 Site-specific hazard analysis required
Ground Motion Criteria:
Site Hazard and Soil Conditions
  Region of high-seismicity
  Seismic Design Category D
  Soil site class D
Spectral Accelerations
  SMS = 1.4
  SM1 = 0.9
  S1 = 0.5
Notes: A graph shows examples of several project-specific earthquake response spectra that could be used for design. These spectra are meant to be a schematic illustration only, so the details of the shapes and magnitudes of the spectra are not relevant.
The building is located in a region of high seismicity, classified as SDC “D”. Since the building is also located on site class D soils, a site-specific hazard analysis is required to determine the response spectrum to be used for design.

## Slide 30: Design Steps
Step I:
Project & Ground Motion Criteria
Step II:
Preliminary Design
Step III:
Isolation System Properties and ELF Analysis
Step VII: Final Specifications
Step IV:
Vertical Earthquake Effects
Step V:
Revisit ELF Analysis & Optimize
Step VI: (if required)
Dynamic Analysis
Notes: An illustration shows the steps for design of a seismically isolated building. The steps are numbered from I through VII, and are to be followed sequentially.
These design steps are adapted from SUNY Dist. Prof. M. C. Constantinou. Although they are specific for a elastomeric (lead-rubber bearing) isolation system, the process is similar for sliding isolation systems.

## Slide 31: Preliminary Design
Reference: MCEER, SUNY, Buffalo, NY
Philosophy:
Use information from previously manufactured and tested bearings, instead of doing theoretical optimizations which give atypical designs.
Latest in knowledge: Constantinou et al 2007 & 2011 MCEER reports (recommend you download, free)
Notes: This slide has illustrations of the covers of two MCEER reports: “Performance of Seismic Isolation Hardware under Service and Seismic Loading” and “LRFD-Based Analysis and Design Procedures for Bridge Bearings and Seismic Isolators.” There is also a small photograph of an elastomeric lead-core seismic isolation bearing.
This preliminary design is specific for lead-rubber bearings, although the philosophy is similar for other systems, and is based on the approach by Constantinou et al. (2011). The goal should be to use information on previously manufactured and tested bearings, instead of doing theoretical/parametric optimizations (which give atypical designs). This gives more certainty and is likely to give less expensive designs which are quicker to manufacture, test and deliver.

## Slide 32: Preliminary Design
O.K
Not acceptable, need ≥ 0.25inch and ≤ 250%, iterate
Select trial bearing dimensions and lower bound properties.
Quickly estimate displacements (and rough compression forces) using the ELF procedure.
Assess the bearings adequacy (stability) and iterate on bearing dimensions
Elastomeric Isolation System:
Notes: There is a small photograph of an elastomeric lead-core seismic isolation bearing.
The manufacturer can be consulted to determine trial bearing dimensions and properties. If unknown, the engineer can progress with recommendations by Constantinou (2011). The design may be conservative at this stage as the analysis is not refined. A spreadsheet aids in the trial an error iteration of the bearing dimensions.

## Slide 33: Isolation System Properties
  typically custom designed and proprietarily constructed, and
  manufactured using non-traditional materials (lead, elastomers, Teflon)
  Much like baked bread, their behavior (taste) may vary significantly between projects (batches) and suppliers (bakers)
Bearings have variability and uncertainty in their properties, since they are:
Notes: Seismic isolators have unique characteristics that are unfamiliar to most engineers. Foremost they have variability and uncertainty in their properties which require thorough testing to quantify. This is because isolators are usually custom designed, are constructed using proprietary technologies and are made of non-traditional civil engineering materials like composites, lead and elastomers. Consequently, there can be a considerable difference in the quality and performance of different isolators, even for identical isolator types produced by different manufacturers.

## Slide 34: Isolation System Properties
Changes over the life of the bearing (i.e. 30-50 years)
Based on qualification test data
For quality manufactures of lead-rubber bearings:
  Stiffness: Shear modulus of rubber, G:
  Strength: Effective yield stress of lead σYL :
Aging & Environmental Effects, λae,max and λae,min
Notes: The aging and environmental λ factors λae,max and λae,min account for the change in properties that occur over the design life of the bearing. Effects include aging, creep, contamination, fatigue, effects of ambient temperature and cumulative travel. For the bearings considered in this example, aging and contamination are the relevant considerations.

## Slide 35: Isolation System Properties
Consult with manufacturer on quality and control procedures and specification tolerance.
For quality manufactures, :
  Stiffness: Shear modulus of rubber, G:
  Strength: Effective yield stress of lead σYL :
Manufacturing Variations, λspec,max and λspec,min
Notes: The specification λ-factors; λspec,max and λspec,min are a manufacturing tolerance assumed for design and written into specifications. Consult with manufactures, as overly tight tolerances may lead to problems and delays.

## Slide 36: Isolation System Properties
Reference: MCEER-15-005, SUNY, Buffalo, NY
Dynamic Prototype (or Similar) Bearing Test Data
Notes: There is a graph of the shear force-displacement curve for an elastomeric, lead-core, isolation bearing tested under dynamic conditions.
For this example, dynamic testing per §17.8.2.2, Item 3 is conducted at a vertical load equal to D + 0.5L on two virgin (unscragged) bearings tested at a normal temperature of 20°C. This test consists of three fully-reversed cycles at a displacement amplitude of DM conducted dynamically at the effective period TM determined from the upper-bound properties. Therefore the speed of loading effects and heating effects are directly accounted for. Note that Eloop is the energy dissipated per cycle (also known as EDC).

## Slide 37: Isolation System Properties
Nominal Properties and λtest,max and λtest,min
Notes: There is no engineering judgement or estimation involved in the determination of the maximum force and displacement or energy dissipated per cycle (EDC). Fmax and Dmax are self-evident and EDC is determined by numerical integration of the record force-displacement data file. The value of these are presented in the previous slide.
However, there is judgement (different methods) in determining the shear modulus of rubber and effective yield stress of lead. This slide shows one such approach.

## Slide 38: Isolation System Properties
Effective yield stress of lead σYL:
λtest,max = First cycle/Nominal = 2.27/1.69 = 1.34
λtest,min = 2nd Cycle*/Nominal = 1.56/1.69 = 0.92
Shear modulus of rubber, G:
λtest,max = Heating effects mask scragging = 1.15 from other data
λtest,min = 1.0
Nominal Properties = average among the three cycles, and averaged for the two bearings
Nominal Properties and λtest,max and λtest,min
Notes: There is some judgement in setting the test λ factors. First cycle properties should be used as the maximum properties.
*It is the opinion of the authors that the lower bound should be based on considerations of the seismic hazard and isolation system properties (strength and stiffness). Response history analysis studies by Warn and Whittaker (2007) demonstrate that about two (and less than three) fully-reversed cycles at the maximum displacement is suitable.

## Slide 39: ELF Procedure
  Calculate the effective damping βM
  Interpolate the damping coefficient BM from Table 17.5-1
  Check the displacement matches what was initially assumed in Step 1
  Assume a displacement, say DM = 11.2 inch
  Calculate the effective stiffness kM
  Calculate the effective period TM
Notes: The ELF procedure is an iterative process and is illustrated in the following equations for the preliminary design bearing dimensions and lower bound properties. The terms are defined in pervious slides.
“Conveniently”, our first guess of the displacement matches the displacement calculated in Step 6. Therefore no further iteration is required.

## Slide 40: ELF Procedure
  Refine analysis with a 3-D model and optimise the isolation system design
  ELF force-deflection behaviour of the “optimized” solution
Notes: Shown on the right side of this slide is an isometric view of the framing system for the example building. At each floor is a horizontal red arrow, indicating that in the Equivalent Lateral Force (ELF) procedure the total base shear is distributed up the height of the building and applied at each floor level. There is also a graph at the lower right side of the slide. This graph shows two Force-Displacement hysteresis loops. One loop is for “upper bound” isolation properties, with a higher value of effective stiffness; the other loop is for “lower bound” isolation system properties, with a lower value of effective stiffness.
A more refined calculation of the bearing axial loads can be done with a 3-D model, using a lateral force distribution according to the Standards equations.
The final (“optimized”) bearing dimensions give the force-deflection behavior for the upper- and lower-bound properties as shown. The peak forces and displacements are based on the ELF procedure, and are used in setting minima values to compare to the more sophisticated dynamic analyses.
Although the isolation system could be optimized further (i.e. use lead rubber bearings in combination with flat sliders to reduce the post-elastic stiffness), this is not done for ease of illustration.

## Slide 41: ELF Procedure
  Check Minimum Requirements for Vs
  Vs = 3449 kip (upper-bound properties)
Notes: Since an OCBF superstructure is used (to save on ductile detailing requirements) the unreduced forces are used for the superstructure design. While the structural shear is quite large (Vs/W=0.34 in upper-bound), keep in mind that this is for unreduced forces (i.e. R=1.0) and for the MCER event. Other building types are designed for the DBE (about 67% of MCER) and large R factors (which means damage).
The value of Vs shall also be checked against Standard §17.5.4.3 to ensure it meets the minimum requirements. As shown, the value of Vs is not governed by the minimum requirements.

## Slide 42: ELF Procedure
  The compression stiffness of a multi-layered elastomeric bearing can be approximated accordingly:
  Bearing Vertical Loads
  Model the bearing (& soil) vertical stiffness, framing stiffness and mass distribution realistically in 3-D.
Notes:   There is a small photograph of an elastomeric lead core bearing with red arrows representing compression forces acting on the bearings. There is also an isometric illustration of the building frame with one of the seismic isolation bearings circled in read to indicate the focus of this slide is the vertical loads acting on an individual bearing.
  The vertical load on each bearing depends on their relative vertical compression stiffness Kv and soil stiffness, the rigidity of the base level diaphragm/framing and the mass distribution. Hence modelling this realistically in 3-D will give an accurate distribution of bearing compression loads.
  In the vertical stiffness equation, A is the bonded rubber area, ti is the individual rubber layers thickness, K is the bulk modulus of rubber, assumed as 290 ksi and Eci is the compression modulus for incompressible material behavior which is dependent on the rubber shear modulus, shape factor and the bearing geometry (see Constantinou et al., 2007 for details).

## Slide 43: ELF Procedure
Symmetry in isolation system and lateral-force resisting system
Notes: An illustration shows the entire floor framing plan of a typical floor. A red box around the upper left quadrant of the floor plan shows that, due to double symmetry, it may be possible to evaluate the results for just one-fourth of the floor plan.
Since the isolation system and lateral-force resisting system have a symmetrical layout (in two directions), only the critical demands need to known in one quadrant (as they are similar in others). That is, loads and displacements at Gridlines 5, 6 and 7 are similar to those at Gridlines 3, 2 and 1, respectively; and loads and displacements at Gridlines D and E are similar to those at Gridlines B and A, respectively. Hence the loads and displacements are only shown per the top-left snippet locations in the following slides.

## Slide 44: ELF Procedure
Bearing Gravity Loads:
Dead and Reduced Live Loads
Critical long-term dead load: 1.2D + 1.6L = 660 kip (C3)
Average load (used for prototype testing): 1.0D + 0.5L = 290 kip
Notes: A drawing shows the grid lines corresponding to the upper left quadrant of the floor plan. There is also a small photograph of an elastomeric lead core bearing with red arrows representing compression forces acting on the bearings.
Values of dead load (D) and reduced live load (L) are shown at each isolator location (click). Long-term gravity design loads on isolators are defined by 1.2D + 1.6L load combination. Long-term design loads on isolators range from about 180 kips at corner isolators (A1) to about 660 kips at an interior isolator (C3).
Based on the load combination, 1.0D + 0.5Lred, the weight on individual bearings varies from about 120 kips to about 460 kip. The typical, or average weight, supported by all bearing is about 290 kips (i.e., 35 bearings x 290 kips/bearing = 10,200 kips). This typical weight is used for prototype testing of isolator units. This is because the mechanical properties of the isolation system are not (materially) affected by fluctuations in the axial load on individual isolators. Rather, the behavior is determined by the average load on all the isolators, which is D+0.5L. It is noted, however, the effect of varying axial load on the properties of individual isolators is of interest as it affects the design of the isolator and of the structure in the vicinity of the isolator.

## Slide 45: ELF Procedure
Upper-Bound Properties
Add vertical earthquake effects later using ±0.2SMSD
Overturning loads due to horizontal earthquake
5% accidental eccentricity in X- and Y- directions
Bearing Earthquake Loads:
Notes: A drawing shows the grid lines corresponding to the upper left quadrant of the floor plan. There is also a small photograph of an elastomeric lead core bearing with red arrows representing compression forces acting on the bearings.
The horizontal earthquake, which has the vertical shear force distribution shown earlier, causes overturning and axial forces in the bearings. This table gives the maximum and minimum demands from horizontal earthquake and additional forces due to the application of an accidental eccentricity. They are enveloped for an earthquake in the forwards or backwards direction. The larger forces occur where the bearing is below the lateral-force resisting system frame (i.e. where the braces end).
The same calculation needs to be done for the lower-bound properties (not shown).

## Slide 46: ELF Procedure
Large tension loads are not desirable – look at NLRHA
Bearing Load Combinations:
Only shown for upper-bound properties
Notes: A drawing shows the grid lines corresponding to the upper left quadrant of the floor plan. There is also a small photograph of an elastomeric lead core bearing with red arrows representing compression forces acting on the bearings.
Using the load combinations 1.2D +0.5L + 1.0E and 0.9D – 1.0E, and incorporating vertical earthquake actions using ±0.2SMSD, gives the maximum and minimum downward vertical forces as shown.
It is noted that tension stresses are developed in a number of locations. This tension stress is acceptable for a high-quality elastomeric bearing if it is less than three times the shear modulus of rubber . This is a capacity 120 kip (i.e. 3GA) for the upper- properties. Hence there are four bearing locations (Gridline A2, E2, A6 and E6) where there is a potential uplift issue.

## Slide 47: ELF Procedure
Where:
PT = ratio of the effective translational to torsional period of the isolation system
y (or x) = distance in plan from center of rigidity to corner
e = actual plus accidental eccentricity
b, d = plan dimensions
≥ 1.15*
*(in commentary)
Increase the maximum (MCER) displacement due to torsion to get the total maximum displacement
Minimum amplification factor:
Total Maximum Displacements:
Notes: An illustration shows the modes of displacement of the structure that are calculated in the process of seismic isolation design. The levels of displacement shown are the design displacement, D-sub-D, the maximum displacement, D-sub-M, and the total maximum displacement (including torsion), D-sub-TM. The figure contains a red shaded area covering the “D-sub-D” label, indicating that D-sub-D is no longer calculated in the current Standard.
This slide illustrates definitions and the equation to calculate the “total” displacement at corners of the isolated structure that includes potential rotation, as well as, translation of the isolation system.
This equation now includes a new term PT, which offers an improvement by relaxing the assumption of equal translation and torsional periods. 5% accidental eccentricity increases corner displacement by about 15% for buildings square in plan, and by abut 30% for buildings that longest dimensions many times greater than the other. Systems with proportional stiffer isolators near the perimeter of structure (e.g., de Young Museum) provide greater resistance to torsion and the effects of actual plus accidental mass eccentricity. Total maximum displacement (DTM) is used to verify stability of isolators and to establish minimum moat clearance.

## Slide 48: 5. ELF Procedure
Minimum amplification varies based on distance from center of mass
Calculate DTM for both upper- and lower-bound
Total Maximum Displacements:
Notes: A drawing shows the grid lines corresponding to the upper left quadrant of the floor plan.
The minimum amplification factors are shown here when enveloped for accidental eccentricity in either X- or Y- directions. The resulting total maximum displacements DTM are shown for the upper- and lower-bound properties.

## Slide 49: ELF Procedure
Design is reasonable! as ti ≥ 0.25 inch for critical bearing location
Could use single bearing type with 19 rubber layers each 0.275 inches thick
Rubber shear strains achievable for quality manufactures
Bearing Stability and Shear Strain
Refined assessment with displacements and vertical loads from compatible locations and for upper- or lower-bound properties
Notes: A drawing shows the grid lines corresponding to the upper left quadrant of the floor plan.
The stability check is illustrated here since its a critical check for the design of the lead-rubber bearings, and may be overly conservative to use enveloped (incompatible) displacements and vertical loads. However, its usually the manufacturers responsibility to do these design checks (as you give them displacements and loads). The equation used to calculate the maximum allowable rubber layer thickness was shown earlier in the preliminary design.
The critical bearing location is Gridlines B4 and D4 which require a rubber thickness less than 0.28 inches which is at the lower limit for what can be satisfactorily constructed by manufactures. Note that all bearings can be design for this worst case so that there is only one bearing type. This would give a final bearing with 5.225/0.275 = 19 rubber layers each 0.275 inches (7 mm) thick. The rubber shear strains due to lateral displacements are high at 294% in the corner locations, but are achievable for a quality manufacturer.

## Slide 50: ELF Procedure
  P-delta Effects
Notes:   A drawing shows the framing plan of the first floor of the structure. Yellow lines along each grid line indicate the locations of heavy steel framing members. These heavy members resist P-delta moments that are induced by the bearings. A second drawing indicates the displaced position of an elastomeric bearing, and the method of computing P-delta moments for the bearing.
  Computer analysis programs may not correctly calculate the large P-delta moments at the isolator level. The slide shows that moments are caused by both displaced vertical loads, P, as well as horizontal shear, V. For the elastomeric bearing, the P-delta moment is split one-half up and one-half down. At the base level, heavier W24 x 146 heavier girders/framing are used. These girders stabilize the bearings by resisting moments due to both vertical P-delta effects and horizontal shear loads.

## Slide 51: Dynamic Analyses
  ELF Procedure permitted for final design
  However, uplift is an issue and more sophisticated analysis may show improved responses
  Analysis Procedure Selection
Notes:   As shown, an ELF Procedure is permitted for final design of this building since all the Standards criteria are met.

## Slide 52: Dynamic Analyses
  Crude approach, but is only addressed in more detail in commentary.
  In ELF Procedure, we simply used ±0.2SMSD
  So it assumes that 100% vertical acceleration is about ±(2/3)SMS = 0.93g
Vertical Response Spectrum Analysis
Notes:   This slide contains an acceleration response spectrum that illustrates a simple method to account for vertical earthquake accelerations. The spectrum shows that vertical earthquake accelerations may be approximated as roughly two-thirds of the maximum amplitude of the MCE-sub-R horizontal earthquake response spectrum.
  The ±0.2SMSD assumes the vertical response spectrum is about 2/3 of the horizontal with 30% combination i.e. 0.67 x 0.3 = 0.2 factor. Hence it assumes the vertical acceleration is about 0.93g for this site.
  Another approach, recommended in commentary, is to compute a more refined vertical spectrum using the 2009 NEHRP Provisions in Chapter 23.

## Slide 53: Dynamic Analyses
  Vertical response spectrum per Chapter 23 of 2009 NEHRP Provisions (retained in 2015 Provisions)
Vertical Response Spectrum Analysis
Notes:   A graph is shown on this slide that indicates the relationship between the horizontal design response spectrum and the vertical design response spectrum. The vertical response spectrum must not fall below 50 percent of the horizontal response spectrum. At periods above about 0.4 seconds it is shown that this limitation governs the vertical response spectrum.
  The 2009 Provisions have a simplified method to calculate the vertical spectrum through the parameter SS (short-period horizontal spectral acceleration), as well as the site class classification. The resulting vertical response spectrum to use for design is shown.

## Slide 54: Dynamic Analyses
  Less than the 0.93g assumed by ELF
  Also gives more realistic distribution over footprint
  Use orthogonal combination rule: 100% + 30% + 30%
Vertical Response Spectrum Analysis:
  Total reaction in the upwards/downwards direction of 7174 kip (0.7g)
Notes:   A drawing shows the grid lines corresponding to the upper left quadrant of the floor plan.
  The vertical response spectrum analysis resulted in a total reaction in the upwards/downwards direction of 7174 kip, which is equivalent to 7174/10200 = 0.7g which is less than that assumed for the ELF analysis.
  These vertical earthquake effects are combined with the two horizontal earthquake components using the orthogonal rule 100%-30%-30%.

## Slide 55: Dynamic Analyses
  Model Verification
Response History Analysis
Notes: A graph illustrates the base shear force-displacement hysteresis loops for static equivalent lateral force (ELF) analysis and for nonlinear response history analysis (NLRHA). The graph shows that all the hysteresis loops from the NLRHA fall inside the bounding loop from the ELF procedure.
Due to the many inputs required for NLRHA it is important to carry out verification checks. This slide shows the NLRHA hysteretic response (base shear vs. displacement) of the isolation system in the X and Y directions from ground motion 5, which compares well to the ELF procedure.

## Slide 56: Dynamic Analyses
  Post-Processing
Response History Analysis
Notes: There is a graph that shows earthquake displacement records for the isolation system, with the horizontal axis labeled “Time (seconds)” running from 0 to 40 seconds. The vertical axis is labeled “Displacement (inch)” running from -12 to 12 inches. One displacement record is labeled “X-direction” and the other “Y-direction”. Also shown on the graph is the square-root-of-sum-of-squares combination of the X and Y displacement records labeled “SRSS”.
This slide shows the displacement history of the isolation system in the X and Y directions for ground motion 5, Loma Prieta, using lower-bound properties. The peak X and Y displacements were 11.9 and 6.5 respectively. Simply taking the SRSS of these maximum X and Y displacements is overly conservative i.e. (11.92+6.52)1/2 = 13.6 inches. The SRSS should be instead be taken at each time step, which gives a maximum displacement of 12.0 inches.

## Slide 57: Dynamic Analyses
Note: The displacement needs to be increased for torsion
  Post-Processing
Response History Analysis
Notes: This table summarizes peak SRSS combinations of isolation system displacements and base shears for each ground motion from the NLRHA. The average of the seven ground motions may be used for design.

## Slide 58: Dynamic Analyses
Increase moat clearance for OCBF = 1.2 x 12.0 = 14.4 round up to 15 inches
Bearing design lower bound
  Post-Processing - Displacements
Response History Analysis
Notes: The table compares the NLRHA to the ELF results. To avoid possible under-design, the Standard establishes minimum limits on results of dynamic analysis to be used for design. These limits are established as a percentage of the corresponding parameter calculated using the ELF procedure equations. Here it is shown that the NLRHA displacement of 8.9 inches is less than the Standards minimum requirements (of 10.4 inches), hence the lower limit governs. Since the superstructure is an ordinary concentrically braced frame (OCBF), which has less stringent ductile detailing requirements, the moat clearance is increased by a factor of 1.2.

## Slide 59: Dynamic Analyses
  Post-Processing – Lateral Forces
Response History Analysis
Notes: This slides contains a graph showing the variation in design story force over the height of the building. The horizontal axis of the graph is labeled “Shear force (kip)” and runs from 0 to 4500 kips. The vertical axis is labeled “Elevation (feet)”, running from -5 to 50 feet. Three lines are shown on the graph. Two are labeled “NLRHA X-direction” and “NLRHA Y-direction”. These two lines begin at 2600 kips and 2200 kips, respectively, at the first story of the building, and both reach a value of about 750 kips at the penthouse story. A third curve, labeled ELF (Equivalent Lateral Force procedure) generally has story shear values greater than the HLRHA curves. The ELF curves starts at 3500 kips at the first story and reduces to about 750 kips at the penthouse story.
The upper-bound properties gave the worst case lateral loadings. Shown is a comparison of the NLRHA and ELF story shears. Torsion is added to these forces using the same approach as ELF procedure.

## Slide 60: Dynamic Analyses
  Post-Processing – Lateral Forces
  All elements above the isolation system shall be designed for lateral force no less than 80% of the ELF Vb for this regular structure. Therefore increase NLRHA forces by:
  All elements below the isolation system shall be designed for lateral force no less than 90% of the ELF Vb
  i.e. increase scale factors above further by 0.9/0.8 = 1.13
Response History Analysis
Notes: Again, the minimum limits of the Standard govern and the NLRHA lateral forces have to be scaled up to meet the minimum criteria. The minimum limits are different for elements above and below the isolators, and also different depending on the configuration of the superstructure.

## Slide 61: Dynamic Analyses
  Post-Processing – Bearing Vertical Loads
  Maximum compression loads are 829 and 986 kip for 100% and 30% of the maximum horizontal displacement, respectively.
  Maximum tension loads are both 74 kip for 100% and 30% of the maximum horizontal displacement.
Response History Analysis
Notes: The combination of vertical/axial loads on the bearings to be used for design consist of static dead and live loads, torsion (from the ELF procedure), vertical earthquake loads per the vertical response spectrum analysis, as well as the overturning/vertical effects of horizontal earthquake loads from the NLRHA (which are increased by scale factors per minimum requirements).
These loads are less critical than the ELF analysis. Although tension still occurs in some bearings, the force is less than 3GA so is manageable for quality manufacturers.

## Slide 62: Testing Requirements
  For setting acceptance criteria of production testing
  To determine nominal properties and λtest factors
  To check durability of isolator for multiple earthquake events
  Stability of isolator in extreme conditions
  Prototype testing of 2 isolators
Notes: This slide illustrates the sequence and cycles of prototype testing required by Section 17.8.2.2 of the Standard.
There are four distinct elements of prototype testing. Firstly, the prototype isolators are tested under the same conditions as that which will be done for production testing, so that acceptance criteria can be set for production isolators. Secondly, cyclic load tests at constant and incremental displacement amplitudes are required to establish the force-deflection properties of isolators (e.g., stiffness, strength and bounds) for typical, maximum, and minimum vertical loads. Thirdly, 14 cycles of load at the 75% of the maximum displacement (DM= 7.8 inches) are required to assess isolator prototype “durability” for typical vertical load (290 kips). The number of cycles is based on the formula, 30 SM1/SMSBM ≥ 10 cycles of load which is a conservative estimate of the effective number of cycles for two maximum considered earthquake events (i.e., main shock plus after shock as large as the main shock) Finally, static load tests are required to check isolator stability at maximum displacement and for both maximum downward load (830 kips) and minimum downward load which includes uplift. Tension is elastomeric isolators is discouraged, although quality isolators can sustain tension stresses up to 3GA. Capabilities and of tension testing should be coordinated with the manufacturer.

## Slide 63: Testing Requirements
  Production testing of all (100%) isolators
Notes:   All isolators must be subjected to a combined compression and shear load cycle before being installed. This is to verify the properties and reveal any defects and is commonly referred to as quality control testing.

## Slide 64: DISCLAIMER
NOTICE: Any opinions, findings, conclusions, or recommendations expressed in this publication do not necessarily reflect the views of the Federal Emergency Management Agency. Additionally, neither FEMA nor any of its employees make any warranty, expressed or implied, nor assume any legal liability or responsibility for the accuracy, completeness, or usefulness of any information, product or process included in this publication.
The opinions expressed herein regarding the requirements of the NEHRP Recommended Seismic Provisions, the referenced standards, and the building codes are not to be used for design purposes. Rather the user should consult the jurisdiction’s building official who has the authority to render interpretation of the code.
Any modifications made to the file represent the presenters' opinion only.