## Slide 1: Seismically Isolated Structures
Disclaimer
William McVitty, P.E., M.S., Andrew Taylor, S.E., Ph.D
Notes: Graphic shows cover of the NEHRP Provisions FEMA P-1052.
The 2015 NEHRP Recommended Seismic Provisions are a new resource document that facilitates and translates the state-of-the-art knowledge into design practice. To help in understanding these new Provisions, design examples are also published which apply the new requirements of FEMA P-1051. This presentation complements the Chapter 15 design example of a seismically isolated building.
This set of instructional slides is the second of two 90 minute presentations. The first presentation provides information on the basic principles of seismic isolation and background on both the current and new seismic design requirements.

## Slide 2: Presentation Objectives
Illustrate application of the new NEHRP Provisions through a design example
  Hypothetical three-story emergency operation center (EOC) located in a region of high seismicity is isolated.
  Note: A full replacement of Chapter 17, ASCE 7-2016 (the Standard) was recommended.
Notes: A graphic shows the cover of the document FEMA P-1050-1, 2015 Edition, “NEHRP Recommended Seismic Provisions for New Buildings and Other Structures”
The objective of this second presentation is to illustrate a typical application of the NEHRP Provisions requirements. This is achieved through the design of a hypothetical seismically-isolated building, located in a region of high seismicity.
Due to the large number of changes, the 2015 NEHRP Provisions have recommended a full replacement of Chapter 17 in the 2016 edition of ASCE 7 (referred to hereafter as the Standard).

## Slide 3: Overview of Design Example
Project Information
Design Steps
Preliminary Design
Isolation System Properties
Equivalent Lateral Force (ELF) Procedure
Dynamic Analysis
  Vertical Response Spectrum
  Response History
Testing Requirements
Notes: This presentation closely follows the design example sections and is ordered in the way that design progresses.

## Slide 4: 1. Project Information
Structural Description
Notes: This illustration shows an Emergency Operations Centre (EOC), which is a three story, steel frame structure with a large, centrally located mechanical penthouse. Story heights are 14 feet at the first floor to accommodate computer access flooring and other architectural and mechanical systems and 12 feet at the second, third and penthouse floors. The roof and penthouse roof decks are designed for significant live load to accommodate a helicopter landing pad and to meet other functional requirements of the EOC.

## Slide 5: 1. Project Information
Notes: This illustration shows the structure plan, which is regular and symmetrical in configuration, and which has plan dimensions of 100 feet by 150 feet at all floors except for the penthouse. The penthouse is approximately 50 feet by 100 feet in plan. Columns are spaced at 25 feet in both directions. 35 lead-rubber bearings are used to isolate the building and are located beneath each column.
This figure shows typical floor framing - 4 bays x 6 bays. The beams sizes on the base level, just above the isolators, are larger and with moment-resisting connections.

## Slide 6: 1. Project Information
Notes: This figure is a plan view showing penthouse roof framing, measuring 50 feet by 100 feet.
Note the labeling of the longitudinal (X-direction) in the left-right direction of the page, and transverse (Y-direction) in the up-down direction of the page.

## Slide 7: 1. Project Information
This structure is purposely configured to the minimize uplift (tension) demands, through:
  Increasing the number of bays with bracing at lower stories.
  Locating braces at interior (rather than perimeter) gridlines since they have greater gravity loading.
  Avoiding common end columns for bracing in the transverse and longitudinal directions.
Notes: Early in the project the designer should consider how they can configure the structure (or use specific lateral-force resisting systems) which minimize uplift forces on the bearings. Isolation bearings are rather poor at sustaining tension loads and it adds complication to analysis and testing if designing for uplift.
The following slides show how the framing was configured to minimize tension in the bearings.

## Slide 8: 1. Project Information
Notes: This figure is an elevation view showing longitudinal bracing on Lines B and D. The lateral force resisting system consists of a roughly symmetrical pattern of concentrically braced frames. These frames are located on Gridlines B and D in the longitudinal direction and on Gridlines 2, 4 and 6 in the transverse direction. It should be noted that the locations of the braced frames spread out gradually, and the number of braces increases, from the top of the building to the bottom. This distributes overturning forces to many bays, which minimizes the uplift force in any individual bay.

## Slide 9: 1. Project Information
Notes: This figure is similar to the figure on the previous slide, but it shows two transverse cross sections, illustrating transverse bracing on Lines 2 and 6 on the left, and Line 4 bracing on the right. As in the previous slide, braces are spread out near the base of the building to minimize uplift forces in any individual bay.

## Slide 10: 1. Project Information
Notes: This drawing shows an elevation of an elastomeric bearing on top of a concrete footing. Above the isolator is a steel column and large steel beams framing into the column just above the isolator.
Girders at the first-floor gridlines are much heavier than the girders at other floor levels and have moment-resisting connections to columns. These girders stabilize the bearings by resisting moments due to both vertical P-delta effects and horizontal shear loads. Column extensions from the first floor to the top plates of the bearings are stiffened in both horizontal directions to resist these moments and to serve as stabilizing haunches for the beam-column moment connections.

## Slide 11: 1. Project Information
Seismic Weight = 10,200 kip (D+0.5Lred)
Gravity Loads
Notes: This slide shows an elevation of a typical column at Grid D. Running horizontally at each floor level is a tabulation of the dead and live loads tributary for all of the columns at that level. At the bottom of the diagram is a tabulation of the total column loads carried by the seismic isolation bearings at the bottom of the columns. Total dead load is 9100 kips and total unreduced live load is 5500 kips.
The weight of each floor and distribution of the total weight on isolators must be determined as a necessary first step in the design of the isolation system. This figure shows the gravity loads by floor level. The total dead load weight on isolators is 9,100 kips with an additional reduced (40% of unreduced) live load weight of 2,200 kips. The seismic weight used for lateral force design and analysis is taken as this dead load plus half of the reduced live load for consistency with the vertical load combination contained in Ch17 of the Standard. The total seismic weight carried by the isolation bearing, which is the total dead load plus one-half the reduced total live load, is 10,200 kips

## Slide 12: 1. Project Information
Performance Criteria:
Emergency Operation Centre: Occupancy Category IV
Project specific goals are to:
Resist minor and moderate earthquakes without damage.
Resist major earthquakes without failure of the isolation system, or significant damage to structural and nonstructural components, or major disruption to facility function.
Implicitly achieved by using a Standard-compliant isolated building, accordingly:
  Occupancy Importance Factor: Ie = 1.0 for all isolated structures (Ie = 1.5 for other conventional Category IV structures)
Notes: Seismic isolation is an appropriate design strategy for EOCs and other essential facilities where the goal is to limit earthquake damage and protect facility function. Although damage control is not an explicit objective of the Standard, the design to limit inelastic response of the structural system directly reduces the level of damage in an isolated building that would be otherwise be occurring (in a fixed-base building). Furthermore the structure and isolation system are designed and tested for the MCER hazard instead of the DBE.
Functional and economic performance objectives are not explicitly addressed by seismic-code design requirements. Rather, it is hoped that additional design strength (i.e., Ie = 1.5) will adequately protect a Category IV structure from damage that could close a critical facility (i.e., hospital) and that somehow, nonstructural systems and contents can survive the shaking without loss of function or significant economic loss. This approach of increasing the strength is a crude method compared to seismic isolation.

## Slide 13: 1. Project Information
   §11.4.7 Site-specific hazard analysis required
Ground Motions Criteria:
Site Hazard and Soil Conditions
  Region of high-seismicity
  Seismic Design Category D
  Soil site class D
Spectral Accelerations
  SMS = 1.4
  SM1 = 0.9
  S1 = 0.5
Notes: A graph shows examples of several project-specific earthquake response spectra that could be used for design. These spectra are meant to be a schematic illustration only, so the details of the shapes and magnitudes of the spectra are not relevant.
The following three slides summarize pertinent design criteria for the example EOC. The building is located in a region of high seismicity, classified as SDC “D”. Since the building is also located on site class D soils, a site-specific hazard analysis is required to determine the response spectrum to be used for design.

## Slide 14: 1. Project Information
Design Basis:
Seismic force-resisting system (50ft high):
  Can use a steel Ordinary CBF (§17.2.5.4), provided:
    OCBF remains elastic for MCER (RI = 1.0)
    Increase displacement capacity by 120%
Horizontal or Vertical irregularities of superstructure:
  None (Standard Tables 12.3-1, 12.3-2)
Redundancy factor
  ρ = 1.0 (§17.2.3)
Notes: Although Table 12.2-1 of the Standard limits the height of fixed-base ordinary steel concentrically braced frames (OCBFs) to 35 feet for this Seismic Design Category D building, new provisions (§17.2.5.4) permit the use of OCBFs in seismic isolation applications for heights up to 160 feet. This is permitted provided 1) the OCBF remains elastic for the MCER event and 2) the displacement capacity to which the isolation system lock-up or impact the moat wall shall be increased by a factor of 1.2.
The redundancy factor is taken as ρ = 1.0, although a larger value may be required by the Standard if the structure was not isolated.

## Slide 15: 1. Project Information
Design Basis:
Isolation System: 35 lead-rubber bearings
Lateral analysis procedure:
  Equivalent Lateral Force (ELF) analysis permitted
  However, Response History analysis also conducted for verification and to investigate uplift.
Reference: MCEER-11-0004
SUNY, Buffalo, NY
Notes: A photograph shows an elastomeric isolation bearing that has a wedge cut out of it to indicate the internal construction of the isolator. Internal alternating layers of rubber and steel are visible, with the rubber layers about 10 mm thick and the steel layers about 3 mm thick. Also visible at the interior of the bearing is a vertical lead cylinder which is inserted into a vertical hole at the center of the isolator.
The isolation system consists of one type of lead-rubber bearing, although other types of isolators or combinations of isolators could have been used.
The analysis and design of the whole building was permitted to be with the ELF procedure, however for illustration and to further investigate uplift forces, a NLRHA was conducted.

## Slide 16: 2. Design Steps
Step I:
Project & Ground Motion Criteria
Step II:
Preliminary Design
Step III:
Isolation System Properties and ELF Analysis
Step VII: Final Specifications
Step IV:
Vertical Earthquake Effects
Step V:
Revisit ELF Analysis & Optimize
Step VI: (if required)
Dynamic Analysis
Notes: An illustration shows the steps for design of a seismically isolated building. The steps are numbered from I through VII, and are to be followed sequentially.
These design steps are adapted from SUNY Dist. Prof. M. C. Constantinou. Each step is explained in more detail in the following slides. Although they are specific for a elastomeric (lead-rubber bearing) isolation system, the process is similar for sliding isolation systems.

## Slide 17: 2. Design Steps
Step 1: Ground Motion Criteria
Determine the sites spectral accelerations using the USGS website.
Check if a site-specific hazard analysis is required to develop the response spectrum.
If a NLRHA is likely, also select and scale ground motions and determine proximity to faults.
Notes: This slide contains three illustrations. The first two, on the right side of the slide, are from a screen capture from the USGS web site that provides site-specific seismic design spectra. The upper illustration shows a vicinity map for the project and the lower illustration shows design response spectra provided by the web site. The third illustration is at the bottom of the slide. It shows two earthquake accelerographs, with the vertical axes labeled “Acceleration Amplitude 1, (g)” and “Acceleration Amplitude 2, (g), with scales running from -0.8 g to 0.8 g. The horizontal axes are the time scale, running from 0 to 40 seconds. These two plots are meant to illustrate schematically that a typical earthquake record for seismic isolation design consists of two orthogonal components applied simultaneously to the structure.
The first step is to quantify the seismic hazard at the site. Traditionally a site-specific hazard analysis is used to define a multi-period response spectrum to be use for design. Also nonlinear-response history analysis (NLRHA) requires seven pairs of earthquake records be selected and scaled to meet the target spectrum. Steps 1 b) & c) require that specialist expertise is engaged. Furthermore the design reviewer should be engaged at this early stage to help set and verify criteria.

## Slide 18: 2. Design Steps
Not acceptable, need ≥ 0.25inch and ≤ 250%, iterate
Select trial bearing dimensions and lower bound properties.
Quickly estimate displacements (and rough compression forces) using the ELF procedure.
Assess the bearings adequacy (stability) and iterate on bearing dimensions
Step 2: Preliminary Design (Elastomeric System)
Notes: A photograph shows an elastomeric isolation bearing that has a wedge cut out of it to indicate the internal construction of the isolator. Internal alternating layers of rubber and steel are visible, with the rubber layers about 10 mm thick and the steel layers about 3 mm thick. Also visible at the interior of the bearing is a vertical lead cylinder which is inserted into a vertical hole at the center of the isolator.
The following preliminary design approach is considered more practical than theoretical/parametric analyses. The manufacturer can be consulted to determine trial bearing dimensions and properties. If unknown, the engineer can progress with recommendations by Constantinou (2011) as explained later in this presentation. The design may be conservative at this stage as the analysis is not refined. A spreadsheet aids in the trial an error iteration of the bearing dimensions.

## Slide 19: 2. Design Steps
When bearing design appears promising:
Proceed with formal determination of isolation system properties.
Conduct ELF procedure for upper- and lower-bound properties using a 3-D ETABS model.
Designer may want to alter distribution of bearing types (e.g. some with and without lead cores so that torsion is minimized)
Step 3: Equivalent Lateral Force (ELF) Analysis
Notes: There is a graph at the right side of the slide. This graph shows two Force-Displacement hysteresis loops. One loop is for “upper bound” isolation properties, with a higher value of effective stiffness; the other loop is for “lower bound” isolation system properties, with a lower value of effective stiffness. Also shown on the slide is an isometric view of the framing system for the example building. At each floor is a horizontal red arrow, indicating that in the Equivalent Lateral Force (ELF) procedure the total base shear is distributed up the height of the building and applied at each floor level.
Calculate bearing displacement demands, story shear forces, story drifts and additional axial bearing loads using the 3-D computer model. Note that for the calculations of the axial loads the designer will have to perform a static analysis of the frame, including torsion effects.

## Slide 20: 2. Design Steps
Could be as simple at ±0.2SMSD
Or by more refined analysis:
Construct a vertical response spectrum and perform a vertical response spectrum analysis. Use orthogonal combination rule: 100% + 30% + 30%
Explicitly include vertical acceleration record in NLRHA
Step 4: Vertical Earthquake Effects
Notes: A graph is shown on this slide that indicates the relationship between the horizontal design response spectrum and the vertical design response spectrum. The vertical response spectrum must not fall below 50 percent of the horizontal response spectrum. At periods above about 0.4 seconds it is shown that this limitation governs the vertical response spectrum.
There is no requirement for a vertical earthquake analysis. However the designer may choose to do a more sophisticated analysis of the vertical earthquake effects if considering the acceleration response of floors and other building components, or if they believe there may be savings on the ±0.2SMSD approach.
Furthermore, vertical ground acceleration may affect the behavior of axial-load dependent isolators in the horizontal direction, due to potential coupling between horizontal and vertical response of the building structure.

## Slide 21: 2. Design Steps
Assess adequacy of bearings, again, but using the more refined ELF analysis (Step 3) and vertical earthquake analysis.
If uplift/tension is a problem, modify the structure to reduce to acceptable amount.
Assess other governing design requirements, and if not satisfied then modify the structure and/or isolation system. (Optimize)
Step 5: ELF Analysis (revisited)
Notes: Preferably the design should be optimized before dynamic analysis (i.e. NLRHA). The designer may also try to optimize the design using different systems, i.e. combination of lead-rubber and low-damping rubber, or lead-rubber and flat sliders, or additional energy dissipation devices such as viscous dampers. For easy of illustration, this design example only uses lead-rubber bearings at is not optimized further.

## Slide 22: 2. Design Steps
First check if a response spectrum or response history analysis is required?
The applicability of the ELF Procedure has been widened in this code cycle.
Depends on the site, structures and isolation systems characteristics
Step 6: Dynamic Analyses
Notes: Sophisticated response history analyses have traditionally been done, but are not necessary for every project. Provided the structure meets certain requirements, an ELF procedure is an adequate and simpler way to do design.

## Slide 23: 2. Design Steps
Base Shear Force-Displacement Behavior of Isolation System for Lower Bound Properties, comparison of ELF and NLRHA for Ground Motion 5
Model and analyze the structure in the lower- and the upper-bound conditions for the MCER using seven ground motions.
Decide method of accounting for vertical earthquake effects
Consider how to account for accidental torsion effects
Step 6: Dynamic Analyses (Response History)
Notes: A graph on the right side of the slide illustrates the base shear force-displacement hysteresis loops for static equivalent lateral force (ELF) analysis and for nonlinear response history analysis (NLRHA). The graph shows that all the hysteresis loops from the NLRHA fall inside the bounding loop from the ELF procedure.
Nonlinear response history analysis is the most sophisticated analysis and can be used for all building types. It has a number of important assumptions, such as how to model the nonlinear behavior of the isolators.
The designer needs to decide on how to include vertical earthquake effects. Options are to include nothing and simply add later the axial load effect due to the vertical earthquake determined in Step 4, or add a +ag or –ag constant vertical earthquake in the dynamic analysis where a is a portion of the acceleration determined in the vertical earthquake response spectrum analysis (say if the peak value was 1.2g, then a = 0.3x1.2 = 0.36), or explicitly include vertical acceleration record.
Also, the designer needs to consider torsion. The best approach is to model only the actual eccentricities and not artificially shift the center of mass. Accidental torsion can instead be added using the same approach as in the ELF procedure or by using amplification factors.

## Slide 24: 2. Design Steps
Decide on final design actions (i.e. story shears, drifts, etc) by comparing NLRHA and ELF results.
Specify final bearing displacements, axial forces, properties and bounds for manufacturers design and testing.
Step 7: Final Specifications
Notes: This slides contains a graph showing the variation in design story force over the height of the building. The horizontal axis of the graph is labeled “Shear force (kip)” and runs from 0 to 4500 kips. The vertical axis is labeled “Elevation (feet)”, running from -5 to 50 feet. Three lines are shown on the graph. Two are labeled “NLRHA X-direction” and “NLRHA Y-direction”. These two lines begin at 2600 kips and 2200 kips, respectively, at the first story of the building, and both reach a value of about 750 kips at the penthouse story. A third curve, labeled ELF (Equivalent Lateral Force procedure) generally has story shear values greater than the HLRHA curves. The ELF curves starts at 3500 kips at the first story and reduces to about 750 kips at the penthouse story.
The final step is to write the specifications for bearing manufacturers (i.e. testing requirements, required properties and bounds, etc), which involves deciding on the final values for bearing displacements and forces to be used in assessing adequacy of the bearings. These values will be from the response history analysis values if its values are larger than the ELF values; otherwise the values for evaluation cannot be less than a certain portion of the ELF values per the Standard §17.6.4.

## Slide 25: 3. Preliminary Design
Reference: MCEER, SUNY, Buffalo, NY
Philosophy:
Use information from previously manufactured and tested bearings, instead of doing theoretical optimizations which give atypical designs.
Following is applicable for lead-rubber bearings and is based on Constantinou et al 2007 & 2011 MCEER reports (recommend you download, free)
Notes: This slide has illustrations of the covers of two MCEER reports: “Performance of Seismic Isolation Hardware under Service and Seismic Loading” and “LRFD-Based Analysis and Design Procedures for Bridge Bearings and Seismic Isolators.” There is also a small photograph of an elastomeric lead-core seismic isolation bearing.
This preliminary design is specific for lead-rubber bearings, although the philosophy is similar for other systems, and is based on the approach by Constantinou et al. (2011). The goal should be to use information on previously manufactured and tested bearings, instead of doing theoretical/parametric optimizations (which give atypical designs). This gives more certainty and is likely to give less expensive designs which are quicker to manufacture, test and deliver.

## Slide 26: 3. Preliminary Design
G = Shear modulus of rubber
DB= Diameter of the bearing
Tr = Total thickness of rubber (sum of the individual rubber layers)
Post-elastic stiffness,
DL = Diameter of the lead core
σYL = Effective yield stress of lead
Characteristic strength,
Reference: MCEER-15-0005SUNY, Buffalo, NY
Bi-linear Idealization
Dynamic test data
Force-Displacement Behavior
Notes: This slide contains an illustrative force-displacement plot for dynamic cyclic testing of lead-rubber isolation bearing. There is also a plot showing an idealized, straight-line representation of the same test data. In addition, there is a small photograph of an elastomeric lead-core seismic isolation bearing.
The actual force-deflection behavior of bearings are variable and is simplified by using a bilinear model and bounding. The two key parameters that characterize the behavior are the characteristic strength Qd, which is primarily dependent on the mechanical properties of lead, and the post-elastic stiffness kd , which is primarily dependent on the mechanical properties of rubber.
Other parameters shown are KM the effective stiffness, DM the MCER displacement, and Y the yield displacement. The parameter fL accounts for the effect of the lead core on the kd and ranges in value from 1.0 to about 1.2. Only after repeated cycling is the value of fL close to unity.

## Slide 27: 3. Preliminary Design
Values of G taking into account uncertainty in the nominal value, scragging and aging effects :
Default Nominal Properties and Bounding
Values of σYL taking into account uncertainty in the nominal value, speed of motion and heating effects are:
Notes: There is a small photograph of an elastomeric lead-core seismic isolation bearing.
The two important properties to determine are the effective yield stress of lead σYL and the shear modulus of rubber G. There is uncertainty in σYL as it is dependent on the speed of motion, size and confinement of the lead core (i.e. vertical load, manufacturer details), and degrades from cycle to cycle due to heating effects. The shear modulus of rubber G depends on the rubber compound and manufacturing processes, which are proprietary, as well as the on the frequency and conditions of loading. Shown are default properties for quality manufactures based on Constantinou el al (2011).
The significance of this slide to earthquake engineering is that it explains the preliminary design of isolated buildings.

## Slide 28: 3. Preliminary Design
Reference: MCEER, SUNY, Buffalo, NY with edits
Section
Plan
Size the lead core, DL so that the strength of the isolation system is some desirable proportion of the seismic weight, W (i.e. Qd/W ≥ 0.05)
DB should be in the range of 3DL to 6DL
Tr should be about equal to or larger than DL
Select Trial Bearing Dimensions
Approximate values for the variables DL, DB and/or Tr
Notes: There is a small photograph of an elastomeric lead-core seismic isolation bearing. Also shown are schematic drawings of the plan view and elevation of a lead-core seismic isolation bearing.
In general Qd,total/W should be about 0.05 or greater in the lower bound analysis. For this example a ratio of 0.08 gives a system strength Qd,total of 816 kips and, by the equation shown earlier, a lead core diameter of DL = 4.5 inches for 35 LR bearings.
The significance of this slide to earthquake engineering is that it explains the preliminary design of isolated buildings.

## Slide 29: 3. Preliminary Design
Isolation System Behavior
Using the equations, default nominal properties and trial bearing dimensions in the previous slides, calculate the overall behavior for the lower bound properties:
Notes: There is a small photograph of an elastomeric lead-core seismic isolation bearing. Also shown is a graph showing a straight-line idealization of the load-deflection behavior of an elastomeric, lead-core bearing.
Construct a bilinear force-displacement model of the isolation system. This is simply the sum of individual bearings strengths and stiffnesses (35 in total) since the bearings are acting in parallel across the isolation plane. The ELF procedure is then conducted to calculate the maximum bearing displacement DM.

## Slide 30: 3. Preliminary Design
Quickly estimate displacement, DTM, and compression force, Pu, using the ELF procedure.
May be conservative as design is not refined
Estimate Displacements and Forces
Notes: There is a small photograph of an elastomeric lead-core seismic isolation bearing.
This step involves estimating the critical combination of displacement (including torsion) and vertical load for the bearing stability calculation. Since this is preliminary design, conservative assumptions can be made by calculating the displacement for a corner bearing and combining with the maximum vertical load which occurs at any interior bearing. Increase displacements for torsion (here a 1.2 factor, say) and include overturning and vertical earthquake effects in you estimate of the bearing compression load.

## Slide 31: 3. Preliminary Design
Calculate the maximum allowable rubber layer thickness for stability:
and shear strain (DTM /Tr )
Acceptable designs have about t ≥ 0.25inch and shear strain ≤ 250%
Bearing Adequacy
Notes: There is a small photograph of an elastomeric lead-core seismic isolation bearing.
The empirical equations shown are from Constantinou et al. (2011). The bearing stability is a critical (typically governing) check and is critical at maximum displacements and high axial loads, hence the lower bound properties are used.
The first design iteration required a rubber thickness of 0.072 of an inch and had a shear strain of over 300%, which is not practical to construct. Therefore the size of the lead core and diameter of the bearing were increased to get a rubber layer thickness that is practical to construct and to reduce the shear strain.

## Slide 32: 4. Isolation System Properties
  typically custom designed and proprietarily constructed, and
  manufactured using non-traditional materials (lead, elastomers, Teflon)
  Much like baked bread, their behavior (taste) may vary significantly between projects (batches) and suppliers (bakers)
Bearings have variability and uncertainty in their properties, since they are:
Introduction
Notes: Seismic isolators have unique characteristics that are unfamiliar to most engineers. Foremost they have variability and uncertainty in their properties which require thorough testing to quantify. This is because isolators are usually custom designed, are constructed using proprietary technologies and are made of non-traditional civil engineering materials like composites, lead and elastomers. Consequently, there can be a considerable difference in the quality and performance of different isolators, even for identical isolator types produced by different manufacturers.

## Slide 33: 4. Isolation System Properties
Our bearing’s force-deflection model assumes constant properties, however a bearing’s properties are variable… So:
Use a property modification (λ) factor approach and bounding procedures to account for this.
Standard uses three categories of λ factors:
  λae.max and λae.min which account for aging and environmental effects. (i.e. aging, contamination, low temperatures, cumulative travel)
  λtest,max and λtest.min which account for scragging, hysteretic heating and speed of loading (observed in dynamic prototype testing)
  λspec,max and λspec.min which account for manufacturing variations.
Bounding Procedures
Notes: Since bearings/isolators have variable properties, the Standard requires explicit consideration for three categories of effects, namely: 1) aging effects and environmental conditions, 2) hysteretic heating and speed of loading effects, and 3) manufacturing variations.
Bounding procedures are used as a simplifying and practical approach to account for the probabilistic range in isolator properties. Two analyses are necessary as either the maximum or minimum probable isolator properties may govern for design. For instance, an upper-bound analysis may govern the sizing of the building frame whereas a lower-bound analysis may govern the sizing of the isolation hardware and surrounding moat clearance.

## Slide 34: 4. Isolation System Properties
Changes over the life of the bearing (i.e. 30-50 years)
Based on qualification test data
For quality manufactures of lead-rubber bearings:
  Stiffness: Shear modulus of rubber, G:
  Strength: Effective yield stress of lead σYL :
Aging & Environmental Effects, λae,max and λae,min
Notes: The aging and environmental λ factors λae,max and λae,min account for the change in properties that occur over the design life of the bearing. Effects include aging, creep, contamination, fatigue, effects of ambient temperature and cumulative travel. For the bearings considered in this example, aging and contamination are the relevant considerations.

## Slide 35: 4. Isolation System Properties
Consult with manufacturer on quality and control procedures and specification tolerance.
For quality manufactures, :
  Stiffness: Shear modulus of rubber, G:
  Strength: Effective yield stress of lead σYL :
Manufacturing Variations, λspec,max and λspec,min
Notes: The specification λ-factors; λspec,max and λspec,min are a manufacturing tolerance assumed for design and written into specifications. Consult with manufactures, as overly tight tolerances may lead to problems and delays.

## Slide 36: 4. Isolation System Properties
Reference: MCEER-15-0005
SUNY, Buffalo, NY
Dynamic Prototype (or Similar) Bearing Test Data
Notes: There is a graph of the shear force-displacement curve for an elastomeric, lead-core, isolation bearing tested under dynamic conditions.
For this example, dynamic testing per §17.8.2.2, Item 3 is conducted at a vertical load equal to D + 0.5L on two virgin (unscragged) bearings tested at a normal temperature of 20°C. This test consists of three fully-reversed cycles at a displacement amplitude of DM conducted dynamically at the effective period TM determined from the upper-bound properties. Therefore the speed of loading effects and heating effects are directly accounted for. Note that Eloop is the energy dissipated per cycle (also known as EDC)

## Slide 37: 4. Isolation System Properties
Nominal Properties and λtest,max and λtest,min
Notes: There is no engineering judgement or estimation involved in the determination of the maximum force and displacement or energy dissipated per cycle (EDC). Fmax and Dmax are self-evident and EDC is determined by numerical integration of the record force-displacement data file. The value of these are presented in the previous slide.
However, there is judgement (different methods) in determining the shear modulus of rubber and effective yield stress of lead. This slide shows one such approach.

## Slide 38: 4. Isolation System Properties
Effective yield stress of lead σYL:
λtest,max = First cycle/Nominal = 2.27/1.69 = 1.34
λtest,min = 2nd Cycle*/Nominal = 1.56/1.69 = 0.92
Shear modulus of rubber, G:
λtest,max = Heating effects mask scragging = 1.15 from other data
λtest,min = 1.0
Nominal Properties = average among the three cycles, and averaged for the two bearings
Nominal Properties and λtest,max and λtest,min
Notes: There is some judgement in setting the test λ factors. First cycle properties should be used as the maximum properties.
*It is the opinion of the authors that the lower bound should be based on considerations of the seismic hazard and isolation system properties (strength and stiffness). Response history analysis studies by Warn and Whittaker (2007) demonstrate that about two (and less than three) fully-reversed cycles at the maximum displacement is suitable.

## Slide 39: 4. Isolation System Properties
Upper- & Lower-Bound Behavior
Notes: A graph shows the later force vs. displacement characteristics of an isolation bearing evaluated for both lower bound and upper bound properties. The graph illustrates that for upper bound properties the shear stiffness and shear strength of the isolation bearing are both higher than when the evaluation is carried out using lower bound properties.
The maximum and minimum λ factors for the shear modulus of rubber and effective yield stress of lead are calculated based on Equations 17.2-1 and 17.2-2. Note that the code limits on these equations do not apply as the λ factors were based on test data. Furthermore, the Standard presumes a “system property adjustment factor” of 0.75, to account for the conservative assumption that many events with occurring simultaneously (specifically, of having full aging and environmental effects when the governing earthquake occurs).
Shown are the upper- and lower- bound force-displacement behavior of the preliminary sized elastomeric isolation system, based on the nominal values and λ-factors in the previous slides.

## Slide 40: 5. ELF Procedure
  Single-degree-of-freedom, displacement-based method.
  Assumes linear-elastic behaviour (effective stiffness and effective damping) of the nonlinear isolators.
  Iterative procedure
Notes: Two small figures appear at the bottom of this slide. The figure on the left shows a simple single-degree-of-freedom oscillator, consisting of a flexible shaft fixed at the bottom end, and with a lumped mass attached to the top end. The flexible shaft is labelled “Isolation System”. The figure on the right is a load-displacement plot showing a typical hysteresis loop from a seismic isolation system. The area within the hysteresis loop is the energy dissipated by the isolation system during a single cycle of oscillation. This energy can be related to the damping of the isolation system, which is labeled “beta-sub-eff” on the drawing. There is also an inclined line from the origin of the plot to the upper right corner of the hysteresis loop, indicating the effective stiffness of the isolation system, and labeled “k-sub-eff”.
The equivalent lateral force (ELF) procedure is a single-degree-of freedom displacement-based method that uses simple equations to determine an isolated structures response. Although the ELF procedure is considered a linear method of analysis, the equations incorporate amplitude-dependent values of effective stiffness and effective damping to account implicitly for the nonlinear properties of the isolation system. The equations assume that the superstructure is rigid and lateral displacements occur primarily in the isolation system.

## Slide 41: 5. ELF Procedure
  Calculate the effective damping βM
  Interpolate the damping coefficient BM from Table 17.5-1
  Check the displacement matches what was initially assumed in Step 1
  Assume a displacement, say DM = 11.2 inch
  Calculate the effective stiffness kM
  Calculate the effective period TM
Notes: The ELF procedure is an iterative process and is illustrated in the following equations for the preliminary design bearing dimensions and lower bound properties. The terms are defined in pervious slides.
“Conveniently”, our first guess of the displacement matches the displacement calculated in Step 6. Therefore no further iteration is required.

## Slide 42: 5. ELF Procedure
  Refine analysis with a 3-D model and optimise the isolation system design
  ELF force-deflection behaviour of the “optimized” solution
Notes: Shown on the right side of this slide is an isometric view of the framing system for the example building. At each floor is a horizontal red arrow, indicating that in the Equivalent Lateral Force (ELF) procedure the total base shear is distributed up the height of the building and applied at each floor level. There is also a graph at the lower right side of the slide. This graph shows two Force-Displacement hysteresis loops. One loop is for “upper bound” isolation properties, with a higher value of effective stiffness; the other loop is for “lower bound” isolation system properties, with a lower value of effective stiffness.
A more refined calculation of the bearing axial loads can be done with a 3-D model, using a lateral force distribution according to the Standards equations.
The final (“optimized”) bearing dimensions give the force-deflection behavior for the upper- and lower-bound properties as shown. The peak forces and displacements are based on the ELF procedure, and are used in setting minima values to compare to the more sophisticated dynamic analyses.
Although the isolation system could be optimized further (i.e. use lead rubber bearings in combination with flat sliders to reduce the post-elastic stiffness), this is not done for ease of illustration.

## Slide 43: 5. ELF Procedure
RI can be up to 2.0, but is 1.0 for this OCBF example
  Superstructure designed to remain “essentially” elastic for MCER
  Lateral Forces
  Three types to design different components:
Notes: On the right side of this slide is a schematic illustration of an elevation of the example building. This figure illustrates that the forces contributing to the superstructure base shear are derived from the second level and higher. The figure also shows that the forces contributing the seismic isolation base shear are derived from the first level and higher.
The lateral shear force required for the design of the isolation system, foundation and other structural elements below the isolation system is given by Vb. The overturning loads (i.e. axial loads) from the superstructure, which are used for the design of the isolation system, foundation, and elements below the isolation system is given by the unreduced lateral force Vst. Subject to the limits of §17.5.4.3, the base shear, Vs , for the design of superstructure above the isolation level is taken as Vst reduced by the RI factor.

## Slide 44: 5. ELF Procedure
  Check Minimum Requirements for Vs
  Vs = 3449 kip (upper-bound properties)
Notes: Since a OCBF superstructure is used (to save on ductile detailing requirements) the unreduced forces are used for the superstructure design. While the structural shear is quite large (Vs/W=0.34 in upper-bound), keep in mind that this is for unreduced forces (i.e. R=1.0) and for the MCER event. Other building types are designed for the DBE (about 67% of MCER) and large R factors (which means damage).
The value of Vs shall also be checked against Standard §17.5.4.3 to ensure it meets the minimum requirements. As shown, the value of Vs is not governed by the minimum requirements.

## Slide 45: 5. ELF Procedure
  ELF Upper- and Lower-bound cumulative shears
  Vertical Distribution
  New equations for calculating lateral force distribution
Notes: This slide contains two graphs. The first graph at the lower left shows story shear force vs. elevation. The horizontal axis is labeled “Shear force (kip)” and runs from 0 to 5000 kips. The vertical axis is labeled “Elevation (feet)” and runs from -5 to 50 feet. Two lines are shown on the graph “Upper Bound ELF” and “Lower Bound ELF”. The graph illustrates that the story shear forces for upper bound ELF properties are greater than the story shear forces for lower bound ELF properties at all levels of the building. The second graph illustrates the distribution of story forces over the height of the building. This graph shows that the story forces do not increase uniformly from the base to the top of the building, as was the case in the previous edition of the Standard, but that the story forces vary over the height with low values near the base, increasing to higher values near mid height, then decreasing again at the roof level.
The Standard has been revised to incorporate a more realistic distribution of lateral forces over the buildings height. A comparison of the lateral force calculated for a fixed-based building (Ch12.8.3) and isolated building (Ch17.5.5) is given. Seismically isolated buildings have a more uniform distribution over the building height. Note that the penthouse has a lower weight, hence lower force.
The new method calculates the force of the base level, immediately above the isolation plane, then distributes the remainder of the base shear among the other levels. The vertical distribution of the upper- and lower-bound unreduced lateral forces is shown for the example building.

## Slide 46: 5. ELF Procedure
  The compression stiffness of a multi-layered elastomeric bearing can be approximated accordingly:
  Bearing Vertical Loads
  Model the bearing (& soil) vertical stiffness, framing stiffness and mass distribution realistically in 3-D.
Notes:   There is a small photograph of an elastomeric lead core bearing with red arrows representing compression forces acting on the bearings. There is also an isometric illustration of the building frame with one of the seismic isolation bearings circled in read to indicate the focus of this slide is the vertical loads acting on an individual bearing.
  The vertical load on each bearing depends on their relative vertical compression stiffness Kv and soil stiffness, the rigidity of the base level diaphragm/framing and the mass distribution. Hence modelling this realistically in 3-D will give an accurate distribution of bearing compression loads.
  In the vertical stiffness equation, A is the bonded rubber area, ti is the individual rubber layers thickness, K is the bulk modulus of rubber, assumed as 290 ksi and Eci is the compression modulus for incompressible material behavior which is dependent on the rubber shear modulus, shape factor and the bearing geometry (see Constantinou et al., 2007 for details).

## Slide 47: 5. ELF Procedure
Symmetry in isolation system and lateral-force resisting system
Notes: An illustration shows the entire floor framing plan of a typical floor. A red box around the upper left quadrant of the floor plan shows that, due to double symmetry, it may be possible to evaluate results from just one-fourth of the floor plan.
Since the isolation system and lateral-force resisting system have a symmetrical layout (in two directions), only the critical demands need to known in one quadrant (as they are similar in others). That is, loads and displacements at Gridlines 5, 6 and 7 are similar to those at Gridlines 3, 2 and 1, respectively; and loads and displacements at Gridlines D and E are similar to those at Gridlines B and A, respectively. Hence the loads and displacements are only shown per the top-left snippet locations in the following slides.

## Slide 48: 5. ELF Procedure
Bearing Gravity Loads:
Dead and Reduced Live Loads
Critical long-term dead load: 1.2D + 1.6L = 660 kip (C3)
Average load (used for prototype testing): 1.0D + 0.5L = 290 kip
Notes: A drawing shows the grid lines corresponding to the upper left quadrant of the floor plan. There is also a small photograph of an elastomeric lead core bearing with red arrows representing compression forces acting on the bearings.
Values of dead load (D) and reduced live load (L) are shown at each isolator location (click). Long-term gravity design loads on isolators are defined by 1.2D + 1.6L load combination. Long-term design loads on isolators range from about 180 kips at corner isolators (A1) to about 660 kips at an interior isolator (C3).
Based on the load combination, 1.0D + 0.5Lred, the weight on individual bearings varies from about 120 kips to about 460 kip. The typical, or average weight, supported by all bearing is about 290 kips (i.e., 35 bearings x 290 kips/bearing = 10,200 kips). This typical weight is used for prototype testing of isolator units. This is because the mechanical properties of the isolation system are not (materially) affected by fluctuations in the axial load on individual isolators. Rather, the behavior is determined by the average load on all the isolators, which is D+0.5L. It is noted, however, the effect of varying axial load on the properties of individual isolators is of interest as it affects the design of the isolator and of the structure in the vicinity of the isolator.

## Slide 49: 5. ELF Procedure
Bearing Earthquake Loads:
Overturning loads due to horizontal earthquake
5% accidental eccentricity in X- and Y- directions
Add vertical earthquake effects later using ±0.2SMSD
Notes: A drawing shows the grid lines corresponding to the upper left quadrant of the floor plan. There is also a small photograph of an elastomeric lead core bearing with red arrows representing compression forces acting on the bearings.
The horizontal earthquake, which has the vertical shear force distribution shown earlier, causes overturning and axial forces in the bearings. This table gives the maximum and minimum demands from horizontal earthquake and additional forces due to the application of an accidental eccentricity. They are enveloped for an earthquake in the forwards or backwards direction. The larger forces occur where the bearing is below the lateral-force resisting system frame (i.e. where the braces end). The same calculation needs to be done for the lower-bound properties (not shown).

## Slide 50: 5. ELF Procedure
Large tension loads are not desirable – look at NLRHA
Bearing Load Combinations:
Only shown for upper-bound properties
Notes: A drawing shows the grid lines corresponding to the upper left quadrant of the floor plan. There is also a small photograph of an elastomeric lead core bearing with red arrows representing compression forces acting on the bearings.
Using the load combinations 1.2D +0.5L + 1.0E and 0.9D – 1.0E, and incorporating vertical earthquake actions using ±0.2SMSD, gives the maximum and minimum downward vertical forces as shown.
It is noted that tension stresses are developed in a number of locations. This tension stress is acceptable for a high-quality elastomeric bearing if it is less than three times the shear modulus of rubber . This is a capacity 120 kip (i.e. 3GA) for the upper- properties. Hence there are four bearing locations (Gridline A2, E2, A6 and E6) where there is a potential uplift issue.

## Slide 51: 5. ELF Procedure
Where:
PT = ratio of the effective translational to torsional period of the isolation system
y (or x) = distance in plan from center of rigidity to corner
e = actual plus accidental eccentricity
b, d = plan dimensions
≥ 1.15*
*(in commentary)
Increase the maximum (MCER) displacement due to torsion to get the total maximum displacement
Minimum amplification factor:
Total Maximum Displacements:
Notes: An illustration shows the modes of displacement of the structure that are calculated in the process of seismic isolation design. The levels of displacement shown are the design displacement, D-sub-D, the maximum displacement, D-sub-M, and the total maximum displacement (including torsion), D-sub-TM. The figure contains a red shaded area covering the “D-sub-D” label, indicating that D-sub-D is no longer calculated in the current Standard.
This slide illustrates definitions and the equation to calculate the “total” displacement at corners of the isolated structure that includes potential rotation, as well as, translation of the isolation system.
This equation now includes a new term PT, which offers an improvement by relaxing the assumption of equal translation and torsional periods. 5% accidental eccentricity increases corner displacement by about 15% for buildings square in plan, and by abut 30% for buildings that longest dimensions many times greater than the other. Systems with proportional stiffer isolators near the perimeter of structure (e.g., de Young Museum) provide greater resistance to torsion and the effects of actual plus accidental mass eccentricity. Total maximum displacement (DTM) is used to verify stability of isolators and to establish minimum moat clearance.

## Slide 52: 5. ELF Procedure
Minimum amplification varies based on distance from center of mass
Calculate DTM for both upper- and lower-bound
Total Maximum Displacements:
Notes: A drawing shows the grid lines corresponding to the upper left quadrant of the floor plan.
The minimum amplification factors are shown here when enveloped for accidental eccentricity in either X- or Y- directions. The resulting total maximum displacements DTM are shown for the upper- and lower-bound properties.

## Slide 53: 5. ELF Procedure
Rubber shear strains achievable for quality manufactures
Could use single bearing type with 19 rubber layers each 0.275 inches thick
Design is reasonable! as ti ≥ 0.25 inch for critical bearing location
Bearing Stability and Shear Strain
Refined assessment with displacements and vertical loads from compatible locations and for upper- or lower-bound properties
Notes: A drawing shows the grid lines corresponding to the upper left quadrant of the floor plan.
The stability check is illustrated here since its a critical check for the design of the lead-rubber bearings, and may be overly conservative to use enveloped (incompatible) displacements and vertical loads. However, its usually the manufacturers responsibility to do these design checks (as you give them displacements and loads). The equation used to calculate the maximum allowable rubber layer thickness was shown earlier in the preliminary design.
The critical bearing location is Gridlines B4 and D4 which require a rubber thickness less than 0.28 inches which is at the lower limit for what can be satisfactorily constructed by manufactures. Note that all bearings can be design for this worst case so that there is only one bearing type. This would give a final bearing with 5.225/0.275 = 19 rubber layers each 0.275 inches (7 mm) thick. The rubber shear strains due to lateral displacements are high at 294% in the corner locations, but are achievable for a quality manufacturer.

## Slide 54: 5. ELF Procedure
  P-delta Effects
Notes:   A drawing shows the framing plan of the first floor of the structure. Yellow lines along each grid line indicate the locations of heavy steel framing members. These heavy members resist P-delta moments that are induced by the bearings. A second drawing indicates the displaced position of an elastomeric bearing, and the method of computing P-delta moments for the bearing.
  Computer analysis programs may not correctly calculate the large P-delta moments at the isolator level. The slide shows that moments are caused by both displaced vertical loads, P, as well as horizontal shear, V. For the elastomeric bearing, the P-delta moment is split one-half up and one-half down. At the base level, heavier W24 x 146 girders/framing on column (isolator) lines are required to resist moments due to P-d loads and horizontal shear in isolators.

## Slide 55: 6. Dynamic Analyses
  ELF Procedure permitted for final design
  However, uplift is an issue and more sophisticated analysis may show improved responses
  Analysis Procedure Selection
Notes:   As shown, an ELF Procedure is permitted for final design of this building since all the Standards criteria are met.

## Slide 56: 6. Dynamic Analyses
  Vertical Response Spectrum Analysis
  In ELF Procedure, we simply used ±0.2SMSD
  So it assumes that 100% vertical acceleration is about ±(2/3)SMS = 0.93g
  Crude approach, but is only addressed in more detail in commentary.
Notes:   This slide contains an acceleration response spectrum that illustrates a simple method to account for vertical earthquake accelerations. The spectrum shows that vertical earthquake accelerations may be approximated as roughly two-thirds of the maximum amplitude of the MCE-sub-R horizontal earthquake response spectrum.
  The ±0.2SMSD assumes the vertical response spectrum is about 2/3 of the horizontal with 30% combination i.e. 0.67 x 0.3 = 0.2 factor. Hence it assumes the vertical acceleration is about 0.93g for this site.
  Another approach, recommended in commentary, is to compute a more refined vertical spectrum using the 2009 NEHRP Provisions in Chapter 23.

## Slide 57: 6. Dynamic Analyses
  Vertical response spectrum per Chapter 23 of 2009 NEHRP Provisions (retained in 2015 Provisions)
  Vertical Response Spectrum Analysis
Notes:   A graph is shown on this slide that indicates the relationship between the horizontal design response spectrum and the vertical design response spectrum. The vertical response spectrum must not fall below 50 percent of the horizontal response spectrum. At periods above about 0.4 seconds it is shown that this limitation governs the vertical response spectrum.
  The 2009 Provisions have a simplified method to calculate the vertical spectrum through the parameter SS (short-period horizontal spectral acceleration), as well as the site class classification. The resulting vertical response spectrum to use for design is shown.

## Slide 58: 6. Dynamic Analyses
1/kseries = 1/kbearings + 1/ ksoil
kseries = 17,920 kip/inch
Vertical Period:
Vertical acceleration using refined response spectrum = 1.09g
ksoil = 540 kip/inch x 35 shallow pads
kbearings = 10,000 kip/inch x 35 bearings
  Vertical period (ELF approximation)
  Vertical Response Spectrum Analysis
Notes:   A drawing shows a simple single-degree-of-freedom (SDOF) vertical oscillator as a way of illustrating the approach to performing vertical response spectrum analysis. Two springs are shown in series, the upper spring representing the stiffness of the bearings, and the lower spring representing the stiffness of the soil. At the top of the springs a mass is shown, representing the total mass of the superstructure.
  A single degree of freedom analysis should be used initially to estimate the vertical period and resulting vertical base reaction. Here the vertical stiffness only considers the bearings and soil-structure interaction (where geotechnical expertise is required).

## Slide 59: 6. Dynamic Analyses
  ETABS modelling requires careful considerations (i.e. adding more degrees of freedom so that the mass is realistically distributed across the building footprint)
  Vertical period from ETABS modal analysis = 0.34 sec
  Add refined vertical response spectrum to ETABS and conduct vertical response spectrum analysis
  Vertical Response Spectrum Analysis
Notes:   Our practices for modelling buildings are focused on horizontal actions, not vertical. Hence special modelling considerations are necessary, as outlined in the Standard commentary §C17.6.2. The multi-degree of freedom ETABS model shows that the longest period for a vertical mode shape is around 0.34 seconds, so we would expect a lower base reaction than 1.09g using the vertical response spectrum analysis.

## Slide 60: 6. Dynamic Analyses
  Less than the 0.93g assumed by ELF
  Also gives more realistic distribution over footprint
  Use orthogonal combination rule: 100% + 30% + 30%
  Vertical Response Spectrum Analysis:
  Total reaction in the upwards/downwards direction of 7174 kip (0.7g)
Notes:   A drawing shows the grid lines corresponding to the upper left quadrant of the floor plan.
  The vertical response spectrum analysis resulted in a total reaction in the upwards/downwards direction of 7174 kip, which is equivalent to 7174/10200 = 0.7g which is less than that assumed for the ELF analysis.
  These vertical earthquake effects are combined with the two horizontal earthquake components using the orthogonal rule 100%-30%-30%.

## Slide 61: 6. Dynamic Analyses
  Ground Motion Records:
    Minimum of seven ground motions
    Preferably selected from actual earthquake records
    Scale to exceed MCER spectrum over period range of interest (i.e. 0.75TM,UB to 1.25TM,LB for amplitude scaling)
  Response History Analysis
Notes:   Two graphs are shown at the bottom of the slide. The left graph shows acceleration response spectra for seven different ground motions, as well as a smoothed “target” spectrum. The seven response spectra fall in a range both above and below the target spectrum. The right graph is also an acceleration response spectrum plot. On this graph are shown the target response spectrum from the previous graph along with the average of the seven records from previous graph. The average response spectrum matches the target response spectrum closely over the period range of interests, from approximately 1.1 to 2.7 seconds.
  Selection and scaling of appropriate ground motions should be performed by a ground motion expert. It is noted that ground motion criteria for seismically isolated structures is different from that required for the NLRHA of other structures in the Standard (ASCE 7-2016).

## Slide 62: 6. Dynamic Analyses
  Structural Analysis & Modelling
    Two orthogonal components of horizontal earthquake acceleration applied to ETABS model
    Apply in only one random orientation as active fault > 3 km away
  Response History Analysis
Notes:   At the center of this slide are shown two earthquake accelerographs, with the vertical axes labeled “Acceleration Amplitude 1, (g)” and “Acceleration Amplitude 2, (g), with scales running from -0.8 g to 0.8 g. The horizontal axes are the time scale, running from 0 to 40 seconds. These two plots are meant to illustrate schematically that a typical earthquake record for seismic isolation design consists of two orthogonal components applied simultaneously to the structure.
  Only for sites within 3 miles of an active fault does the Standard specify how the two scaled components of each record should be applied to a three-dimensional model (i.e., how the two components of each record should be oriented with respect to the axes of the model). For other sites, the Standards commentary states that individual pairs of horizontal ground motion components need not be applied in multiple orientations.

## Slide 63: 6. Dynamic Analyses
Zero elastic torsional stiffness
Elastic bending stiffness about X & Y axes (arbitrary value shown)
Lower-bound isolator properties in U2 & U3 directions
Mid-height of LRB
Used in Nonlinear Modal History (FNA) analysis. Set as a low value to avoid damping leakage
Vertical stiffness in U1 direction
Approximate mass and rotational inertias of individual isolator (arbitrary values shown)
  Defining Link Elements- Rubber Isolators (ETABS)
  Response History Analysis
Notes:   This slide shows five different screen shots from input tables of the structural analysis software ETABS. Properties that must be entered in the software include the following: Approximate mass and rotational inertias of individual isolators; vertical stiffness in U1 direction; linear isolator properties, used in nonlinear modal history analysis; mid-height of isolation bearing; lower bound isolator properties in U2 and U3 directions; zero elastic torsional stiffness, and elastic bending stiffness about X and Y axes.
  For most types of isolators, force-deflection properties can be approximated by bilinear, hysteretic curves that can be modeled using commercially available nonlinear structural analysis programs. The initial stiffness, yield strength and post yield stiffness ratio of a single bearing for the lower-bound properties specified in ETABS is given. It is noted that ETABS also asks for linear properties which are used in the nonlinear modal history analysis. It is recommended to specify a low effective stiffness, say equal to the post-elastic stiffness, and zero effective damping.

## Slide 64: 6. Dynamic Analyses
Include acceleration in all 6 degrees of freedom and include link elements
Sufficiently large number of modes so that vertical loads are fully applied (may require convergence analysis)
Ritz vectors are recommended
  Defining Modal Case for Analysis (ETABS)
  Response History Analysis
Notes:   This slide illustrates a screen shot from the structural analysis software ETABS, showing the definition of the modal case for analysis, which is used for the Fast-Nonlinear Analysis (FNA).

## Slide 65: 6. Dynamic Analyses
Specify constant damping of 2% for all modes (as superstructure performs elastically) with manual override for purely isolated modes (i.e. first 6 modes)
Recommended to be equal to the number of time steps and step size in the ground motion record
Original (measured) earthquake record can be scaled here (i.e. 1158/386 = 3.0 scale factor)
Earthquake should start at end of vertical load case. In this load case is where the gravitational acceleration can be modified up or down for maximum and minimum vertical effects.
Fast Nonlinear Analysis (FNA)
  Defining Load Cases for Analysis (ETABS)
  Response History Analysis
Notes:   This slide illustrates a screen shot from the structural analysis software ETABS, showing the definition of load cases for time history analysis. Guidance is shown for ETABS inputs for each of the earthquake records.

## Slide 66: 6. Dynamic Analyses
  Model Verification
  Response History Analysis
Notes: A graph illustrates the base shear force-displacement hysteresis loops for static equivalent lateral force (ELF) analysis and for nonlinear response history analysis (NLRHA). The graph shows that all the hysteresis loops from the NLRHA fall inside the bounding loop from the ELF procedure.
Due to the many inputs required for NLRHA it is important to carry out verification checks. This slide shows the NLRHA hysteretic response (base shear vs. displacement) of the isolation system in the X and Y directions from ground motion 5, which compares well to the ELF procedure.

## Slide 67: 6. Dynamic Analyses
  Post-Processing
  Response History Analysis
Notes: There is a graph that shows earthquake displacement records for the isolation system, with the horizontal axis labeled “Time (seconds)” running from 0 to 40 seconds. The vertical axis is labeled “Displacement (inch)” running from -12 to 12 inches. One displacement record is labeled “X-direction” and the other “Y-direction”. Also shown on the graph is the square-root-of-sum-of-squares combination of the X and Y displacement records labeled “SRSS”
This slide shows the displacement history of the isolation system in the X and Y directions for ground motion 5, Loma Prieta, using lower-bound properties. The peak X and Y displacements were 11.9 and 6.5 respectively. Simply taking the SRSS of these maximum X and Y displacements is overly conservative i.e. (11.92+6.52)1/2 = 13.6 inches. The SRSS should be instead be taken at each time step, which gives a maximum displacement of 12.0 inches.

## Slide 68: 6. Dynamic Analyses
Note: The displacement needs to be increased for torsion
  Post-Processing
  Response History Analysis
Notes: This table summarizes peak SRSS combinations of isolation system displacements and base shears for each ground motion from the NLRHA. The average of the seven ground motions may be used for design.

## Slide 69: 6. Dynamic Analyses
Increase moat clearance for OCBF = 1.2 x 12.0 = 14.4 round up to 15 inches
Bearing design lower bound
Including torsion using amplification factor
  Post-Processing - Displacements
  Response History Analysis
Notes: The table compares the NLRHA to the ELF results. To avoid possible under-design, the Standard establishes minimum limits on results of dynamic analysis to be used for design. These limits are established as a percentage of the corresponding parameter calculated using the ELF procedure equations. Here it is shown that the NLRHA displacement of 8.9 inches is less than the Standards minimum requirements (of 10.4 inches), hence the lower limit governs.

## Slide 70: 6. Dynamic Analyses
  Post-Processing – Lateral Forces
  Response History Analysis
Notes: This slides contains a graph showing the variation in design story force over the height of the building. The horizontal axis of the graph is labeled “Shear force (kip)” and runs from 0 to 4500 kips. The vertical axis is labeled “Elevation (feet)”, running from -5 to 50 feet. Three lines are shown on the graph. Two are labeled “NLRHA X-direction” and “NLRHA Y-direction”. These two lines begin at 2600 kips and 2200 kips, respectively, at the first story of the building, and both reach a value of about 750 kips at the penthouse story. A third curve, labeled ELF (Equivalent Lateral Force procedure) generally has story shear values greater than the HLRHA curves. The ELF curves starts at 3500 kips at the first story and reduces to about 750 kips at the penthouse story.
The upper-bound properties gave the worst case lateral loadings. Shown is a comparison of the NLRHA and ELF story shears. Torsion is added to these forces using the same approach as ELF procedure.

## Slide 71: 6. Dynamic Analyses
  Post-Processing – Lateral Forces
  All elements above the isolation system shall be designed for lateral force no less than 80% of the ELF Vb for this regular structure. Therefore increase NLRHA forces by:
  All elements below the isolation system shall be designed for lateral force no less than 90% of the ELF Vb
  i.e. increase scale factors above further by 0.9/0.8 = 1.13
  Response History Analysis
Notes: Again, the minimum limits of the Standard govern and the NLRHA lateral forces have to be scaled up to meet the minimum criteria. The minimum limits are different for elements above and below the isolators, and also different depending on the configuration of the superstructure.

## Slide 72: 6. Dynamic Analyses
  Post-Processing – Bearing Vertical Loads
  Maximum compression loads are 829 and 986 kip for 100% and 30% of the maximum horizontal displacement, respectively.
  Maximum tension loads are both 74 kip for 100% and 30% of the maximum horizontal displacement.
  Response History Analysis
Notes: The combination of vertical/axial loads on the bearings to be used for design consist of static dead and live loads, torsion (from the ELF procedure), vertical earthquake loads per the vertical response spectrum analysis, as well as the overturning/vertical effects of horizontal earthquake loads from the NLRHA (which are increased by scale factors per minimum requirements).
These loads are less critical than the ELF analysis. Although tension still occurs in some bearings, the force is less than 3GA so is manageable for quality manufacturers.

## Slide 73: 7. Testing Requirements
  For setting acceptance criteria of production testing
  To determine nominal properties and λtest factors
  To check durability of isolator for multiple earthquake events
  Stability of isolator in extreme conditions
  Prototype testing of 2 isolators
Notes: This slide illustrates the sequence and cycles of prototype testing required by Section 17.8.2.2 of the Standard.
There are four distinct elements of prototype testing. Firstly, the prototype isolators are tested under the same conditions as that which will be done for production testing, so that acceptance criteria can be set for production isolators. Secondly, cyclic load tests at constant and incremental displacement amplitudes are required to establish the force-deflection properties of isolators (e.g., stiffness, strength and bounds) for typical, maximum, and minimum vertical loads. Thirdly, 14 cycles of load at the 75% of the maximum displacement (DM= 7.8 inches) are required to assess isolator prototype “durability” for typical vertical load (290 kips). The number of cycles is based on the formula, 30 SM1/SMSBM ≥ 10 cycles of load which is a conservative estimate of the effective number of cycles for two maximum considered earthquake events (i.e., main shock plus after shock as large as the main shock) Finally, static load tests are required to check isolator stability at maximum displacement and for both maximum downward load (830 kips) and minimum downward load which includes uplift. Tension is elastomeric isolators is discouraged, although quality isolators can sustain tension stresses up to 3GA. Capabilities and of tension testing should be coordinated with the manufacturer.

## Slide 74: 7. Testing Requirements
Reference: MCEER-11-0004 SUNY, Buffalo, NY
  Positive incremental restoring force capacity for re-centering
  Reliable force-deflection properties with limited manufacturing variations
  3. & 4. Measured lateral force-displacement response that lies between the limits set forth by the engineer-of-record for the specified cycles of dynamic loading & is durable for multiple earthquakes.
  5. Remain stable under worst case loading conditions
  Prototype units are acceptable if they have:
Notes: A graph shows the later force vs. displacement characteristics of an isolation bearing evaluated for both lower bound and upper bound properties. The graph illustrates that for upper bound properties the shear stiffness and shear strength of the isolation bearing are both higher than when the evaluation is carried out using lower bound properties.
The Standard provides acceptance criteria of the isolators with (the authors interpretation) of each clause’s intent as follows:
The test specimens should have increasing resistance with displacement to verify that the isolation system will not accumulate residual displacement in a given direction.
To ensure limited variation due to manufacturing, the two test specimens should have the similar/reliable properties.
(3) & (4) The measured force-displacement response should lie between the limits set forth by the engineer-of-record (i.e., the shaded region contained by the sample shear force-lateral displacement loops in the Figure, as adjusted for the project-specific application) for the specified cycles of dynamic loading. The bearing should also be durable (i.e. have limited degradation & or recoverable properties) such that the isolation system would still be functional during aftershocks
(5) remains stable for maximum earthquake loads – the tests specimens must be shown capable of supporting maximum (and minimum) vertical load at total maximum (MCER) earthquake displacement.

## Slide 75: 7. Testing Requirements
  Production testing of all (100%) isolators
Notes:   All isolators must be subjected to a combined compression and shear load cycle before being installed. This is to verify the properties and reveal any defects and is commonly referred to as quality control testing.

## Slide 76: DISCLAIMER
NOTICE: Any opinions, findings, conclusions, or recommendations expressed in this publication do not necessarily reflect the views of the Federal Emergency Management Agency. Additionally, neither FEMA nor any of its employees make any warranty, expressed or implied, nor assume any legal liability or responsibility for the accuracy, completeness, or usefulness of any information, product or process included in this publication.
The opinions expressed herein regarding the requirements of the NEHRP Recommended Seismic Provisions, the referenced standards, and the building codes are not to be used for design purposes. Rather the user should consult the jurisdiction’s building official who has the authority to render interpretation of the code.
Any modifications made to the file represent the presenters' opinion only.