## Slide 1: Soil-Structure Interaction Robert Pekelnicky, P.E., S.E., Insung Kim, P.E., S.E.
Disclaimer
8
Notes: Title slide, includes an image of the cover of the data disk containing the 2015 NEHRP Recommended Seismic Provisions, and the name of the author of the 2015 Design Provisions Examples.
This presentation is a brief introduction to the theory behind soil structure interaction and it’s affect on building performance during seismic events.

## Slide 2: Soil-Structure Interaction
Foundation Force-Deformation
  Foundation Flexibility
  Soil-Foundation Interface Yielding
Foundation Damping
  Radiation Damping
  Soil Hysteretic Damping
Kinematic Interaction
  Base Slab Averaging
  Embedment
Notes: This slide lists the three major factors contributing to soil-structure interaction effects
Soil structure interaction is comprised primarily of inertial effects and kinematic effects. Inertial effects include foundation flexibility, yielding at the interface, and foundation damping. Kinematic effects include base slab averaging and embedment effects

## Slide 3: What We Should Do
Notes: Slide is a picture of a modelling configuration used to represent the structure, link elements representing the foundation, a mesh element representing the soil, and a transmitting boundary at the ends of the soil elements
There are two analysis methods to capture soil-structure interaction (SSI) effects, the Direct Method and the Substructure Method. In the direct method depicted here, we would have one model representing the soil, foundation, and structure and the earthquake motion would be applied to the ends of the soil elements. This method would most accurately reflect the true condition. However, this method is computationally demanding and rarely used. A more common approach is to partition each contributing factor and combine the results of each part to observe a global response

## Slide 4: What We Actually Do Geotechnical Engineer
Spatially-INCOHERENT ground motions from the rock motion through the soil column
nonlinear-inelastic soil spring-dashpots at each soil lens
Notes: Slide is an image of model representing SSI effects. It is a complicated soil model including soil spring and dashpots, with varying ground motions applied at the ends of each soil element. On top of the soil model is a very simple single-degree of free building model
Geotechnical engineers have a vast understanding of soil characteristics and can accurately model its response to earthquake motions that vary over the depth, but they often lack that level of detail when it comes to modelling the structure itself. This figure depicts a sophisticated model of the soil and basement of a structure, which would be used to generate the response spectrum that the structural engineer would use to design the structure.

## Slide 5: What We Actually Do USGS Maps
Notes: Slide is an image of a single degree of freedom oscillator which has deflected after some force, F, has been applied
Structural engineers typically design buildings using a response spectrum, which is the response of a single degree of freedom oscillator, shown above, to ground shaking. This is what the spectral response values found on the USGS website are based on.

## Slide 6: What We Actually Do Structural Engineer
Notes: Slide is an image of a simple 6-story building model with one basement level, a rigid foundation, and an earthquake ground motion applied to the ground level
Structural engineers model the entire building earthquake response using principles of dynamics, but consider the base of the building to be rigid. That does not consider the varying effects of different soils or foundations. Often the basement is not even modeled and is designed separately.

## Slide 7: ASCE 7-16/ 2015 NEHRP Provisions
Based on ATC-83 Report (NIST NIST GCR 12-917-21)
Direct inclusion of soil flexibility
Merger ASCE 41-13 Provisions with ASCE 7-10
Updated foundation damping equations
Update & clarify limitations on use
Notes: Slide lists a brief history of the development of the SSI chapter in ASCE 7-16 and the 2015 NEHRP provisions
The new SSI chapter in the Provisions is based on a recent NIST report and provides direction on how to include of the flexibility of the soil, an import of the ASCE 41-13 SSI provisions in to ASCE 7, updated foundation damping equations for rectangular foundations, provisions to use Kinematic Interaction SSI and clarifications on the limitations of use for SSI. This presentation will discuss the different types of SSI.

## Slide 8: Foundation Flexibility
Notes: Slide is an image of a modelling scheme for a foundation, shown as a rigid U-shape with vertical and horizontal springs and dashpots connected to a surface fixed in translation
One way in which to consider foundation flexibility is to model the base of the building on vertical and horizontal springs with stiffness based on the characteristics of the surrounding subsurface medial (soil) or based on the behavior of the piles or piers in the subsurface media . These values are not always provided by the geotechnical engineer, but can be derived from empirical formulas or requested from a geotechnical engineer. When requesting them it is important to get the parameters specific to the level of earthquake shaking that is being used for design. Horizontal springs can also be used to represent soil passive pressure on the basement walls. Parameters can be computed to approximate the damping at the soil-foundation interface.

## Slide 9: Foundation Flexibility - Example
Reinforced concrete shear wall building
4 Story + 1 Basement
Site class D soil
Oakland, California
Notes: Slide is an image of a building elevation with 5 bays and four stories. Gridlines and story heights are shown.
The easiest way to explain SSI is to use an example building to illustrate it. Consider the four story reinforced concrete wall building located on a site that would be classified as Sit Class D. The building used for the example is approximately 53 feet tall and the basement is 15 feet below grade.

## Slide 10: Foundation Flexibility - Example
Notes: Slide is a plan view image of the same building shown in elevation on the previous slide. In plan it is 6 bays by 5 bays, each 30 feet wide
The building is rectangular with a north south dimension of 180 feet and an east-west dimension of 150 feet. Floor slabs are reinforced concrete flat plates and the columns are rectangular cast-in-place concrete situated on spread footings. The lateral forces are resisted by cast-in-place special reinforced concrete shear walls. There is a reinforced concrete wall around the entire basement. The interior walls and columns are founded on spread footings and the basement wall is founded on a continuous strip footing.

## Slide 11: Foundation Flexibility - Example
Fixed Base Modal Period
T = 0.39 sec
Flexible Base Modal Period
T = 0.49 sec
25% increase in period due to foundation flexibility
Notes: Slide lists the first mode period obtained by two methods of analysis, one considering a rigid base and one consider a flexible base
When the building is model in a conventional structural analysis program, including the basement, but assuming fixity at the base of the walls, the fundamental period is computed to be 0.39 seconds. When springs are added to approximate the stiffness of the surrounding soil in both the horizontal and vertical directions, the period of the structural system increases to 0.49 seconds. This is a 25% increase in the period due to flexibility, which means movement at the base of the building due to the flexibility of the subsurface media accounts for an additional 50% increase in the overall flexibility.

## Slide 12: Foundation Flexibility - Example
Chart: Period, T (sec)
| 0 | 0.05 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.25 | 1.5 | 1.75 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5
Sa_MCER_(MaxDir) | 0.7307 | 0.85 | 1.1 | 1.35 | 1.5 | 1.513 | 1.522 | 1.539 | 1.517 | 1.5 | 1.5 | 1.5 | 1.2857 | 1.206 | 1.132 | 1.069 | 0.9104 | 0.7913 | 0.6886 | 0.6117 | 0.4994 | 0.4185 | 0.357 | 0.3104 | 0.2756 | 0.2477
Sa_DE_(MaxDir) | 0.48713 | 0.56667 | 0.73333 | 0.9 | 1 | 1.0087 | 1.0147 | 1.026 | 1.0113 | 1 | 1 | 1 | 0.85714 | 0.804 | 0.75467 | 0.71267 | 0.60693 | 0.52753 | 0.45907 | 0.4078 | 0.33293 | 0.279 | 0.238 | 0.20693 | 0.18373 | 0.16513
Notes: Slide is an image of a response spectrum showing the maximum considered earthquake (MCE) and design level earthquake (DE) with vertical lines for the two period values listed in the previous slide
Both the rigid base and flexible base periods are plotted on the MCE and DE spectrum. In this instance, both periods land on the peak, and there is not much change in the design forces because of the increased flexibility.

## Slide 13: Foundation Flexibility - Example
Notes: Slide is an image of a spectral acceleration graph with multiple motions plotted. The motion with the highest peak shows a measurable reduction in spectral acceleration when the flexible base foundation is considered (from about 2 to 1.3 g’s). It also shows that if the fixed base period falls on the ascending branch of the spectrum then considering a flexible base can actually increase the design loads.
Depending on the shape of the spectrum at a given location and hazard level, foundation flexibility can have a range of effects on the design forces and the response of the building. If the rigid base period falls at the peak, then the flexible base will result in a lower spectral acceleration, however, if the rigid base period is on the ascending branch of the spectrum, then considering a flexible base can actually increase the design loads. Something important to note is that for the bottom response spectra, where the fixed base period has a lower spectral ordinate than the flexible base period, SSI increases design forces instead of lowering them.

## Slide 14: Foundation Yielding
Currently no requirement for foundation to be stronger than superstructure
Foundations and soil actions designed with same forces
Soil actions typically ASD
Notes: Slide is a list of statements regarding foundation yielding
Current seismic design philosophy ensures ductile behavior by designing elements to be flexurally controlled, and typically attempts to control which elements in the structure will yield and which will remain elastic. However, this philosophy is not currently extended to the foundation. It is therefore possible that the foundation element or soil can move into the non-linear range before the structure itself because there are no overstrength or capacity design requirements on the foundation elements or soil actions.

## Slide 15: ASCE 7-16 => LRFD Soil Design
Introduced provisions to allow LRFD for soil actions
Phi factors based on material (clay vs. sand) and level of testing
Notes: Slide is a list of statements regarding the new SSI provisions in ASCE 7-16
New measures will be introduced in ASCE 7-16 to address soil loading. Methodology will be LRFD instead of ASD, which is typically used for soil actions, and the phi factors will vary based on soil type and the level of geotechnical investigation performed.

## Slide 16: Foundation Yielding – Example
Code Design: 40’x18’ footing 14-#7 Long & #7@12” Trans
Soil stronger than wall: 40’x24’ footing 16-#8 Long & #8@12” Trans
Footing stronger than soil or wall
40’x18’ footing 14-#8 Long & #8@12” Trans
Notes: Slide has an image on the left of a plan view of a concrete wall on a concrete footing. Information on the right is given regarding the design of the footing and wall
This example shows the design of a foundation for one of the walls. The first design simply follows ASCE 7-16 and the Provisions by using the same R-factor reduced forces to design a base area based on bearing capacity of the soil and size the thickness and reinforcement of the footing for the forces of the analysis. No attempt is made to ensure a mechanism in the wall above. The second design attempts to proportion the foundation so yielding in the wall above is guaranteed. This leads to a wider, thicker and more heavily reinforced footing. The last design attempts to proportion a footing such that either the wall or the soil yields before the foundation has shear failure or flexure yielding. This leads to an increase in the thickness and the reinforcement. Currently the code does not require either of the latter two designs, but some engineers believe that at minimum the last option should be followed to prevent nonductile failures in the footing.

## Slide 17: Foundation Damping
Soil Hysteretic damping affects shaking building feels
Waves from structure moving interfere with ground motion waves
Notes: Slide is an image of a way in which to model a building considering SSI effects. Shows a structure with foundation on vertical and horizontal springs and dashpots where the ends of the horizontal springs are subjected to an earthquake motion that varies over the depth.
Foundation is comprised of two different types of damping, radiation and soil hysteresis. Movement of the foundation (translation and rotation) generate waves emanating from the foundation which interfere with the earthquake waves coming through the soil. Radiation damping represents this interference. Soil Hysteretic damping occurs as the earthquake waves move through the soil medium to the soil-foundation interface and is proportional to the intensity of shaking at the site and the stiffness of the soil.

## Slide 18: Foundation Damping
Radiation damping & soil hysteretic damping addressed
Modification of the design base-shear or response spectrum
Explicit damping elements required for nonlinear analysis
Notes: Slide is a list of statements regarding foundation damping
Foundation damping is comprised of radiation damping and soil hysteretic damping, and ASCE 7-16 includes equations representing both. One way in which SSI can be incorporated into building design is by calculating the foundation damping and reducing spectral acceleration by using a damping ratio higher than the 5% number used to develop the general response spectrum. However, when performing non-linear analysis including SSI effects, specific elements much be included to account for foundation damping, simple damping relationships that reduce the target response spectrum are not permitted.

## Slide 19: Foundation Damping
Notes: slide shows four images, two plots of spectral acceleration versus period, one is on a linear scale and the other is on a log scale. Both show the effects of including foundation flexibility and foundation damping. The other two images are single degree of freedom representations of the rigid base model and the flexible base model. The flexible model shows rotation at the base.
Plots show that foundation flexible increases the first mode period moving “down” the spectrum, and foundation damping reduces the entire spectrum. So while foundation damping reduces the response spectrum, the increase in period due to flexibility at the soil-foundation interface can lead to an increase in design forces.

## Slide 20: Foundation Damping & the R-Factor
How much SSI is in the R-factor?
ASCE 7-10 limited to a 30% reduction
Notes: Slide is a series of statements regarding the R-Factor and an equation representing the base shear including SSI effects
The R-factor is a global spectral ordinate reduction to account for structural yielding that permits the designer to that was developed to provide engineers with a minimum force to proportion a structural system with appropriate toughness to resist seismic shaking. There is an argument that some soil structure interaction effects are already inherently included in the R factor and that by combining SSI effects with a traditional design approach will be “double counting.” For this reason ASCE 7-10 capped the benefits from doing an SSI analysis to a max of 30% reduction in base shear for low R-factor systems. The equation for base shear including SSI is shown.

## Slide 21: ASCE 7-16 Foundation Damping
Notes: Slide shows equations included in ASCE 7-16
ASCE 7-16 recognizes that if the structure is very ductile, meaning it has a high R-factor, then the majority of the energy will be dissipated through structural yielding and not SSI. That is why the equations including SSI that modify the base shear are capped at 10% for high ductility systems and 30% for low ductility systems.

## Slide 22: Soil Damping
 |  | Effective Peak Acceleration, SDS /2.51 |  |  | 
Site Class | SDS /2.5 = 0 |  | SDS /2.5 = 0.1 | SDS /2.5 = 0.4 | SDS /2.5 = 0.8
A | 0.01 |  | 0.01 | 0.01 | 0.01
B | 0.01 |  | 0.01 | 0.01 | 0.02
C | 0.01 |  | 0.01 | 0.03 | 0.05
D | 0.01 |  | 0.02 | 0.07 | 0.15
E | 0.01 |  | 0.05 | 0.20 | *
F | * |  | * | * | *
Notes: Slide is a table of soil damping (Beta-s) values based on effective peak acceleration and site class
Table of estimated soil damping (Beta-s) values based on effective peak acceleration and site class. As can be seen, soil damping increases with the magnitude of the seismic shaking and the flexibility of the soil.

## Slide 23: Radiation Damping
(Eq. 19.3-14)
(Eq. 19.3-13)
(Eq. 19.3-12)
(Eq. 19.3-11)
(Eq. 19.3-10)
(Eq. 19.3-9)
(Eq. 19.3-8)
r=[1/(T/Ty)2]y+[1/(T/Txx)2]xx (Eq. 19.3-5)
(Eq. 19.3-6)
(Eq. 19.3-7)
Notes: Slide shows a series of equations from chapter 19 of the NEHRP provisions for radiation damping
Foundation is comprised of radiation damping and soil damping. The following series of equations are used to determine the radiation damping value. The y term is for radiation damping due to translational (sliding) movement and the xx term is for rotational (overturning) radiation damping. The Ky and Kxx terms calculate the stiffness of a rigid plate on the soil in translation and rotation, they are then converted to periods based on the mass of the structure atop. The damping is proportional to the different in flexibility between the structure above and the foundation translating and rotating as a rigid body. The stiffer the structure, the more radiation damping. The majority of these equations rely on the modulus of the subgrade, G, which should be provided by a geotechnical engineer and be based on soil properties under seismic shaking.

## Slide 24: Foundation Damping Example
Structural Damping, β = 5%
Radiation Damping, βf = 11%
Soil Damping, βf = 7%
Foundation Damping
Total Damping
Notes: Slide shows a sample calculation using the equations listed previously for foundation damping, total damping and a spectral acceleration reduction factor, B_SSI
To determine the overall damping ration for the soil-structure system, the following equations are used and sample values are provided to give context. In this example, the overall damping should be 16% as opposed to the standard 5%. For the best results, the geotechnical engineer should develop the site specific spectrum with a 16% damping ratio, however, the 5% damping spectrum can also be reduced by the factor B_SSI.

## Slide 25: Foundation Damping Example
Damping Base Shear Reduction
Base Shear
R-factor limit
Revised base shear based on limit
Notes: Slide is a summary of how foundation damping is incorporated, it has an equation with sample calculations for damping base shear reduction, base shear, R factor limit and the revised overall base shear
Using the example calculation, we see that the overall structural base shear is reduced from V = 0.2W to V = 0.17W

## Slide 26: Foundation Damping Example
Property | Fixed Base – No SSI | Flexible Base – SSI
Wall Thickness | 14 inches | 12 inches
Horizontal Reinf. | #5 @ 12” o.c. | #4 @ 12” o.c.
Vertical Reinf. | #5 @ 12” o.c. | #4 @ 12” o.c.
Boundary Region | 14 - #7 | None
Footing Dimensions | 40-ft x 14-ft | 40-ft x 14-ft
Footing Long. Reinf. | 14 - #7 T&B | 12 - #7 T&B
Footing Trans Reinf. | #7 @ 12” T&B | #7 @ 14” T&B
Notes: The slide shows a table comparing and contrasting a design considering a rigid base and a flexible base
As can be seen from the table comparing the same design with and without considering a flexible base, gains can be had in terms of smaller member sizes and less steel when designing with SSI effects. These can translate to cost savings due to reduced reinforcement and eliminating the need for confined boundary regions.

## Slide 27: Kinematic Interaction
Spatial variability of input ground motion along the foundation
  Embedment Effects – Deamplification of ground motion with depth (Vertical)
  Base-Slab Averaging – Wave incoherence across foundation (Horizontal)
Affects high-frequency input
Multi-support excitation required
in modeling
Notes: Slide introduces the concept of kinematic effects with bullets and an image on the bottom right. The image is repeated from the “Foundation damping” slide, showing a building model with horizontal and vertical springs and dashpots. The horizontal springs can be excited with a ground motion that varies over depth, and the vertical springs can experience multi-support excitation
The presence of foundation elements inherently affects the free-field ground motions that are transmitted to the structure and therefore the ground motion felt by a structure is never exactly the same as what is recorded at the site if the structure was not present, know as the free-field record. This is the concept behind kinematic effects which is comprised of base slab averaging and embedment effects.

## Slide 28: Base Slab Averaging
Prof. Jonathan Stewart
uFIM (w)  ug (w)
Low frequency components…
2003 Off-Miyagi Eqk
FF, s-wave window
Notes: Figure on left depicts the particle motion of a point from earthquake shaking. Figure on the right is a plan view of a foundation with vectors representing the ground motion felt at varying points on the slab. For low frequencies, these vectors are well correlated and point in the same direction.
The first of two kinematic interaction phenomena is base slab averaging, which is when a large, rigid base of the structure filters out high frequency, out-of-phase ground motion. That results in decrease in the spectral ordinates at short periods. Free field response spectra assumes that all the ground shaking is in-phase over the base of the structure.

## Slide 29: Base Slab Averaging
Prof. Jonathan Stewart
uFIM (w) < ug (w)
High frequency components…
2003 Off-Miyagi Eqk
FF, p-wave window
Notes: Slide is two images. On the left is a graph of the motion of a particle motion due to earthquake shaking. On the right is the same plan view of a foundation slab with vectors representing the earthquake at different points on the slab. These vectors are all varying in direction and magnitude.
In reality the ground motion is not completely in phase at every point under the base of the structure. In fact the high frequency motion can be very out-of-phase over large base distances. I the base is rigid reltative to the vertical elements of the lateral force resisting system, then the base filters the out-of-phase, high frequency motion, leading to reduced response for short period structures and higher modes that have low periods.

## Slide 30: Embedment Effect
Prof. Jonathan Stewart
Low frequency
Long wavelength
l = Vs/f
uFIM  ug
qFIM  0
Notes: Slide is a picture of a building basement surrounded by soil. At a distance away from the basement is where the ground motion is being recorded. Displacement varies with depth in a wave pattern with a low frequency. On the right are a few statement regarding embedment effects.
A similar filtering of high frequency motion occurs as the depth of the structure’s base extends below the ground.

## Slide 31: Embedment Effect
Prof. Jonathan Stewart
High frequency
Short wavelength
l = Vs/f
uFIM < ug
qFIM > 0
Notes: Same image of a building basement on the left, where the ground motion is being recorded, displacement varies with depth in a wave pattern with a higher frequency than the previous slide. On the right statements regarding embedment effects with high frequency motions
High frequency ground motions are not as prevalent at depths below the ground surface. Therefore a structure with a deep, rigid base, will see a similar filtering out of high frequency motion as occurs with base slab averging.

## Slide 32: Kinematic Interaction
Notes: Slide is an image of a spectral acceleration plot versus period. Three series are plotted, the unreduced MCE spectra, the base slab averaged reduced spectra, and the factor resulting from dividing the two spectra
As can be seen, considering base slab averaging can have a significant reduction in the design spectrum. The reduction factor is also plotted on the same chart where we see that base slab averaging has an affect in the short period range, however after a period of about 1.5 seconds considering base slab averaging has little effect. For structures with large base areas, over say 40,000 sf, the effect can be significant. Similar reductions are seen with structures embedded more than 10 feet below the surface.

## Slide 33: Ground Motions – Free Field
Notes: Slide shows a plot of spectral acceleration for a series of actual recorded (free field) motions and the SRSS average of the motions.
The practical effect of Kinematic SSK is that is lead to a reduction in the target response spectrum and therefore different ground motion response histories. The picture above shows the ground motion response histories that would be used to match the free-field spectra.

## Slide 34: Ground Motions – At-Depth Amp-Scaled
Notes: Slide shows a plot of the same spectral acceleration for a series of recorded motions that are scaled to represent the motion felt at depth. The SRSS average is also shown along with the scale factor representing the difference from the free field motion.
This figure shows the ground motions that would be selected to meet the site spectra that is reduced due to

## Slide 35: ASCE 41-06
Concerns / Issues
Base slab averaging reduction is unlimited at short periods
Base slab averaging equation predicts negative values at large base dimensions
Embedment & base slab averaging can reduce PGA to 0.3 second values to 0.22*Free Field
Kinematic effects greatest at short periods, but no requirement to include foundation flexibility
Notes: Slide is a bulleted list of statements regarding kinematic effects
The original provisions for KSSI were found in the ASCE 41 standard. However, there were several issues with those provisions, which in turn lead to what some believed to be unconservative reductions in response.

## Slide 36: Combined BSA & Embedment
Notes: Slide shows two plots. On the right is spectral acceleration versus period for the unreduced free-field spectrum, the base slab averaged (BSA) reduced spectrum, the embedment effects reduced spectrum, and the combined BSA-Embedment Effects reduced spectrum. On the left is a plot of the reduction factors from each of the same three factors
As can be seen, combining both kinematic effects using the theoretical equations can result in extreme reductions in spectral acceleration at short periods.

## Slide 37: Scatter on Observed Data
Notes: This slide is an image of the observed scatter for the spectral acceleration graphs shown on the previous slide
There is also significant scatter in the data that has measured the actual phenomena of base slab averaging when comparing foundation instruments to free-field instruments of buildings that have experienced earthquake shaking.

## Slide 38: Look at Existing Data – Wadsworth Hospital
Ratio between basement and free-field record (average)
ASCE 41-06 BSA + Embedment Effects
Notes: Slide is a series of images. The background image is a plot of the response spectrum modification factor for the base slab averaging & embedment effects reduction factor as defined by ASCE 41-06 and the ratio between measured free-field response for the Northridge earthquake and the measured response at the basement of the Wadsworth Veterans Affairs hospital in Los Angeles for the same ground motion. On the left are two additional images including a satellite image of the greater Los Angeles region and a street level view of the VA hospital.
In this example the reduction factor is well correlated with the measured data, up to the point where the theoretical equations predict significant reductions. There is lots of variation in the short period range, where the reduction is greatest.

## Slide 39: ASCE 41-13
Issues addressed
Require soil flexibility modeled
Provide overall kinematic limit of 50%
Temper reductions for kinematic effects
Limit base area for BSA
Update equations for BSA
Notes: Slide is a list of bulleted issues that have been addressed in ASCE 41 regarding soil structure interaction
In the 2013 update to the ASCE 41 standard a number of the issues related to kinematic interaction effects were addressed. The changes required explicit modeling of the flexibility of the foundation and subsurface media if one wanted to use KSSI, since the reductions are dependent upon period. Excluding the flexibility of the foundation and the soil can predict a shorter period and lead to a larger KSSI reduction. There was an overall reduction limit of 50% placed on the KSSI theoretical equations. Further, a factor was applied to temper the reduction to approximately one standard deviation from the mean. Lastly, limits on the maximum base area were applied and an updated base slab averaging reduction equation was proposed.

## Slide 40: Kinematic Soil-Structure Interaction
Chart: 
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.2 | 1.4 | 1.6 | 1.8 | 2 | 3 | 4
 | 0.4 | 1 | 1 | 1 | 1 | 1 | 1 | 0.85714 | 0.75 | 0.66667 | 0.6 | 0.5 | 0.42857 | 0.375 | 0.33333 | 0.3 | 0.2 | 0.15
 | 0.10374 | 0.25934 | 0.25934 | 0.52946 | 0.66903 | 0.74984 | 0.80138 | 0.71714 | 0.64659 | 0.58749 | 0.53763 | 0.45871 | 0.39942 | 0.35342 | 0.31678 | 0.28693 | 0.19473 | 0.14723
 | 0.2 | 0.5 | 0.5 | 0.66184 | 0.78068 | 0.84413 | 0.88493 | 0.78183 | 0.69823 | 0.62965 | 0.57266 | 0.4839 | 0.41833 | 0.36809 | 0.32846 | 0.29643 | 0.19893 | 0.14955
41-06
41-13
Notes: Slide is a spectral acceleration plot comparing three spectra; the fixed base condition, and the condition considering SSI under the parameters for ASCE 41-06 (which is lower by ~0.1g for virtually the entire period range) and ASCE 41-13 (which is higher by about 0.2 – 0.5 g) for virtually all period ranges.
The result of the ASCE 41-13 changes are lower reductions due to KSSI, but the reductions can still be significant.

## Slide 41: Kinematic Interaction
Base Slab Averaging & Embedment Equations Updated
Base area limited based on testing limits, 260 feet.
0.75 factor reduces the reduction
Max reduction can only be 50%
Notes: Slide is a summary of equations for reductions due to base slab averaging and embedment effects. The maximum reduction is 50%.
The equations for base slab averaging and embedment effects are shown here. The BSA reduction can be represented by a Bessel function with the main parameter for BSA is the average base dimension, which is the square root of the base area. That parameter is limited to 260 feet, which is the upper-bound of the structures that were studied to validate the theoretical equations. For embedment, the main parameters are the soil stiffness and the embedment. In both equations a 0.75 factor is placed on the reduction to temper them to approximately one standard deviation as a means of acknowledging the scatter in the data.

## Slide 42: ASCE 7-16 Kinematic Interaction
Only can be used with nonlinear response history
Limited to 20% reduction from site specific
Limited to 30% reduction from USGS spectra
2015 NEHRP allowed to 40% with peer review
  40% eliminated in ASCE 7-16
Must model soil flexibility
Notes: Slide is a series of statements regarding the reductions allowed for kinematic interactions
The Provisions and ASCE 7-16 adopt the ASCE 41-13 provisions with some additional limitations. The most significant limitation is the requirement that kinematic interaction only be used with nonlinear procedures. That is because there has not been sufficient study to correlate kinematic interaction effects with yielding in the structure and there was concern of double-counting reductions. The other modifications were to temper the maximum reduction from kinematic interaction.

## Slide 43: Kinematic Interaction - Example
Chart: RISK TARGEDTED MCE AND KINEMATIC INTERACTION MODIFIED SPECTRUM
| 0.01 | 0.05 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.25 | 1.5 | 1.75 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5
Sa_MCE | 0.7307 | 0.85 | 1.1 | 1.35 | 1.5 | 1.513 | 1.522 | 1.539 | 1.517 | 1.5 | 1.5 | 1.5 | 1.2857 | 1.206 | 1.132 | 1.069 | 0.9104 | 0.7913 | 0.6886 | 0.6117 | 0.4994 | 0.4185 | 0.357 | 0.3104 | 0.2756 | 0.2477
Sa_MCE (SSI 7-16) | 0.58456 | 0.68 | 0.88 | 1.08 | 1.2 | 1.2104 | 1.2176 | 1.2866 | 1.3238 | 1.3476 | 1.3757 | 1.4129 | 1.2306 | 1.1662 | 1.1024 | 1.0464 | 0.89802 | 0.78382 | 0.68381 | 0.60844 | 0.4977 | 0.41751 | 0.35638 | 0.30999 | 0.27531 | 0.24749
Sa_MCE (2015 NEHRP) | 0.43842 | 0.51 | 0.66 | 0.81 | 0.9 | 1.0533 | 1.1894 | 1.2866 | 1.3238 | 1.3476 | 1.3757 | 1.4129 | 1.2306 | 1.1662 | 1.1024 | 1.0464 | 0.89802 | 0.78382 | 0.68381 | 0.60844 | 0.4977 | 0.41751 | 0.35638 | 0.30999 | 0.27531 | 0.24749
Notes: Slide shows a graph of the site specific response spectrum compared to the kinematic interaction modified spectrum per the Standard and the NEHRP Provisions assuming there is Peer Review.
The kinematic interaction modified spectrum per the Provisions and ASCE 7-16 still shows significant reductions in spectral accelerations at short periods. The dashed blue line shows the additional reduction that can be achieved per the NEHRP Provisions when Peer Review is provided. This additional reduction was not adopted by the standard.

## Slide 44: Kinematic Interaction - Example
Chart: Displacement
| 4.17 | 3.15 | 2.13 | 1.1399999999999999 | 0.23 | 0.158
Sa_MCER | 67 | 54 | 41 | 28 | 13 | 0
Sa_MCE (SSI 7-16) | 67 | 54 | 41 | 28 | 13 | 0
Sa_MCE (2015 NEHRP) | 67 | 54 | 41 | 28 | 13 | 0
Notes: Slide shows a graph of the building displacements calculated using response history analysis and compares those computed with the site specific response spectrum and the kinematic interaction modified spectrum per the Standard and per the NEHRP Provisions with Peer Review.
As can be seen, accounting for the kinematic interactions in the non linear analysis results in a considerable reduction in story displacement. It should also be noted that the story displacements calculated per the NEHRP Provisions with Peer Review are slightly larger than those calculated per the Standard with the cap on the maximum reduction at the lower periods of the modified spectra. This is because the larger reduction in the 2nd mode modified spectrum ordinate lessens the contribution of that modes effect on the structure. Since the second mode acts to reduce some of the fundamental modes response, this modal interaction is lessened, and the global structure response is increased.

## Slide 45: Kinematic Interaction - Example
Chart: Story Drift Ratio
| 6.5384615384615381E-3 | 6.5384615384615381E-3 | 6.346153846153846E-3 | 5.0555555555555553E-3 | 4.6153846153846158E-4 | 0
Sa_MCER | 67 | 54 | 41 | 28 | 13 | 0
Sa_MCE (SSI 7-16) | 67 | 54 | 41 | 28 | 13 | 0
Sa_MCE (2015 NEHRP) | 67 | 54 | 41 | 28 | 13 | 0
Notes: Slide shows a graph of the building displacements calculated using response history analysis and compares those computed with the site specific response spectrum and the kinematic interaction modified spectrum per the Standard and per the NEHRP Provisions with Peer Review.
As can be seen, accounting for the kinematic interactions in the non linear analysis results in a considerable reduction in story displacement. It should also be noted that the story displacements calculated per the NEHRP Provisions with Peer Review are slightly larger than those calculated per the Standard with the cap on the maximum reduction at the lower periods of the modified spectra. This is because the larger reduction in the 2nd mode modified spectrum ordinate lessens the contribution of that modes effect on the structure. Since the second mode acts to reduce some of the fundamental modes response, this modal interaction is lessened, and the global structure response is increased.

## Slide 46: ASCE 7-16 / 2015 NEHRP Provisions Chapter 19: Soil-Structure Interaction
Robert Pekelnicky, PE, SE
Principal, Degenkolb Engineers
March 16, 2015

## Slide 47: DISCLAIMER
NOTICE: Any opinions, findings, conclusions, or recommendations expressed in this publication do not necessarily reflect the views of the Federal Emergency Management Agency. Additionally, neither FEMA nor any of its employees make any warranty, expressed or implied, nor assume any legal liability or responsibility for the accuracy, completeness, or usefulness of any information, product or process included in this publication.
The opinions expressed herein regarding the requirements of the NEHRP Recommended Seismic Provisions, the referenced standards, and the building codes are not to be used for design purposes. Rather the user should consult the jurisdiction’s building official who has the authority to render interpretation of the code.
Any modifications made to the file represent the presenters' opinion only.