## Slide 1: Soil-Structure Interaction Design Examples
Disclaimer
Robert Pekelnicky, P.E., S.E.,
Insung Kim, P.E., S.E.
8
Notes: Title slide, includes an image of the cover of the data disk containing the 2015 NEHRP Recommended Seismic Provisions, and the name of the author of the 2015 Design Provisions Examples.

## Slide 2: Design Example
Instructional Material Complementing FEMA 1051, Design Examples
Soil-Structure Interaction
Structure
  4 Stories (53 ft tall)
  Reinforced concrete shear wall system
  One Basement level (15 ft below grade) w/ concrete walls
  RC flat plate slabs with rectangular cast-in-place concrete
Site Conditions
  Within 5 miles of active fault
  Site Class = D
  Vs100 = 800 ft/s
  SDS = 1.0, SD1 = 0.71
  Seismic Design Category = E
Notes: Slide is a list of bullets describing the basic information for the example building

## Slide 3: Spectral Acceleration
Soil-Structure Interaction
Chart: Period, T (sec)
| 0 | 0.05 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.25 | 1.5 | 1.75 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5
Sa_MCER_(MaxDir) | 0.7307 | 0.85 | 1.1 | 1.35 | 1.5 | 1.513 | 1.522 | 1.539 | 1.517 | 1.5 | 1.5 | 1.5 | 1.2857 | 1.206 | 1.132 | 1.069 | 0.9104 | 0.7913 | 0.6886 | 0.6117 | 0.4994 | 0.4185 | 0.357 | 0.3104 | 0.2756 | 0.2477
Sa_DE_(MaxDir) | 0.48713 | 0.56667 | 0.73333 | 0.9 | 1 | 1.0087 | 1.0147 | 1.026 | 1.0113 | 1 | 1 | 1 | 0.85714 | 0.804 | 0.75467 | 0.71267 | 0.60693 | 0.52753 | 0.45907 | 0.4078 | 0.33293 | 0.279 | 0.238 | 0.20693 | 0.18373 | 0.16513
Notes: Slide is an image of a response spectrum showing the maximum considered earthquake (MCE) and design level earthquake (DE) for the building
Structure is located in a region of relatively high seismicity

## Slide 4: Building Elevation
Soil-Structure Interaction
Notes: Slide is an image of the building elevation, it has 5 bays in the direction shown

## Slide 5: Building Plan & Floor Weights
Soil-Structure Interaction
Story | Weight
Fourth | 4,000 kips
Third | 4,100 kips
Second | 4,100 kips
First | 4,400 kips
Basement | 4,700 kips
Total | 21,200 kips
Total w/o Basement | 16,500 kips
Notes: Slide is an image of the foundation plan. It is 150 ft x 180 ft. The columns and interior walls are supported by reinforced concrete footings, and the perimeter wall is supported by a continuous strip footing
Building is 150 ft x 180 ft. The columns and interior walls are supported by reinforced concrete footings, and the perimeter wall is supported by a continuous strip footing

## Slide 6: Fixed Base Design - General
Soil-Structure Interaction
Foundation pinned against vertical and lateral translation
Wall footings fixed for rotation
Base of building at 1st floor
  Common in practice
  Full building period must be less than 1.1 x period of upper portion alone
    Example → Ttotal = 1.3 x Tupper
Notes: Slide is a description of the fixed base model on the left, and an image of the building model on the right
Foundation was considered to be pinned and the footings were fixed against rotation. The ground floor of the building model was considered to be at the first level instead of the basement level which is allowed per §12.2.3.2 but the period of the full building must be less than 10% greater than the period of the upper portion alone.

## Slide 7: Fixed Base Design
Soil-Structure Interaction
Model 1st floor as stiff or rigid?
Modal Analysis
T1 = 0.5 sec
V = 2,700 kips
Scale Factor = 1.2
Linear Procedures
Ta = 0.39 sec (w/ basement)
Ta = 0.27 sec (w/o basement)
Cs = 0.2
V = CsW = 3,300 kips
Notes: slide is a list of bullets summarizing the first mode period and base shear between a fixed base model using linear static procedures (on the left) and a fixed base model using a modal analysis (on the right).
The results of the modal analysis must be scaled up so that the base shear for the modal analysis is equal to that obtained using linear static procedures.
Modelling the 1st floor as rigid would overestimate the forces transferring out of the vertical shear walls at the first floor and into the basement walls. This would reduce the overturning demand at the base of the shear walls and the footings they are supported on. For this reason the firs floor was modelled as “stiff” instead of rigid and partially contributed to the greater than 10% difference in first mode period between the “no basement” model and the “basement included” model.

## Slide 8: Fixed Base Design
Soil-Structure Interaction
Notes: Slide is two images illustrating the design of one shear wall in the building. In the upper left, a plan view of the building layout is shown with the wall under consideration shown. Below is a section view of the wall showing its size, reinforcement, boundary elements, and the footing it is supported by.

## Slide 9: Flexible Base Design
Soil-Structure Interaction
Vertical Stiffness under Footings | 3.4 (kip/in)/ft2
Horizontal Stiffness under Base | 14 (kip/in)/ft2
Horizontal Stiffness under/against basement wall | 14 (kip/in)/ft2
Spring Properties for:
  Footings, passive soil pressure, basement walls, shearing between soil and building base
Spring properties bounded by ± 50%
T1 = 0.49 sec
  T1,upper = 0.49 sec
  T1,lower = 0.5 sec
Notes: On the left is a list of the elements that were modelled as springs for the flexible base model, a statement regarding how the spring properties were bounded for analysis, and the first mode period results of the model with a flexible base. On the right is a simplified SDOF model with a flexible base showing horizontal and vertical springs at the base, with a table of the spring properties used below.
To consider the flexibility if the base, springs were used to model the footings, passive soil pressure, basement walls, and shearing between soil and building base. Vertical point springs were placed under the columns, and vertical distributed springs were modelled under the walls, and the horizontal springs were applied as area springs over the basement wall shell elements.

## Slide 10: Spectral Acceleration
Soil-Structure Interaction
Chart: Period, T (sec)
| 0 | 0.05 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.25 | 1.5 | 1.75 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5
Sa_MCER_(MaxDir) | 0.7307 | 0.85 | 1.1 | 1.35 | 1.5 | 1.513 | 1.522 | 1.539 | 1.517 | 1.5 | 1.5 | 1.5 | 1.2857 | 1.206 | 1.132 | 1.069 | 0.9104 | 0.7913 | 0.6886 | 0.6117 | 0.4994 | 0.4185 | 0.357 | 0.3104 | 0.2756 | 0.2477
Sa_DE_(MaxDir) | 0.48713 | 0.56667 | 0.73333 | 0.9 | 1 | 1.0087 | 1.0147 | 1.026 | 1.0113 | 1 | 1 | 1 | 0.85714 | 0.804 | 0.75467 | 0.71267 | 0.60693 | 0.52753 | 0.45907 | 0.4078 | 0.33293 | 0.279 | 0.238 | 0.20693 | 0.18373 | 0.16513
Fixed Base
Notes: Slide is the spectral acceleration plot for this site with vertical lines for the fixed base model and the flexible base model
As seen here, the increase in period does not affect this design because both models land on the peak of the spectrum, however, it is easy to see that a site with a spectrum can see that the flexible base period can land on the descending branch of the spectrum.

## Slide 11: Flexible Base Effects
Soil-Structure Interaction
Lack of consideration for foundation actions
  Bending/shear failure in footing
  Bearing failure of underlying soil
  Flexural yielding of wall
CBC requires foundation design for Em forces
  State owned buildings
  School/Hospitals
  Example → Increased foundation thickness & reinforcement
Inclusion of non-linear foundation elements
Soil and Foundation Yielding
Notes: Slide is a series of bullets regarding soil and foundation yielding
Current practice to design the foundation for the forces determined from analysis without considering the foundation and soil as a potential yielding element in the system. No additional requirements to ensure that flexural/shear failure does not occur in the foundation before yielding of the soil or structural elements as they are designed to do.
Exception is the California Building Code (CBC) which requires the foundations be designed for the amplified seismic load, Em, if it is a state owned building, a school or a hospital. In this example, that requirement would lead to an increased foundation thickness and additional reinforcement.
In a nonlinear analysis, foundation actions can be modeled as explicit nonlinear actions to capture yielding at the soil-foundation interface or those actions must be treated as force-controlled actions

## Slide 12: Flexible Base Effects
Soil-Structure Interaction
Foundation damping → Increased overall damping
Shallow foundations only
  Spread/strip footings
  Mat foundation
Most pronounced for stiff structures on flexible soils
  , Period Lengthening
Stiff/rigid floor diaphragm
Foundation Damping
Notes: On the right is an isometric sketch of a mat foundation with a coordinate system and dimensions defining it. On the left is a series of statements regarding general foundation damping concepts
Typically max acceleration is determined assuming 5% inherent damping, by considering the additional effects of foundation damping, the overall damping ratio can be significantly higher therefore reducing the spectral acceleration. At this time, foundation damping is only applicable to shallow foundations because of how the equations were derived.
Foundation damping has the greatest effect when a stiff building is on a site with soft soil. In this cases the ratio of the rigid base period to the flexible base period (period lengthening) is much higher

## Slide 13: Flexible Base Effects
Soil-Structure Interaction
βs
Soil Damping:
Radiation Damping:
Foundation Damping:
β
Structural Damping:
Overall Damping:
Foundation Damping
Notes: Slide is a list of equations for overall damping, foundation damping, and radiation damping. The variables for structural damping and soils damping are also listed
The overall damping ratio is a combination of foundation damping and structural damping. Foundation damping is comprised of soil damping and radiation damping.

## Slide 14: Flexible Base Effects
Soil-Structure Interaction
B | ½ Shorter Foundation Dimension | 75 ft
L | ½ Longer Foundation Dimension | 90 ft
T | Fixed Base Period | 0.39 sec
 | Flexible Base Period | 0.49 sec
vs | Effective shear wave velocity | 570 ft/s
G | Shear modulus over depth equal B | 1,200 k/ft2
ν | Poisson’s ratio of soil | 0.3
M* | Fundamental modal effective mass | 14,500 kips
h* | Effective structure height at fundamental mode = h / (Γϕroof) | 41.5 ft
B | ½ Shorter Foundation Dimension | 75 ft
L | ½ Longer Foundation Dimension | 90 ft
T | Fixed Base Period | 0.39 sec
 | Flexible Base Period | 0.49 sec
vs | Effective shear wave velocity | 570 ft/s
G | Shear modulus over depth equal B | 1,200 k/ft2
ν | Poisson’s ratio of soil | 0.3
M* | Fundamental modal effective mass | 14,500 kips
h* | Effective structure height at fundamental mode = h / (Γϕroof) | 41.5 ft
Foundation Damping
Notes: Slide is a table defining variables used in the foundation damping equations and listing their value for this design example

## Slide 15: Flexible Base Effects
Soil-Structure Interaction
Rotational Radiation Damping, βxx
Translational Radiation Damping, βy
Original Condition
Energy radiating away from the foundation in the form of stress waves due to the foundation’s lateral movement and rocking
Radiation Damping
Notes: Slide further defines radiation damping as the energy that is radiating away from the foundation in the form of stress waves resulting from the translational and rotational movement of the foundation. The equation is repeated in the upper left and three pictures in the middle depict the original soil deposit, the soil deposit with an embedded foundation element translating with energy waves emanating away, and the soil deposit wit an embedded foundation element rotating with energy waves emanating away.
Radiation damping is the result of energy radiating away from the foundation in the form of stress waves due to the translational and rotational movement of the foundation. The two components of radiation damping are pictorially represented by a soil deposit with an embedded foundation element translating with energy waves emanating away, and the soil deposit wit an embedded foundation element rotating with energy waves emanating away.

## Slide 16: Flexible Base Effects
Soil-Structure Interaction
Translational Damping Ratio,
Dimensionless Frequency,
Translational Stiffness,
Fictitious Period,
Translational Contribution
Radiation Damping
Notes: Slide solves a series of equations using values from the example building to determine the radiation damping ratio from translation.

## Slide 17: Flexible Base Effects
Soil-Structure Interaction
Radiation Damping Ratio
0.34
Rotational Damping Ratio,
and 0.68
Dimensionless frequency a0 and Dynamic stiffness modifier αxx,
Rotational Stiffness,
Fictitious Period,
Rotational Contribution
Radiation Damping
Notes: Slide solves a series of equations using values from the example building to determine the radiation damping ratio from rotation. The total radiation damping ratio is also solved by combining the translational and rotational contributors.
In this example, radiation damping alone is 11% which is a significant increase over the standard 5% structural damping.

## Slide 18: Flexible Base Effects
Soil-Structure Interaction
 | Effective Peak Acceleration, SDS /2.51 |  |  | 
Site Class | SDS /2.5 = 0 | SDS /2.5 = 0.1 | SDS /2.5 = 0.4 | SDS /2.5 = 0.8
A | 0.01 | 0.01 | 0.01 | 0.01
B | 0.01 | 0.01 | 0.01 | 0.02
C | 0.01 | 0.01 | 0.03 | 0.05
D | 0.01 | 0.02 | 0.07 | 0.15
E | 0.01 | 0.05 | 0.20 | *
F | * | * | * | *
Soil Damping
Notes: Slide is a table of soil damping (Beta-s) values based on effective peak acceleration and site class
Table of estimated soil damping (Beta-s) values based on effective peak acceleration and site class. For this design example, the building is on Site Class D and SDS = 1.0, therefore SDS/2.5 = 0.4

## Slide 19: Foundation-Structure Damping
Soil-Structure Interaction
Overall system damping ratio dependent on effective period ratio
=
Total Foundation Damping:
Notes: This slide has a series of evaluated equations for foundation damping, effective period ratio, and overall soil-structure system damping.
The foundation damping is combined with a factored structure damping ratio based on the effective period ratio to determine the effective damping ratio of the system. This effective period ratio incorporates a parameter representing the amount of structural yielding that is happening in the structure, μ. This value should be determined by dividing the maximum base shear by the elastic base shear, but can be approximated as R/Ω to avoid doing a non-linear analysis.

## Slide 20: Foundation-Structure Damping
Soil-Structure Interaction
weight in fundamental mode
Therefore spectral response parameters based off 16% critical damping.
  Ideal is for geotechnical engineer to develop site specific spectra
  Standard provides equation to account for increase in assumed damping
Notes: This slide has a series of evaluated equations to compute the reduction in base shear with the increase in assumed damping using the total soil-structure system damping ratio .
Using the total effective damping ratio of the soil-structure system = 0.16, the reduction in base shear is estimated using equations provided by the Standard. Ideally, however, a site specific response spectrum would be developed by a geotechnical engineer. Once the reduced base shear is calculated, it is compared against the maximum permissible reduction allowed. The maximum reduction governs and the SSI modified seismic base shear is 0.17W = 2,700 kips, an 18% reduction in design forces.

## Slide 21: Foundation-Structure Damping
Soil-Structure Interaction
Chart: DESIGN EARTHQUAKE RESPONSE SPECTRUM AND SSI MODIFIED SPECTRUM
| 0 | 0.05 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.25 | 1.5 | 1.75 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5
Sa_DE_(MaxDir) | 0.48713 | 0.56667 | 0.73333 | 0.9 | 1 | 1.0087 | 1.0147 | 1.026 | 1.0113 | 1 | 1 | 1 | 0.85714 | 0.804 | 0.75467 | 0.71267 | 0.60693 | 0.52753 | 0.45907 | 0.4078 | 0.33293 | 0.279 | 0.238 | 0.20693 | 0.18373 | 0.16513
Sa_DE_(SSI) | 0.48713 | 0.53904 | 0.59746 | 0.64286 | 0.71429 | 0.72048 | 0.72476 | 0.73286 | 0.72238 | 0.71429 | 0.71429 | 0.71428 | 0.61224 | 0.57429 | 0.53905 | 0.50905 | 0.43352 | 0.37681 | 0.3279 | 0.29129 | 0.23781 | 0.19929 | 0.17 | 0.14781 | 0.13124 | 0.11795
Notes: This slide shows a graphic comparison between the design earthquake response spectrum and the soil-structure interaction modified response spectrum.
The graphic demonstrates the significant reduction to the design earthquake response spectrum when modified to account for the increased damping of the total soil-structure system.

## Slide 22: Foundation-Structure Damping
Soil-Structure Interaction
For nonlinear procedures the foundation damping in a nonlinear response history analysis is significantly more complex than linear procedures as the reductions used for the response spectrum cannot be used to modify the target spectra that the ground motions are scaled to.
Nonlinear spring and dashpot elements need to be modeled to directly capture the force-displacement relationship and damping at the soil-foundation interface.
 See NIST GCR 12-917-21 for guidance on developing dashpots to model foundation damping.
Notes: Slide is a all text summarizing how to model foundation damping for nonlinear response history analysis.
The previous equations used to account the reduction in design forces due to SSI can only be used for linear procedures. For nonlinear response history analysis nonlinear spring and dashpot elements need to be created in the model to capture the force-displacement relationships directly at the soil-foundation interface. The NIST GCR 12-917-21 document provides guidance on how to develop dashpots for the above.

## Slide 23: Kinematic Interaction
Soil-Structure Interaction
FOUNDATION LENGTH
FOUNDATION WIDTH
FONDATION SIZE (LENGTH X WIDTH) AFFECT FOUNDATION INPUT MOTION
FOUNDATION DEPTH AFFECT FOUNDATION INPUT MOTION
Accounts for differences in free-field ground motions and foundation input motion
  Affected by foundation size, base slab averaging, and foundation depth, embedment.
Notes: Slide provides high level explanation of kinematic interaction. Includes example building elevation and foundation plan to highlight that foundation size and depth are two factors that most strongly influence kinematic soil structure interaction.
Kinematic soil structure interaction considers the differences observed between free-field condition ground motions, used to create the USGS seismic parameters, and the foundation input motions. The main cause of the difference between them being the size of the foundation, where the ground motion input is more likely to be different a two different points of the building for larger foundations, and foundation depth, where there may be lower accelerations are higher frequency than at the surface. These two types of kinematic interaction are called 1. Base Slab Averaging, and 2. Embedment.

## Slide 24: Kinematic Interaction
Soil-Structure Interaction
Standard account for both types kinematic interactions using theoretical models that adjust the response spectrum parameters based off:
  Base size,
  Base embedment depth,
  Site class,
  Fundamental period of soil-structure system
Adjustment factors for both types are cumulative
For a more thorough discussion refer to FEMA 440 and NIST GCR 12-917-21
Notes: Slide provides text describing how Standard accounts for both kinematic interaction types.
The Standard accounts for both base slab averaging and embedment depth using theoretical models that adjust the response spectrum parameters based on the base size, embedment depth, site class, and fundamental period of the soil-structure system. The adjustment factors are cumulative and result in a reduction of the response spectrum parameters, but the reduction is limited. For additional information refer to FEMA440 and NIST GCR 12-917-21.

## Slide 25: Kinematic Interaction - Limits
Soil-Structure Interaction
Maximum reduction in Standard
Modified response spectrum ≥ 80% of site specific response spectrum or ≥ 70% of the general response spectrum.
NEHRP Provisions wave these limits where this is Peer Review
Kinematic interaction provisions cannot be used with a simple elastic linear analysis per Chapter 12. However, the Section 16.1 of the Standard requires a verification of forces per Chapter 12. For these forces, the reductions due to Kinematic Interaction can be applied.
Notes: Slide provides text describing how Standard limits use kinematic interaction procedures, and limits the reductions to the response spectrum.
The Standard and NEHRP Provisions both limit the reduction to the response spectrum when accounting for kinematic interaction effects to at least 80% of the site specific response spectrum, or 70% of the general response spectrum using the USGS mapped values. However, in the NEHRP Provisions there is a caveat that these limits may be waved in the case that there is a Peer Review conducted.
Additionally, when the response spectrum parameters are reduced the kinematic interaction provisions can only be used in a nonlinear analysis to reduce the target response spectrum. This is for two reasons, one, the kinematic interaction provisions are highly dependent on the period of the building, and since most buildings designed by the Standard will experience yielding in the superstructure and potentially also in the foundation/soil interface, the period of the entire soil-structure system will lengthen. Therefore, if the elastic period is used to determine the reduction in response due to kinematic effects, it is likely that the reduction would be overestimated as the reductions decrease at longer periods. Additionally, there is presently not enough research to understand the cumulative reduction in response when considering structural yielding, soil or foundation yielding, and kinematic interaction to understand the appropriate reduction for all these effects combined. However, Section 16.1 of the Standard will require minimum structural capacities per an elastic linear analysis per Chapter 12. For these calculations, the base-slab averaging and embedment force reductions may be applied cumulatively to the design Base Shear.

## Slide 26: Kinematic Interaction -
Soil-Structure Interaction
:
Base-Slab Averaging
Applicable only to Site Classes C, D, and E.
Applicable only when base slab or mat or 1st floor is rigid
Notes: Slide details where base-slab averaging kinematic interaction can be used, and details equations to calculate reduction in target response spectrum using base slab averaging. Base-slab averaging reduction to response spectrum ordinate is then calculated.
Base-slab averaging may reduce the foundation input accelerations because there can be a phase shift in the ground-motions at different points in the structure. This phase shift filters out much of the high frequency motion and reduces the response spectrum ordinates at short periods. These reductions are only applicable for Site Classes C, D, and E. This is because the very little reductions have been observed in rocky soils typical of Site Classes A and B, and because the significant nonlinearity typical to Site Class F is beyond the current state of research.
The reduction to the response spectrum ordinate is provided in the equations shown, as can be seen the reduction is 0.98 at the fundamental mode of 0.49 seconds. This reduction increases to 0.82 at the second mode of 0.11 seconds after being capped at the 0.20 seconds.

## Slide 27: Kinematic Interaction -
Soil-Structure Interaction
For the elastic analysis required by Section 16.1 the reduction in force effects can be determined by combine base-shear averaging and depth reductions:
Embedment depth
Standard limits embedment depth to 20 feet.
Standard requires at least 75% of foundation footprint to be at considered embedment depth.
At sloping sites, uses shallowest depth.
Notes: Slide explains where embedment depth kinematic interaction reductions can be used, and details equations to calculate reduction in target response spectrum using base slab averaging. Embedment depth reduction to response spectrum ordinate is then calculated.
Embedment depth affects the foundation input motion, primarily, there is a lower acceleration at high frequencies. The maximum embedment depth that can be used is 20 feet because the reduction has not been verified at greater depths. Additionally, a minimum of 75% of the foundation footprint must be at the embedment depth. This is to ensure that the majority of the structure is subject to the kinematic interaction effect. For sloping sites, the smallest embedment should be used.
The reduction to the response spectrum ordinate is provided in the equations shown, as can be seen the reduction is 0.93 at the fundamental mode of 0.49 seconds. This reduction increases to 0.61 at the second mode of 0.11 seconds after being capped at the 0.20 seconds.
For the elastic analysis of Chapter 12 required by Section 16.1 the reduction in force effects can be determined by combine base-shear averaging and depth reductions as shown.

## Slide 28: Kinematic Interaction - Example
Soil-Structure Interaction
Chart: RISK TARGEDTED MCE AND KINEMATIC INTERACTION MODIFIED SPECTRUM
| 0.01 | 0.05 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.25 | 1.5 | 1.75 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5
Sa_MCE | 0.7307 | 0.85 | 1.1 | 1.35 | 1.5 | 1.513 | 1.522 | 1.539 | 1.517 | 1.5 | 1.5 | 1.5 | 1.2857 | 1.206 | 1.132 | 1.069 | 0.9104 | 0.7913 | 0.6886 | 0.6117 | 0.4994 | 0.4185 | 0.357 | 0.3104 | 0.2756 | 0.2477
Sa_MCE (SSI 7-16) | 0.58456 | 0.68 | 0.88 | 1.08 | 1.2 | 1.2104 | 1.2176 | 1.2866 | 1.3238 | 1.3476 | 1.3757 | 1.4129 | 1.2306 | 1.1662 | 1.1024 | 1.0464 | 0.89802 | 0.78382 | 0.68381 | 0.60844 | 0.4977 | 0.41751 | 0.35638 | 0.30999 | 0.27531 | 0.24749
Sa_MCE (2015 NEHRP) | 0.43842 | 0.51 | 0.66 | 0.81 | 0.9 | 1.0533 | 1.1894 | 1.2866 | 1.3238 | 1.3476 | 1.3757 | 1.4129 | 1.2306 | 1.1662 | 1.1024 | 1.0464 | 0.89802 | 0.78382 | 0.68381 | 0.60844 | 0.4977 | 0.41751 | 0.35638 | 0.30999 | 0.27531 | 0.24749
Notes: Slide shows a graph of the site specific response spectrum compared to the kinematic interaction modified spectrum per the Standard and the NEHRP Provisions assuming there is Peer Review.
The kinematic interaction modified spectrum shows significant reductions in spectral accelerations at short periods. The dashed blue line shows the additional reduction that can be achieved per the NEHRP Provisions when Peer Review is provided. This additional reduction was not adopted by the standard.

## Slide 29: Kinematic Interaction - Example
Soil-Structure Interaction
Chart: Displacement
| 4.17 | 3.15 | 2.13 | 1.1399999999999999 | 0.23 | 0.158
Sa_MCER | 67 | 54 | 41 | 28 | 13 | 0
Sa_MCE (SSI 7-16) | 67 | 54 | 41 | 28 | 13 | 0
Sa_MCE (2015 NEHRP) | 67 | 54 | 41 | 28 | 13 | 0
Notes: Slide shows a graph of the building displacements calculated using response history analysis and compares those computed with the site specific response spectrum and the kinematic interaction modified spectrum per the Standard and per the NEHRP Provisions with Peer Review.
As can be seen, accounting for the kinematic interactions in the non linear analysis results in a considerable reduction in story displacement. It should also be noted that the story displacements calculated per the NEHRP Provisions with Peer Review are slightly larger than those calculated per the Standard with the cap on the maximum reduction at the lower periods of the modified spectra. This is because the larger reduction in the 2nd mode modified spectrum ordinate lessens the contribution of that modes effect on the structure. Since the second mode acts to reduce some of the fundamental modes response, this modal interaction is lessened, and the global structure response is increased.

## Slide 30: Kinematic Interaction - Example
Soil-Structure Interaction
Chart: Story Drift Ratio
| 6.5384615384615381E-3 | 6.5384615384615381E-3 | 6.346153846153846E-3 | 5.0555555555555553E-3 | 4.6153846153846158E-4 | 0
Sa_MCER | 67 | 54 | 41 | 28 | 13 | 0
Sa_MCE (SSI 7-16) | 67 | 54 | 41 | 28 | 13 | 0
Sa_MCE (2015 NEHRP) | 67 | 54 | 41 | 28 | 13 | 0
Notes: Slide shows a graph of the building story drift ratio calculated using response history analysis and compares those computed with the site specific response spectrum and the kinematic interaction modified spectrum per the Standard and per the NEHRP Provisions with Peer Review.
As can be seen, accounting for the kinematic interactions in the non linear analysis results in a considerable reduction in story drift ratio.

## Slide 31: ASCE 7-16 / 2015 NEHRP Provisions Chapter 19: Soil-Structure Interaction
Soil-Structure Interaction
Robert Pekelnicky, PE, SE
Principal, Degenkolb Engineers
March 16, 2015

## Slide 32: DISCLAIMER
NOTICE: Any opinions, findings, conclusions, or recommendations expressed in this publication do not necessarily reflect the views of the Federal Emergency Management Agency. Additionally, neither FEMA nor any of its employees make any warranty, expressed or implied, nor assume any legal liability or responsibility for the accuracy, completeness, or usefulness of any information, product or process included in this publication.
The opinions expressed herein regarding the requirements of the NEHRP Recommended Seismic Provisions, the referenced standards, and the building codes are not to be used for design purposes. Rather the user should consult the jurisdiction’s building official who has the authority to render interpretation of the code.
Any modifications made to the file represent the presenters' opinion only.