## Slide 1
Disclaimer
Instructional Slides developed by S. K. Ghosh, PhD,
Notes: Title slide
The presentation will cover examples of application of the provisions for earthquake design to precast concrete systems.

## Slide 2: Precast Concrete Design
Seismic design of precast concrete using the NEHRP Recommended Provisions
Review of design examples to illustrate the application of the provisions
Notes: Overview slide:
Scope of the chapter: This chapter illustrates the seismic design of precast concrete members using the NEHRP Recommended Provisions (referred to herein as the Provisions) for buildings in several different seismic design categories.
Scope of the presentation: The presentation does not repeat the text that describes provisions or procedures, but instead is focused on design examples which illustrate these points through the applications of those provisions.

## Slide 3: Some Terms used in this Presentation
Standard – 2016 Edition of ASCE 7
Provisions – 2015 NEHRP Provisions
ACI 318 – 2014 Edition of ACI 318
Notes: This slide introduces the abbreviated versions of the different reference documents that will be used throughout the presentation.

## Slide 4: Requirements for Precast Concrete Systems
Precast seismic systems used in structures assigned to Seismic Design Category C must be intermediate or special moment frames, or intermediate precast or special structural walls.
Precast seismic systems used in structures assigned to Seismic Design Category D must be special moment frames, or intermediate precast (up to 40 feet) or special structural walls.
Precast seismic systems used in structures assigned to Seismic Design Category E or F must be special moment frames or special structural walls.
Prestress provided by prestressing steel resisting earthquake-induced flexural and axial loads in frame members must be limited to 700 psi or f’c/6 in plastic hinge regions.
Notes: Introduction slide 1: three slides cover the introduction of the chapter
In the introduction, a brief summary of the requirements for precast concrete systems from the provisions is presented to set the context for the following design examples. The first introductory slide describes the precast concrete systems that must be used in increasingly severe seismic design categories. The terminology in the provisions now characterizes relative seismic risk using seismic design categories instead of seismic zones or the ACI terminology of low, moderate and high seismic risk. The system descriptions link the ACI 318 provision detailing requirements to the level of seismic risk.
This introductory slide also introduces limitations imposed on the level of average effective prestressing stress for precast concrete systems that are prestressed. The limitation is imposed because prestressing strand lacks the range of post-yield ductility of mild steel reinforcement. Flexural stress that is sufficient to cause cracking in highly prestressed concrete components may cause sudden and brittle failure.

## Slide 5: Requirements for Precast Concrete Systems
An ordinary precast structural wall is defined as one that satisfies ACI 318 Chapters 1-13, 15, 16, and 19 through 26.
An intermediate precast structural wall must meet additional requirements for its connections beyond those defined in ACI 318 Section 18.5. These are given in Section 14.2.2.4 of ASCE 7-16.
A special structural wall constructed using precast concrete must satisfy ACI 318 Section 18.10 and 18.5.2. In other words, it must meet the requirements of a special cast-in-place concrete shear wall and an intermediate precast shear wall at the same time. Special shear walls constructed using precast concrete and unbonded post-tensioning tendons and not satisfying the above requirements are permitted, provided they satisfy the requirements of ACI ITG-5.1 Acceptance Criteria for Special Unbonded Post-Tensioned Precast Structural Walls Based on Validation Testing.
Notes: Introduction slide 2: three slides cover the introduction of the chapter
The second introductory slide covers precast concrete wall requirements in the progression of severity of seismic risk.

## Slide 6: Requirements for Precast Concrete Systems: Design Examples
The example in Section 11.1 illustrates the design of untopped and topped precast concrete floor and roof diaphragms of three five-story masonry buildings
The example in Section 11.2 illustrates the design of an intermediate precast concrete shear wall building in a region of low or moderate seismicity. The precast concrete walls in this example resist the seismic forces for a three-story office building.
The example in Section 11.3 illustrates the design of a special precast concrete shear wall for a single-story industrial warehouse building.
The example in Section 11.4 is a partial example for the design of a special moment frame constructed using precast concrete per ACI 318 Section 18.9.
Notes: Introduction slide 3: three slides cover the introduction of the chapter
The third introductory slide briefly describes the examples that will be covered in the presentation. These diaphragm examples are related to content in Chapter 10 of P751 that covers the design of masonry wall buildings.

## Slide 7: 11.1 Horizontal Diaphragms
Hollow core plank floor plan for diaphragm examples
Notes: The figure shows the hollow core plank floor plan. The plan dimensions of the floor are 152 ft. x 72 ft. The interior portion of the plan includes walls spaced at 24 ft. in the transverse direction. The 40 ft. bays at either end of the plan include walls spaced at 24 ft. in the longitudinal direction.
Horizontal diaphragms examples; 1st slide shows the floor plan that is used for the example. The layout is the same used in Chapter 13, Sec. 13.2, which illustrates the design of a five-story masonry residential building.

## Slide 8: 11.1 Horizontal Diaphragms
Building Elevation
Notes: The figure shows a building elevation plan. The building is 45’-4” tall consisting of five stories, each 8’-8” high, and a 2’ high parapet.
Horizontal diaphragms examples; 2nd slide shows the elevation of the building used for the example.

## Slide 9: Horizontal Diaphragms
Structural diaphragms are horizontal or nearly horizontal elements, such as floors and roofs, that transfer seismic inertial forces to the vertical seismic force-resisting members.
Precast concrete diaphragms may be constructed using topped or untopped precast elements depending on the Seismic Design Category.
Reinforced concrete diaphragms constructed using untopped precast concrete elements are not addressed explicitly in the Standard, in the Provisions, or in ACI 318, but are not prohibited if they can be designed by Standard Sections 12.10.3 and 14.2.4, using high-deformability connector elements.
Topped precast concrete diaphragms, which act compositely or noncompositely for gravity loads, are designed using the requirements of ACI 318 Section 18.12.
Notes: Horizontal diaphragms: slide gives four basic points on precast concrete diaphragms including:
Definition
Precast construction types with or without cast-in-place concrete topping
Code criteria
The slide notes that there is an absence of specific criteria for diaphragm design without concrete topping. In fact, ACI 318 lacks direct criteria for the design of diaphragms in precast or cast-in-place concrete in regions of low or moderate seismic risk (SDC A, B or C.) The provisions for precast concrete diaphragms in ACI 318 are included in Chapter 21 only applicable to SDC D, E and F.

## Slide 10: General Design Requirement
Untopped precast diaphragms are permitted by ACI 318 only in Seismic Design Categories A through C.
Per ACI 318 Section 18.2.1.5, diaphragms in Seismic Design Categories D through F are required to meet ACI 318 Section 18.12, which does not allow untopped diaphragms.
Static rational models can be used to determine shears and moments on joints as well as shear and tension/compression forces on connections. Dynamic modeling of seismic response is not required.
A relevant publication on this topic is (Cleland and Ghosh, 2002). In the 2009 Provisions Part 3, a Resource Paper describing emerging procedures for the seismic design of topped and untopped diaphragms is included.
Notes: Horizontal diaphragms: slide gives four basic points on precast concrete diaphragms including:
Definition
Precast construction types with or without cast-in-place concrete topping
Code criteria
The slide notes that there is an absence of specific criteria for diaphragm design without concrete topping. In fact, ACI 318 lacks direct criteria for the design of diaphragms in precast or cast-in-place concrete in regions of low or moderate seismic risk (SDC A, B or C.) The provisions for precast concrete diaphragms in ACI 318 are included in Chapter 21 only applicable to SDC D, E and F.

## Slide 11: General Design Requirement
The difficulty of evaluation of precast concrete diaphragms is the jointed nature of the construction.
With hollow core slabs, mechanical connections using plate anchorage and welded plates is not practical because the components are most commonly made by an extrusion process.
Diaphragm connections in untopped floors are limited to reinforcement in joints, or in cores that are broken open so the bars can be grouted in.
When planks intersect with orthogonal orientation, as occurs in the example building layout, it may be necessary to break the top of a plank so that reinforcing with hooks can be placed and grouted in to match joints in the intersecting planks.
Notes: Horizontal diaphragms: slide gives four basic points on precast concrete diaphragms including:
Definition
Precast construction types with or without cast-in-place concrete topping
Code criteria
The slide notes that there is an absence of specific criteria for diaphragm design without concrete topping. In fact, ACI 318 lacks direct criteria for the design of diaphragms in precast or cast-in-place concrete in regions of low or moderate seismic risk (SDC A, B or C.) The provisions for precast concrete diaphragms in ACI 318 are included in Chapter 21 only applicable to SDC D, E and F.

## Slide 12: General Design Requirement
The design method used here follows Moustafa (1981 and 1982) and makes use of the shear friction provisions of ACI 318 with the friction coefficient, μ, being equal to 1.0. To use μ = 1.0, ACI 318 requires grout or concrete placed against hardened concrete that has clean, laitance-free, and intentionally roughened surfaces with a total amplitude of approximately 1/4 in. (peak to valley). Roughness for formed edges is provided either by saw tooth keys along the length of the plank or by hand-roughening with chipping hammers. Details from the PCI Hollow Core Manual are used to develop the connection details. Note that grouted joints with edges not intentionally roughened can be used with μ = 0.6.
Notes: Horizontal diaphragms: slide gives four basic points on precast concrete diaphragms including:
Definition
Precast construction types with or without cast-in-place concrete topping
Code criteria
The slide notes that there is an absence of specific criteria for diaphragm design without concrete topping. In fact, ACI 318 lacks direct criteria for the design of diaphragms in precast or cast-in-place concrete in regions of low or moderate seismic risk (SDC A, B or C.) The provisions for precast concrete diaphragms in ACI 318 are included in Chapter 21 only applicable to SDC D, E and F.

## Slide 13: General Design Requirement
For precast concrete diaphragms including chords and collectors in structures assigned to SDC C through F, Standard Section 12.10.3 defines the diaphragm seismic design force.
All other diaphragms and their chords and collectors can be designed for the seismic design forces given in Standard Sections 12.10.1 and 12.10.2 or Section 12.10.3, except that steel deck diaphragms are not permitted to be deigned by Standard Section 12.10.3.
When designing by Standard Sections 12.10.1 and 12.10.2, for SDC C through F, Standard Section 12.10.2.1 requires that collector elements, collector splices and collector connections to the vertical seismic force-resisting members be designed in accordance with Standard Section 12.4.3, which amplifies design forces by Ωo. When designing by Standard Section 12.10.3, the same forces are required to be amplified by a factor of 1.5, with three exceptions (Standard Section 12.10.3.4).
Notes: Horizontal diaphragms: slide gives four basic points on precast concrete diaphragms including:
Definition
Precast construction types with or without cast-in-place concrete topping
Code criteria
The slide notes that there is an absence of specific criteria for diaphragm design without concrete topping. In fact, ACI 318 lacks direct criteria for the design of diaphragms in precast or cast-in-place concrete in regions of low or moderate seismic risk (SDC A, B or C.) The provisions for precast concrete diaphragms in ACI 318 are included in Chapter 21 only applicable to SDC D, E and F.

## Slide 14: Untopped Diaphragm Examples
This example illustrates untopped precast floor and roof diaphragm design for five-story masonry buildings assigned to
  Seismic Design Category B
  Seismic Design Category C
Notes: First slide to introduce the design of untopped precast diaphragms using hollow core floor plank. The design is linked to the Chapter 10 masonry wall example for SDC B using Birmingham., Alabama. The use of seismic acceleration parameters for New York for SDC C differs from Chapter 10.

## Slide 15: Untopped Diaphragm Design Parameters
Notes: First slide to introduce the design of untopped precast diaphragms using hollow core floor plank. The design is linked to the Chapter 10 masonry wall example for SDC B using Birmingham., Alabama. The use of seismic acceleration parameters for New York for SDC C differs from Chapter 10.

## Slide 16: Design of Building Assigned to Seismic Design Category B

## Slide 17: Diaphragm Design Forces
The weight tributary to the roof and floor diaphragms (wpx) is the total story weight (wi) at Level i minus the weight of the walls parallel to the direction of loading.
  Roof:
    Total weight = 861 kips
    Walls parallel to force = (45 psf)(277 ft)(8.67 ft / 2) = -54 kips
    wpx = 807 kips
  Floors:
    Total weight = 963 kips
    Walls parallel to force = (45 psf)(277 ft)(8.67 ft) = -108 kips
    wpx = 855 kips
Notes: Weight used for the diaphragm design is given for floor and roof. The weight used for the design of the diaphragm does not include the weight of walls parallel to the direction of loading because the wall weight does not contribute to the inertial force in the floor. That must be collected and distributed to the walls,

## Slide 18: Diaphragm Design Forces
Since the building is assigned to SDC B, the diaphragm design forces are permitted to be determined from the provisions of Standard Sections 12.10.1 and 12.10.2, or Section 12.10.3. Both calculations are shown here for comparison purposes.
Notes: Weight used for the diaphragm design is given for floor and roof. The weight used for the design of the diaphragm does not include the weight of walls parallel to the direction of loading because the wall weight does not contribute to the inertial force in the floor. That must be collected and distributed to the walls,

## Slide 19: Diaphragm Design Forces
Standard equation 12.10-1
A. Computation of diaphragm forces in accordance with Standard Sections 12.10.1 and 12.10.2:
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 20: Diaphragm Design Forces
Table 11.1-2A SDC B Fpx Calculations |  |  |  |  |  | 
Level | wi (kips) | (kips) | Fi (kips) | (kips) | wpx (kips) | Fpx (kips)
Roof | 861 | 861 | 175 | 175 | 807 | 164
4 | 963 | 1,824 | 156 | 331 | 855 | 155
3 | 963 | 2,787 | 117 | 448 | 855 | 137
2 | 963 | 3,750 | 78 | 526 | 855 | 120
1 | 963 | 4,713 | 39 | 565 | 855 | 103
1.0 kip = 4.45 kN. |  |  |  |  |  | 
Calculations for Fpx are provided in Table 11.1-2A.
Notes: The table with the values of the calculated diaphragm forces is given for the Birmingham example.

## Slide 21: Diaphragm Design Forces
The minimum value of Fpx = 0.2SDSIewpx
= 0.2(0.21)1.0(807 kips) = 33.9 kips (roof)
= 0.2(0.21)1.0(855 kips) = 35.9 kips (floors)
The maximum value of Fpx = 0.4SDSIewpx
= 2(33.9 kips) = 67.8 kips (roof)
= 2(35.9 kips) = 71.8 kips (floors)
Note that the calculated Fpx in Table 11.1-2A is substantially larger than the specified maximum limit value of Fpx.
Notes: The slide presents the calculation of the maximum and minimum limits for diaphragm design forces. The maximum diaphragm design forces from the provisions are significantly less than calculated by Eq. 12.10-1, and these governs the design forces.

## Slide 22: Diaphragm Design Forces
To simplify the design, the diaphragm design force used for all levels will be the maximum force at any level
= 72 kips.
Notes: The slide presents the calculation of the maximum and minimum limits for diaphragm design forces. The maximum diaphragm design forces from the provisions are significantly less than calculated by Eq. 12.10-1, and these governs the design forces.

## Slide 23: Diaphragm Design Forces
B. Computation of diaphragm forces in accordance with Standard Section 12.10.3:
Step 1: Determine Rs, Diaphragm Design Force Reduction Factor (Standard Table 12.10-1)
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
Step 3: Determine Fpx, Diaphragm Design Force at Level x
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 24: Diaphragm Design Forces
Step 1: Determine Rs, Diaphragm Design Force Reduction Factor (Standard Table 12.10-1)
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 25: Diaphragm Design Forces
Step 1: Determine Rs, Diaphragm Design Force Reduction Factor (Standard Table 12.10-1)
For SDC B, the Diaphragm Seismic Demand Level is Low. So all diaphragm design options are allowed; the Basic Design Option (BDO) is chosen.
The issue of connector deformability is moot, because there are no connectors involved.
Rs = 1.0
Shear over strength factor = 1.4Rs = 1.4.
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 26: Diaphragm Design Forces
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
To determine Cpx, three parameters must be determined - Cp0, Cpi, and Cpn
Determination of Cp0:
Cp0 = 0.4SDSIe = 0.4×0.21×1.0 = 0.084
Determination of Cpi
Cpi is the greater of the values given by:
  Cpi = Cp0 = 0.084, and
  Cpi = 0.9Γm1 Ω0 Cs
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 27: Diaphragm Design Forces
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
Determination of Cpi
  Γm1 is the first mode contribution factor
  Γm1 = 1 + 0.5zs(1 – 1/N)
  where
  zs = modal contribution coefficient modifier dependent on seismic force-resisting system
  N = Number of stories
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 28: Diaphragm Design Forces
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
Determination of Cpi
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 29: Diaphragm Design Forces
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
Determination of Cpi
  Γm1 is the first mode contribution factor
  Γm1 = 1 + 0.5zs(1 – 1/N) = 1 + 0.5x1.0 (1 – 1/5) = 1.4
  Cpi = 0.9Γm1 Ω0 Cs = 0.9x1.4x2.5x0.105 = 0.331 > 0.084
  Governing Cpi = 0.331
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 30: Diaphragm Design Forces
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
Determination of Cpn
  Cpn =
  where
  Γm2 is the higher mode contribution factor
  Γm2 = 0.9zs(1 – 1/N)2 = 0.9x1.0 (1 – 1/5)2 = 0.576
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 31: Diaphragm Design Forces
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
Determination of Cpn
  Cs2 is higher mode seismic response coefficient, and is the smallest of:
  Cs2 = (0.15N + 0.25)IeSDS = (0.15x5 + 0.25)x1.0x0.21 = 0.21
  Cs2 = IeSDS = 1.0x0.21 = 0.21
  and for N ≥ 2
  Cs2 = IeSD1 / [0.03(N-1)] = 1.0x0.12 / [0.03(5-1)] = 1.00
  Governing Cs2 = 0.21
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 32: Diaphragm Design Forces
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
Determination of Cpn
  Cpn = = 0.387
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 33: Diaphragm Design Forces
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
Using Standard Figure 12.10.3-1, Cpx is determined at various floor levels, as shown in Table 11.1-2B
Notes: The figure shows two graphs both with hx /hn in the y-axis with ascending gradations from 0 to 1, and in the x-axis with gradations left to right of diaphragm design acceleration coefficient for level x, Cpx from 0 to Cpn. hx /hn is the ratio of the height from the base to level x, hx to the vertical distance from the base to the highest level of the seismic force-resisting system of the structure., hn. On the left-hand side graph for building two stories or less in height, the design acceleration coefficient curve begins at Cp0,0 and rises linearly to Cpn,1. On the right-hand side graph for building three stories or more in height, the curve begins at Cp0,0 and rises linearly to Cpi,0.8, then rises in a straight line from Cpi,0.8 to Cpn,1. Cp0, Cpi, and Cpn are diaphragm design acceleration coefficient at the structure base, diaphragm design acceleration coefficient at 80 percent of the structural height above the base, hn, and diaphragm design acceleration coefficient at the structural height, hn, respectively.

## Slide 34: Diaphragm Design Forces
Table 11.1-2B Fpx Calculations for SDC B |  |  |  |  | 
Level | hx (ft) | Cpx | wpx (kips) | Fpx (kips) | Fpx,min (kips)
Roof | 43.34 | 0.39 | 807 | 312 | 33.90
4 | 34.67 | 0.33 | 855 | 283 | 35.90
3 | 26.00 | 0.27 | 855 | 230 | 35.90
2 | 17.33 | 0.21 | 855 | 177 | 35.90
1 | 8.67 | 0.15 | 855 | 125 | 35.90
1.0 kip = 4.45 kN. |  |  |  |  | 
Step 3: Determine Fpx, Diaphragm Design Force at Level x
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 35: Design of Building Assigned to Seismic Design Category C

## Slide 36: Diaphragm Design Forces
The weight tributary to the roof and floor diaphragms (wpx) is the total story weight (wi) at Level i minus the weight of the walls parallel to the direction of loading.
  Roof:
    Total weight = 870 kips
    Walls parallel to force = (48 psf)(277 ft)(8.67 ft / 2) = -58 kips
    wpx = 812 kips
  Floors:
    Total weight = 978 kips
    Walls parallel to force = (48 psf)(277 ft)(8.67 ft) = -115 kips
    wpx = 863 kips
Notes: Weight used for the diaphragm design is given for floor and roof. The weight used for the design of the diaphragm does not include the weight of walls parallel to the direction of loading because the wall weight does not contribute to the inertial force in the floor. That must be collected and distributed to the walls,

## Slide 37: Diaphragm Design Forces
Since the building is assigned to SDC C, the precast concrete diaphragm design forces are required to be
determined by the provisions of Standard Section 12.10.3:
Step 1: Determine Rs, Diaphragm Design Force Reduction Factor (Standard Table 12.10-1)
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
Step 3: Determine Fpx, Diaphragm Design Force at Level x
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 38: Diaphragm Design Forces
Step 1: Determine Rs, Diaphragm Design Force Reduction Factor (Standard Table 12.10-1)
For SDC C, the Diaphragm Seismic Demand Level is Low. So all diaphragm design options are allowed; the Basic Design Option (BDO) is chosen.
The issue of connector deformability is moot, because there are no connectors involved.
Rs = 1.0
Shear over strength factor = 1.4Rs = 1.4.
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 39: Diaphragm Design Forces
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
To determine Cpx, three parameters must be determined - Cp0, Cpi, and Cpn
Determination of Cp0:
Cp0 = 0.4SDSIe = 0.4×0.37×1.0 = 0.148
Determination of Cpi
Cpi is the greater of the values given by:
  Cpi = Cp0 = 0.148, and
  Cpi = 0.9Γm1 Ω0 Cs
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 40: Diaphragm Design Forces
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
Determination of Cpi
  Γm1 is the first mode contribution factor
  Γm1 = 1 + 0.5zs(1 – 1/N) = 1 + 0.5x1.0 (1 – 1/5) = 1.4
  Cpi = 0.9Γm1 Ω0 Cs = 0.9x1.4x2.5x0.106 = 0.334 > 0.148
  Governing Cpi = 0.334
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 41: Diaphragm Design Forces
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
Determination of Cpn
  Cpn =
  where
  Γm2 is the higher mode contribution factor
  Γm2 = 0.9zs(1 – 1/N)2 = 0.9x1.0 (1 – 1/5)2 = 0.576
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 42: Diaphragm Design Forces
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
Determination of Cpn
  Cs2 is higher mode seismic response coefficient, and is the smallest of:
  Cs2 = (0.15N + 0.25)IeSDS = (0.15x5 + 0.25)x1.0x0.37 = 0.37
  Cs2 = IeSDS = 1.0x0.37 = 0.37
  and for N ≥ 2
  Cs2 = IeSD1 / [0.03(N-1)] = 1.0x0.15 / [0.03(5-1)] = 1.25
  Governing Cs2 = 0.37
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 43: Diaphragm Design Forces
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
Determination of Cpn
  Cpn = = 0.428
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 44: Diaphragm Design Forces
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
Using Standard Figure 12.10.3-1, Cpx is determined at various floor levels, as shown in Table 11.1-3
Notes: The figure shows two graphs both with hx /hn in the y-axis with ascending gradations from 0 to 1, and in the x-axis with gradations left to right of diaphragm design acceleration coefficient for level x, Cpx from 0 to Cpn.
hx /hn is the ratio of the height from the base to level x, hx to the vertical distance from the base to the highest level of the seismic force-resisting system of the structure., hn. On the left-hand side graph for building two stories or less in height, the design acceleration coefficient curve begins at Cp0,0 and rises linearly to Cpn,1. On the right-hand side graph for building three stories or more in height, the curve begins at Cp0,0 and rises linearly to Cpi,0.8, then rises in a straight line from Cpi,0.8 to Cpn,1. Cp0, Cpi, and Cpn are diaphragm design acceleration coefficient at the structure base, diaphragm design acceleration coefficient at 80 percent of the structural height above the base, hn, and diaphragm design acceleration coefficient at the structural height, hn, respectively.

## Slide 45: Diaphragm Design Forces
Table 11.1-3 Fpx Calculations for SDC C |  |  |  |  | 
Level | hx (ft) | Cpx | wpx (kips) | Fpx (kips) | Fpx,min (kips)
Roof | 43.34 | 0.43 | 812 | 347 | 60.10
4 | 34.67 | 0.33 | 863 | 288 | 63.90
3 | 26.00 | 0.29 | 863 | 248 | 63.90
2 | 17.33 | 0.24 | 863 | 208 | 63.90
1 | 8.67 | 0.19 | 863 | 168 | 63.90
1.0 kip = 4.45 kN. |  |  |  |  | 
Step 3: Determine Fpx, Diaphragm Design Force at Level x
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 46: Static Analysis of Diaphragms
The balance of this example will use the controlling diaphragm seismic design force of 347 kips for the building in SDC C.
A common approach to diaphragm design is to consider the horizontal plane of the floor as a beam, and to calculate force and moment demands on joints based on their locations within that beam.
Since the building is assigned to SDC C, collector elements will be designed for 1.5 times the diaphragm force per Standard Section 12.10.3.4.
Notes: The load and reaction diagram from the example is shown to illustrate the support provides by the walls to a continuous beam. The uniform diaphragm loads vary by building segment because the transverse walls on the ends are included in the distributed weights, but the supporting walls in the center section are not included in the diaphragm load.

## Slide 47: Static Analysis of Diaphragms
Notes: The figure shows a cross section of a diaphragm with a total length of 152’-0”. The diaphragm has one 40’-0” long span on each end and three 24’-0” long spans in the middle. From left to right, spans are identified by gridlines A through F. Uniform gravity load W1 is applied from the top on side spans while middle three spans are subjected to uniform gravity load of magnitude W2. Upward reaction force of magnitude F is applied to the diaphragm from the bottom on gridlines B, C, D, and E.

## Slide 48: Static Analysis of Diaphragms
With a rigid diaphragm assumption, assuming the four shear walls have the same stiffness and ignoring torsion, the diaphragm reactions at the transverse shear walls (F as shown in figure on the previous slide) are computed as:
F = 347 kips/4 = 86.8 kips
Notes: Based on the assumption that the diaphragm in this example is rigid, the reaction forces on the four transverse walls are taken as equal. The slide shows the calculation of the uniform lateral force in each section of the building based on the diaphragm load for each section.

## Slide 49: Static Analysis of Diaphragms
The uniform diaphragm demands are proportional to the distributed weights of the diaphragm in different areas
W1 = [67 psf (72 ft) + 48 psf (8.67 ft)4](347 kips / 863 kips) = 2,610 lb/ft
W2 = [67 psf (72 ft)](347 kips / 863 kips) = 1,940 lb/ft
Notes: Based on the assumption that the diaphragm in this example is rigid, the reaction forces on the four transverse walls are taken as equal. The slide shows the calculation of the uniform lateral force in each section of the building based on the diaphragm load for each section.

## Slide 50: Static Analysis of Diaphragms
The joints in the floor plan for this example include
  Longitudinal joints between adjacent planks, located in the two orthogonal directions
  Transverse joints between the ends of planks, transverse joint between the ends of planks at masonry walls, end joints at masonry wall bearings
  Joints at the intersection of longitudinal and transverse planks at masonry walls and away from masonry walls
Notes: Based on the assumption that the diaphragm in this example is rigid, the reaction forces on the four transverse walls are taken as equal. The slide shows the calculation of the uniform lateral force in each section of the building based on the diaphragm load for each section.

## Slide 51: Static Analysis of Diaphragms
Force demands for loads crossing or within these joints include
  Chord forces
  Shear friction forces
  Integrity tie forces
Notes: Based on the assumption that the diaphragm in this example is rigid, the reaction forces on the four transverse walls are taken as equal. The slide shows the calculation of the uniform lateral force in each section of the building based on the diaphragm load for each section.

## Slide 52: Static Analysis of Diaphragms
ACI 318 does not recognize dowel behavior of reinforcing embedded in concrete nor friction in grouted joints without shear friction tension strength.
The steel requirements for friction transfer come only from shear friction calculations.
The shear transfer, however, is actually through the grout in the longitudinal joint.
Notes: Based on the assumption that the diaphragm in this example is rigid, the reaction forces on the four transverse walls are taken as equal. The slide shows the calculation of the uniform lateral force in each section of the building based on the diaphragm load for each section.

## Slide 53: Critical regions of the diaphragm to be considered in this design
Joint 1: Maximum transverse shear parallel to the panels at panel-to-panel joints
Joint 2: Maximum transverse shear parallel to the panels at the panel-to-wall joint
Joint 3: Maximum transverse moment and chord force
Joint 4: Maximum longitudinal shear perpendicular to the panels at the panel-to-wall connection (exterior longitudinal walls) and anchorage of exterior masonry wall to the diaphragm for out-of-plane forces
Joint 5: Collector element and shear for the interior longitudinal walls
Notes: The slide bullet points describe the five critical regions shown in the previous slide. These locations are used in the design example for the calculation of forces and to illustrate the reinforcing detailing.

## Slide 54: Critical regions of the diaphragm to be considered in this design
1
2
3
4
5
Notes: The plan view of the floor is repeated with the dimensions removed and the critical regions for design identified with the numbered circles and arrows for reference to detailed sections.

## Slide 55: Joint Forces
Joint 1 – Transverse forces:
  Shear, Vu1 = 2.61 kips/ft (36 ft) = 94 kips
  Moment, Mu1 = 94 kips (36 ft / 2) = 1692 ft-kips
  Chord tension, Tu1 = M/d = 1692 ft-kips / 71 ft = 23.8 kips
Joint 2 – Transverse forces:
  Shear, Vu2 = 2.61 kips/ft (40 ft) = 104.4 kips
  Moment, Mu2 = 104.4 kips (40 ft / 2) = 2088 ft-kips
  Chord tension, Tu2 = M/d = 2088 ft-kips / 71 ft = 29.4 kips
Notes: Calculations for joint forces at critical regions 1 and 2 are given. These calculations follow simple principles of statics.

## Slide 56: Joint Forces
Joint 3 – Transverse forces:
  Shear, Vu3 = 104.4 kips + 1.94 kips/ft (24 ft) – 86.8 kips = 64.2 kips
  Moment, Mu3 = 104.4 kips (44 ft) + 46.6 kips (12 ft) – 86.8 kips (24 ft) = 3070 ft-kips
  Chord tension, Tu3 = M/d = 3070 ft-kips / 71 ft = 43.2 kips
Joint 4 – Longitudinal forces:
  Wall force, F = 347 kips / 8 = 43.4 kips
  Wall shear along wall length, Vu4 = 43.4 kips (36 ft)/(152 ft / 2) = 20.6 kips
  Collector force at wall end, 1.5Tu4 = 1.5Cu4 = 1.5(43.4 kips – 20.6 kips) = 34.2 kips
Notes: Calculation for joint forces at critical regions 3 and 4 (longitudinal) are given.

## Slide 57: Joint Forces
Joint 4 – Out-of-Plane Forces:
  The Standard has several requirements for out-of-plane forces. None are unique to precast diaphragms and all are less than the requirements in ACI 318 for precast construction regardless of seismic considerations. Assuming the planks are similar to beams and comply with the minimum requirements of Standard Section 12.14 (Seismic Design Category B and greater), the required out-of-plane horizontal force is:
  0.05(D+L)plank = 0.05(67 psf + 40 psf)(24 ft / 2) = 64.2 plf
Notes: Calculation for joint forces at critical regions 3 and 4 (longitudinal) are given.

## Slide 58: Joint Forces
Joint 4 – Out-of-Plane Forces:
  According to Standard Section 12.11.2.1 (Seismic Design Category B and greater), structural wall anchorage must be designed for a force computed as::
  Fp = 0.4(SDS)(ka)(Ie)(Wwall)
  = 0.4(0.37)(1.0)(1.0) [(48 psf)(8.67 ft)] = 61.6 plf
  where
  ka = 1.0 + Lf/100 = 1.0 for rigid diaphragms
  From its geometry, this diaphragm is likely to be classified as rigid. However, the relative deformations of the wall and diaphragm must be checked in accordance with Standard Section 12.3.1.3 to validate this assumption.
Notes: Calculation for joint forces at critical regions 3 and 4 (longitudinal) are given.

## Slide 59: Joint Forces
Joint 5 – Longitudinal forces:
  Wall force, F = 347 kips / 8 = 43.4 kips
  Wall shear along each side of wall, Vu5 = 43.4 kips [2(36 ft) / 152 ft]/2 = 10.3 kips
  Design collector force at wall end, 1.5Tu5 = 1.5Cu5 = 1.5[43.4 kips - 2(10.3 kips)] = 34.2 kips
Joint 5 – Shear flow due to transverse forces:
  Shear at Joint 2, Vu2 = 104.4 kips
Q = A d: A = (0.67 ft) (24 ft) = 16 ft2 , d = 24 ft
Q = (16 ft2) (24 ft) = 384 ft3
I = (0.67 ft) (72 ft)3 / 12 = 20,840 ft4
Vu2Q/I = (104.4 kip) (384 ft3) / 20,840 ft4 = 1.923 kip/ft maximum shear flow
Joint 5 length = 40 ft
Total transverse shear in joint 5, Vu5 = 1.923 kip/ft) (40 ft)/2 = 38.5 kips
Notes: Force calculations for Joint 5 are shown for longitudinal and transverse forces. The transverse force effect is shear flow, calculated using VQ/I to determine the total joint force.

## Slide 60: Joint Forces
ACI 318 Section 16.2.1.8 also has minimum connection force requirements for structural integrity in accordance with 16.2.4 or 16.2.5.
ACI 318 Section 16.2.4.1 reads: “Except where the provisions of 16.2.5 govern, longitudinal and transverse integrity ties shall connect precast members to a lateral-force-resisting system, and vertical integrity ties shall be provided in accordance with 16.2.4.3 to connect adjacent floor and roof levels.”
ACI 318 Section 16.2.5 has the title “Integrity tie requirements for precast concrete bearing wall structures three stories or more in height.”
The structure being designed is a masonry bearing wall structure with precast concrete slabs acting as diaphragms; it is 5-stories tall. It has been decided to apply Section 16.2.5 requirements to the precast slabs, in which case, Sections 16.2.4.2 and 16.2.4.3 do not apply.
Notes: Force calculations for Joint 5 are shown for longitudinal and transverse forces. The transverse force effect is shear flow, calculated using VQ/I to determine the total joint force.

## Slide 61: Joint Forces
According to ACI 318 Section 16.2.5.1, the horizontal tie force requirements for a precast bearing wall structure three or more stories in height are:
  1500 plf parallel and perpendicular to the span of the floor members. The maximum spacing of ties parallel to the span is 10 feet. The maximum spacing of ties perpendicular to the span is the distance between supporting walls or beams.
  16 kips parallel to the perimeter of a floor or roof located within 4 feet of the edge at all edges.
Notes: Force calculations for Joint 5 are shown for longitudinal and transverse forces. The transverse force effect is shear flow, calculated using VQ/I to determine the total joint force.

## Slide 62: Diaphragm Design and Details
The phi factors used for this example are as follows:
  Tension control (bending and ties): f = 0.90
  Shear: f = 0.75
  Compression control in tied members: f = 0.65
Notes: Force calculations for Joint 5 are shown for longitudinal and transverse forces. The transverse force effect is shear flow, calculated using VQ/I to determine the total joint force.

## Slide 63: Diaphragm Design and Details
The required shear strength on the diaphragm is amplified by a factor of 1.4Rs = 1.4×1.0 = 1.4, as required by Standard Section 14.2.4.1.3.
The minimum tie force requirements given in ACI 318 Section 16.2.5 are specified as nominal values, meaning that f = 1.00 for those forces.
Notes: Force calculations for Joint 5 are shown for longitudinal and transverse forces. The transverse force effect is shear flow, calculated using VQ/I to determine the total joint force.

## Slide 64: Diaphragm Design and Details – Joint 1
1
Notes: The floor plan is shown with Joint 1 highlighted to identify the application of the following calculations. This joint is the first interior transverse joint away from the transverse wall between the outer and inner floor plates.

## Slide 65: Diaphragm Design and Details – Joint 1
Chord reinforcement, As1 = Tu1/ϕfy = (23.8 kips)/[0.9(60 ksi)] = 0.44 in.2 (The collector force from the Joint 4 calculations at 34.2 kips is not directly additive.)
Shear friction reinforcement, Avf1 = 1.4Vu1/ϕμfy = (1.4)(94 kips)/[(0.75)(1.0)(60 ksi)] = 2.92 in.2
Total reinforcement required = 2(0.44 in.2) + 2.92 in.2 = 3.80 in.2
ACI tie force = (1.5 kips/ft)(72 ft) = 108 kips; reinforcement = (108 kips)/(60 ksi) = 1.80 in.2
Provide four #6 bars (two at each of the outside edges) plus four #7 bars (two each at the interior joint at the ends of the plank) for a total area of reinforcement of 4(0.44 in.2) + 4(0.60 in.2) = 4.16 in.2
Notes: Calculations for Joint 1 reinforcement are provided. The design must provide sufficient reinforcement for chord forces as well as shear friction connection forces. The section of bars and placement is given. The selection of bars is given to satisfy the steel area calculation.

## Slide 66: Diaphragm Design and Details – Joint 1
Anchorage region for shear reinforcement
Interior Joint
Notes: Figures from the example that illustrate the placement of reinforcement are provided in this slide. At the interior joint, two horizontal bars are place in the grouted joint between the ends of plank and parallel with the support beam. In the second figure, the flange of the plank is broken at he edge to open the edge core and permit placement of #7 bars and grout in the core, filling the profile and joint to the finished floor.

## Slide 67: Diaphragm Design and Details – Joint 2
2
Notes: Floor plan with highlighting for joint 2 is shown to identify joint. This joint is the joint between the outside diaphragm and the transverse wall between the outside and inside floor plates.

## Slide 68: Diaphragm Design and Details – Joint 2
Chord reinforcement, As2 = Tu2/fy = (29.4 kips)/[0.9(60 ksi)] = 0.55 in.2
The shear force may be reduced along Joint 2 by the shear friction resistance provided by the supplemental chord reinforcement (2Achord - As2) and by the four #7 bars projecting from the interior longitudinal walls across this joint. The supplemental chord bars, which are located at the end of the walls, are conservatively excluded here.
The shear force along the outer joint of the wall where the plank is parallel to the wall is modified as follows:
Vu2Mod = 1.4Vu2 – fymA4#7 = 1.4 x 104.4 – 0.75x60x1.0x(4x0.6)
= 38.16 kips
Notes: Calculations for Joint 1 reinforcement are provided. The design must provide sufficient reinforcement for chord forces as well as shear friction connection forces. The section of bars and placement is given. The selection of bars is given to satisfy the steel area calculation.

## Slide 69: Diaphragm Design and Details – Joint 2
Using the arrangement shown in the figure below
Notes: Detail at Joint 2 is shown to show the placement of reinforcing in the masonry wall an in an opened core of the hollow core plank. Note the detail shows diagonal bars to transfer forces mostly in tension and compression rather than by dowel shear or shear friction. The block just below the bearing in the masonry wall is a bond beam with two #5 bars grouted in as part of the diaphragm reinforcement.

## Slide 70: Diaphragm Design and Details – Joint 2
The required shear friction reinforcement (Avf2) is computed as:
Use two #3 bars placed at 26.6 degrees (2-to-1 slope) across the joint at 6 feet from the ends of the plank (two sets per plank for a total of 6 sets). The angle (αf) used above provides development of the #3 bars while limiting the grouting to the outside core of the plank. The total shear reinforcement provided is 6(0.11 in.2) = 0.66 in.2 Note that the spacing of these connectors will have to be adjusted at the stair location.
Notes: Detail at Joint 2 is shown to show the placement of reinforcing in the masonry wall an in an opened core of the hollow core plank. Note the detail shows diagonal bars to transfer forces mostly in tension and compression rather than by dowel shear or shear friction. The block just below the bearing in the masonry wall is a bond beam with two #5 bars grouted in as part of the diaphragm reinforcement.

## Slide 71: Diaphragm Design and Details – Joint 3
3
Notes: Floor plan with highlighting for joint 2 is shown to identify joint. This joint is the joint between the outside diaphragm and the transverse wall between the outside and inside floor plates.

## Slide 72: Diaphragm Design and Details – Joint 3
Compute the required amount of chord reinforcement at Joint 3 as:
As3 = Tu3/fy = (43.2 kips)/[0.9(60 ksi)] = 0.8 in.2
Use two #6 bars, As = 2(0.44) = 0.88 in.2 along the exterior edges (top and bottom of the plan). Require cover for chord bars and spacing between bars at splices and anchorage zones per ACI 318 Section 18.12.7.6 (optional).
Notes: Calculations for Joint 1 reinforcement are provided. The design must provide sufficient reinforcement for chord forces as well as shear friction connection forces. The section of bars and placement is given. The selection of bars is given to satisfy the steel area calculation.

## Slide 73: Diaphragm Design and Details – Joint 3
Notes: The figure shows a cross section of an 8” thick hollow core panel. The first three cores from the left edge are shown where the first core is filled with concrete to shape a chord joint. The joint is reinforced with two continuous No. 6 bars extending in the perpendicular to the plane direction. The bars have 3” cover on the left, 3” cover on the top, 3” cover on the bottom, and 3” spacing in the longitudinal direction. Spliced bars are shown with dash circles in contact with the main bars. 4” diameter spiral of ¼” wire with 2” pitch is enclosing the bars and may be required over the lap splice.

## Slide 74: Diaphragm Design and Details – Joint 3
Joint 3 must also be checked for the minimum ACI tie forces. The chord reinforcement obviously exceeds the 16 kip perimeter force requirement. To satisfy the 1.5 kips per foot requirement, a 6 kip tie is needed at each joint between the planks, which is satisfied with a #3 bar in each joint (0.11 in.2 at 60 ksi = 6.6 kips). This bar is required at all bearing walls and is shown in subsequent details.
Notes: Calculations for Joint 1 reinforcement are provided. The design must provide sufficient reinforcement for chord forces as well as shear friction connection forces. The section of bars and placement is given. The selection of bars is given to satisfy the steel area calculation.

## Slide 75: Diaphragm Design and Details – Joint 4
4
Notes: Floor plan is shown with Joint 4 highlighted. This joint is between the outside diaphragm plank and the outside longitudinal wall,

## Slide 76: Diaphragm Design and Details – Joint 4
The required shear friction reinforcement along the wall length is computed as:
Avf4 = 1.4Vu4/μfy = (1.4×20.6 kips)/[(0.75)(1.0)(60 ksi)] = 0.64 in.2
Based upon the ACI tie requirement, provide #3 bars at each plank-to-plank joint. For eight bars total, the area of reinforcement is 8(0.11) = 0.88 in.2, which is more than sufficient even considering the marginal development length, which is less favorable at Joint 2. The bars are extended 2 feet into the grout key, which is more than the development length and equal to half the width of the plank.
Notes: Calculations for Joint 1 reinforcement are provided. The design must provide sufficient reinforcement for chord forces as well as shear friction connection forces. The section of bars and placement is given. The selection of bars is given to satisfy the steel area calculation.

## Slide 77: Diaphragm Design and Details – Joint 4
The required collector reinforcement is computed as:
As4 = 1.5Tu4/fy = (34.2 kips)/[0.9(60 ksi)] = 0.63 in.2
The two #6 bars, which are an extension of the transverse chord reinforcement, provide an area of reinforcement of 0.88 in.2
The reinforcement required by the Standard for out-of-plane force (62 plf) is far less than the ACI 318 requirement.
Notes: Calculations for Joint 1 reinforcement are provided. The design must provide sufficient reinforcement for chord forces as well as shear friction connection forces. The section of bars and placement is given. The selection of bars is given to satisfy the steel area calculation.

## Slide 78: Diaphragm Design and Details – Joint 4
Notes: Detail at Joint 4 is shown to illustrate the placement of reinforcing at the end of plank and in the masonry walls for a “dry” system. The top flange in the end of the hollow core plank is broken way to permit access to the cores so that the cores at the end of the plank, the bearing space in the wall beyond the plank, and the bond beam below the bearing of the plank can be reinforced and grouted.

## Slide 79: Diaphragm Design and Details – Joint 5
5
Notes: Floor plan is shown with Joint 5 highlighted. This joint is between the outside diaphragm plank and the outside longitudinal wall,

## Slide 80: Diaphragm Design and Details – Joint 5
The required shear friction reinforcement along the wall length is computed as:
Avf5 = 1.4Vu5/μfy = (1.4×38.5 kips)/[(0.75)(1.0)(0.85)(60 ksi)] = 1.41 in.2
Provide #4 bars at each plank-to-plank joint for a total of 8 bars.
Notes: Calculations for Joint 1 reinforcement are provided. The design must provide sufficient reinforcement for chord forces as well as shear friction connection forces. The section of bars and placement is given. The selection of bars is given to satisfy the steel area calculation.

## Slide 81: Diaphragm Design and Details – Joint 5
The required collector reinforcement is computed as:
As5 = 1.5Tu5/fy = (34.2 kips)/[0.9(60 ksi)] = 0.63 in.2
Two #7 bars specified for the design of Joint 1 above provide an area of reinforcement of 1.20 in.2
Notes: Calculations for Joint 1 reinforcement are provided. The design must provide sufficient reinforcement for chord forces as well as shear friction connection forces. The section of bars and placement is given. The selection of bars is given to satisfy the steel area calculation.

## Slide 82: Diaphragm Design and Details – Joint 5
Notes: The figure shows a cross section of a panel-to-wall joint. Hollow core panels are extending in the longitudinal direction on both sides of the wall and meet at a 4” long joint. The joint is reinforced by:
Two No. 7 continuous collector bars located in the joint adjacent to the wall’s vertical bar and extended in the perpendicular to the plane direction.
One 4’-8” long longitudinal No. 4 bar located between the two collector bars and grouted into each key joint with equal extensions on both sides of the joint.
Two No. 5 continuous bars located in the masonry bond beam at the top of the wall below the joint and extended in the perpendicular to the plane direction.

## Slide 83: Topped Precast Concrete Diaphragm for Five-Story Masonry Building Assigned to SDC D

## Slide 84: Topped Precast Concrete Diaphragm for Five-Story Masonry Building Located in Los Angeles
This design shows the floor and roof diaphragms using topped precast units in the five-story masonry building when it is assigned to SDC D. The topping thickness exceeds the minimum thickness of 2 inches as required for composite topping slabs by ACI 318 Section 18.12.6. The topping is lightweight concrete (weight = 115 pcf) with a 28-day compressive strength (f'c) of 4,000 psi and is to act compositely with the 8 inch-thick hollow-core precast, prestressed concrete plank.
Topped diaphragms may be used in any Seismic Design Category. ACI 318 Section 18.12 provides design provisions for topped precast concrete diaphragms. Standard Section 12.10.3 specifies the forces to be used in designing the precast concrete diaphragms in buildings assigned to SDC C or higher.
Notes: The example for a topped precast floor is introduced with requirements of the provisions for higher seismic design categories. The seismic force for this example is compared to the SDC B example. Note also that it is the diaphragm force used to determine the collector and transfer requirement, and not the distributed lateral force used for the vertical elements of the lateral force-resisting system.

## Slide 85: Topped Diaphragm Design Parameters
Notes: First slide to introduce the design of untopped precast diaphragms using hollow core floor plank. The design is linked to the Chapter 10 masonry wall example for SDC B using Birmingham., Alabama. The use of seismic acceleration parameters for New York for SDC C differs from Chapter 10.

## Slide 86: Diaphragm Design Forces
The weight tributary to the roof and floor diaphragms (wpx) is the total story weight (wi) at Level i minus the weight of the walls parallel to the direction of loading.
  Roof:
    Total weight = 1166 kips
    Walls parallel to force = (60 psf)(277 ft)(8.67 ft / 2) = -72 kips
    wpx = 1094 kips
  Floors:
    Total weight = 1302 kips
    Walls parallel to force = (60 psf)(277 ft)(8.67 ft) = -144 kips
    wpx = 1158 kips
Notes: Weight used for the diaphragm design is given for floor and roof. The weight used for the design of the diaphragm does not include the weight of walls parallel to the direction of loading because the wall weight does not contribute to the inertial force in the floor. That must be collected and distributed to the walls,

## Slide 87: Diaphragm Design Forces
Since the building is assigned to SDC D, the precast concrete diaphragm design forces are required to be
determined by the provisions of Standard Section 12.10.3:
Step 1: Determine Rs, Diaphragm Design Force Reduction Factor (Standard Table 12.10.3.5-1)
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
Step 3: Determine Fpx, Diaphragm Design Force at Level x
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 88: Diaphragm Design Forces
Step 1: Determine Rs, Diaphragm Design Force Reduction Factor (Standard Table 12.10.3.5-1)
For SDC D, the Reduced Design Option (RDO) is chosen.
Rs = 1.4
Shear over strength factor = 1.4Rs = 2.0.
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 89: Diaphragm Design Forces
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
To determine Cpx, three parameters - Cp0, Cpi, and Cpn
Determination of Cp0:
Cp0 = 0.4SDSIe = 0.4×1.0×1.0 = 0.4
Determination of Cpi
Cpi is the greater of the values given by:
  Cpi = Cp0 = 0.4, and
  Cpi = 0.9Γm1 Ω0 Cs
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 90: Diaphragm Design Forces
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
Determination of Cpi
  Γm1 is the first mode contribution factor
  Γm1 = 1 + 0.5zs(1 – 1/N) = 1 + 0.5x1.0 (1 – 1/5) = 1.4
  Cpi = 0.9Γm1 Ω0 Cs = 0.9x1.4x2.5x0.2 = 0.63 > 0.4
  Governing Cpi = 0.63
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 91: Diaphragm Design Forces
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
Determination of Cpn
  Cpn =
  where
  Γm2 is the higher mode contribution factor
  Γm2 = 0.9zs(1 – 1/N)2 = 0.9x1.0 (1 – 1/5)2 = 0.576
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 92: Diaphragm Design Forces
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
Determination of Cpn
  Cs2 is higher mode seismic response coefficient, and is the smallest of:
  Cs2 = (0.15N + 0.25)IeSDS = (0.15x5 + 0.25)x1.0x1.0 = 1.0
  Cs2 = IeSDS = 1.0x1.0 = 1.0
  and for N ≥ 2
  Cs2 = IeSD1 / [0.03(N-1)] = 1.0x0.6 / [0.03(5-1)] = 5.0
  Governing Cs2 = 1.0
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 93: Diaphragm Design Forces
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
Determination of Cpn
  Cpn = = 0.907
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 94: Diaphragm Design Forces
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
Using Standard Figure 12.10.3-1, Cpx is determined at various floor levels, as shown in Table 11.1-5
Notes: The figure shows two graphs both with hx /hn in the y-axis with ascending gradations from 0 to 1, and in the x-axis with gradations left to right of diaphragm design acceleration coefficient for level x, Cpx from 0 to Cpn. hx /hn is the ratio of the height from the base to level x, hx to the vertical distance from the base to the highest level of the seismic force-resisting system of the structure., hn. On the left-hand side graph for building two stories or less in height, the design acceleration coefficient curve begins at Cp0,0 and rises linearly to Cpn,1. On the right-hand side graph for building three stories or more in height, the curve begins at Cp0,0 and rises linearly to Cpi,0.8, then rises in a straight line from Cpi,0.8 to Cpn,1. Cp0, Cpi, and Cpn are diaphragm design acceleration coefficient at the structure base, diaphragm design acceleration coefficient at 80 percent of the structural height above the base, hn, and diaphragm design acceleration coefficient at the structural height, hn, respectively.

## Slide 95: Diaphragm Design Forces
Table 11.1-5 Fpx Calculations for SDC C |  |  |  |  | 
Level | hx (ft) | Cpx | wpx (kips) | Fpx (kips) | Fpx,min (kips)
Roof | 43.34 | 1094 | 0.91 | 708 | 218.80
4 | 34.67 | 1158 | 0.63 | 521 | 231.60
3 | 26.00 | 1158 | 0.57 | 474 | 231.60
2 | 17.33 | 1158 | 0.51 | 426 | 231.60
1 | 8.67 | 1158 | 0.46 | 378 | 231.60
1.0 kip = 4.45 kN. |  |  |  |  | 
Step 3: Determine Fpx, Diaphragm Design Force at Level x
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 96: Static Analysis of Diaphragms
The example will use the controlling diaphragm seismic design force of 708 kips.
A common approach to diaphragm design is to consider the horizontal plane of the floor as a beam, and to calculate force and moment demands on joints based on their locations within that beam.
Since the building is assigned to SDC D, collector elements will be designed for 1.5 times the diaphragm force per Standard Section 12.10.3.4.
Notes: The load and reaction diagram from the example is shown to illustrate the support provides by the walls to a continuous beam. The uniform diaphragm loads vary by building segment because the transverse walls on the ends are included in the distributed weights, but the supporting walls in the center section are not included in the diaphragm load.

## Slide 97: Static Analysis of Diaphragms
The force is approximately twice that used to design the untopped diaphragm for the design of the building in SDC C due to the higher seismic demand.
Joint forces from SDC C example are multiplied by 2.0.
Notes: Based on the assumption that the diaphragm in this example is rigid, the reaction forces on the four transverse walls are taken as equal. The slide shows the calculation of the uniform lateral force in each section of the building based on the diaphragm load for each section.

## Slide 98: Critical regions of the diaphragm to be considered in this design
1
2
3
4
5
Notes: The plan view of the floor is repeated with the dimensions removed and the critical regions for design identified with the numbered circles and arrows for reference to detailed sections.

## Slide 99: Joint Forces
Joint 1 – Transverse forces:
  Shear, Vu1 = 94 kips x 2.0 = 188 kips
  Moment, Mu1 = 1692 ft-kips x 2.0 = 3384 ft-kips
  Chord tension, Tu1 = M/d = 3384 ft-kips / 71 ft = 47.7 kips
Joint 2 – Transverse forces:
  Shear, Vu2 = 104.4 kips x 2.0 = 208.8 kips
  Moment, Mu2 = 2088 ft-kips x 2.0 = 4176 ft-kips
  Chord tension, Tu2 = M/d = 4176 ft-kips / 71 ft = 58.8 kips
Notes: Calculations for joint forces at critical regions 1 and 2 are given. These calculations follow simple principles of statics.

## Slide 100: Joint Forces
Joint 3 – Transverse forces:
  Shear, Vu3 = 64.2 kips x 2.0 = 128.4 kips
  Moment, Mu3 = 3070 ft-kips x 2.0 = 6140 ft-kips
  Chord tension, Tu3 = M/d = 6140 ft-kips / 71 ft = 86.5 kips
Joint 4 – Longitudinal forces:
  Wall force, F = 43.4 kips x 2.0 = 86.8 kips
  Wall shear along wall length, Vu4 = 20.6 kips x 2.0 = 41.2 kips
  Collector force at wall end, 1.5Tu4 = 34.2 kips x 2.0 = 68.4 kips
Notes: Calculation for joint forces at critical regions 3 and 4 (longitudinal) are given.

## Slide 101: Joint Forces
Joint 4 – Out-of-Plane Forces:
  The Standard has several requirements for out-of-plane forces. None are unique to precast diaphragms and all are less than the requirements in ACI 318 for precast construction regardless of seismic considerations. Assuming the planks are similar to beams and comply with the minimum requirements of Standard Section 12.14 (Seismic Design Category B and greater), the required out-of-plane horizontal force is:
  0.05(D+L)plank = 0.05(67 psf + 40 psf)(24 ft / 2) = 64.2 plf
Notes: Calculation for joint forces at critical regions 3 and 4 (longitudinal) are given.

## Slide 102: Joint Forces
Joint 4 – Out-of-Plane Forces:
  According to Standard Section 12.11.2.1 (Seismic Design Category B and greater), structural wall anchorage must be designed for a force computed as:
  Fp = 0.4(SDS)(ka)(Ie)(Wwall)
  = 0.4(1.0)(1.0)(1.0) [(60 psf)(8.67 ft)] = 208 plf
  where
  ka = 1.0 + Lf/100 = 1.0 for rigid diaphragms
  From its geometry, this diaphragm is likely to be classified as rigid. However, the relative deformations of the wall and diaphragm must be checked in accordance with Standard Section 12.3.1.3 to validate this assumption.
Notes: Calculation for joint forces at critical regions 3 and 4 (longitudinal) are given.

## Slide 103: Joint Forces
Joint 5 – Longitudinal forces:
  Wall force, F = 708 kips / 8 walls = 88.5 kips
  Wall shear along each side of wall, Vu5 = 10.3 kips x 2.0 = 20.6 kips
  Design collector force at wall end, 1.5Tu5 = 34.2 kips x 2.0 = 68.4 kips
Joint 5 – Shear flow due to transverse forces:
  Shear at Joint 2, Vu2 = 208.8 kips
Q = A d: A = (0.67 ft) (24 ft) = 16 ft2 , d = 24 ft
Q = (16 ft2) (24 ft) = 384 ft3
I = (0.67 ft) (72 ft)3 / 12 = 20,840 ft4
Vu2Q/I = (208.8 kip) (384 ft3) / 20,840 ft4 = 3.85 kip/ft maximum shear flow
Joint 5 length = 40 ft
Total transverse shear in joint 5, Vu5 = 3.85 kip/ft) (40 ft)/2 = 77 kips
Notes: Force calculations for Joint 5 are shown for longitudinal and transverse forces. The transverse force effect is shear flow, calculated using VQ/I to determine the total joint force.

## Slide 104: Joint Forces
ACI 318 Section 16.2.1.8 also has minimum connection force requirements for structural integrity in accordance with 16.2.4 or 16.2.5.
ACI 318 Section 16.2.4.1 reads: “Except where the provisions of 16.2.5 govern, longitudinal and transverse integrity ties shall connect precast members to a lateral-force-resisting system, and vertical integrity ties shall be provided in accordance with 16.2.4.3 to connect adjacent floor and roof levels.”
ACI 318 Section 16.2.5 has the title “Integrity tie requirements for precast concrete bearing wall structures three stories or more in height.”
The structure being designed is a masonry bearing wall structure with precast concrete slabs acting as diaphragms; it is 5-stories tall. It has been decided to apply Section 16.2.5 requirements to the precast slabs, in which case, Sections 16.2.4.2 and 16.2.4.3 do not apply.
Notes: Force calculations for Joint 5 are shown for longitudinal and transverse forces. The transverse force effect is shear flow, calculated using VQ/I to determine the total joint force.

## Slide 105: Joint Forces
According to ACI 318 Section 16.2.5.1, the horizontal tie force requirements for a precast bearing wall structure three or more stories in height are:
  1500 pounds per foot parallel and perpendicular to the span of the floor members. The maximum spacing of ties parallel to the span is 10 feet. The maximum spacing of ties perpendicular to the span is the distance between supporting walls or beams.
  16,000 pounds parallel to the perimeter of a floor or roof located within 4 feet of the edge at all edges.
Notes: Force calculations for Joint 5 are shown for longitudinal and transverse forces. The transverse force effect is shear flow, calculated using VQ/I to determine the total joint force.

## Slide 106: Diaphragm Design and Details
The phi factors used for this example are as follows:
  Tension control (bending and ties): f = 0.90
  Shear: f = 0.75
  Compression control in tied members: f = 0.65
Notes: Force calculations for Joint 5 are shown for longitudinal and transverse forces. The transverse force effect is shear flow, calculated using VQ/I to determine the total joint force.

## Slide 107: Diaphragm Design and Details
The required shear strength on the diaphragm is amplified by a factor of 1.4Rs = 1.4×1.4 = 2.0, as required by Standard Section 14.2.4.1.3.
The minimum tie force requirements given in ACI 318 Section 16.2.5 are specified as nominal values, meaning that f = 1.00 for those forces.
Notes: Force calculations for Joint 5 are shown for longitudinal and transverse forces. The transverse force effect is shear flow, calculated using VQ/I to determine the total joint force.

## Slide 108: Topped Precast Concrete Diaphragm for Five-Story Masonry Building
Notes: The floor plan showing walls and the diaphragm layout is shown for the SDC D example. This is the same building layout used in the earlier examples but the joints between the hollow core plank in the interior areas of the floor have been removed. This reflects the presence of cast-in-place concrete topping with welded wire reinforcement to carry diaphragm forces, so the location of these interior joints is not a design consideration.

## Slide 109: Minimum Reinforcement for 2.5-inch Topping
ACI 318 Section 18.12.7.1 references ACI 318 Section 24.4, which requires a minimum
As = 0.0018bd for Grade 60 welded wire reinforcement.
= 0.054 in.2 per foot for a 2.5 in. topping
WWR 10×10 – W4.5×W4.5 provides 0.054 in.2/ft. However, as shown later, WWR 10×10 – W8×W8 (As = 0.096 in.2) must be provided as minimum.
Satisfies the minimum permitted wire spacing of 10 in. and the maximum permitted spacing of 18 in.
Notes: Force calculations for Joint 5 are shown for longitudinal and transverse forces. The transverse force effect is shear flow, calculated using VQ/I to determine the total joint force.

## Slide 110: Boundary Members
Joint 3 has the maximum bending moment and is used to determine the boundary member reinforcement of the chord along the exterior edge.
The need for transverse boundary member reinforcement is reviewed using ACI 318 Section 18.12.7.5. Calculate the compressive stress in the chord with the ultimate moment using a linear elastic model and gross section properties of the topping.
It is conservative to ignore the precast units, but this is not necessary since the joints between precast units are grouted.
Notes: Force calculations for Joint 5 are shown for longitudinal and transverse forces. The transverse force effect is shear flow, calculated using VQ/I to determine the total joint force.

## Slide 111: Boundary Members
The chord compressive stress is:
6Mu3/hd2 = 6(6140×12)/(2.5)(72×12)2 = 237 psi
The chord compressive stress is less than 0.2f'c = 0.2(4000) = 800 psi. Transverse reinforcement in the boundary member is not required.
The required chord reinforcement is:
As3 = Tu3/fy = (86.5 kips)/[0.9(60 ksi)] = 1.6 in.2
Notes: Force calculations for Joint 5 are shown for longitudinal and transverse forces. The transverse force effect is shear flow, calculated using VQ/I to determine the total joint force.

## Slide 112: Boundary Members
Notes: The figure shows a cross section of a topped hollow core panel. The first three cores from the left edge are shown where the first core is filled with concrete to shape a chord joint. The joint is reinforced with two continuous No. 8 bars extending in the perpendicular to the plane direction. The bars have 3.5” cover on the left, 2.5” cover on the right, 3” cover on the top, and 3” spacing. Spliced bars are shown with dash circles in contact with the main bars. 4” diameter spiral of ¼” wire with 2” pitch is enclosing the bars over the lap splice. The 2.5” topping is reinforced with WWF bend down into the chord at the edge.

## Slide 113: Collectors – Joint 5
The design for Joint 4 collector reinforcement at the end of the exterior longitudinal walls and for Joint 5 at the interior longitudinal walls is the same.
As4 = As5 = 1.5Tu4/fy = (68.4 kips)/[0.9(60 ksi)] = 1.27 in.2
Use two #8 bar (As = 2 × 0.79 = 1.58 in.2) along the exterior edges, along the length of the exterior longitudinal walls and along the length of the interior longitudinal walls.
Notes: Force calculations for Joint 5 are shown for longitudinal and transverse forces. The transverse force effect is shear flow, calculated using VQ/I to determine the total joint force.

## Slide 114: Collectors – Joint 5
Notes: The figure shows a cross section of an interior panel-to-panel joint. Two longitudinal 8” thick hollow core panels with 2” topping meet at a 3” long joint which is supported by an I-shaped section. The joint is reinforced by two No. 8 collector bars extending in the perpendicular to the plane direction. The bars have 2.5” cover on the top (below the topping), 2.5” cover on the bottom and 3” spacing in between. The topping is reinforced with WWF.

## Slide 115: Shear at Joints 1 and 2
The required shear strength on the diaphragm is amplified by a factor of 1.4Rs = 1.4×1.4 = 2.0, as required by Standard Section 14.2.4.1.3.
Required shear in Joint 1, 2.0×Vu1 = 2×188 kips = 376 kips
Required shear in Joint 2, 2.0×Vu2 = 2×208.8 kips = 418 kips
Notes: Force calculations for Joint 5 are shown for longitudinal and transverse forces. The transverse force effect is shear flow, calculated using VQ/I to determine the total joint force.

## Slide 116: Shear at Joints 1 and 2
In thin composite and noncomposite topping slabs on precast floor and roof members, joints typically are tooled during construction, resulting in cracks forming at the joint between precast members. Therefore, the shear resistance of the topping slab is limited to the shear friction strength of the reinforcing crossing the joint.
ACI 318 Section 18.12.9.1 provides an equation for the shear strength of the diaphragm, which includes both concrete and reinforcing components. However, for noncomposite topping slabs on precast floors and roofs where the only reinforcing crossing the joints is the field reinforcing in the topping slab, the shear friction capacity at the joint will always control the design.
Notes: Force calculations for Joint 5 are shown for longitudinal and transverse forces. The transverse force effect is shear flow, calculated using VQ/I to determine the total joint force.

## Slide 117: Shear Resistance – Joint 1
ACI 318 Section 18.12.9.3 defines the shear strength at the joint as follows:
Vn,WWR = Avffy = 0.75(0.096 in.2/ft)(60 ksi)(1.0)(0.85) = 3.67 kips/ft
Note that  = 1.0 is used since the joint is assumed to be pre-cracked.
The shear resistance in the transverse direction is:
3.67 kips/ft (72 ft) = 264 kips
Notes: Force calculations for Joint 5 are shown for longitudinal and transverse forces. The transverse force effect is shear flow, calculated using VQ/I to determine the total joint force.

## Slide 118: Shear Resistance – Joint 1
Shear friction from the collector reinforcement (4#8) at the interior longitudinal walls:
Vn,collector = Avffy = 0.75(4×0.79)(60 ksi)(1.0)(0.85) = 120 kips
Total shear resistance: Vn = 264 kips + 120 kips
= 384 kips > 2.0Vu1
Notes: Force calculations for Joint 5 are shown for longitudinal and transverse forces. The transverse force effect is shear flow, calculated using VQ/I to determine the total joint force.

## Slide 119: Shear Resistance – Joint 2
Collector: 4#8
WWR 10×10 – W8×W8
At the plank adjacent to Joint 2, the shear strength of the diaphragm in accordance with ACI 318 Section 18.12.9.1 is:
Notes: Force calculations for Joint 5 are shown for longitudinal and transverse forces. The transverse force effect is shear flow, calculated using VQ/I to determine the total joint force.

## Slide 120: Shear Resistance – Interior Longitudinal Wall
The required shear reinforcement along the interior longitudinal wall (Joint 5) is:
Avf5 = 2Vu5/μfy = (2×77 kips)/[(0.75)(1.0)(0.85)(60 ksi)]
= 4.03 in.2
Number 4 dowels spaced at 16 in. o.c. provide Av = (0.20 in.2) (40 ft x 12 in./ft) / 16 in. = 6.0 in.2
Number 4 dowels are used to provide continuity of the topping slab welded wire reinforcement across the masonry walls.
Notes: Force calculations for Joint 5 are shown for longitudinal and transverse forces. The transverse force effect is shear flow, calculated using VQ/I to determine the total joint force.

## Slide 121: Shear Resistance – Interior Longitudinal Wall
Notes: The figure shows a cross section of a panel-to-wall joint. Topped hollow core panels are extending in the longitudinal direction on both sides of the wall and meet at a 4” long joint. The topping is reinforced with WWF 10x10 W8 x W8. The joint is reinforced by:
Two No. 8 continuous collector bars located in the joint adjacent to the wall’s vertical bar and extended in the perpendicular to the plane direction.
One 4’-0” long longitudinal No. 4 bar with equal extensions on both sides of the joint located in the topping and lapped with WWF.
Two No. 5 continuous bars located in the masonry bond beam at the top of the wall below the joint and extended in the perpendicular to the plane direction.

## Slide 122: Shear Resistance – Exterior Longitudinal Wall (Joint 4)
The required shear reinforcement along the exterior longitudinal wall (Joint 4) is:
Avf4 = 2Vu4/μfy = (2×41.2 kips)/[(0.75)(1.0)(0.85)(60 ksi)]
= 2.15 in.2
Number 5 dowels spaced at 48 in. o.c. provide Av = (0.31 in.2) (36 ft x 12 in./ft) / 48 in. = 2.79 in.2
Notes: Force calculations for Joint 5 are shown for longitudinal and transverse forces. The transverse force effect is shear flow, calculated using VQ/I to determine the total joint force.

## Slide 123: Out-of-Plane Forces – Exterior Longitudinal Wall (Joint 4)
Out-of-Plane forces at Joint 4 = 208 plf
With bars at 4 feet on center, required reinforcement:
As = (4 ft)(0.208 klf)/[(0.9)(60 ksi)] = 0.015 in.2
Number 5 dowels spaced at 48 in. o.c. provided at this joint is adequate.
This detail satisfies the tie force of 1.5 klf required by ACI 318 Section 16.2.5.1.
The bars are extended 2 ft into the grout key, which is more than the development length.
Notes: Force calculations for Joint 5 are shown for longitudinal and transverse forces. The transverse force effect is shear flow, calculated using VQ/I to determine the total joint force.

## Slide 124: Joint 4 Reinforcement Detail
Notes: The figure shows a cross section of a panel-to-perimeter-wall joint. Topped hollow core panel extending in the longitudinal direction meets the wall from the right. The topping is reinforced with WWF 10x10 W8 x W8. The joint is reinforced by:
One 2’-6” long No. 5 bar with standard hooks at 4’-0” spacing located in the topping, lapped with WWF, and bend into the joint with 2” clear cover from the inner face of the wall.
Two No. 8 continuous collector bars located in the joint adjacent to the wall’s vertical bar and extended in the perpendicular to the plane direction.
Two No. 5 continuous bars located in the masonry bond beam at the top of the wall below the joint and extended in the perpendicular to the plane direction.

## Slide 125: Three-Story Office Building with Intermediate Precast Concrete Shear Walls

## Slide 126: Three-Story Office Building with Intermediate Precast Concrete Shear Walls
Notes: The figure slide shows the plan of the building. The plan is 150 ft long and 120 ft long with interior stairs and interior elevator cores.
Design example for intermediate precast walls in three-story office in Seismic Design Category B. These walls can be used up to any height in Seismic Design Categories B and C but are limited to 40 feet for Seismic Design Categories D, E, and F.
ACI 318 Section 21.4.2 requires that yielding between wall panels or between wall panels and the foundation be restricted to steel elements. However, the Provisions are more specific in their means to accomplish the objective of providing reliable post-elastic performance. Provisions Section 21.4.3 (ACI 318 Sec. 21.4.4) requires that connections that are designed to yield be capable of maintaining 80 percent of their design strength at the deformation induced by the design displacement. Alternatively, they can use Type 2 mechanical splices.
This precast concrete building is a three-story office building (Occupancy Category II) in southern New England on Site Class D soils. The structure utilizes 10-foot-wide by 18-inch-deep prestressed double tees (DTs) spanning 40 feet to prestressed inverted tee beams for the floors and the roof. The DTs are to be constructed using lightweight concrete. Each of the above-grade floors and the roof are covered with a 2‑inch-thick (minimum), normal-weight cast-in-place concrete topping. The vertical seismic force-resisting system is to be constructed entirely of precast concrete walls located around the stairs and elevator/mechanical shafts. The only features illustrated in this example are the rational selection of the seismic design parameters and the design of the reinforcement and connections of the precast concrete shear walls.

## Slide 127: Three-Story Office Building with Intermediate Precast Concrete Shear Walls
Table 11.2-1 Design Parameters | 
Design Parameter | Value
Risk Category | II
Importance Factor, Ie | 1.0
SS | 0.266
S1 | 0.08
Site Class | D
Fa | 1.59
Fv | 2.4
SMS = FaSS | 0.425
SM1 = FvS1 | 0.192
Seismic Parameters
Notes: The precast walls are estimated to be 8 inches thick for building mass calculations. These walls are normal-weight concrete with a 28-day compressive strength, f'c, of 5,000 psi. Reinforcing bars used at the ends of the walls and in welded connectors are ASTM A706 (60 ksi yield strength). The concrete for the foundations and below-grade walls has a 28-day compressive strength, f'c, of 4,000 psi.
Design example for intermediate precast walls in three-story office. Slide shows the seismic parameters from the Table in the example.

## Slide 128: Three-Story Office Building with Intermediate Precast Concrete Shear Walls
Table 11.2-1 Design Parameters | 
Design Parameter | Value
SDS = 2/3 SMS | 0.283
SD1 = 2/3 SM1 | 0.128
Seismic Design Category | B
Basic Seismic Force-Resisting System | Bearing Wall System
Wall Type | Intermediate Precast Shear Walls
R | 4
Ω0 | 2.5
Cd | 4
Seismic Parameters
Notes: The precast walls are estimated to be 8 inches thick for building mass calculations. These walls are normal-weight concrete with a 28-day compressive strength, f'c, of 5,000 psi. Reinforcing bars used at the ends of the walls and in welded connectors are ASTM A706 (60 ksi yield strength). The concrete for the foundations and below-grade walls has a 28-day compressive strength, f'c, of 4,000 psi.
Design example for intermediate precast walls in three-story office. Slide shows the seismic parameters from the Table in the example.

## Slide 129: Structural Design Considerations
Precast Shear Wall System. This system is designed to yield in bending at the base of the precast shear walls without shear slip at any of the joints. The remaining connections (shear connectors and flexural connectors away from the base) are then made strong enough to ensure that the inelastic action is forced to the intended location.
The basic load combinations require that seismic forces and gravity loads be combined in accordance with the factored load combinations presented in Standard Section 12.4.2.3.
Notes: The slide provides the description of the intent of design for the intermediate precast concrete wall system. The design develops a ductile mechanism for energy dissipation, and then designs other connection elements in the load path to remain elastic.
Although it would be desirable to force yielding to occur in a significant portion of the connections, it frequently is not possible to do so with common configurations of precast elements and connections. The connections are often unavoidable weak links. Careful attention to detail is required to assure adequate ductility in the location of first yield and to preclude premature yielding of other connections.

## Slide 130: Load Combinations
The relevant load combinations from ASCE 7 are as follows:
(1.2 + 0.2SDS)D ± QE + 0.5L
(0.9 - 0.2SDS)D ± QE
Substituting SDS as determined above and  as 1.0 for SDC B, these load combinations become:
1.26D + QE + 0.5L
0.843D - QE
Notes: The slide provides the description of the intent of design for the intermediate precast concrete wall system. The design develops a ductile mechanism for energy dissipation, and then designs other connection elements in the load path to remain elastic.
Although it would be desirable to force yielding to occur in a significant portion of the connections, it frequently is not possible to do so with common configurations of precast elements and connections. The connections are often unavoidable weak links. Careful attention to detail is required to assure adequate ductility in the location of first yield and to preclude premature yielding of other connections.

## Slide 131: Seismic Weight
For the roof and two floors:
18-inch double tees (32 psf) + 2-inch topping (24 psf) = 56.0 psf
Precast beams at 40 feet = 12.5 psf
16-inch square columns = 4.5 psf
Ceiling, mechanical, miscellaneous = 4.0 psf
Exterior cladding (per floor area) = 5.0 psf
Partitions = 10.0 psf
Total = 92.0 psf

## Slide 132: Seismic Weight
The weight of each floor including the precast shear walls is:
(120 ft)(150 ft)(92 psf / 1,000) +
[(15 ft)4 + (25 ft)2](12 ft)(0.10 ksf) = 1788 kips
Considering the roof to be the same weight as a floor, the total building weight is W = 3(1788 kips) = 5364 kips.

## Slide 133: Base Shear
Equation 12.8-2:
except that it need not exceed the value from Standard Equation 12.8-3 computed as:
where T is the fundamental period of the building computed using the approximate method of Standard Equation 12.8-7:
Therefore, use Cs = 0.0708, which is larger than the minimum specified in Standard Equation 12.8-5:
Cs = 0.044(SDS)(Ie) ≥ 0.01 = 0.044(0.283)(1.0) = 0.012
The total seismic base shear is then calculated using Standard Equation 12.8-1 as: V = CsW = (0.0708)(5,364) = 380 kips
Notes: Calculation of base shear from the equivalent lateral force equations of the provisions is shown with the values determined in the example. Note that this force is substantially larger than a design wind would be. If a nominal 20 psf were applied to the long face and then amplified by a load factor of 1.6, the result would be less than half this seismic force already reduced by an R factor of 4.

## Slide 134: Vertical Distribution of Seismic Base Shear
Since the period, T, is less than 0.5 seconds, k = 1 in both building directions.
The seismic lateral force, Fx, at any level is determined in accordance with Standard Section 12.8.3:
Resulting values of Fx are as follows:
  Roof: Fr = 190 kips
  Third Floor: F3 = 127 kips
  Second Floor: F2 = 63 kips

## Slide 135: Horizontal Distribution of Seismic Force and Torsion
Longitudinal Direction:
Design each of the 25-ft-long walls at the elevator/mechanical shafts for half the total shear. Since the longitudinal walls are very close to the center of rigidity, assume that torsion will be resisted by the 15-ft-long stairwell walls in the transverse direction. The forces for each of the longitudinal walls are shown in the next figure.

## Slide 136: Forces on the longitudinal walls
Notes: Vertical distribution of base shear is shown in the example calculations for the entire structure.
The seismic lateral force ,Fx, at any level is determined in accordance with Standard Section 12.8.3.
Since the period, T, is less than 0.5 seconds, k = l in both building directions. The total lateral forces are calculated as:
Roof: Cvr = 0.50; Fr = 190 kips
Third Floor: Cv3 = 0.333; F3 = 127 kips
Second Floor: Cv2 = 0.167; F2 = 63 kips
Since torsion is assumed to be carried by the walls in the transverse direction, the forces to each of two walls (as shown in the slide) in the direction under consideration is half the total, and these are the forces illustrated in the figure.

## Slide 137: Overturning Moment on Longitudinal Walls
ME = (95 kips)(36 ft) + (63.5 kips)(24 ft) + (31.5 kips)(12 ft) = 5,320 ft-kips
Notes: The figure shows the free-body diagram for one longitudinal wall. The tension connection at the base of the precast panel to the below-grade wall is governed by the seismic overturning moment and the dead loads of the panel and supported floors and roof. In this example, the weights for an elevator penthouse, with a floor and equipment load at 180 psf between the shafts and a roof load at 20 psf, are included. The weight for the floors includes double tees, ceiling, and partitions (total load of 70 psf) but not beams and columns. Floor live load is 50 psf, except 100 psf is used in the elevator lobby. Roof snow load is 30 psf.

## Slide 138: Overturning
Using the load combinations described before, the vertical loads for combining with the overturning moment are computed as:
Pmax = 1.26D + 0.5L + 0.2S = 397 kips
Pmin = 0.843D = 239 kips
The tension reinforcement can be found from a simple couple.
The effective moment arm is:
jd = 25 - 1.5 = 23.5 ft
Notes: Calculation of tension reinforcing considering the gravity load effects, reduced by .9-SDS is shown.

## Slide 139: End Reinforcement
The required reinforcement is:
As = Tu/ϕfy = (107 kips)/[0.9(60 ksi)] = 1.98 in.2
Use two #9 bars (As = 2.0 in.2) at each end with Type 2 couplers for each bar at each panel joint. Since the flexural reinforcement must extend a minimum distance, d, (the flexural depth) beyond where it is no longer required, use both #9 bars at each end of the panel at all three levels for simplicity
At this point a check per ACI 318 Section 16.2.5 will be made. Bearing walls must have vertical ties with a nominal strength exceeding 3 kips per foot and there must be at least two ties per panel. With one tie at each end of a 25-foot panel, the demand on the tie is:
Tu = (3 kip/ft)(25 ft)/2 = 37.5 kips
The two #9 bars are more than adequate for the ACI requirement.
Notes: Design shear panels to resist overturning by means of reinforcing bars at each end with a direct tension coupler at the joints.
The results of the calculation for overturning and selection of the end reinforcing is covered on this slide.
Although the transverse direction walls are covered in the guide, they are not covered here in the interest of time.

## Slide 140: End Reinforcement
Notes: Figure on the left shows an along-the-height cross section of an 8” thick precast longitudinal shear wall. The wall is reinforced by two No. 9 full height vertical bars at each end. Direct tension coupler is used to transfer the force in the bars wherever required. Figure on the right shows a cross section of the base of a precast shear wall supported by a 28” thick reinforced concrete foundation. Dowels with standard hook are used to develop overturning reinforcement with a 3” minimum clear cover from the bottom of the foundation.

## Slide 141: Shear Connections and Reinforcement
Panel joints often are designed to resist the shear force by means of shear friction, but that technique is not used for this example because the joint at the foundation will open due to flexural yielding.
Alternatively, the joint can be designed with direct shear connectors that will prevent slip along the joint. That concept is developed here.
Notes: Notes on base shear design for the guide are covered here.
The joint opening would concentrate the shear stress on the small area of the dry-packed joint that remains in compression. This distribution can be affected by the shims used in construction. With care taken to detail the grouted joint, shear friction can provide a reliable mechanism to resist this shear.

## Slide 142: Shear Connection Force
The design shear force is based on the yield strength of the flexural connection. The flexural strength of the connection can be approximated as follows:
Therefore, the design shear, Vu, at the base is 1.5(1.41)(190 kips) = 402 kips.
Notes: Base shear design is based 1.5 times the strength of the yielding connection in accordance with the provisions.

## Slide 143: Shear Connection Detail
Notes: The figure illustrates a welded connection with an embedded plate with tail bars developed in the wall and a foundation plate anchored with headed anchor studs. The connection is made with two face plates, one on each side of the wall.
The base shear connection is shown in the figure and is to be flexible vertically but stiff horizontally in the plane of the panel. The vertical flexibility is intended to minimize the contribution of these connections to overturning resistance, which would simply increase the shear demand.

## Slide 144: Shear Connection Design
Assembly with two face plates measuring 3/8" × 4" × 12" connected by a C8x18.75 and with diagonal #5 bars as shown in the figure. In the field, weld an L4×3×5/16 × 0'‑8", long leg horizontal, on each face. The shear capacity of this connection is checked as follows:
Shear in the two loose angles:
ϕVn = ϕf(0.6Fu)tl(2) = (0.75)(0.6)(58 ksi)(0.3125 in.)(8 in.)(2) = 130.5 kips
Weld at toe of loose angles:
ϕVn = ϕ(0.6Fu)tel(2) = (0.75)(0.6)(70 ksi)(0.25 in./(√2)(8 in.)(2) = 89.1 kips
Weld at face plates, using Table 8-8 in AISC Manual (14th edition):
ϕVn= 0.75(1.73)(1.0)(4)(8)(2) = 83.0 kips
Bearing of concrete at steel channel:
fc = f(0.85f'c) = 0.65(0.85)(5 ksi) = 2.76 ksi
Notes: All of the links in the load path should be checked . The slide shows the calculations for shear strength of the connection by checking this load path.

## Slide 145: Shear Connection Design
The bearing will be controlled by bending in the web: compute the width (b) of flange loaded at 2.76 ksi that develops the plastic moment in the web:
Mp = ϕFytw2/4 = (0.9)(50 ksi)(0.4872 in.2)/4 = 2.67 in.-kip/in.
Mu = fc[(b-tw)2/2 - (tw/2)2/2] = 2.76[(b - 0.243 in.)2 - (0.243 in.)2]/2
setting the two equal results in b = 1.65 in.
Therefore, bearing on the channel is:
ϕVc = fc(2 - tw)(l) = (2.76 ksi)[(2(1.65) - 0.487 in.](6 in.) = 46.6 kips
To the bearing capacity on the channel is added the four #5 diagonal bars, which are effective in tension and compression;
ϕ = 0.75 for shear is used here:
ϕVs = ϕfyAscosα = (0.75)(60 ksi)(4)(0.31 in.2)(cos45°) = 39.5 kips Thus, the total capacity for transfer to concrete is:
ϕVn = ϕVc + ϕVs = 46.6 + 39.6 = 86.1 kips
Notes: The bearing strength is considered in the load path, and the calculations for the bearing strength limit of the connection are included.

## Slide 146: Shear Connection Design: Foundation Plate
In the foundation, provide an embedded plate 1/2" × 12" × 1'‑6" with six 3/4-in.-diameter headed anchor studs.
The capacity of the plate in the foundation is governed by the headed anchor studs. Capacity in shear for anchors located far from an edge of concrete, such as these and with sufficient embedment to avoid the pryout failure mode is governed by the capacity of the steel, which is required by ACI 318 Section 17.5.1:
ϕVsa =ϕ n Ase futa = (0.65)(6 studs)(0.44 in.2 per stud)(60 ksi) = 103 kips
Notes: Design for anchorage to concrete of the foundation embed plate is covered.

## Slide 147: Shear Connection Summary
The various shear capacities of the connection are as follows:
  Shear in the two loose angles: 130.5 kips
  Weld at toe of loose angles: 89.1 kips
  Weld at face plates: 83.0 kips
  Transfer to concrete: 86.1 kips
  Headed anchor studs at foundation: 103 kips
The number of embedded plates (n) required for a panel is:
n =402/83.0 = 4.8
Use five connection assemblies, equally spaced along each side (4'-0" on center works well to avoid the end reinforcement). The plates are recessed to position the #5 bars within the thickness of the panel and within the reinforcement of the panel.
Consider how much moment capacity is added by these connections to the vertical uplift at the joint.
Notes: Shear connection design summary is given and the selection of the number of connections is shown in this slide.
The total demand moment, for which the entire system is proportioned, is 5,320 ft-kips. Thus, these connections will add approximately 5 percent to the resistance, and ignoring this contribution is reasonable. If a straight plate measuring 1/4 inch by 8 inches (which would be sufficient) were used and if the welds and foundation embedment did not fail first, the tensile capacity would be 72 kips each, a factor of 42 increase over the angles, and the shear connections would have the unintended effect of more than doubling the flexural resistance, which would require a much higher shear resistance to develop a plastic hinge at the wall base.

## Slide 148: One-Story Precast Shear Wall Building

## Slide 149: One-Story Precast Shear Wall Building
This example illustrates the design of a precast concrete shear wall for a single-story building assigned to a high seismic design category.
The precast concrete building is a single-story industrial warehouse building (Risk Category II) on Site Class C soils.
The precast wall panels used in this building are typical DT wall panels.
Walls are designed using intermediate precast structural walls.
Notes: The design example is for a single story building with perimeter shear wall panels. This example shows the design for intermediate precast concrete walls in SDC D.
The structure has 8-foot-wide by 12.5-inch-deep prestressed double tee (DT) wall panels. The roof is light gage metal decking spanning to bar joists that are spaced at 4 feet on center to match the location of the DT legs. The center supports for the joists are joist girders spanning 40 feet to steel tube columns. The vertical seismic force-resisting system is the precast/prestressed DT wall panels located around the perimeter of the building. The average roof height is 20 feet, and there is a 3-foot parapet.
The slide describes the precast building.

## Slide 150: One-Story Precast Shear Wall Building
Notes: The figure shows a plan of the building. The building is 120 ft long and 96 ft wide.
The precast wall panels used in this building are typical DT wall panels commonly found in many locations but not normally used in southern California. For these wall panels, an extra 1/2 inch has been added to the thickness of the deck (flange). This extra thickness is intended to reduce cracking of the flanges and provide cover for the bars used in the deck at the base.
The wall panels are normal-weight concrete with a 28-day compressive strength of f'c = 5,000 psi. Reinforcing bars used in the welded connections of the panels and footings are ASTM A706 (60 ksi). The concrete for the foundations has a 28-day compressive strength of f'c = 4,000 psi.

## Slide 151: One-Story Precast Shear Wall Building
Table 11.3-1 Design Parameters | 
Design Parameter | Value
Risk Category | II
Importance Factor, Ie | 1.0
SS | 1.5
S1 | 0.6
Site Class | C
Fa | 1.0
Fv | 1.3
SMS = FaSS | 1.5
SM1 = FvS1 | 0.78
Seismic Parameters
Notes: In Standard Table 12.2-1 the values for special reinforced concrete shear walls are for both cast-in-place and precast walls. In Section 2.3, ACI 318 defines a special structural wall as “a cast-in-place structural wall in accordance with 18.2.3 through 18.2.8 and 18.10; or a precast structural wall in accordance with 18.2.3 through 18.2.8 and 18.11.” ACI 318 Section 18.11 defines requirements for special structural walls constructed using precast concrete, including that the wall must satisfy all of the requirements of ACI 318 Section 18.10.
Unfortunately, several of the requirements of ACI 318 Section 18.10 are problematic for a shear wall system constructed using DT wall panels. Therefore, these walls will be designed using the ACI category of intermediate precast structural walls.
Design parameter table for the example building using intermediate precast concrete walls is given in this slide and the next slide.

## Slide 152: One-Story Precast Shear Wall Building
Table 11.3-1 Design Parameters | 
Design Parameter | Value
SDS = 2/3 SMS | 1.0
SD1 = 2/3 SM1 | 0.52
Seismic Design Category | D
Basic Seismic Force-Resisting System | Bearing Wall System
Wall Type | Intermediate Precast Shear Walls
R | 4
Ω0 | 2.5
Cd | 4
Seismic Parameters

## Slide 153: Intermediate Precast Concrete Wall Panels
The intent of the intermediate precast structural wall requirements is to provide yielding in a dry connection in flexure at the base of each precast shear wall panel while maintaining significant shear resistance in the connection.
The flexural connection for a wall panel at the base is located in one DT leg while the connection at the other leg is used for compression. Per ACI 318 Section 18.5, these connections must yield only in steel elements or reinforcement
All other elements of the connection (including shear resistance) must be designed for 1.5 times the force associated with the flexural yield strength of the connection.
Notes: A summary of the requirements and design intent for intermediate precast concrete shear walls is provided.
Yielding will develop in the dry connection at the base by bending in the horizontal leg of the steel angle welded between the embedded plates of the DT and footing. The horizontal leg of this angle is designed in a manner to resist the seismic tension of the shear wall due to overturning and then yield and deform inelastically. The connections on the two legs of the DT are each designed to resist 50 percent of the shear. The anchorage of the connection into the concrete is designed to satisfy the 1.5Sy requirements of ACI 318 Section 21.4.3. Careful attention to structural details of these connections is required to ensure tension ductility and resistance to large shear forces that are applied to the embedded plates in the DT and footing.

## Slide 154: System Force Calculations
Flexible diaphragm
Equivalent lateral force method
Load combinations
Earthquake forces
  Building weight
  Base shear
  Horizontal distribution without torsion for flexible diaphragm
Notes: Design assumptions and steps in calculation for lateral forces are listed:
The metal deck roof acts as a flexible horizontal diaphragm to distribute seismic inertia forces to the walls parallel to the earthquake motion (Standard Sec. 12.3.1.1).
The building is regular both in plan and elevation.
The redundancy factor, ρ, is determined in accordance with Standard Section 12.3.4.2. For this structure, which is regular and has more than two perimeter wall panels (bays) on each side in each direction, ρ = 1.0. The structural analysis to be used is the ELF procedure (Standard Sec. 12.8) as permitted by Standard Table 12.6-1.
Orthogonal load combinations are not required for flexible diaphragms in Seismic Design Category D (Standard Sec. 12.5.4).
The basic load combinations (Standard Sec. 12.4.2.3) require that seismic forces and gravity loads be combined in accordance with the following factored load combinations:
(1.2 + 0.2SDS)D ± rQE + 0.5L+ 0.2S
(0.9 - 0.2SDS)D ± rQE + 1.6H
At this flat site, both S and H equal 0. Note that roof live load need not be combined with seismic loads, so the live load term, L, can be omitted from the equation. Therefore:
1.4D + rQE
0.7D - rQE
These load combinations are for the in-plane direction of the shear walls.
The earthquake force considerations are listed by bullet points due to the limited time for the presentation. The detailed calculations can be found in the guide.

## Slide 155: Longitudinal Direction Design
Vu = 4.25 kips/panel
Notes: The figures shows the free-body diagram of the longitudinal wall panel.
The total shear along each side of the building is V/2 = 46.75 kips. The maximum shear on longitudinal panels (at the side with the openings) is:
Vlu = 46.75/11 = 4.25 kips
On each side, each longitudinal wall panel resists the same shear force as shown in the free-body diagram of the figure, where D1 represents roof joist reactions and D2 is the panel weight.

## Slide 156: Tension and Shear Forces at the Panel Base
Design each precast shear panel to resist the seismic overturning moment by means of a ductile tension connector at the base of the panel.
  A steel angle connector will be provided at the connection of each leg of the DT panel to the concrete footing.
  The horizontal leg of the angle is designed to yield in bending as needed in an earthquake.
  ACI 318 Section 18.5 requires that dry connections at locations of nonlinear action comply with applicable requirements of monolithic concrete construction and satisfy both of the following:
    Where the moment action on the connection is assumed equal to 1.5My, the co-existing forces on all other components of the connection other than the yielding element shall not exceed their design strength.
    The nominal shear strength for the connection shall not be less than the shear associated with the development of 1.5My at the connection.
Notes: Base connection design yielding and design for overstrength of other connection actions. The slide describes the connection and the actions considered.

## Slide 157: Longitudinal Direction
The maximum tension for the connection at the base of the precast panel to the concrete footing is governed by the seismic overturning moment and the dead loads of the panel and the roof.
At the base:
ME = (4.25 kips)(20 ft) = 85.0 ft-kips
Dead loads:
SD = 2(1.08) + 7.73 = 9.89 kips
1.4D = 13.8 kips
0.7D = 6.92 kips
Compute the tension force due to net overturning based on an effective moment arm, d, of 4.0 ft (the distance between the DT legs). The maximum is found when combined with 0.7D:
Tu = ME/d - 0.7D/2 = 85.0/4 - 6.92/2 = 17.8 kips
Notes: Base connection tension from overturning moment and sustained gravity resistance calculation is shown. Notes that 0.7D comes from the load combination (0.9-0.2SDS) and 1.4 comes from (0.9+0.2SDS). These factors consider the vertical acceleration effects.

## Slide 158: Size the Yielding Angle
Notes: The angle, which is the ductile element of the connection, is welded between the plates embedded in the DT leg and the footing. This angle is an L5×3-1/2×3/4 × 0'‑6-1/2" with the long leg vertical. The steel for the angle and embedded plates will be ASTM A572, Grade 50. The horizontal leg of the angle needs to be long enough to provide significant displacement at the roof, although this is not stated as a requirement in either in a code or standard. This will be examined briefly here. The angle and its welds are shown in the figure.

## Slide 159: Size the Yielding Angle
The location of the plastic hinge in the angle is at the toe of the fillet (at a distance, k, from the heel of the angle.) The bending moment at this location is:
Mu = Tu(3.5 - k) = 17.8(3.5 - 1.1875) = 41.2 in.-kips
Using ACI 318 Section 18.5.2.2, the tension force for the remainder of this connection and the balance of the wall design are based upon a probable strength equal to 150 percent of the yield strength. Thus:
Notes: Calculation of the bending in connection angle and tension resistance are shown in the slide.
The calculation shows that the calculated strength is slightly less than the demand, but providing a stronger angle (e.g., a shorter horizontal leg) will simply increase the demands on the remainder of the assembly.

## Slide 160: Size the Yielding Angle
The amplifier, required for the design of the balance of the connection, is:
The shear on the connection associated with this force in the angle is:
Check the welds for the tension force of 27.0 kips and a shear force 6.46 kips.
Notes: Using ACI 318 Section 18.5.2.2, the tension force for the remainder of this connection and the balance of the wall design are based upon a probable strength equal to 150 percent of the yield strength.

## Slide 161: Size the Yielding Angle
The Provisions Section 14.2.2.4 (ACI 318 18.5) requires that connections that are designed to yield be capable of maintaining 80 percent of their design strength at the deformation induced by the design displacement. For yielding of a flat bar (angle leg), this can be checked by calculating the ductility capacity of the bar and comparing it to Cd.
Notes: The Provisions Section 14.2.2.4 (ACI 318 18.5) requires that connections that are designed to yield be capable of maintaining 80 percent of their design strength at the deformation induced by the design displacement. For yielding of a flat bar (angle leg), this can be checked by calculating the ductility capacity of the bar and comparing it to Cd. Note that the element ductility demand (to be calculated below for the yielding angle) and the system ductility, Cd, are only equal if the balance of the system is rigid. This is a reasonable assumption for the intermediate precast structural wall system described in this example.
The idealized yield deformation of the angle is calculated as shown in the slide.

## Slide 162: Welds to Connection Angle
Welds will be fillet welds using E70 electrodes.
For the base metal, ϕRn = ϕ(Fy)ABM.
For which the limiting stress is ϕFy = 0.9(50) = 45.0 ksi.
For the weld metal, ϕRn = ϕ(Fy)Aw = 0.75(0.6)70(0.707)Aw.
For which the limiting stress is 22.3 ksi.
Size a fillet weld, 6.5 inches long at the angle to the embedded plate in the footing. Using an elastic approach:
Resultant force =
Aw = 27.8/22.3 = 1.24 in.2
t = Aw/l =1.24 in.2 / 6.5 in. = 0.19 in.
For a ¾-in. angle leg, use a 5/16-in. fillet weld. Given the importance of this weld, increasing the size to 3/8 in. would be a reasonable step.
Notes: Weld design calculations are also based on providing the overstrength required.

## Slide 163: Welds to Connection Angle
It is conservative to limit the maximum strain in the bar to esh = 15ey. At this strain, a flat bar would be expected to retain all its strength and thus meet the requirement of maintaining 80 percent of its strength.
Assuming a plastic hinge length equal to the section thickness:
Since the ductility capacity at strain hardening is 0.112/0.012 = 9.3 is larger than Cd = 4 for this system, the requirement of Provision Section 14.2.2.4 (ACI 318 Sec. 18.5) is met.
Notes: Weld design calculations, continued. The displacement from plastic hinge rotation is compared to yield deflection to determine the ductility of the connection compared to the design displacement amplification factor.

## Slide 164: Base Connection Detail
Notes: Base connection detail from the design calculations. The figure shows anchorage of the plate embedded in the double tee to include bars that project into the stem for development.
Although the design examples continues with overstrength design of the precast panel, the requirements for overstrength design of the provisions are limited to the non-yielding elements of connections.

## Slide 165: Special Moment Frame Constructed Using Precast Concrete

## Slide 166: Special Moment Frame Constructed Using Precast Concrete
As for special moment frames of concrete, the Standard does not distinguish between a cast-in-place and a precast concrete special moment frame in Table 12.2-1.
ACI 318 Section 18.9 provides requirements for special moment frames constructed using precast concrete.
That section provides requirements for designing special precast concrete frame systems using either ductile connections (ACI 318 Sec. 18.9.2.1) or strong connections (ACI 318 Sec. 18.9.2.2).
Notes: Introduction to review of special moment frames constructed using precast concrete construction. This method is considered “emulation” of monolithic cast-in-place concrete.

## Slide 167: Ductile Connectors
For moment frames constructed using ductile connections, ACI 318 allows plastic hinges to form in the connection region. All of the requirements for special moment frames must still be met, plus there is a factor larger than 1.0 that must be applied in computing the shear demand at the joint.
It is interesting to note that while Type 2 connectors can be placed anywhere (including in a plastic hinge region) in a cast-in-place frame or a precast frame with strong connections, these same connectors cannot be placed closer than h/2 from the joint face in a precast frame with ductile connections. The objective of a Type 2 connector is that it directs the yielding away from the connector, into the bar itself.
Notes: Description of requirements for ductile connections form the text is provided. In a precast frame with ductile connections, inelastic deformations take place within the region between a joint face and the connector at least h/2 away from it. The minimum distance of h/2 is intended to avoid strain concentrations over the short length of reinforcement between the joint face and the adjacent splice device.

## Slide 168: Ductile Connectors
Notes: Figure showing offset of Type 2 splice from face of column for ductile connection design. The figure shows a space between the end of the precast beam and the face of the precast column that permits the offset of the splice to meet the distance of h/2 from the face of the support. This space would be filled with cast-in-place concrete to complete the joint.

## Slide 169: Strong Connections
ACI 318 also provides design rules for strong connections used in special moment frames. The concept is to provide connections that are strong enough to remain elastic when plastic hinges form in the beam away from the connections.
Notes: Description and figure for strong connections with ductile region offset from face of column. The figure shows splice couplers at the face of the column, but the reinforcing must be proportioned to ensure sufficient strength in the region of the splice so that yielding occurs in the beam beyond the ends.

## Slide 170: Strong Connection Example
A single-bay frame is designed to meet the requirements of a precast frame using strong connections at the beam-column interface.
Reinforcing the beam with three #10 bars top and bottom, the nominal moment strength of the beam is:
Notes: Calculation of moment strength of beam in frame example

## Slide 171: Strong Connection Example
This is the moment strength at the plastic hinge location. The strong precast connection must be designed for the loads that occur at the connection when the beam at the plastic hinge location develops its probable strength. The moment strength at the beam-column interface (which also is the precast joint location) must be at least:
Notes: Calculation of the probable moment strength of beam joint in frame example is shown in the slide.

## Slide 172: Strong Connection Example
Therefore, the design strength of the connection must be at least:
Using #14 bars to the column side of the Type 2 coupler:
which is greater than the load at the connection (843 ft-kips) when the plastic hinge develops.
Notes: Calculation of moment strength for strong connection of beam in frame example is shown.
If column-to-column connections are required, ACI 318 Section 18.9.2.2(e) requires a 1.4 amplification factor, in addition to loads associated with the development of the plastic hinge in the beam. Locating the column splice near the point of inflection, while difficult for construction, can help to make these forces manageable.

## Slide 173: Examples for Seismic Design of Precast Concrete
Diaphragms in moderate and high seismic design categories
Intermediate precast concrete shear walls in moderate and high seismic design categories
Special moment frames constructed using precast concrete with emulation details
Notes: This is a slide provided as a summary of the examples covered in the presentation.

## Slide 174: Seismic Design of Precast Concrete
Precast concrete designs must reflect the jointed nature of the material assembly
Precast concrete code requirements include detailing to add ductility and redundancy to allow comparison with (emulation of) monolithic cast-in-place concrete
Special moment frames constructed using precast concrete with emulation details include requirements beyond monolithic construction for bar splices
Notes: A summary slide on the general considerations for the seismic design of precast concrete structural systems.

## Slide 175: Seismic Design of Precast Concrete
Precast concrete designs that recognize certain benefits of the jointed nature of the construction are recognized by ACI 318.
Special moment-resisting frames using a hybrid system are covered under ACI 374.1-05 and TI.2-03.
Special precast concrete shear walls using unbonded post-tensioning are covered under ACI ITG 5.1 and ITG 5.2.
Notes: A slide to recognize that precast systems based on jointed behavior rather than emulation of monolithic cast-in-place concrete can also be used, but these are beyond the scope of the provision.

## Slide 176: Questions
Notes: This slide is a placeholder for opening the floor up to questions

## Slide 177: DISCLAIMER
NOTICE: Any opinions, findings, conclusions, or recommendations expressed in this publication do not necessarily reflect the views of the Federal Emergency Management Agency. Additionally, neither FEMA nor any of its employees make any warranty, expressed or implied, nor assume any legal liability or responsibility for the accuracy, completeness, or usefulness of any information, product or process included in this publication.
The opinions expressed herein regarding the requirements of the NEHRP Recommended Seismic Provisions, the referenced standards, and the building codes are not to be used for design purposes. Rather the user should consult the jurisdiction’s building official who has the authority to render interpretation of the code.
Any modifications made to the file represent the presenters' opinion only.