## Slide 1: Composite Steel/Concrete
Disclaimer
Notes: Title slide, consisting of an image of the cover of the data disk containing the 2015 NEHRP Recommended Seismic Provisions. The author for this section, titled “Composite Steel and Concrete” is Clinton O. Rex.
This is an introductory slide
Explain that Chapter 12 is dealing with Composite Steel and Concrete seismic lateral force resisting systems; but, that the only system covered in the examples at this point is the C-PRMF system. Other systems are viable and recognized by the Provisions and AISC Seismic; but, none have the maturity of the C-PRMFsystem as of yet. The 2012 AISC Seismic Manual has examples of other composite systems such as steel link beam coupled shear walls.

## Slide 2: Introduction
Outline For The Presentation
Background and Overview
Example Building
PR Composite Connection Design
Loads and Load Combinations
Analysis
ASCE 7-10 and AISC Design Checks
Questions
Notes: The consists of text outlining the key topics in this presentation. Topics include background, an example building, composite PR connections, loads, an analysis of a PR building, code checks, and finally questions.
This is a slide with the outline of the presentation
Going to convey the major design issues involved in the design of a C-PRMF system by introducing some background material and then walking through each of the major design considerations via an example building design.
First we will go through the literature that forms the basis for the design approach.
Second we will introduce you to the example building parameters.
Third we will focus on the Composite PR connection itself as it is the fundamental building block used to design this lateral system.
Fourth we will look into special considerations that one has to take care with regarding loads and their application.
Fifth we will focus on special aspects of analysis of a PR building
Sixth we will review a few of the basic code required design checks
Finally we will open it up for questions

## Slide 3: Background & Overview
Composite Partially Restrained Moment Frame (C-PRMF)
Typically Consists Of:
  Standard W-Shape Steel Columns
  Composite W-Shape Steel Beams
  Partially Restrained Composite Connections (PRCC)
Notes: This slide contains an image of a composite partially restrained moment frame, or C-PRMF frame.
This slide illustrates the basic structural components of a C-PRMF system
To date, most C-PRMF systems have been comprised of standard W-shape columns, W-shape composite beams, and the PRCC itself.
The frames are typically strong axis only frames (no bi-axial columns)
Testing has been done on bi-axial PRCC connections; however, to date, they are not widely used
HSS columns could be used and may be advantageous for the biaxial condition; however, the author is not aware of PRCC tests with HSS columns at this time
The typical PRCC connection has the component shown in the figure; however, there are other versions of this type of connection that have been tested.
Despite the testing of other versions, only the above version has been fully developed in the literature to a point that truly allows for the connection’s design

## Slide 4: Background & Overview
Different From A Typical Moment Frame
The PRCC is what makes the difference
  Not as strong (Partial Strength Vs. Full Strength)-Typically designed as partial strength
  Not as stiff (Angle between beam end and column does not stay at right angle)
  Can’t neglect the connection behavior through simplifying assumptions in the analysis
Notes: The figure on the left illustrates the true connection moment-rotation behavior (connection moment vs. relative rotation of the beam end relative to the column face), it also illustrates several connection stiffness values that could be used depending on where the connection is along its true behavior curve. The figure on the right illustrates the idea that if connections are stiff and strong enough to fall into the FR zone then the little bit of relative rotation that does occur has little affect on the analysis. At the other end, when a connection rotates very freely then the little bit of moment developed has little affect on the analysis. Between these two idealized zones of behavior lies the PR behavior zone. In this zone the relative rotation and the connection moments cannot be ignored.
This slide illustrates the Primary Differences Between C-PRMF and Typical Moment Frame
The connection is not as strong as the beam it is attaching to the column (what is known as partial strength).
Consequently the hinging occurs in the connection and not in the beam
PR (partially restrained) connections are not as stiff as FR (Fully restrained) connections, they allow relative rotation between the beam end and the column axis
The connection stiffness no longer allows us to conduct our analysis with the idealized assumptions of fully rigid or fully pinned (simple).
A reasonable approximation of the connection stiffness has to be considered in the frame analysis
The figure on the left illustrates the true connection moment-rotation behavior (connection moment vs. relative rotation of the beam end relative to the column face), it also illustrates several connection stiffness values that could be used depending on where the connection is along its true behavior curve
The figure on the right illustrates the idea that if connections are stiff and strong enough to fall into the FR zone then the little bit of relative rotation that does occur has little affect on the analysis. At the other end, when a connection rotates very freely then the little bit of moment developed has little affect on the analysis. Between these two idealized zones of behavior lies the PR behavior zone. In this zone the relative rotation and the connection moments cannot be ignored.

## Slide 5: Background & Overview
Different From A Typical Moment Frame
The connections become the seismic fuses for seismic energy dissipation (need ductile connections)
Limited yielding of beams and columns
Required to engage more frames because of the reduced stiffness and strength
Highly redundant lateral force resisting system
Typically simple fabrication and erection details are used allowing quicker fabrication and erection
Cannot delegate the design to the fabricator
PRCC connections are not fully effective until the concrete hardens – similar to waiting for moment connections to get welded
Notes: This slide consists entirely of text further developing the difference between a C-PRMF and typical moment frame.
This slide continues with the Primary Differences Between C-PRMF and Typical Moment Frame
Because the connections become the hinges in the system it is important that the connections be detailed in such a way to remain ductile through the expected rotations cycles the connection will see
Little to any yielding will be seen in the actual beams and columns since the connections are not capable of developing the yielding capacity of these elements
Because of the additional flexibility in the system that results from the weaker and less stiff PRCC connections it does become necessary to engage more columns and beams in the overall lateral load resisting system
More lower strength frames results in a highly redundant lateral load resisting system
Most traditional moment frame connections involve significant shop or field welding; as compared to the PRCC connections which involve no welding only bolting and the placing of reinforcing steel. This allows quick fabrication and erection
Unlike most simple connections and even some lateral connections (such as braced frame connections) the EOR cannot delegate the design of the PRCC connection since the details of the connection directly influence the lateral load resisting system response
The PRCC uses reinforcing steel and concrete in the slab as a major component of the connection. Consequently, until the slab has cured the connections are relatively weak and the building may require temporary guying

## Slide 6: Background & Overview
Table 12.2-1
ASCE 7-16 Provisions
Notes: This slide contains an image of the ASCE 7 provisions table (Table 12.2-1) highlighting the basis for the C-PRMF.
This slide illustrates the ASCE 7 provisions table as the basis for the system
The C-PRMF system is recognized in Section 12.2 of the Provisions as a pre-qualified seismic lateral load resisting system.
It is only allowed in seismic design categories (SDC A to D)
Note the height restrictions, these reflect limits of what has been theoretically studied for this type of system as well as some practical limits when one considers the increased connection demands for taller structures
Note that the system is assigned an R=6 which is between that for intermediate and special steel moment frames, so it is expected to see a good bit of deformation during a seismic event

## Slide 7: Background & Overview
ASCE 7-16 Provisions
14.3 – Composite Steel and Concrete Structures
14.3.1 Reference Documents
  The design, construction, and quality of composite steel and concrete members that resist seismic forces shall conform to the applicable requirements of the following:
  1. AISC 341
  2. AISC 360
  3. ACI 318, excluding Chapter 22
14.3.2 General
  Systems of structural steel acting compositely with reinforced concrete shall be designed in accordance with AISC 360 and ACI 318, excluding Chapter 22. Where required, the seismic design of composite steel and concrete systems shall be in accordance with the additional provisions of Section 14.3.3.
Notes: This slide contains text explaining further ASCE 7 provisions and other reference documents.
This slide outlines some of the ASCE 7 provisions
ASCE 7 really does not address the design of this system other than to say that one must design it in accordance with these reference standards

## Slide 8: Background & Overview
ASCE 7-16 Provisions
14.3 – Composite Steel and Concrete Structures
14.3.3 Seismic Requirements for Composite Steel and Concrete Structures
  Where a response modiﬁcation coefﬁcient, R, in accordance with Table 12.2-1 is used for the design of systems of structural steel acting compositely with reinforced concrete, the structures shall be designed and detailed in accordance with the requirements of AISC 341.
Notes: This slide contains text discussing the R factor for a C-PRMF
This slide outlines some of the ASCE 7 provisions
Under previous versions of ASCE 7, designers were designing the C-PRMF system with an R=3 and not requiring all the rules of AISC 341 (Seismic Provisions) be enforced.
Under the new ASCE 7 provisions, that is no longer allowed. This issue has also been directly addressed in AISC 360-16. It specifically states that all composite lateral systems have to be designed in accordance with AISC 341.

## Slide 9: Background & Overview
AISC 341-05 Provisions
Section G4. COMPOSITE PARTIALLY RESTRAINED (PR)
MOMENT FRAMES (C-PRMF)
G4.1. Scope
  This Section is applicable to frames that consist of structural steel columns and composite beams that are connected with partially restrained (PR) moment connections that meet the requirements in Specification Section B3.4b(b). Composite partially restrained moment frames (C-PRMF) shall be designed so that under earthquake loading yielding occurs in the ductile components of the composite PR beam-to-column moment connections. Limited yielding is permitted at other locations, such as column base connections. Connection flexibility and composite beam action shall be accounted for in determining the dynamic characteristics, strength and drift of C-PRMF.
Notes: This slide contains text outlining the AISC 341-05 provisions on C-PRMF.
Slide outlines provisions of AISC 341-05
At the time the 2009 NEHRP Provisions were being developed and published the AISC 341 in effect was the 2005 version. Consequently the AISC 341 rules described here are from the 2005 version rather than the 2010 version.
First, the rules for this system are found in Part II of the AISC Provisions. This section was dedicated to composite systems.
The primary issue to focus on from Section 8.1 is the fact that the connection flexibility cannot be ignored, the designer has to account for this flexibility in the frame design.

## Slide 10: Background & Overview
AISC 341-16 Provisions
Section G4
G4.5a. Columns
  Steel columns shall satisfy the requirements of Sections D1.1 for
  moderately ductile members.
G4.5b. Beams
  Composite beams shall be unencased, fully composite and shall meet the requirements of Section D1.1. A solid slab shall be provided for a distance of 12 in. (300 mm) from the face of the column in the direction of moment transfer. .
G4.6. Connections
  The required strength of the beam-to-column PR moment connections shall be determined considering the effects of connection flexibility and second-order moments. In addition, composite connections shall have a nominal strength that is at least equal to 50 percent of Mp, where Mp is the nominal plastic flexural strength of the connected structural steel beam ignoring composite action. Connections shall meet the requirements of Chapter I and shall have a total interstory drift angle of 0.02 radians that is substantiated by cyclic testing as described in Section G4.6d.
Notes: This slide contains text outlining additional provisions from AISC 341-05 on C-PRMF.
Slide outlines provisions of AISC 341-05
Section G4.5a invokes some of the typical seismic requirements on steel columns
Section G4.5b outlines the rules for the beams
  100% composite is required at this time because of the limited testing of beams with less than 100% composiite
  The effective moment of inertia accounts for the averaging of the negative and positive moments of inertia for a composite beam with reinforcing steel at the ends, this will be gone into more detail later in the presentation
Section G4.6 outlines the rules for the PRCC connections
  Second order analysis required
  The 50% requirement is an attempt to avoid having a building very weak connections that might be fully yielded (i.e. tangent stiffness of the connection near zero) under typical gravity loads
  Because most of the story drift associated with a C-PRMF building is concentrated at the connections itself, the interstory drift angle requirement amounts to a connection rotational ductility requirement. The idea is to provide a connection detail that can sustain repeated cycles of up to 20 mrad without significant degradation of strength and stiffness. Tests of the connections outlined in this example have shown their ability to meet this requirement

## Slide 11: Background & Overview
Other Design Guidance
AISC Design Guide 8 – 1996
ASCE Design Guide for Partially
Restrained Composite
Connections – 1998 (Journal
of Structural Engineering)
Notes: The picture shows an image of C-PRMF.
Slide gives additional resources used for the design of this system
As seen so far, there is really very little code guidance and very few rules found in the actual design codes for this seismic lateral force resisting system (in direct contrast to very specific rules for say a SMF)
To fill in the gap, the designer has to turn to the literature
The two primary pieces of literature that form the basis for the design of the C_PRMF system are above.
Of these the 1998 Journal paper is the latest and forms the majority of the basis for design; however, the 1996 design guide still provides information not in the ASCE journal paper which is still pertinent to the design of this type of frame
While both of these documents provide guidance for design of PRCC, the method presented in this design example deviates from that guidance based on more recent code requirements for stability and on years of experience in designing C-PRMF systems.

## Slide 12: Example Building
Building Plan
Notes: This image shows the building plan of the example building.
Slide shows example building plan
The example building is a four-story steel framed medical office building located in Denver, Colorado.
The building is free of plan and vertical irregularities.
Floor and roof slabs are 4.5-inch normal-weight reinforced concrete on 0.6-inch form deck (total slab depth of 4.5 inches.).
Typically slabs are supported by open web steel joists which are supported by composite steel girders.
Composite steel beams replace the joists at the spandrel locations to help control cladding deflections and provide the C-PRMF frames for the N-S lateral direction
Note that every column is engaged in the lateral load resisting system in one direction or the other
The PRCC connections are illustrated by the dots at the face of the column beam interface in the figure
Stair/Elevator opening is ignored for computing seismic mass

## Slide 13: Example Building
Building Elevations
Notes: This picture shows an image of an example building north, east and west side elevations.
Slide shows example building Elevations
The building is located in a relatively low seismic hazard region, but localized internal storage loading and Site Class E are used in this example to provide somewhat higher seismic design forces for purposes of illustration and to push the example building into Seismic De
The floor and roof slabs serve as horizontal diaphragms distributing the seismic forces and by inspection they are stiff enough to be considered as rigidsign Category C
The typical bay spacing is 25 feet.
Architectural considerations allowed an extra column at the end bay of each side in the north-south direction, which is useful in what is the naturally weaker direction.
Note the pins of the east-west frames at the end columns (coming into the weak axis of the end column)

## Slide 14: Example Building
Building 3-D SAP 2000 Model
Notes: This picture shows an image of an example building 3-D SAP model.
Slide shows example building 3-D SAP Model
The example building was modeled using the SAO 2000 analysis program v. 14.0 (Computers and Structures, Inc., Berkeley, CA)
Only the primary frame beams and columns were included in the model
Beams were connected to the columns via rotational spring elements
Column bases were considered “fixed” for analysis purposes

## Slide 15: PR Composite Connection Design
Typical W18x35 PRCC
Notes: This picture shows a typical PRCC at a W 18x35 beam to column.
Slide gives Details of a Typical PRCC at a W18x35 Beam to Column
This basic connection configuration is what has the most testing behind it in the literature and is what is directly addressed in terms of design guidance in the 1998 Journal paper and the AISC Design Guide 8
The primary components of the connection include a reinforced composite slab, a bolted-bolted double angle web connection, and a bolted seat angle connection
In real partially restrained building design, it is advantageous to select and design the complete PRCC simply based on beam depth and element capacities.
Generally it is impractical to “tune” connections to beam plastic moment capacities and/or lateral load demands.
This allows the designer to develop an in-house suite of PRCC details and associated behavior curves for each nominal beam depth ahead of time.
Slight adjustments can be made later to account for real versus nominal beam depth
The designer generally starts by maxing out the connection design capacity based on the practical limits of the pieces involved. . For instance, the largest angle leg commonly available is 8 inches, which can reasonably accommodate four 1-inch-diameter bolts. As a result, the maximum shear that can be delivered from the beam flange to the seat angle is limited by shear in four A490-X bolts. Bolt shear failure is generally considered to be non-ductile, so the rest of the connection design and detailing aims to maximize moment capacity of the connection while avoiding this limit state.

## Slide 16: PR Composite Connection Design
Typical W18x35 PRCC
Notes: This picture shows an image of reinforcing in a composite slab in plan.
Slide gives Details of the Reinforced Composite Slab
Reinforcing plays a key role in the behavior of the connection
Longitudinal bars (bars in line with the frame direction) are used to develop one component of the connection moment couple
Transverse steel is required to help provide equilibrium in the load transfer path from the slab to the column as well as to prevent transverse splitting of the slab immediately over the frame beams

## Slide 17: PR Composite Connection Design
    (ASCE TC, Eq. 4) Negative moment-rotation behavior (slab in tension):
    (ASCE TC, Eq. 3) Positive moment-rotation behavior (slab in compression):
Connection Moment-Rotation Curves
Two Curves Required:
  Service Analysis Curves From ASCE TC Paper
Notes: This slab contains two equations that are used to estimate the moment rotation behavior for the PRCC.
Slide gives the equations that are used to estimate the moment-rotation behavior for the PRCC connections
The above equations are found in the ASCE Journal Paper
Two different curves are provided to characterize the negative and the positive moment-rotation behavior
The above parametric moment rotation curves do not represent the results of any single test
The above parametric equations were developed by fitting the curves to lots of test data (both real and numerical)
Real test curves have jumps in them that result from bolt slip; however, these curves have smeared out those deformations into a single smooth curve
The above curves are considered to represent the “Nominal” behavior of the connection
This behavior is what we will use for service level design checks

## Slide 18: PR Composite Connection Design
McDAM = 0.85 Mc
    Elastic Stiffness Reduction:
    Strength Reduction:
Connection Moment-Rotation Curves
Two Curves Required:
  Strength Analysis Curves Based on Modifications of the Service Analysis Curves to Account for Direct Analysis Approach to Design
Notes: Slide contains more equations indicating the modifications for the moment ration curves if strength design is implemented.
Slide indicates what modifications have to be made to these curves when using them for strength design
The nominal moment-rotation behavior has to be modified to account for the requirements of the direct analysis procedure that is used for the design of the frames
First a 20% stiffness reduction is required
In order to apply a stiffness reduction, one must know the predicted stiffness of the connection. Because the connection behavior is non-linear from the start, the ASCE Journal paper recommends using the Secant stiffness at 2.5 mrad as the initial stiffness
Note that this will be different values for the positive and negative branches of the PR curves
The second modification required is to reduce the strength. The ASCE Journal paper recommends using a strength reduction factor of 0.85 (i.e. a 15% reduction in strength) on the nominal behavior to account for variability in the connection strength

## Slide 19: PR Composite Connection Design
Connection Moment-Rotation Curves
W18x35 PRCC Moment Rotation Curves
Notes: A graph with two moment rotation curves of a PRCC, one being the nominal curve and the other is the modified curve.
Slide shows the Resulting Moment Rotation Curves
The resulting moment rotation curves for the typical PRCC on a W18x35 is shown in this figure
The solid red line represents the nominal behavior
The dashed black line represents the modified behavior
Note the differences in positive and negative behavior (for example how much stiffer the connection is in negative bending (slab in tension) than in positive bending (angle in tension)

## Slide 20: PR Composite Connection Design
Table 9.2-1 Key Connection Values From Moment-Rotation Curves |  | 
 | W18x35 PRCC | W21x44 PRCC
Kci- (kip-in/rad) (nominal) | 704,497 | 1,115,253
Kci+ (kip-in/rad) (nominal) | 338,910 | 554,498
Mc- @ 20 mrad (kip-ft) (nominal/modified) | 232/206 | 367/326
Mc+ @ 10 mrad (kip-ft) (nominal/modified) | 151/127 | 240/202
Connection Moment-Rotation Curves
W18x35 PRCC Key Connection Curve Values
Notes: This slide contains a table of key values taken from the moment rotation curves for the two typical connection types used in the example building.
Slide shows the key values taken from the moment rotation curves for the two typical connection types used in the example building
From the curves there are a few key quantities that we will need later on in the design example for doing our analysis and for checking some of the code required checks
Because the curves are non-linear, one has to pick a rational point along the curve to identify as the moment capacity
The 10 mrad and 20 mrad points used above are what is recommended in the ASCE Journal paper for positive and negative moment portions of the curve
Again note the significant difference in strength and stiffness depending on the bending direction of the connection

## Slide 21: PR Composite Connection Design
Longitudinal Reinforcing Steel
Notes: This figure contains an image of longitudinal steel reinforcing of the composite slab, shown in plan.
Slide shows the composite slab reinforcing used in the example building
The typical reinforcing details for the example building are shown in the above figure
Key is using several small diameter well distributed reinforcing bars rather than a few large diameter bars
The primary negative moment resistance derives from tensile yielding of slab reinforcing steel.
Since ductile response of the connection requires that the reinforcing steel yield and elongate prior to failure of other connection components, providing too much reinforcing is not a good thing.
The following recommendations are from the ASCE Journal Paper

## Slide 22: PR Composite Connection Design
Longitudinal Reinforcing Steel
Minimum 6 Bars Distributed Evenly Over An Effective Width of 7 Column Flanges
Choose Sufficient Reinforcing To Reach Desired Strength Goals
Limit Reinforcing To Ensure Ductile Failure of Reinforcing Before Other Possible Non-Ductile Connection Failures
Use #6 or Smaller Bar Size
Distribute As Close to Equal on Each Side of Column Center Line As Possible
  Minimum Of 33% of Reinforcing On One Side Of Column
  Minimum Of 3 Bars On One Side Of Column
All Bars Should Extend ¼ Of The Beam Span Or 24 Bar Diameters Past the Inflection Point
For Seismic Design – Detail 50% of Bars As Continuous
Continuous bars should be spliced with Class B lap per ACI 318
Minimum cover per ACI 318
Notes: This slide contains text outlining the rules for longitudinal reinforcing steel.
Slide outlines the Rules for Longitudinal Reinforcing Steel
Go through each of the above rules
Note that in this example building you are using 8 # 5 bars (4 of which are continuous)
Distributing over 36” each side of the column (10” column x 7 = 70”, 70”/2 = 35”, say 36”)

## Slide 23: PR Composite Connection Design
Transverse Reinforcing Steel
Notes: An image of longitudinal steel reinforcing of the composite slab, shown in plan view.
Slide shows the composite slab reinforcing used in the example building
The typical reinforcing details for the example building are shown in the above figure
Key is using several small diameter well distributed reinforcing bars rather than a few large diameter bars
The purpose of the transverse reinforcing steel is to help promote the force transfer from the tension reinforcing to the column and to prevent potential shear splitting of the slab over the beams, thus allowing the beam studs to transfer the reinforcing tension force into the beam.
The following recommendations are from the ASCE Journal Paper

## Slide 24: PR Composite Connection Design
Transverse Reinforcing Steel
Provided To Promote The Force Transfer From Longitudinal Steel To Column And To Beam Flange
Allows Development Of Strut And Tie Fields For Force Transfer To Column – Basis For Selection Of Reinforcing
Prevents Longitudinal Splitting Over Beam To Allow Force Transfer To Studs Then To Beam Flange – Reason To Keep Transverse Steel Below Top Of Shear Studs
Use #6 Or Smaller Bars
Typically Same Number As
Longitudinal Steel
Extend 12 bar diameters or 12”
Past Outside Longitudinal Bars
Notes: An image of a column and surrounding slab reinforcing that illustrates force transfer into the column.
Slide outlines the Rules for Longitudinal Reinforcing Steel
Size transvers reinforcing based on the above strut-tie model of the force transfer, or in the worst case, the transverse reinforcing can simply equal the longitudinal reinforcing
Go through other rules presented here

## Slide 25: PR Composite Connection Design
Concrete to Column Force Transfer
Transfer Slab Compression Force From One Side Of Connection Combined With Slab Tension Force From Other Side Of Connection Through Bearing Of Concrete On Column Flanges
  Typically Taken As The Combination Of Mc- And Mc+ Of The Connection
Limit Bearing Stress to 1.8 f’c
Check Flange Local Bending
Check Web Local Yielding
Concrete Between Flanges
Provide Sufficient Studs
To Develop Slab Forces
Within Inflection Points
Each Side Of Column
Notes: Slide has two images: one is the same as last slide, showing a column and surrounding slab reinforcing that illustrates force transfer into the column and the other is a section of a beam/slab and column bolted connection.
Slide outlines the rules for checking concrete bearing stresses and illustrates the mechanism at work via two figures
The primary means of turning the moment from the beam ends into the column is through slab concrete bearing on the encased flanges and through the seat angle bearing or pulling at the bottom of the beam.
The maximum moment that can be delivered from the system to the column is simply the sum of the plastic moment capacities of the connections on each side of the column.
For the W21x44 of our example this summation of moment capacities is 367 + 240 = 607 k-ft
Depth between compression centroid at slab and bottom of beam is approximately 20.7” (depth of W21x44) + 4.5”/2 = 22.95”
Thus concrete bearing force at flange is approximately 607k-ft/22.95” = 317 kips
A W10x88 column has a 10.3‑inch-wide flange. Assuming uniform bearing of the concrete on each flange, the bearing stress would be 317 kips / 2 flanges / 4.5‑inch-thick slab / 10.3‑inch-wide flange = 3.42 ksi, which is less than the recommended limit of .
It is also necessary to check this force against the flange local bending and web local yielding limit states given in Chapter J of AISC 360.
It is important to have concrete filling the gap between column flanges; otherwise, the force must be transferred by a single column flange.

## Slide 26: PR Composite Connection Design
Connection Moment Capacity Limits
AISC 341 Section G4 Requires A Minimum Nominal Connection Capacity Of 50% Of Nominal Bare Steel Beam, Mp
ASCE TC Recommends 75% As The Target With 50% Lower Limit And 100% Upper Limits
Determine Nominal Connection Strengths At Target Rotations:
  20 mrad For Negative Connection Moment Capacity
  10 mrad For Positive Connection Moment Capacity
Not Clear If This Requirement Applies To Both Negative And Positive Capacity When A Connection Has Different Capacity In Each Direction – Commentary of AISC 341 – 16 Suggests That Limit Is Applicable To Both Directions
Example:
  W21x44 Negative Ratio 0.92
  W21x44 Positive Ratio 0.60
Notes: This slide contains text outlining the checks of connection moment capacity ratios.
Slide outlines the checking of connection moment capacity ratios
AISC 341 requires 50% min
However, ASCE Journal paper recommends targeting 75% with 50% as a lower bound and 100% as an upper bound
The two values for negative and positive connection capacity (@ 20 mrad and 10 mrad respectively) divided by the bare beam Mp are presented above

## Slide 27: PR Composite Connection Design
Seat Angle Design
Minimum Width Of 9” To Allow Typical Bolt Gage Of 5.5” and 1.75” Minimum Edge Distance For Sheared Edges At 1” Bolts
Minimum Horizontal Angle Leg Area:
  Asamin = 1.33 × Fyrd × Arb / Fya
Minimum Horizontal Leg Length Of 8” To Allow 4 – 1” Diameter Bolts
Vertical Leg Length Chosen To Allow Ductile Hinging Of The Seat Angle When Connection Is In Full Positive Bending
Limit tsa / b’ To < 0.5 To Allow
Development Of Proper Hinges And
To Ignore Shear Bending Interaction
Notes: An image on the right depicting a connection highlighting the seat angle.
Slide outlines the guidelines for proportioning the bottom seat angle
Most of the angle proportioning is dictated by geometric issues of fitting bolts
There is an As min required per the AISC Design Guide
You want as long an outstanding leg as possible to allow as many bolts in this leg as possible in order to get the most moment capacity out of the connection. This is typically the limiting factor for the moment capacity of the connection.
The vertical leg bolt location and thickness should allow a ductile hinge mechanism to form without brittle shearing of the angle or tension failure of the bolt. When the connection is in positive bending, this is the source of the ductility.
By detailing to the above suggested limits, one can ensure a ductile failure mode and also eliminate significant interaction between bending and shear failures of the angle
This last rule is a guideline developed by the author and not found in any of the research literature

## Slide 28: PR Composite Connection Design
Seat Angle Bolts
Bolts In Vertical Leg:
  Oversize Holes For Mill Tolerance
  Bolts In Vertical Leg Should Be Designed For Maximum Bolt Tension
  Including Prying Action (See Paper) Magnified By Ry From AISC 341
  Table I-6-1.
    Ry × Bsa
Bolts In Horizontal Leg:
  Generally This Is The Limiting Factor In The PRCC Design
  Maximize Bolt Capacity By Using A490-X Bolts
  1” Diameter Is A Practical Upper Limit On Bolt Size For The Typical
  Angle Size and Connected Beams
  Check Against Full Plastic Capacity Of
  Longitudinal Steel And Web Angles Magnified
  By Appropriate Ry Factors
    Ry × Twa + Ry × Fyrd × Arb
Notes: An image showing three bolts in an angle.
Slide outlines the basic checks one has to make for the bolts in the bottom seat angle
Vertical Leg Bolts
  The bolts in the vertical leg need to be able to develop the tension that can be delivered by the angle as it develops its hinge in the portion of the leg above the bolt.
  The example problem in the paper goes into detail on how one would determine the hinging capacity of the angle and the associated additional prying forces in the bolt.
  In order to ensure the bolts are capable of handling potential overstrength of the angle, an Ry factor is applied
Horizontal Leg Bolts
  4 – 1” bolts is about as many as one can fit given standard angle sizes
  The source of shear comes from tension yielding of the reinforcing steel and hinging of the web angles being pulled in tension away from the column face (similar to the hinge mechanism of the seat angle)
  Ry factors are applied to ensure overstength issues are covered, the Ry for rebar comes from the ASCE Journal paper

## Slide 29: PR Composite Connection Design
Double Angle Web Connection
Primary Purpose To Carry The Connection Shear Demand
Seismic Shear Demand Associated With Full Connection Strength At Each End Should Be Added To Gravity Shear Demand With Appropriate Load Factors To Determine Total Shear Demand
Detail Gage With Same Ductility Concept As Seat Angle Of twa / b’ To < 0.5 To Allow Web Angles To Hinge As The Connection Rotates
Notes: Image of connections.
Slide outlines the guidelines for proportioning and detailing the double web angle shear connection
Primary purpose is to carry beam shear; however, they do participate in the connection moment rotation behavior as well so they still should be sized by the EOR and not delegated
The shear to be considered would be the full gravity plus seismic. The seismic shear is determined assuming full hinges at both ends of the beam
The gage for the bolts to the column should be detailed to allow ductile tension hinging of the web angles as discussed when we talked about the seat angle connection, again this guideline presented is not a rule; but, merely a guideline that will ensure ductile failure

## Slide 30: Loads And Load Combinations
Table 9.3-1 Gravity Load and Seismic Weight |  |  | 
 |  | Gravity Load | Seismic Weight
Non-Composite Dead Loads (Dnc) |  |  | 
 | 4.5-in. Slab on 0.6-in. Form Deck (4.5‑in. total thickness) plus Concrete Ponding | 58 psf | 58 psf
 | Joist and Beam Framing | 6 psf | 6 psf
 | Columns | 2 psf | 2 psf
 | Total: | 66 psf | 66 psf
Composite Dead Loads (Dc) |  |  | 
 | Fire Insulation | 4 psf | 4 psf
 | Mechanical and Electrical | 6 psf | 6 psf
 | Ceiling | 2 psf | 2 psf
 | Total: | 12 psf | 12 psf
 | Precast Cladding System | 800 plf | 800 plf
Live Loads (L) |  |  | 
 | Typical Area Live and Partitions (Reducible) | 70 psf | 10 psf
 | Records Storage Area Live (Non-Reducible) | 200 psf | 100 psf
Gravity Loads and Seismic Weight
Notes: This slide contains a table summarizing the gravity type loads applied to the example building.
Slide summarizes all the gravity type loads applied to the example building
The design gravity loads and the associated seismic weights for the example building are summarized above.
The seismic weight of the storage live load is taken as 50 percent of the design gravity load (a minimum of 25 percent is required by Standard Section 12.7.2).
To simplify this design example, the roof design is assumed to be the same as the floor design and floor loads are used rather than considering special roof and snow loads
The reason for categorizing dead loads as non-composite and composite is explained later.
Live loads are applied to beams in the analytical model, with corresponding live load reductions appropriate for beam design.
Column live loads are adjusted to account for different live load reduction factors, including the 20 percent reduction on storage loads for columns supporting two or more floors per Standard Section 4.8.2.

## Slide 31: Loads And Load Combinations
Table 12.2-1
Seismic Loads
Equivalent Lateral Force Procedure Permitted Per Table 12.6-1
Notes: This slide contains an image of the ASCE 7 provisions table (Table 12.2-1) highlighting the basis for the C-PRMF.
Slide shows the ASCE 7 table and the associated seismic design values associated with a C-PRMF system
For Seismic Design Category C, the height limit is 160 feet, so the selected system is permitted for this 52-foot-tall example building.
The building is regular in both plan and elevation; consequently, the Equivalent Lateral Force Procedure of Section 12.8 is permitted in accordance with Standard Table 12.6 1.
Other applicable parameters regarding site are given in the example problem

## Slide 32: Loads And Load Combinations
Seismic Loads – ELF Building Period Determination
Approximate Period – Per Equation 12.8-7 & Table 12.8-2
Ta = 0.66 sec
Notes: This slide contains table 12.8-2 from ASCE 7 which shows how to approximate period of the structure.
Slide illustrates the table from ASCE 7 where you choose the approximate period coefficients
The approximate period is determined to be 0.66 seconds using Equation 12.8-7 and the steel moment-resisting frame parameters of Table 12.8-2.

## Slide 33: Loads And Load Combinations
Seismic Loads – ELF Building Period Determination
Upper Limit Period – Per Table 12.8-1
SD1 = 0.14 so Cu = 1.62
Tmax = 0.66 x 1.62 =1.07 sec
Notes: This slide contains Table 12.8-1 from ASCE 7 which illustrates the upper bound coefficient for period determination.
Slide illustrates the table from ASCE 7 where you choose the upper bound coefficient for the period determination
The coefficient for upper limit on calculated period, Cu, from Table 12.8-1 is 1.62 (interpolated between values in table), resulting in Tmax of 1.07 seconds for purposes of determining strength-level seismic forces.

## Slide 34: Loads And Load Combinations
Seismic Loads – ELF Building Period Determination
Dynamic Analysis Period From 3-D SAP Model
Use Kci For Connection Stiffness To Estimate Shortest Possible Analytical Building Period
Tdynamic = 2.13 sec North-South And 1.95 sec East-West
Summary of Periods:
  Ta = 0.66 sec
  Tmax = 1.07 sec
  Tdynamic = 2.13 sec North-South And 1.95 sec East-West
  Use T = 1.07 sec To Determine Strength Level Forces
  Could Use Tdynamic For Drift Check Forces If Need Be
Notes: This slide contains text on the process of finalizing the period determination used for calculating seismic forces.
Slide outlines the basic thoughts on how one goes about finalizing the period determination that will be used for determining seismic forces
A specific value for PRCC stiffness must be selected in order to conduct a dynamic analysis to determine the building period. Can’t do a dynamic analysis to determine a single period when using a non-linear connection curve.
It is recommended that the designer use Kci of the negative moment-rotation behavior given in Section 9.2.2 above for this analysis.
This should result in the shortest possible analytical building period and thus the largest seismic design forces.
For the example building, the computed periods of vibration in the first modes are 2.13 and 1.95 seconds in the north-south and east-west directions, respectively. These values exceed Tmax, (given above) so strength-level seismic forces must be computed using Tmax (given above) for the period.
The final calculation of building base shear and the vertical distribution of forces is exactly like any other building and is detailed in the example
Note that if seismic drift was becoming a problem you could use the calculated period to determine a set of seismic forces for drift checking

## Slide 35: Loads And Load Combinations
Notional Loads
AISC 360 Requires The Application Of Notional Loads To the Gravity-Only Load Combination For This Example Building
Notional Loads Are Taken As 0.2% Of Gravity Loads
Example Building
NDnc = 4,258 kips × 0.002 = 8.516 kips / 4 floors = 2.13 kips/floor
NDc = 2,393 kips × 0.002 = 4.786 kips / 4 floors = 1.20 kips/floor
NL = 4,469 kips × 0.002 = 8.938 kips / 4 floors = 2.23 kips/floor
Because The Center Of Building Loading Corresponds To The Centroid Of The Building For This Example, These Notional Loads Can Be Applied At Building Centroid
  Typically Notional Loads Are Determined On A Column By Column Basis Thus Capturing The Actual Gravity Load Distribution
Notes: Slide contains text outlining the rules for determining notional loads for the example building.
Slide outlines rules for determining notional loads for the example building
Note that wind loads were considered; but, were substantially less than the seismic loads so they are not discussed here and there is nothing unique about calculating them associated with the C-PRMF system
AISC 360 now requires that notional loads be included in the building analysis.
This example building qualifies for application of notional loads to gravity-only load combinations. This is typically the case.
Notional loads are taken as 0.2% of gravity loads
The notional loads are applied in the same manner as the seismic and wind loads in each orthogonal direction of the building and they are factored by the same load factors that are applied to their corresponding source (such as 1.2 or 1.4 for dead loads).
It is important to note that, in general, notional loads should be determined, at a minimum, on a column-by-column basis rather than for an entire floor as done above. This will allow the design to capture the effect of gravity loads that are not symmetric about the center of the building.
The example building happens to have gravity loads that are concentric with the center of the building, so it does not matter in this case.

## Slide 36: Loads And Load Combinations
Expand For Vertical And Horizontal EQ Effects, Breakout Non-Composite And Composite Dead Loads, And Add Notional Loads
Basic Load Combinations Considered From Section 2.3.2:
Load Combinations
Notes: Slide contains text of the different load combinations that control the design of the example building.
Slide outlines the load combinations that control the design of the example building
The above load combinations are the primary combinations controlling the design of this example building
The loads have to be broken out into pre-composite and post composite loads for proper application of the loads to the building due to the 2-stage behavior of the connection that is discussed later. In addition, the seismic coefficients are expanded to give the expanded combinations above.

## Slide 37: Loads And Load Combinations
Column Design From Stage 2
Beam Design From Linear Combination Of Stage 1 & 2
Load Combinations
Two-Stage Connection Behavior Requires Two-Stage Building Analysis And Thus Different Load Combinations For Each Phase And Separate Applications Of Dead Loads To Beams And Columns
Notes: Slide contains text that illustrates how the basic load combinations have to be expanded to include two stages of analysis and breaking about pre-composite and post-composite loads
Slide illustrates how the basic load combinations have to be expanded to include two stages of analysis and breaking about pre-composite and post-composite loads
Because the PRCC has two distinct stages of moment-rotation behavior, the analysis and application of load has to be consistent with that.
This requires not only separating pre and post composite loads; but, also dead loads on columns from dead loads on beams.
Further explanation of why these are broken out is still coming up.

## Slide 38: Loads And Load Combinations
All Typical Permeations Of Above Load Combinations For North-South And East-West Directions Have To Be Generated
Load Combinations
Seismic And Wind Drift Checks Based On Non-Linear Analysis Thus You Need Full Load Combinations In Order To Capture Connection Behavior And Building Second Order Effects:
Notes: 508 note: Slide contains text highlighting additional load combinations to be used for service level design checks.
Slide outlines loads combinations to be used for service level design checks
All drift checks are done from the results of a non-linear analysis
Linear superposition of non-linear results won’t cut it
Drift from wind or seismic alone won’t cut it because the gravity loads soften the connections
Consequently, the above complete load combinations have to be run in order to get a wind or seismic drift
The last note here is just to indicate that the above load combinations (and on previous slides) would have to have all the normal east-west, north-south directions and torsions applied.

## Slide 39: Analysis
Preliminary Design
Design All Framing For Pure Gravity Loading Assuming All PR Connections As Pins
PR Frame Beams To Be Designed As 100% Composite
Filler Beams Designed As Typical
Perform 1st Order Lateral Analysis Assuming All PR Connections As Rigid
  Review Beam End Moments From EQ And Wind And Compare To Previously Determined Connection Design Capacity (Would Like To Be Below About 75% Of Connection Design Capacity)
  Review Building Drift Assuming PR Building Drift Will Be Approximately 2 x Above Model Drift
  If Fail:
    Increase Number Of Frames
    Increase Column / Beam Sizes (& Thus Connections)
Notes: Slide contains text outlining a procedure that can be used for the initial proportioning of frame members.
Slide outlines a procedure that can be used for the initial proportioning of frame members
The goal of an efficient partially restrained building design is to have a sufficient number of beams, columns and connections participating in the lateral system so that the forces developed in any of these elements from lateral loads is relatively small compared to the gravity design.
Design for gravity as if the connections are pinned; add the connections and check to see if any beams or columns must be upsized to handle the lateral loads. The goal is that you won’t have to.
The steps above are intended to get the designer close to their final result before stepping into the full blown non-linear analysis that is required for the final design confirmation of the building
Go through above steps

## Slide 40: Analysis
Application of Load
Pre-Composite PR Connection Behavior Assumed As Pinned
  Stage 1 Analysis Applies Pre-Composite Gravity Loads To Beams Only
Post-Composite PR Connection Behavior Based On Previously Determined Curves
  Stage 2 Analysis Applies Pre-Composite Gravity Loads To Columns Only And Post-Composite Gravity Loads To Beams (With Exception Of Seismic Vertical Loading Associated With Pre-Composite Loads)
Notes: Slide contains text explaining why loads must be applied in two stages due to two stage behavior in the PRCC connections.
Slide outlines how the loads have to be applied in two stages because of the two stage behavior that exists with the PRCC connections
The true behavior of a PRCC consists of two stages.
The first stage is the bare steel connection (double web angles and seat angle)
The second stage is the full composite connection
We typically assume the first stage behaves as a pinned connection and the second stage behaves as our prediction curves have suggested
So we do a Stage 1 analysis of just pre-composite gravity loads on beams only in order to get the proper moment distribution of these loads in these beams assuming pin ended connections.
We then do a Stage 2 analysis which only has the post-composite loads on the beams and all loads on the columns in order to capture the post-composite moment distribution and frame analysis.
The reason for getting all the loads on the columns in the Stage 2 analysis is to ensure the second order effects from these loads are captured; however, we don’t put these loads on the beams in this stage because they occurred before the concrete hardened

## Slide 41: Analysis
Application of Load
Stage 2 Load Combination 5
Notes: Slide contains illustrations depicting the two stage process of applying loads.
Slide presents an illustration to help clarify how the loads are applied to the building frame in the second stage for load combination 5
This slides shows how the different load types are applied for the Stage 2 version of Load Combination 5
Note how the pre-composite loads that would normally be applied to the beams are directly applied to the columns instead. This way the columns have the correct total loading while the beams only have the post-composite loading
This is why the beams have to be designed for the linear combination of Stage 1 and Stage 2 results

## Slide 42: Analysis
Application of Load
Stage 2 Load Combination 7
Notes: Slide contains illustrations depicting the two stage process of applying loads.
Slide presents an illustration to help clarify how the loads are applied to the building frame in the second stage for load combination 7
This slides shows how the different load types are applied for the Stage 2 version of Load Combination 7
Here you should note that there is actually a negative dead load applied to the beams to account for the vertical component of the seismic force that comes about during a seismic event which is considered to occur in the post-composite stage of the structure life

## Slide 43: Analysis
Beam & Column Moment of Inertia
Beam Moment Of Inertia
  Ieq = 0.6ILB+ + 0.4ILB- For Drift
    ILB = Lower Bound Moment Of Inertia Of Composite Beam
    ILB+ Positive Bending – From AISC Manual
    ILB- Negative Bending – Typical Assume Bare Steel
  0.8 x Ieq For Strength (Direct Analysis)
Column Moment Of Inertia
  Icol For Drift
  0.8 x tb x Icol For Strength (Direct Analysis)
    tb Only Applies If Pr/Py > 0.5
Notes: Slide contains text discussing the effective moment of inertia to be used for beam and columns
This slide discusses the effective moment of inertia to be used for beam and columns
The beam moment of inertia is a weighted average of the inertia in the positive bending zone and the inertia in the negative bending zones. This equation comes from the ASCE Journal Paper
The lower bound moment of inertia for the positive zone is reported in the steel manual
The lower bound moment of inertia for the negative zone is typically taken as the bare steel beam moment of inertia; but, it can be taken as the composite moment of inertia including the area of reinforcing steel
The 20% reduction in the moment of inertia is required for the strength design per the direct analysis rules
The column is simply the bare column for drift checks and has the same 20% reduction for the strength design per the direct analysis rules

## Slide 44: Analysis
Connection Behavior Modeling
For Each Connection There Are 4 Connection Models
  Linear Spring Using Kci For Dynamic Analysis For Determining Building Period
  Non-Linear Spring Using Nominal Connection Behavior Curve For Service Level Analysis
  Pin For Stage 1 Gravity Analysis Of Beams
  Non-Linear Spring Using Reduced Connection Behavior Curve For Stage 2 Strength Level Analysis
  SAP 2000 Allows 2 Connection Behavior Definitions – One For Linear Analysis And One For Non-Linear Analysis When Using The Multi-Linear Elastic Link Option
Conduct A Path Independent Analysis Where Connection Behavior Always Remains On Connection Curve
Notes: This slide contains text discussing the 4 different ways that the PR spring at the beam to column connection is modeled during the analysis
This slide discusses the 4 different ways that the PR spring at the beam to column connection is modeled during the analysis
First we assign a linear spring so we can conduct a dynamic analysis
We assign the nominal nonlinear connection curve for service level type checks
We assign a pin behavior for the Stage 1 strength analysis
We assign the modified nonlinear connection curve for the Stage 2 strength analysis
All of these analysis are done using a path independent approach. This simply means that the sequence and timing of load application does not change the answer. A path dependent approach takes into account the sequence and magnitude level that the loads are applied.

## Slide 45: Analysis
Reason For Not Reducing Beam Sizes
Connection Behavior Modeling
Path Independent Vs. Path Dependent
Notes: This slide contains a graph illustrating the difference between path independence and path dependence.
This slide further illustrates the difference between path independent and path dependent
A path independent analysis forces equilibrium to occur with the connection in a moment-rotation state along the dotted curve
Reality is that when a connection starts to unload, it does not travel along the curve; but, instead it takes an almost linear unloading path (as shown where the connections go from Step 4 to Step 6 in the slide above)
.This path-dependent analysis is more accurate and allows consideration of connection shakedown to be captured in the model; however, it is also much more complicated when compared to the path-independent analysis.
Since the simpler, path-independent connection modeling approach does not capture connection shakedown behavior, the author does not recommend reducing beam sizes from the pure simple pinned gravity design discussed previously

## Slide 46: ASCE 7-16 & AISC Design Checks
Building Drift and P-D Checks
Use Service Moment-Rotation Curves and Full Member Moment of Inertia
Nonlinear Analysis Required Because of Connection Curves (Requires Non-Linear Load Combinations)
Check Wind and Seismic Drift Using P-D Analysis
  Wind Drift: hsx/400 Limit Applied
  Torsional Irregularity Check ASCE 7-16 Table 12.3-1
  Seismic Drift Check ASCE 7-16 Table 12.12-1
Check P-D Effect and Story Stability Coefficient (q) By Comparing and Contrasting Analysis Results With and Without P-D.
  Check For P-D Effect to Be Less Than 1.5 to Meet AISC 360 Requirement For Using Notional Loads As Minimum Lateral Load (Factored Load Check)
  Check For q per Section 12.8.7 of ASCE 7-10 (No Load Factor > 1.0)
Notes: This slide contains text outlining the approach to checking common service load code checks, and two equations for calculating the roataion.
This slide outlines the approach to checking common service level code checks
When checking drift, irregularity, and p-delta effects, we typically use the nominal moments of inertia and connection curve.
These require a non-linear analysis with the load combinations that were presented previously.
Discuss other limits outlined above
The specific values and checks for the example building are provided in the example problem and are not reiterated here
Note: The example problem is not correct in its discussion of checking this value, it was based on an earlier draft of the Standard before the final was voted on. The final version kept this part of the standard un-changed.

## Slide 47: ASCE 7-16 & AISC Design Checks
Beam Design
Design As Composite Beam For 100% Composite Action
Shear Stud Distribution Needs To Allow For Development of Slab Reinforcing Between Column and Inflection Point But Does Not Need to Develop 100% Composite Action Between These Points
AISC 341 Section G4 Does Not Specifically Address Beam Compactness Criteria – Suggest Using AISC 360 Compact Criteria (Note AISC 341-16 Will Require Seismic Compact Criteria)
Notes: This slide contains text outlining the requirement for beam design and distribution of shear studs.
This slide outlines the requirements for beam design and distribution of shear studs
100% composite required because of the testing done on these connections to date
Studs between column and inflection point need to be sufficient to off load the tension in the reinforcing steel
Compact requirements are not currently addressed in the AISC 341; however, the AISC 341-10 does address this issue and will require seismic compactness. The example problem presumes that only typical compact requirements will be needed since it was done before the AISC 341-10 was finalized.

## Slide 48: ASCE 7-16 & AISC Design Checks
Beam Design
Because Beam Is Now Part Of Lateral System, It May Go Into Negative Moment At One End Resulting In Possibly Considering The Entire Beam As Un-braced For Lateral-Torsional Buckling Checks – Consider Using Alternative Cb Equations For Special Beam Cases (Yura, Helwig – Beam Buckling and Bracing)
Notes: An image of a loading and bending moment diagram that illustrates the issues associated with the potential of lateral torsional buckling of beams that are part of the frame
This slide illustrates the issues associated with the potential of lateral torsional buckling of beams that are part of the frame
Have to consider potential un-braced lengths of beams and potential lateral torsional buckling that can occur because of the bottom flange going into compression
Inflection point is not a brace point, so unless braces come into side of beam have to consider entire length un-braced
Recommend using alternative Cb equations in order to avoid adding bracing or bumping beam size to meet the LTB requirements

## Slide 49: ASCE 7-16 & AISC Design Checks
Column Design
AISC 341 Section G4.5 Requires Columns Meet Requirements Of AISC 341 Section D2
Material Requirements of Section 6 Are Met By All W10 Columns of A992 Steel
AISC 341 Requires Special Load Combination If Pu/fcPn Exceeds 0.4.
AISC 360 Allow Use Of K = 1.0 By Direct Analysis Method
AISC 341 Does Require Compactness Criteria.
Strong Column Weak Beam Concept For C-PRMF Not Addressed By AISC 341 Currently But ASCE TC Recommends:
Notes: This slide contains text outlining the current rules in AISC and guidance for checking the columns in the C-PRMF, and an equation used in the column check procedure.
This slide outlines the current rules and guidance for checking the columns in the C-PRMF
Part 1 of the AISC 341 has some material and over strength check requirements for columns
The only columns in the example building that would be affected by the over strength check are the interior columns where the axial load from seismic is minor compared to the gravity load and would consequently make no difference in the design checks
Since we used a direct analysis we get to use K=1
Again the compact requirements are not addressed in AISC 341-05; however, they will be addressed in AISC 341-10 and they will require Seismic Compact
Can check compact limits by hand or by using tables found in the seismic design manual
Strong column weak beam concept now takes the form of strong column weak connection concept
This is not addressed in AISC 341-05 but is addressed in the ASCE Journal paper and is addressed in the commentary of the AISC 341-10
Numerical checks for one sample column of the example building are provided in the example

## Slide 50: ASCE 7-16 & AISC Design Checks
This Is Not The Case If Using Linear Springs To Model The Connection Behavior
Example Problem:
Table 9.4-5 Connection Moment Demand vs. Capacity (kip-ft) |  |  |  | 
 | W21 PRCC |  | W18 PRCC | 
 | (-) M-q | (+) M-q | (-) M-q | (+) M-q
Demand | 136 | 87.0 | 126 | 37.0
Capacity | 312 | 204 | 197 | 128
Ratio | 0.44 | 0.43 | 0.64 | 0.29
Connection Checks
Because Using Non-Linear Curve, A Check Against Connection Capacity Is Not Really Necessary; However, It Is Of Interest To Understand How Hard The Connections Are Being Pushed.
Notes: This slide contains text and a table outlining the requirements for final checking of the PRCC in the building.
This slide outlines requirements for final checking of the PRCCs in the building
There is really little to do with the connection design at this stage because the full nonlinear connection behavior is being used in the analysis. This means that the connection moments will never exceed the connection capacity during the analysis. This is in contrast to any analysis method that models the connections with linear behavior. When the connections are modeled with linear behavior, it is up to the designer to confirm that the final connection results are consistent with the expected connection behavior. This might be very easy for building designs where connection moments are small; however, when the connections are being pushed close to their capacity, that sort of independent connection check by the designer can be problematic.
Although not entirely necessary, it is useful to check where the connections are along the expected behavior curves for any given analysis so one can see just how hard the connections are being pushed. The connection moment demand versus design capacities (including phi) are presented in Table above. The demand values are from different load combinations. A quick check of this table indicates that this building design is not being pushed particularly hard and that there is likely significant reserve capacity in the lateral system.

## Slide 51: Questions
Notes: This slide is a placeholder used to open up the floor for questions.
This slide is a placeholder for an opening the floor up to questions

## Slide 52: DISCLAIMER
NOTICE: Any opinions, findings, conclusions, or recommendations expressed in this publication do not necessarily reflect the views of the Federal Emergency Management Agency. Additionally, neither FEMA nor any of its employees make any warranty, expressed or implied, nor assume any legal liability or responsibility for the accuracy, completeness, or usefulness of any information, product or process included in this publication.
The opinions expressed herein regarding the requirements of the NEHRP Recommended Seismic Provisions, the referenced standards, and the building codes are not to be used for design purposes. Rather the user should consult the jurisdiction’s building official who has the authority to render interpretation of the code.
Any modifications made to the file represent the presenters' opinion only.