## Slide 1
Disclaimer
Instructional Slides developed by S. K. Ghosh, PhD,
Notes: Title slide
The presentation will cover examples of application of the provisions for earthquake design to precast concrete systems.

## Slide 2: Precast Concrete Design
Seismic design of precast concrete using the NEHRP Recommended Provisions
Review of design examples to illustrate the application of the provisions
Notes: Overview slide:
Scope of the chapter: This chapter illustrates the seismic design of precast concrete members using the NEHRP Recommended Provisions (referred to herein as the Provisions) for buildings in several different seismic design categories.
Scope of the presentation: The presentation does not repeat the text that describes provisions or procedures, but instead is focused on design examples which illustrate these points through the applications of those provisions.

## Slide 3: Some Terms used in this Presentation
Standard – 2016 Edition of ASCE 7
Provisions – 2015 NEHRP Provisions
ACI 318 – 2014 Edition of ACI 318
Notes: This slide introduces the abbreviated versions of the different reference documents that will be used throughout the presentation.

## Slide 4: 11.1 Horizontal Diaphragms
Hollow core plank floor plan for diaphragm examples
Notes: The figure shows the hollow core plank floor plan. The plan dimensions of the floor are 152 ft x 72 ft. The interior portion of the plan includes walls spaced at 24 ft in the transverse direction. The 40 ft bays at either end of the plan include walls spaced at 24 ft in the longitudinal direction.
Horizontal diaphragms examples; 1st slide shows the floor plan that is used for the example. The layout is the same used in Chapter 13, Sec. 13.2, which illustrates the design of a five-story masonry residential building.

## Slide 5: 11.1 Horizontal Diaphragms
Building Elevation
Notes: The figure shows a building elevation plan. The building is 45’-4” tall consisting of five stories, each 8’-8” high, and a 2’ high parapet.
Horizontal diaphragms examples; 2nd slide shows the elevation of the building used for the example.

## Slide 6: Untopped Diaphragm Examples
This example illustrates untopped precast floor and roof diaphragm design for five-story masonry buildings assigned to
  Seismic Design Category B
  Seismic Design Category C
Notes: First slide to introduce the design of untopped precast diaphragms using hollow core floor plank. The design is linked to the Chapter 10 masonry wall example for SDC B using Birmingham., Alabama. The use of seismic acceleration parameters for New York for SDC C differs from Chapter 10.

## Slide 7: Untopped Diaphragm Design Parameters
Notes: First slide to introduce the design of untopped precast diaphragms using hollow core floor plank. The design is linked to the Chapter 10 masonry wall example for SDC B using Birmingham., Alabama. The use of seismic acceleration parameters for New York for SDC C differs from Chapter 10.

## Slide 8: Design of Building Assigned to Seismic Design Category B

## Slide 9: Diaphragm Design Forces
The weight tributary to the roof and floor diaphragms (wpx) is the total story weight (wi) at Level i minus the weight of the walls parallel to the direction of loading.
  Roof:
    Total weight = 861 kips
    Walls parallel to force = (45 psf)(277 ft)(8.67 ft / 2) = -54 kips
    wpx = 807 kips
  Floors:
    Total weight = 963 kips
    Walls parallel to force = (45 psf)(277 ft)(8.67 ft) = -108 kips
    wpx = 855 kips
Notes: Weight used for the diaphragm design is given for floor and roof. The weight used for the design of the diaphragm does not include the weight of walls parallel to the direction of loading because the wall weight does not contribute to the inertial force in the floor. That must be collected and distributed to the walls,

## Slide 10: Diaphragm Design Forces
Since the building is assigned to SDC B, the diaphragm design forces are permitted to be determined from the provisions of Standard Sections 12.10.1 and 12.10.2, or Section 12.10.3. Both calculations are shown here for comparison purposes.
Notes: Weight used for the diaphragm design is given for floor and roof. The weight used for the design of the diaphragm does not include the weight of walls parallel to the direction of loading because the wall weight does not contribute to the inertial force in the floor. That must be collected and distributed to the walls,

## Slide 11: Diaphragm Design Forces
Table 11.1-2A SDC B Fpx Calculations |  |  |  |  |  | 
Level | wi (kips) | (kips) | Fi (kips) | (kips) | wpx (kips) | Fpx (kips)
Roof | 861 | 861 | 175 | 175 | 807 | 164
4 | 963 | 1,824 | 156 | 331 | 855 | 155
3 | 963 | 2,787 | 117 | 448 | 855 | 137
2 | 963 | 3,750 | 78 | 526 | 855 | 120
1 | 963 | 4,713 | 39 | 565 | 855 | 103
1.0 kip = 4.45 kN. |  |  |  |  |  | 
Calculations for Fpx are provided in Table 11.1-2A.
Notes: The table with the values of the calculated diaphragm forces is given for the Birmingham example.

## Slide 12: Diaphragm Design Forces
The minimum value of Fpx = 0.2SDSIewpx
= 0.2(0.21)1.0(807 kips) = 33.9 kips (roof)
= 0.2(0.21)1.0(855 kips) = 35.9 kips (floors)
The maximum value of Fpx = 0.4SDSIewpx
= 2(33.9 kips) = 67.8 kips (roof)
= 2(35.9 kips) = 71.8 kips (floors)
Note that the calculated Fpx in Table 11.1-2A is substantially larger than the specified maximum limit value of Fpx.
Notes: The slide presents the calculation of the maximum and minimum limits for diaphragm design forces. The maximum diaphragm design forces from the provisions are significantly less than calculated by Eq. 12.10-1, and these governs the design forces.

## Slide 13: Diaphragm Design Forces
To simplify the design, the diaphragm design force used for all levels will be the maximum force at any level
= 72 kips.
Notes: The slide presents the calculation of the maximum and minimum limits for diaphragm design forces. The maximum diaphragm design forces from the provisions are significantly less than calculated by Eq. 12.10-1, and these governs the design forces.

## Slide 14: Diaphragm Design Forces
B. Computation of diaphragm forces in accordance with Standard Section 12.10.3:
Step 1: Determine Rs, Diaphragm Design Force Reduction Factor (Standard Table 12.10-1)
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
Step 3: Determine Fpx, Diaphragm Design Force at Level x
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 15: Diaphragm Design Forces
Step 1: Determine Rs, Diaphragm Design Force Reduction Factor (Standard Table 12.10-1)
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 16: Diaphragm Design Forces
Step 1: Determine Rs, Diaphragm Design Force Reduction Factor (Standard Table 12.10-1)
For SDC B, the Diaphragm Seismic Demand Level is Low. So all diaphragm design options are allowed; the Basic Design Option (BDO) is chosen.
The issue of connector deformability is moot, because there are no connectors involved.
Rs = 1.0
Shear overstrength factor = 1.4Rs = 1.4.
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 17: Diaphragm Design Forces
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
To determine Cpx, three parameters must be determined - Cp0, Cpi, and Cpn
Determination of Cp0:
Cp0 = 0.4SDSIe = 0.4×0.21×1.0 = 0.084
Determination of Cpi
Cpi is the greater of the values given by:
  Cpi = Cp0 = 0.084, and
  Cpi = 0.9Γm1 Ω0 Cs
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 18: Diaphragm Design Forces
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
Determination of Cpi
  Γm1 is the first mode contribution factor
  Γm1 = 1 + 0.5zs(1 – 1/N)
  where
  zs = modal contribution coefficient modifier dependent on seismic force-resisting system
  N = Number of stories
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 19: Diaphragm Design Forces
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
Determination of Cpi
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 20: Diaphragm Design Forces
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
Determination of Cpi
  Γm1 is the first mode contribution factor
  Γm1 = 1 + 0.5zs(1 – 1/N) = 1 + 0.5x1.0 (1 – 1/5) = 1.4
  Cpi = 0.9Γm1 Ω0 Cs = 0.9x1.4x2.5x0.105 = 0.331 > 0.084
  Governing Cpi = 0.331
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 21: Diaphragm Design Forces
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
Determination of Cpn
  Cpn =
  where
  Γm2 is the higher mode contribution factor
  Γm2 = 0.9zs(1 – 1/N)2 = 0.9x1.0 (1 – 1/5)2 = 0.576
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 22: Diaphragm Design Forces
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
Determination of Cpn
  Cs2 is higher mode seismic response coefficient, and is the smallest of:
  Cs2 = (0.15N + 0.25)IeSDS = (0.15x5 + 0.25)x1.0x0.21 = 0.21
  Cs2 = IeSDS = 1.0x0.21 = 0.21
  and for N ≥ 2
  Cs2 = IeSD1 / [0.03(N-1)] = 1.0x0.12 / [0.03(5-1)] = 1.00
  Governing Cs2 = 0.21
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 23: Diaphragm Design Forces
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
Determination of Cpn
  Cpn = = 0.387
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 24: Diaphragm Design Forces
Step 2: Determine Cpx, Diaphragm Design Acceleration Coefficient at Level x (Standard Section 12.10.3.2)
Using Standard Figure 12.10.3-1, Cpx is determined at various floor levels, as shown in Table 11.1-2B
Notes: The figure shows two graphs both with hx /hn in the y-axis with ascending gradations from 0 to 1, and in the x-axis with gradations left to right of diaphragm design acceleration coefficient for level x, Cpx from 0 to Cpn. hx /hn is the ratio of the height from the base to level x, hx to the vertical distance from the base to the highest level of the seismic force-resisting system of the structure., hn. On the left-hand side graph for building two stories or less in height, the design acceleration coefficient curve begins at Cp0,0 and rises linearly to Cpn,1. On the right-hand side graph for building three stories or more in height, the curve begins at Cp0,0 and rises linearly to Cpi,0.8, then rises in a straight line from Cpi,0.8 to Cpn,1. Cp0, Cpi, and Cpn are diaphragm design acceleration coefficient at the structure base, diaphragm design acceleration coefficient at 80 percent of the structural height above the base, hn, and diaphragm design acceleration coefficient at the structural height, hn, respectively.

## Slide 25: Diaphragm Design Forces
Table 11.1-2B Fpx Calculations for SDC B |  |  |  |  | 
Level | hx (ft) | Cpx | wpx (kips) | Fpx (kips) | Fpx,min (kips)
Roof | 43.34 | 0.39 | 807 | 312 | 33.90
4 | 34.67 | 0.33 | 855 | 283 | 35.90
3 | 26.00 | 0.27 | 855 | 230 | 35.90
2 | 17.33 | 0.21 | 855 | 177 | 35.90
1 | 8.67 | 0.15 | 855 | 125 | 35.90
1.0 kip = 4.45 kN. |  |  |  |  | 
Step 3: Determine Fpx, Diaphragm Design Force at Level x
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 26: Design of Building Assigned to Seismic Design Category C

## Slide 27: Diaphragm Design Forces
The weight tributary to the roof and floor diaphragms (wpx) is the total story weight (wi) at Level i minus the weight of the walls parallel to the direction of loading.
  Roof:
    Total weight = 870 kips
    Walls parallel to force = (48 psf)(277 ft)(8.67 ft / 2) = -58 kips
    wpx = 812 kips
  Floors:
    Total weight = 978 kips
    Walls parallel to force = (48 psf)(277 ft)(8.67 ft) = -115 kips
    wpx = 863 kips
Notes: Weight used for the diaphragm design is given for floor and roof. The weight used for the design of the diaphragm does not include the weight of walls parallel to the direction of loading because the wall weight does not contribute to the inertial force in the floor. That must be collected and distributed to the walls,

## Slide 28: Diaphragm Design Forces
Table 11.1-3 Fpx Calculations for SDC C |  |  |  |  | 
Level | hx (ft) | Cpx | wpx (kips) | Fpx (kips) | Fpx,min (kips)
Roof | 43.34 | 0.43 | 812 | 347 | 60.10
4 | 34.67 | 0.33 | 863 | 288 | 63.90
3 | 26.00 | 0.29 | 863 | 248 | 63.90
2 | 17.33 | 0.24 | 863 | 208 | 63.90
1 | 8.67 | 0.19 | 863 | 168 | 63.90
1.0 kip = 4.45 kN. |  |  |  |  | 
Step 3: Determine Fpx, Diaphragm Design Force at Level x
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 29: Static Analysis of Diaphragms
The balance of this example will use the controlling diaphragm seismic design force of 347 kips for the building in SDC C.
A common approach to diaphragm design is to consider the horizontal plane of the floor as a beam, and to calculate force and moment demands on joints based on their locations within that beam.
Since the building is assigned to SDC C, collector elements will be designed for 1.5 times the diaphragm force per Standard Section 12.10.3.4.
Notes: The load and reaction diagram from the example is shown to illustrate the support provides by the walls to a continuous beam. The uniform diaphragm loads vary by building segment because the transverse walls on the ends are included in the distributed weights, but the supporting walls in the center section are not included in the diaphragm load.

## Slide 30: Static Analysis of Diaphragms
Notes: The figure shows a cross section of a diaphragm with a total length of 152’-0”. The diaphragm has one 40’-0” long span on each end and three 24’-0” long spans in the middle. From left to right, spans are identified by gridlines A through F. Uniform gravity load W1 is applied from the top on side spans while middle three spans are subjected to uniform gravity load of magnitude W2. Upward reaction force of magnitude F is applied to the diaphragm from the bottom on gridlines B, C, D, and E.

## Slide 31: Static Analysis of Diaphragms
With a rigid diaphragm assumption, assuming the four shear walls have the same stiffness and ignoring torsion, the diaphragm reactions at the transverse shear walls (F as shown in figure on the previous slide) are computed as:
F = 347 kips/4 = 86.8 kips
Notes: Based on the assumption that the diaphragm in this example is rigid, the reaction forces on the four transverse walls are taken as equal. The slide shows the calculation of the uniform lateral force in each section of the building based on the diaphragm load for each section.

## Slide 32: Static Analysis of Diaphragms
The uniform diaphragm demands are proportional to the distributed weights of the diaphragm in different areas
W1 = [67 psf (72 ft) + 48 psf (8.67 ft)4](347 kips / 863 kips) = 2,610 lb/ft
W2 = [67 psf (72 ft)](347 kips / 863 kips) = 1,940 lb/ft
Notes: Based on the assumption that the diaphragm in this example is rigid, the reaction forces on the four transverse walls are taken as equal. The slide shows the calculation of the uniform lateral force in each section of the building based on the diaphragm load for each section.

## Slide 33: Static Analysis of Diaphragms
The joints in the floor plan for this example include
  Longitudinal joints between adjacent planks, located in the two orthogonal directions
  Transverse joints between the ends of planks, transverse joint between the ends of planks at masonry walls, end joints at masonry wall bearings
  Joints at the intersection of longitudinal and transverse planks at masonry walls and away from masonry walls
Notes: Based on the assumption that the diaphragm in this example is rigid, the reaction forces on the four transverse walls are taken as equal. The slide shows the calculation of the uniform lateral force in each section of the building based on the diaphragm load for each section.

## Slide 34: Static Analysis of Diaphragms
Force demands for loads crossing or within these joints include
  Chord forces
  Shear friction forces
  Integrity tie forces
Notes: Based on the assumption that the diaphragm in this example is rigid, the reaction forces on the four transverse walls are taken as equal. The slide shows the calculation of the uniform lateral force in each section of the building based on the diaphragm load for each section.

## Slide 35: Static Analysis of Diaphragms
ACI 318 does not recognize dowel behavior of reinforcing embedded in concrete nor friction in grouted joints without shear friction tension strength.
The steel requirements for friction transfer come only from shear friction calculations.
The shear transfer, however, is actually through the grout in the longitudinal joint.
Notes: Based on the assumption that the diaphragm in this example is rigid, the reaction forces on the four transverse walls are taken as equal. The slide shows the calculation of the uniform lateral force in each section of the building based on the diaphragm load for each section.

## Slide 36: Critical regions of the diaphragm to be considered in this design
Joint 1: Maximum transverse shear parallel to the panels at panel-to-panel joints
Joint 2: Maximum transverse shear parallel to the panels at the panel-to-wall joint
Joint 3: Maximum transverse moment and chord force
Joint 4: Maximum longitudinal shear perpendicular to the panels at the panel-to-wall connection (exterior longitudinal walls) and anchorage of exterior masonry wall to the diaphragm for out-of-plane forces
Joint 5: Collector element and shear for the interior longitudinal walls
Notes: The slide bullet points describe the five critical regions shown in the previous slide. These locations are used in the design example for the calculation of forces and to illustrate the reinforcing detailing.

## Slide 37: Critical regions of the diaphragm to be considered in this design
1
2
3
4
5
Notes: The plan view of the floor is repeated with the dimensions removed and the critical regions for design identified with the numbered circles and arrows for reference to detailed sections.

## Slide 38: Joint Forces
Joint 1 – Transverse forces:
  Shear, Vu1 = 2.61 kips/ft (36 ft) = 94 kips
  Moment, Mu1 = 94 kips (36 ft / 2) = 1692 ft-kips
  Chord tension, Tu1 = M/d = 1692 ft-kips / 71 ft = 23.8 kips
Joint 2 – Transverse forces:
  Shear, Vu2 = 2.61 kips/ft (40 ft) = 104.4 kips
  Moment, Mu2 = 104.4 kips (40 ft / 2) = 2088 ft-kips
  Chord tension, Tu2 = M/d = 2088 ft-kips / 71 ft = 29.4 kips
Notes: Calculations for joint forces at critical regions 1 and 2 are given. These calculations follow simple principles of statics.

## Slide 39: Joint Forces
Joint 3 – Transverse forces:
  Shear, Vu3 = 104.4 kips + 1.94 kips/ft (24 ft) – 86.8 kips = 64.2 kips
  Moment, Mu3 = 104.4 kips (44 ft) + 46.6 kips (12 ft) – 86.8 kips (24 ft) = 3070 ft-kips
  Chord tension, Tu3 = M/d = 3070 ft-kips / 71 ft = 43.2 kips
Joint 4 – Longitudinal forces:
  Wall force, F = 347 kips / 8 = 43.4 kips
  Wall shear along wall length, Vu4 = 43.4 kips (36 ft)/(152 ft / 2) = 20.6 kips
  Collector force at wall end, 1.5Tu4 = 1.5Cu4 = 1.5(43.4 kips – 20.6 kips) = 34.2 kips
Notes: Calculation for joint forces at critical regions 3 and 4 (longitudinal) are given.

## Slide 40: Joint Forces
Joint 4 – Out-of-Plane Forces:
  The Standard has several requirements for out-of-plane forces. None are unique to precast diaphragms and all are less than the requirements in ACI 318 for precast construction regardless of seismic considerations. Assuming the planks are similar to beams and comply with the minimum requirements of Standard Section 12.14 (Seismic Design Category B and greater), the required out-of-plane horizontal force is:
  0.05(D+L)plank = 0.05(67 psf + 40 psf)(24 ft / 2) = 64.2 plf
Notes: Calculation for joint forces at critical regions 3 and 4 (longitudinal) are given.

## Slide 41: Joint Forces
Joint 4 – Out-of-Plane Forces:
  According to Standard Section 12.11.2.1 (Seismic Design Category B and greater), structural wall anchorage must be designed for a force computed as::
  Fp = 0.4(SDS)(ka)(Ie)(Wwall)
  = 0.4(0.37)(1.0)(1.0) [(48 psf)(8.67 ft)] = 61.6 plf
  where
  ka = 1.0 + Lf/100 = 1.0 for rigid diaphragms
  From its geometry, this diaphragm is likely to be classified as rigid. However, the relative deformations of the wall and diaphragm must be checked in accordance with Standard Section 12.3.1.3 to validate this assumption.
Notes: Calculation for joint forces at critical regions 3 and 4 (longitudinal) are given.

## Slide 42: Joint Forces
Joint 5 – Longitudinal forces:
  Wall force, F = 347 kips / 8 = 43.4 kips
  Wall shear along each side of wall, Vu5 = 43.4 kips [2(36 ft) / 152 ft]/2 = 10.3 kips
  Design collector force at wall end, 1.5Tu5 = 1.5Cu5 = 1.5[43.4 kips - 2(10.3 kips)] = 34.2 kips
Joint 5 – Shear flow due to transverse forces:
  Shear at Joint 2, Vu2 = 104.4 kips
Q = A d: A = (0.67 ft) (24 ft) = 16 ft2 , d = 24 ft
Q = (16 ft2) (24 ft) = 384 ft3
I = (0.67 ft) (72 ft)3 / 12 = 20,840 ft4
Vu2Q/I = (104.4 kip) (384 ft3) / 20,840 ft4 = 1.923 kip/ft maximum shear flow
Joint 5 length = 40 ft
Total transverse shear in joint 5, Vu5 = 1.923 kip/ft) (40 ft)/2 = 38.5 kips
Notes: Force calculations for Joint 5 are shown for longitudinal and transverse forces. The transverse force effect is shear flow, calculated using VQ/I to determine the total joint force.

## Slide 43: Joint Forces
ACI 318 Section 16.2.1.8 also has minimum connection force requirements for structural integrity in accordance with 16.2.4 or 16.2.5.
ACI 318 Section 16.2.4.1 reads: “Except where the provisions of 16.2.5 govern, longitudinal and transverse integrity ties shall connect precast members to a lateral-force-resisting system, and vertical integrity ties shall be provided in accordance with 16.2.4.3 to connect adjacent floor and roof levels.”
ACI 318 Section 16.2.5 has the title “Integrity tie requirements for precast concrete bearing wall structures three stories or more in height.”
The structure being designed is a masonry bearing wall structure with precast concrete slabs acting as diaphragms; it is 5-stories tall. It has been decided to apply Section 16.2.5 requirements to the precast slabs, in which case, Sections 16.2.4.2 and 16.2.4.3 do not apply.
Notes: Force calculations for Joint 5 are shown for longitudinal and transverse forces. The transverse force effect is shear flow, calculated using VQ/I to determine the total joint force.

## Slide 44: Joint Forces
According to ACI 318 Section 16.2.5.1, the horizontal tie force requirements for a precast bearing wall structure three or more stories in height are:
  1500 plf parallel and perpendicular to the span of the floor members. The maximum spacing of ties parallel to the span is 10 feet. The maximum spacing of ties perpendicular to the span is the distance between supporting walls or beams.
  16 kips parallel to the perimeter of a floor or roof located within 4 feet of the edge at all edges.
Notes: Force calculations for Joint 5 are shown for longitudinal and transverse forces. The transverse force effect is shear flow, calculated using VQ/I to determine the total joint force.

## Slide 45: Diaphragm Design and Details
The phi factors used for this example are as follows:
  Tension control (bending and ties): f = 0.90
  Shear: f = 0.75
  Compression control in tied members: f = 0.65
Notes: Force calculations for Joint 5 are shown for longitudinal and transverse forces. The transverse force effect is shear flow, calculated using VQ/I to determine the total joint force.

## Slide 46: Diaphragm Design and Details
The required shear strength on the diaphragm is amplified by a factor of 1.4Rs = 1.4×1.0 = 1.4, as required by Standard Section 14.2.4.1.3.
The minimum tie force requirements given in ACI 318 Section 16.2.5 are specified as nominal values, meaning that f = 1.00 for those forces.
Notes: Force calculations for Joint 5 are shown for longitudinal and transverse forces. The transverse force effect is shear flow, calculated using VQ/I to determine the total joint force.

## Slide 47: Diaphragm Design and Details – Joint 1
Anchorage region for shear reinforcement
Interior Joint
Notes: Figures from the example that illustrate the placement of reinforcement are provided in this slide. At the interior joint, two horizontal bars are place in the grouted joint between the ends of plank and parallel with the support beam. In the second figure, the flange of the plank is broken at he edge to open the edge core and permit placement of #7 bars and grout in the core, filling the profile and joint to the finished floor.

## Slide 48: Diaphragm Design and Details – Joint 2
Using the arrangement shown in the figure below
Notes: Detail at Joint 2 is shown to show the placement of reinforcing in the masonry wall an in an opened core of the hollow core plank. Note the detail shows diagonal bars to transfer forces mostly in tension and compression rather than by dowel shear or shear friction. The block just below the bearing in the masonry wall is a bond beam with two #5 bars grouted in as part of the diaphragm reinforcement.

## Slide 49: Diaphragm Design and Details – Joint 3
Notes: The figure shows a cross section of an 8” thick hollow core panel. The first three cores from the left edge are shown where the first core is filled with concrete to shape a chord joint. The joint is reinforced with two continuous No. 6 bars extending in the perpendicular to the plane direction. The bars have 3” cover on the left, 3” cover on the top, 3” cover on the bottom, and 3” spacing in the longitudinal direction. Spliced bars are shown with dash circles in contact with the main bars. 4” diameter spiral of ¼” wire with 2” pitch is enclosing the bars and may be required over the lap splice.

## Slide 50: Diaphragm Design and Details – Joint 4
Notes: Detail at Joint 4 is shown to illustrate the placement of reinforcing at the end of plank and in the masonry walls for a “dry” system. The top flange in the end of the hollow core plank is broken way to permit access to the cores so that the cores at the end of the plank, the bearing space in the wall beyond the plank, and the bond beam below the bearing of the plank can be reinforced and grouted.

## Slide 51: Diaphragm Design and Details – Joint 5
Notes: The figure shows a cross section of a panel-to-wall joint. Hollow core panels are extending in the longitudinal direction on both sides of the wall and meet at a 4” long joint. The joint is reinforced by:
Two No. 7 continuous collector bars located in the joint adjacent to the wall’s vertical bar and extended in the perpendicular to the plane direction.
One 4’-8” long longitudinal No. 4 bar located between the two collector bars and grouted into each key joint with equal extensions on both sides of the joint.
Two No. 5 continuous bars located in the masonry bond beam at the top of the wall below the joint and extended in the perpendicular to the plane direction.

## Slide 52: Topped Precast Concrete Diaphragm for Five-Story Masonry Building Assigned to SDC D

## Slide 53: Topped Diaphragm Design Parameters
Notes: First slide to introduce the design of untopped precast diaphragms using hollow core floor plank. The design is linked to the Chapter 10 masonry wall example for SDC B using Birmingham., Alabama. The use of seismic acceleration parameters for New York for SDC C differs from Chapter 10.

## Slide 54: Diaphragm Design Forces
Table 11.1-5 Fpx Calculations for SDC C |  |  |  |  | 
Level | hx (ft) | Cpx | wpx (kips) | Fpx (kips) | Fpx,min (kips)
Roof | 43.34 | 1094 | 0.91 | 708 | 218.80
4 | 34.67 | 1158 | 0.63 | 521 | 231.60
3 | 26.00 | 1158 | 0.57 | 474 | 231.60
2 | 17.33 | 1158 | 0.51 | 426 | 231.60
1 | 8.67 | 1158 | 0.46 | 378 | 231.60
1.0 kip = 4.45 kN. |  |  |  |  | 
Step 3: Determine Fpx, Diaphragm Design Force at Level x
Notes: Equation 12.10-1 for the calculation of diaphragm design forces is provided in this slide. Note that this equation is different from the equation for the vertical distribution of base shear used for the design of the lateral force-resisting system. That distribution must also be considered in the design of the diaphragm

## Slide 55: Critical regions of the diaphragm to be considered in this design
1
2
3
4
5
Notes: The plan view of the floor is repeated with the dimensions removed and the critical regions for design identified with the numbered circles and arrows for reference to detailed sections.

## Slide 56: Joint Forces
Joint 1 – Transverse forces:
  Shear, Vu1 = 94 kips x 2.0 = 188 kips
  Moment, Mu1 = 1692 ft-kips x 2.0 = 3384 ft-kips
  Chord tension, Tu1 = M/d = 3384 ft-kips / 71 ft = 47.7 kips
Joint 2 – Transverse forces:
  Shear, Vu2 = 104.4 kips x 2.0 = 208.8 kips
  Moment, Mu2 = 2088 ft-kips x 2.0 = 4176 ft-kips
  Chord tension, Tu2 = M/d = 4176 ft-kips / 71 ft = 58.8 kips
Notes: Calculations for joint forces at critical regions 1 and 2 are given. These calculations follow simple principles of statics.

## Slide 57: Joint Forces
Joint 3 – Transverse forces:
  Shear, Vu3 = 64.2 kips x 2.0 = 128.4 kips
  Moment, Mu3 = 3070 ft-kips x 2.0 = 6140 ft-kips
  Chord tension, Tu3 = M/d = 6140 ft-kips / 71 ft = 86.5 kips
Joint 4 – Longitudinal forces:
  Wall force, F = 43.4 kips x 2.0 = 86.8 kips
  Wall shear along wall length, Vu4 = 20.6 kips x 2.0 = 41.2 kips
  Collector force at wall end, 1.5Tu4 = 34.2 kips x 2.0 = 68.4 kips
Notes: Calculation for joint forces at critical regions 3 and 4 (longitudinal) are given.

## Slide 58: Joint Forces
Joint 4 – Out-of-Plane Forces:
  The Standard has several requirements for out-of-plane forces. None are unique to precast diaphragms and all are less than the requirements in ACI 318 for precast construction regardless of seismic considerations. Assuming the planks are similar to beams and comply with the minimum requirements of Standard Section 12.14 (Seismic Design Category B and greater), the required out-of-plane horizontal force is:
  0.05(D+L)plank = 0.05(67 psf + 40 psf)(24 ft / 2) = 64.2 plf
Notes: Calculation for joint forces at critical regions 3 and 4 (longitudinal) are given.

## Slide 59: Joint Forces
Joint 4 – Out-of-Plane Forces:
  According to Standard Section 12.11.2.1 (Seismic Design Category B and greater), structural wall anchorage must be designed for a force computed as:
  Fp = 0.4(SDS)(ka)(Ie)(Wwall)
  = 0.4(1.0)(1.0)(1.0) [(60 psf)(8.67 ft)] = 208 plf
  where
  ka = 1.0 + Lf/100 = 1.0 for rigid diaphragms
  From its geometry, this diaphragm is likely to be classified as rigid. However, the relative deformations of the wall and diaphragm must be checked in accordance with Standard Section 12.3.1.3 to validate this assumption.
Notes: Calculation for joint forces at critical regions 3 and 4 (longitudinal) are given.

## Slide 60: Joint Forces
Joint 5 – Longitudinal forces:
  Wall force, F = 708 kips / 8 walls = 88.5 kips
  Wall shear along each side of wall, Vu5 = 10.3 kips x 2.0 = 20.6 kips
  Design collector force at wall end, 1.5Tu5 = 34.2 kips x 2.0 = 68.4 kips
Joint 5 – Shear flow due to transverse forces:
  Shear at Joint 2, Vu2 = 208.8 kips
Q = A d: A = (0.67 ft) (24 ft) = 16 ft2 , d = 24 ft
Q = (16 ft2) (24 ft) = 384 ft3
I = (0.67 ft) (72 ft)3 / 12 = 20,840 ft4
Vu2Q/I = (208.8 kip) (384 ft3) / 20,840 ft4 = 3.85 kip/ft maximum shear flow
Joint 5 length = 40 ft
Total transverse shear in joint 5, Vu5 = 3.85 kip/ft) (40 ft)/2 = 77 kips
Notes: Force calculations for Joint 5 are shown for longitudinal and transverse forces. The transverse force effect is shear flow, calculated using VQ/I to determine the total joint force.

## Slide 61: Topped Precast Concrete Diaphragm for Five-Story Masonry Building
Notes: The floor plan showing walls and the diaphragm layout is shown for the SDC D example. This is the same building layout used in the earlier examples but the joints between the hollow core plank in the interior areas of the floor have been removed. This reflects the presence of cast-in-place concrete topping with welded wire reinforcement to carry diaphragm forces, so the location of these interior joints is not a design consideration.

## Slide 62: Boundary Members
Notes: The figure shows a cross section of a topped hollow core panel. The first three cores from the left edge are shown where the first core is filled with concrete to shape a chord joint. The joint is reinforced with two continuous No. 8 bars extending in the perpendicular to the plane direction. The bars have 3.5” cover on the left, 2.5” cover on the right, 3” cover on the top, and 3” spacing. Spliced bars are shown with dash circles in contact with the main bars. 4” diameter spiral of ¼” wire with 2” pitch is enclosing the bars over the lap splice. The 2.5” topping is reinforced with WWF bend down into the chord at the edge.

## Slide 63: Collectors – Joint 5
Notes: The figure shows a cross section of an interior panel-to-panel joint. Two longitudinal 8” thick hollow core panels with 2” topping meet at a 3” long joint which is supported by an I-shaped section. The joint is reinforced by two No. 8 collector bars extending in the perpendicular to the plane direction. The bars have 2.5” cover on the top (below the topping), 2.5” cover on the bottom and 3” spacing in between. The topping is reinforced with WWF.

## Slide 64: Shear Resistance – Interior Longitudinal Wall
Notes: The figure shows a cross section of a panel-to-wall joint. Topped hollow core panels are extending in the longitudinal direction on both sides of the wall and meet at a 4” long joint. The topping is reinforced with WWF 10x10 W8 x W8. The joint is reinforced by:
Two No. 8 continuous collector bars located in the joint adjacent to the wall’s vertical bar and extended in the perpendicular to the plane direction.
One 4’-0” long longitudinal No. 4 bar with equal extensions on both sides of the joint located in the topping and lapped with WWF.
Two No. 5 continuous bars located in the masonry bond beam at the top of the wall below the joint and extended in the perpendicular to the plane direction.

## Slide 65: Joint 4 Reinforcement Detail
Notes: The figure shows a cross section of a panel-to-perimeter-wall joint. Topped hollow core panel extending in the longitudinal direction meets the wall from the right. The topping is reinforced with WWF 10x10 W8 x W8. The joint is reinforced by:
One 2’-6” long No. 5 bar with standard hooks at 4’-0” spacing located in the topping, lapped with WWF, and bend into the joint with 2” clear cover from the inner face of the wall.
Two No. 8 continuous collector bars located in the joint adjacent to the wall’s vertical bar and extended in the perpendicular to the plane direction.
Two No. 5 continuous bars located in the masonry bond beam at the top of the wall below the joint and extended in the perpendicular to the plane direction.

## Slide 66: Three-Story Office Building with Intermediate Precast Concrete Shear Walls

## Slide 67: Three-Story Office Building with Intermediate Precast Concrete Shear Walls
Notes: The figure slide shows the plan of the building. The plan is 150 ft long and 120 ft long with interior stairs and interior elevator cores.
Design example for intermediate precast walls in three-story office in Seismic Design Category B. These walls can be used up to any height in Seismic Design Categories B and C but are limited to 40 feet for Seismic Design Categories D, E, and F.
ACI 318 Section 21.4.2 requires that yielding between wall panels or between wall panels and the foundation be restricted to steel elements. However, the Provisions are more specific in their means to accomplish the objective of providing reliable post-elastic performance. Provisions Section 21.4.3 (ACI 318 Sec. 21.4.4) requires that connections that are designed to yield be capable of maintaining 80 percent of their design strength at the deformation induced by the design displacement. Alternatively, they can use Type 2 mechanical splices.
This precast concrete building is a three-story office building (Occupancy Category II) in southern New England on Site Class D soils. The structure utilizes 10-foot-wide by 18-inch-deep prestressed double tees (DTs) spanning 40 feet to prestressed inverted tee beams for the floors and the roof. The DTs are to be constructed using lightweight concrete. Each of the above-grade floors and the roof are covered with a 2‑inch-thick (minimum), normal-weight cast-in-place concrete topping. The vertical seismic force-resisting system is to be constructed entirely of precast concrete walls located around the stairs and elevator/mechanical shafts. The only features illustrated in this example are the rational selection of the seismic design parameters and the design of the reinforcement and connections of the precast concrete shear walls.

## Slide 68: Three-Story Office Building with Intermediate Precast Concrete Shear Walls
Table 11.2-1 Design Parameters | 
Design Parameter | Value
Risk Category | II
Importance Factor, Ie | 1.0
SS | 0.266
S1 | 0.08
Site Class | D
Fa | 1.59
Fv | 2.4
SMS = FaSS | 0.425
SM1 = FvS1 | 0.192
Seismic Parameters
Notes: The precast walls are estimated to be 8 inches thick for building mass calculations. These walls are normal-weight concrete with a 28-day compressive strength, f'c, of 5,000 psi. Reinforcing bars used at the ends of the walls and in welded connectors are ASTM A706 (60 ksi yield strength). The concrete for the foundations and below-grade walls has a 28-day compressive strength, f'c, of 4,000 psi.
Design example for intermediate precast walls in three-story office. Slide shows the seismic parameters from the Table in the example.

## Slide 69: Three-Story Office Building with Intermediate Precast Concrete Shear Walls
Table 11.2-1 Design Parameters | 
Design Parameter | Value
SDS = 2/3 SMS | 0.283
SD1 = 2/3 SM1 | 0.128
Seismic Design Category | B
Basic Seismic Force-Resisting System | Bearing Wall System
Wall Type | Intermediate Precast Shear Walls
R | 4
Ω0 | 2.5
Cd | 4
Seismic Parameters
Notes: The precast walls are estimated to be 8 inches thick for building mass calculations. These walls are normal-weight concrete with a 28-day compressive strength, f'c, of 5,000 psi. Reinforcing bars used at the ends of the walls and in welded connectors are ASTM A706 (60 ksi yield strength). The concrete for the foundations and below-grade walls has a 28-day compressive strength, f'c, of 4,000 psi.
Design example for intermediate precast walls in three-story office. Slide shows the seismic parameters from the Table in the example.

## Slide 70: Forces on the longitudinal walls
Notes: Vertical distribution of base shear is shown in the example calculations for the entire structure.
The seismic lateral force ,Fx, at any level is determined in accordance with Standard Section 12.8.3.
Since the period, T, is less than 0.5 seconds, k = l in both building directions. The total lateral forces are calculated as:
Roof: Cvr = 0.50; Fr = 190 kips
Third Floor: Cv3 = 0.333; F3 = 127 kips
Second Floor: Cv2 = 0.167; F2 = 63 kips
Since torsion is assumed to be carried by the walls in the transverse direction, the forces to each of two walls (as shown in the slide) in the direction under consideration is half the total, and these are the forces illustrated in the figure.

## Slide 71: Overturning Moment on Longitudinal Walls
ME = (95 kips)(36 ft) + (63.5 kips)(24 ft) + (31.5 kips)(12 ft) = 5,320 ft-kips
Notes: The figure shows the free-body diagram for one longitudinal wall. The tension connection at the base of the precast panel to the below-grade wall is governed by the seismic overturning moment and the dead loads of the panel and supported floors and roof. In this example, the weights for an elevator penthouse, with a floor and equipment load at 180 psf between the shafts and a roof load at 20 psf, are included. The weight for the floors includes double tees, ceiling, and partitions (total load of 70 psf) but not beams and columns. Floor live load is 50 psf, except 100 psf is used in the elevator lobby. Roof snow load is 30 psf.

## Slide 72: End Reinforcement
Notes: Figure on the left shows an along-the-height cross section of an 8” thick precast longitudinal shear wall. The wall is reinforced by two No. 9 full height vertical bars at each end. Direct tension coupler is used to transfer the force in the bars wherever required. Figure on the right shows a cross section of the base of a precast shear wall supported by a 28” thick reinforced concrete foundation. Dowels with standard hook are used to develop overturning reinforcement with a 3” minimum clear cover from the bottom of the foundation.

## Slide 73: Shear Connection Detail
Notes: The figure illustrates a welded connection with an embedded plate with tail bars developed in the wall and a foundation plate anchored with headed anchor studs. The connection is made with two face plates, one on each side of the wall.
The base shear connection is shown in the figure and is to be flexible vertically but stiff horizontally in the plane of the panel. The vertical flexibility is intended to minimize the contribution of these connections to overturning resistance, which would simply increase the shear demand.

## Slide 74: One-Story Precast Shear Wall Building

## Slide 75: One-Story Precast Shear Wall Building
This example illustrates the design of a precast concrete shear wall for a single-story building assigned to a high seismic design category.
The precast concrete building is a single-story industrial warehouse building (Risk Category II) on Site Class C soils.
The precast wall panels used in this building are typical DT wall panels.
Walls are designed using intermediate precast structural walls.
Notes: The design example is for a single story building with perimeter shear wall panels. This example shows the design for intermediate precast concrete walls in SDC D.
The structure has 8-foot-wide by 12.5-inch-deep prestressed double tee (DT) wall panels. The roof is light gage metal decking spanning to bar joists that are spaced at 4 feet on center to match the location of the DT legs. The center supports for the joists are joist girders spanning 40 feet to steel tube columns. The vertical seismic force-resisting system is the precast/prestressed DT wall panels located around the perimeter of the building. The average roof height is 20 feet, and there is a 3-foot parapet.
The slide describes the precast building.

## Slide 76: One-Story Precast Shear Wall Building
Notes: The figure shows a plan of the building. The building is 120 ft long and 96 ft wide.
The precast wall panels used in this building are typical DT wall panels commonly found in many locations but not normally used in southern California. For these wall panels, an extra 1/2 inch has been added to the thickness of the deck (flange). This extra thickness is intended to reduce cracking of the flanges and provide cover for the bars used in the deck at the base.
The wall panels are normal-weight concrete with a 28-day compressive strength of f'c = 5,000 psi. Reinforcing bars used in the welded connections of the panels and footings are ASTM A706 (60 ksi). The concrete for the foundations has a 28-day compressive strength of f'c = 4,000 psi.

## Slide 77: Special Moment Frame Constructed Using Precast Concrete

## Slide 78: Special Moment Frame Constructed Using Precast Concrete
As for special moment frames of concrete, the Standard does not distinguish between a cast-in-place and a precast concrete special moment frame in Table 12.2-1.
ACI 318 Section 18.9 provides requirements for special moment frames constructed using precast concrete.
That section provides requirements for designing special precast concrete frame systems using either ductile connections (ACI 318 Sec. 18.9.2.1) or strong connections (ACI 318 Sec. 18.9.2.2).
Notes: Introduction to review of special moment frames constructed using precast concrete construction. This method is considered “emulation” of monolithic cast-in-place concrete.

## Slide 79: Examples for Seismic Design of Precast Concrete
Diaphragms in moderate and high seismic design categories
Intermediate precast concrete shear walls in moderate and high seismic design categories
Special moment frames constructed using precast concrete with emulation details
Notes: This is a slide provided as a summary of the examples covered in the presentation.

## Slide 80: Questions
Notes: This slide is a placeholder for opening the floor up to questions

## Slide 81: DISCLAIMER
NOTICE: Any opinions, findings, conclusions, or recommendations expressed in this publication do not necessarily reflect the views of the Federal Emergency Management Agency. Additionally, neither FEMA nor any of its employees make any warranty, expressed or implied, nor assume any legal liability or responsibility for the accuracy, completeness, or usefulness of any information, product or process included in this publication.
The opinions expressed herein regarding the requirements of the NEHRP Recommended Seismic Provisions, the referenced standards, and the building codes are not to be used for design purposes. Rather the user should consult the jurisdiction’s building official who has the authority to render interpretation of the code.
Any modifications made to the file represent the presenters' opinion only.